CSPCWG3-9.1.2A

3rd CSPCWG MEETING

Monaco, 22-24 November 2006

## Paper for Consideration by CSPCWG

## Draft specifications for Reporting Line

| Submitted by: | UK |
| --- | --- |
| Executive Summary: | CSPCWG2 approved a new symbol for a reporting line. This was subsequently endorsed by IHO Member States. |
| Related Documents: | CSPCWG2 record. IHO CLs 30 & 48/2006 |
| Related Projects: | On-going revision of M-4 |

## Introduction / Background

Extract from CSPCWG2 record:

8.5 VTS and Reporting Areas (FI)

Finland presented their proposal for a new symbol for a Reporting Line, explaining the need to differentiate reporting lines from reporting points and VTS areas.

The WG agreed that existing symbols should be combined to form the appropriate limits as necessary, so that a VTS area limit would be a magenta general maritime limit (N1.2) with upright legend (eg VTS Helsinki). A reporting limit would usually include the general maritime limit (N1.2) with small versions of the reporting point symbol (M40) positioned at intervals perpendicular to the line.  The actual limit symbol may be varied if it coincides with another area (eg Territorial Waters, PSSA).  An example should be included in INT 1, when approved by Member States.  This would be the same as the German national symbol currently shown as Mg and should be numbered M40.2. (M40 to be renumbered M40.1). Specifications should be included at M-4 B-488.1.

A CSPCWG Letter would be required to outline the proposal to the full WG for approval in the first instance.  TSMAD and C&SMWG should be given opportunity to comment.

ACTION 17:  Germany to supply dimensions of reporting line symbol to Secretary

ACTION 18:  Secretary to draft CSPCWG Letter outlining Reporting line proposals (to include explanations of VTS, reporting points, areas), for consideration by full WG, TSMAD and C&SMWG.

## Recommendations

  - The new symbol was approved by IHO Member States following consultation by IHO CL 30/2006. Confirmation was given by IHO CL 48/2006. The symbol will be added to INT 1 as described in due course.

  - There remains a need to include a specification for the new symbol (as it has been agreed that all INT symbols should have related entries in M-4). The CSPCWG Secretary has therefore drafted a specification below, to be located in M-4 as stated in Annex B to IHO CL 30/2006.

B-488.1		Radio reporting line. Where vessels are required to report on crossing a defined line, the line must normally be charted by a dashed magenta line (general maritime limit of non-restricted area - N1.2), with small reporting point symbols superimposed across the line:

Insert symbol 	M40.2

Circle radius 1.85mm, triangle base 1.15mm, height 1.50mm. Symbols should be inserted at approximately 40mm intervals.

If the reporting line coincides with another limit (eg Territorial Waters, PSSA), the symbols should be superimposed on that limit.

  - Note:  actual symbols will be generated in accordance with the agreed specifications and included in M-4 when opportunity allows.

## Action Required of CSPCWG

  - The CSPCWG is invited to discuss and endorse the draft specifications.