## Slide 1: Re-scheming Plan NOAA's Electronic Navigational Chart Coverage
Megan Bartlett
Office of Coast Survey
ENCWG3
Contact info: Megan.Bartlett@noaa.gov

## Slide 2: Motivation
Too many alarms on caution areas
•Need more detailed depth areas in key locations
•Need accurate least depths on wrecks and obstructions-we are training our users to ignore the magenta Xs.
•ENCs are not standalone products-they are components of a seamless suite. There are too many discontinuities.
•Symbology is not good for recreational mariners
Feedback from the Mariners on the ENC:

## Slide 3: In addition – ECDIS manufacturers (ECDIS - Electronic Chart Display and Information System)
Vector database of chart features
Built to IHO’s S-57 standard
Displays ENC’s and integrates a variety of real-time information
Meets IHO regulations and is an alternative to paper charts

## Slide 4: Current US ENC coverage
Norfolk
New York

## Slide 5: Current ENC footprints
Legacy data from raster charts (131 RNC scales and 120 ENC scales)
ENC limits copied directly from raster chart boundaries
Easy interim solution
Ex: The English channel/ UKHO & SHOM

## Slide 6: Legacy data issues
Too many scales
Scales don’t conform to IHO (S-57 & S-101) recommended scales
Duplication of coverage
Lacking uniformity, consistency, and coherence
  Not a smooth transition from scale to scale while navigating on ECDIS systems

## Slide 7
Standards are common grounds for argument!

## Slide 8: Vision for the future: Nautical Charting Plan

## Slide 9: Rescheming

## Slide 10
Based on RADAR range
Not compatible for web-services
Requires “re-scaling” current features that are not with ~10% of the proposed scales.

## Slide 11
Scale band | Standard Scale (rounded)
Band 1 | 1:5,120,000
 | 1:2,560,000
Band 2 | 1:1,280,000
 | 1:640,000
Band 3 | 1:320,000
 | 1:160,000
Band 4 | 1:80,000
 | 1:40,000
Band 5 | 1:20,000
 | 1:10,000

## Slide 12: Calculating ENC cell width and height
Scale band | Standard Scale (rounded) | Width | Height
Band 1 | 1:5,120,000 | 38.4 | 38.4
 | 1:2,560,000 | 19.2 | 19.2
Band 2 | 1:1,280,000 | 9.6 | 9.6
 | 1:640,000 | 4.8 | 4.8
Band 3 | 1:320,000 | 2.4 | 2.4
 | 1:160,000 | 1.2 | 1.2
Band 4 | 1:80,000 | 0.6 | 0.6
 | 1:40,000 | 0.3 | 0.3
Band 5 | 1:20,000 | 0.15 | 0.15
 | 1:10,000 | 0.075 | 0.075

## Slide 13: Fishnet tool:

## Slide 14: New York
Current ENC coverage
Future ENC re-scheme coverage

## Slide 15: Great Lakes
Current ENC coverage
Future ENC re-scheme coverage

## Slide 16: Re-scheming at high latitudes
80k
Band 4

## Slide 17: Discussion
Benefits of re-scheming
Meeting more international standards (IHO S-4):
  Depth Contours
Feature as a function of scale
Polar charting
“Rasterization” of the ENC

## Slide 18: Benefits of re-scheming
Smooth transition from scale to scale while navigating
Smooth transition from old to new ENC compilation
Simplified naming convention
Splitting in 4 in case of too much data in one cell
Ease of planning for extending coverage

## Slide 19
BEFORE

## Slide 20
AFTER

## Slide 21
In to the weeds (See the next slides)

## Slide 22
Scale
Coverage: Band 5

## Slide 23
Scale
Coverage: Band 4

## Slide 24
Scale
Coverage: Band 3

## Slide 25
Scale
Coverage: Band 2

## Slide 26: Naming convention:
US 5 SEA EK
Production code
Cell Location
Geographic location
Usage band
Note: We will make sure that a similar name exists in the current ENC suite (especially, cells that end with “M”).

## Slide 27: Naming convention: Production code and usage band
The first two characters in the ENC cell name are the production code (IHO S-62). In the case of NOAA (“US”).
The first digit after “US” is the scale band (usage band).

## Slide 28: Naming convention: Principle ports versus standard state coverage
Standard State coverage - In the re-scheming plan, naming convention will utilize the fourth and fifth characters represent the U.S. state, and sixth character represents a zone within the state.
Principle Ports - In order to differentiate the US Principle Ports from the rest of the re-schemed ENC cells at the same scale band, a three-character port identifier is obtained from the UN/LOCODE Code List 2017-1 for each country (current version was published in July 2017): http://www.unece.org/cefact/locode/service/location.html.

## Slide 29
Naming convention
NYC
PHL
PSM
BOS
PVD
NY1
NY2
CT1
BDR
HVN
PTJ
NY3
RI1
CT1
MA1
MA1
MA1
MA1
NH1
ME1
NJ1
PSM – Portsmouth, NH
BOS – Boston, MA
PVD – Providence, RI
HVN – New Haven, CT
BDR – Bridgeport, CT
PTJ – Port Jefferson, NY
NYC – New York City, NY
PHL – Philadelphia, PA

## Slide 30: Naming convention: Cell location
The last two characters (i.e., seventh and eighth) are the cell location with respect to a given reference. The southwestern corner of the ENC cell grid is the center of origin (“AA”), where the seventh character represents distance from the center of origin in latitude and the eighth character represents distance from the center of origin in longitude.
AA
AB
AC
BA
CA
AX
AY
AZ
…

## Slide 31: Naming convention: Summary
US 5 SEA EK
Production code
Cell Location
Geographic location
Usage band
Note: We will make sure that a similar name exists in the current ENC suite (especially, cells that end with “M”).

## Slide 32
Although most features at similar scale can be copied, bathymetry will need to be recompiled!
Depth (m)

## Slide 33: Recommended depth contours per scale band
Scale band | Standard Scale (rounded) | Width | Height | 
Band 1 | 1:5,120,000 | 38.4 | 38.4 | 100, 200,…
 | 1:2,560,000 | 19.2 | 19.2 | 50,100,150,200,…
Band 2 | 1:1,280,000 | 9.6 | 9.6 | 50,100,150,200,…
 | 1:640,000 | 4.8 | 4.8 | 20 ,50,100,150,200,…
Band 3 | 1:320,000 | 2.4 | 2.4 | 20,30,50,100,150,200,…
 | 1:160,000 | 1.2 | 1.2 | 10, ,20,30,50,100,150,200,…
Band 4 | 1:80,000 | 0.6 | 0.6 | 5, 10, ,20,30,50,100,150,200,…
 | 1:40,000 | 0.3 | 0.3 | 2, 5, 10, ,20,30,50,100,150,200,…
Band 5 | 1:20,000 | 0.15 | 0.15 | 2, 5, 8,10,15,20,30,50,100,150,200,…
 | 1:10,000 | 0.075 | 0.075 | 2,3,4,5,6,7,8,10,15,20,30,50,100,150,200,…
IHO S-4 (B-411)

## Slide 34: Recommended feature per scale band
Scale band | Standard Scale (rounded) | Width | Height | 
Band 1 | 1:5,120,000 | 38.4 | 38.4 | 
 | 1:2,560,000 | 19.2 | 19.2 | 
Band 2 | 1:1,280,000 | 9.6 | 9.6 | 
 | 1:640,000 | 4.8 | 4.8 | 
Band 3 | 1:320,000 | 2.4 | 2.4 | 
 | 1:160,000 | 1.2 | 1.2 | 
Band 4 | 1:80,000 | 0.6 | 0.6 | 
 | 1:40,000 | 0.3 | 0.3 | 
Band 5 | 1:20,000 | 0.15 | 0.15 | 
 | 1:10,000 | 0.075 | 0.075 | 
Hydro
S.L.
MPA
Traffic
Lanes
Lights
Buoys
air-gaps
Topo
Channels