## Slide 1: Maritime Resource Names (MRN) concept S-100 WG TSM5 19-21 September 2017
Raphael Malyankar, Consultant, Portolan Sciences
Eivind Mong, Consultant
Work performed under NOAA sponsorship

## Slide 2: MRN is a naming scheme
Based on the Uniform Resource Name (URN) concept
MRN specification is submitted to The Internet Engineering Task Force (IETF.org) and thus registered
Uniquely identifies any maritime resource on a global scale
Can be used for organizations, employees, a person, a physical or a virtual object (e.g., electronic document), a buoy, a ship, a mariner, a nautical chart or an electronic service

## Slide 3: How the MRN concept works
The MRN namespace is administered by IALA through the website http://mrnregistry.org
The topmost namespace urn:mrn remains fixed
Subsequent name spaces separated by colons
Organizations wishing to issue MRN conformant identifiers apply for a name space from IALA, or from an organization that already has a namespace registered
MRN does not currently define a resolution or limit length of the identifier
Notes: For example, IHO applies for a name space, and subsequently gives all producing agencies a sub name space under the urn:mrn:iho name space; for NOAA this could be urn:mrn:iho:us and for CHS this could be urn:mrn:iho:ca. NOAA and CHS would then administer their respective name spaces as needed and within the MRN rules.

## Slide 4: Rules that apply to MRN name spaces
The Namespace Specific String (NSS) of all URNs that use the "mrn" NID shall have the following structure:
<URN> ::= "urn:mrn:" <OID> ":" <OSS>
<OID> ::= 1*(ALPHA / DIGIT) ; Organizational ID; iho
<OSS> ::= <OSNID> ":" <OSNS> ; Organizational specific string
<OSNID> ::= 1*(ALPHA / DIGIT / "-") ; Organizational specific namespace ID
<OSNS> ::= 1*<URN chars> ; Organizational specific namespace string
Character set used
DIGIT ::= %x30-39 ; 0-9
ALPHA ::= %x61-7A ; a-z
The entire URN is case-insensitive.
Example 1, an identifier for IHO special publications; urn:mrn:iho:pub:s100
Example 2; an identifier for a feature urn:mrn:iho:us:5502201778050

## Slide 5: Use MRN in S-100 for persistent unique identifiers
MRN is an organized and structured identifier concept that is currently utilized in various e-Navigation projects, including Efficiensea2, STM Validation and SMART Navigation
Catalogue items in feature catalogues - feature types, information types, associations, and roles in feature catalogues; e.g., urn:iho:def:s101:1.1::LandArea to mean the LandArea feature in the feature catalogue for revision 1.1 of S:101 (in any clarification of version 1.1).
S-100 based product specifications (e.g., urn:mrn:iho:prd:s101:N:N:N or urn:mrn:iho:prd:s101:N.N:N to identify a specific version of S-101). We recommend that the structure be such that it is possible to use wildcards for clarifications at least (meaning, the clarification number at least should be a separate component which can be ‘wild-carded’ using the ‘::’ construct).

## Slide 6: Implementation considerations
XML syntax rules do not allow the ‘:’ character in certain items such as attributes of the built-in XML type ID, and that when used in XML tags the ‘:’ character is a namespace separator. This means that MRNs cannot be used as the value of any attribute of type ID (in particular, they cannot be used as the values of gml:id attributes, which are mandatory in the GML specification), nor can they be used in XML tags.
Data formats may benefit from devising compact representations that do not require encoding of the same prefix string e.g., “urn:mrn:iho:cc:” in every single feature or information type with a unique identifier. This part of the identifier could be added to metadata.

## Slide 7: Implementation considerations
IHO should develop a management process for the urn:mrn:iho name space, including draft sub name management policy that member states and other organizations with name space under the urn:mrn:iho name space can use as a starting point for their name space management policy.