TSMAD28_DCEG1A – Directional Lights Model

## Light directional

| IHO Definition: DIRECTIONAL LIGHT. A light is a luminous or lighted aid to navigation. (IHO Dictionary – S-32). A directional light is a light illuminating a sector of very narrow angle and intended to mark a direction to follow. (IHO Dictionary – S-32). |
| --- |
| S-101 Geo Feature: Light directional (LIGHTS) |
| Primitives: Point |
| Real World | Paper Chart Symbol | ECDIS Symbol |
| S-101 Attribute | S-57 Acronym | Allowable Encoding Value | Type | Multiplicity |
| Exhibition condition of light | (EXCLIT) | 1 : light shown without change of character 2 : daytime light 3 : fog light 4 : night light | EN | 0,1 |
| Feature name |  |  | C | 0,* (ordered) |
| Category of name |  | 1 : official name 2 : alternate name 3 : common name 4 : short name 5 : display name | (S) EN | 0,1 |
| Display name |  |  | (S) BO | 0,1 |
| Language |  | ISO 639-3 | (S) TE | 0,1 |
| Name | (OBJNAM) (NOBJNM) |  | (S) TE | 1,1 |
| Fixed date range |  |  | C | 0,1 |
| Date end | (DATEND) | ISO 8601: 2004 | (S) DA | 0,1 |
| Date start | (DATSTA) | ISO 8601: 2004 | (S) DA | 0,1 |
| Height | (HEIGHT) |  | RE | 0,1 |
| Marks navigational – system of | (MARSYS) | 1 : IALA A 2 : IALA B 9 : no system 10 : other system 11 : CEVNI | EN | 0,1 |
| Moiré effect |  |  | BO | 0,1 |
| Multiplicity of features |  |  | C | 0,1 |
| Multiplicity known |  |  | (S) BO | 1,1 |
| Number of features | (MLTYLT) |  | (S) IN | 0,1 |
| Orientation |  |  | C | 1,1 |
| Orientation uncertainty |  |  | (S) RE | 0,1 |
| Orientation value | (ORIENT) |  | (S) RE | 1,1 |
| Periodic date range |  |  | C | 0,* |
| Date end | (PEREND) | ISO 8601: 2004 | (S) DA | 1,1 |
| Date start | (PERSTA) | ISO 8601: 2004 | (S) DA | 1,1 |
| Rhythm of light |  |  | C | 1,* |
| Light characteristic | (LITCHR) | 1 : fixed 2 : flashing 3 : long-flashing 4 : quick-flashing 5 : very quick-flashing 6 : ultra quick-flashing 7 : isophased 8 : occulting 9 : interrupted quick-flashing 10 : interrupted very quick flashing 11 : interrupted ultra quick flashing 12 : morse 13 : fixed and flash 14 : flash and long-flash 15 : occulting and flash 16 : fixed and long-flash 17 : occulting alternating 18 : long-flash alternating 19 : flash alternating 25 : quick-flash plus long-flash 26 : very quick-flash plus long flash 27 : ultra quick-flash plus long flash 28 : alternating 29 : fixed and alternating flashing | (S) EN | 1,1 |
| Light sector |  |  | (S) C | 1,* |
| Colour | (COLOUR) | 1 : white 2 : black 3 : red 4 : green 5 : blue 6 : yellow 7 : grey 8 : brown 9 : amber 10 : violet 11 : orange 12 : magenta 13 : pink | (S) EN | 1,* (ordered) |
| Light visibility | (LITVIS) | 1 : high intensity 2 : low intensity 3 : faint 4 : intensified 5 : unintensified 6 : visibility deliberately restricted 7 : obscured 8 : partially obscured 9 : visible in line of range | (S) EN | 0,* |
| Sector limit |  |  | (S) C | 1,1 |
| Sector limit one | (SECTR1) |  | (S) RE | 1,1 |
| Sector limit two | (SECTR2) |  | (S) RE | 1,1 |
| Value of nominal range | (VALNMR) |  | (S) RE | 0,1 |
| Information |  |  | (S) C | 0,* |
| Language |  | ISO 639-3 | (S) TE | 0,1 |
| Text | (INFORM) (NINFOM) |  | (S) TE | 1,1 |
| Sector extension |  |  | (S) IN | 0,1 |
| Signal group | (SIGGRP) |  | (S) TE | 0,* (ordered) |
| Signal period | (SIGPER) |  | (S) RE | 0,1 |
| Signal sequence | (SIGSEQ) |  | (S) C | 0,* (ordered) |
| Signal duration |  |  | (S) RE | 1,1 |
| Signal status |  | 1 : lit/sound 2 : eclipsed/silent | (S) EN | 1,1 |
| Status | (STATUS) | 1 : permanent 2 : occasional 4 : not in use 5 : periodic/intermittent 6 : reserved 7 : temporary 8 : private 11 : extinguished 14 : public 15 : synchronized 16 : watched 17 : un-watched | EN | 0,* |
| Value of nominal range | (VALNMR) |  | RE | 0,1 |
| Vertical datum | (VERDAT) | 1 : Mean low water springs 2 : Mean lower low water springs 3 : Mean sea level 4 : Lowest low water 5 : Mean low water 6 : Lowest low water springs 7 : Approximate mean low water springs 8 : Indian spring low water 9 : Low water springs 10 : Approximate lowest astronomical tide 11 : Nearly lowest low water 12 : Mean lower low water 13 : Low water 14 : Approximate mean low water 15 : Approximate mean lower low water 16 : Mean high water 17 : Mean high water springs 18 : High water 19 : Approximate mean sea level 20 : High water springs 21 : Mean higher high water 22 : Equinoctial spring low water 23 : Lowest astronomical tide 24 : Local datum 25 : International great lakes datum 1985 26 : Mean water level 27 : Lower low water large tide 28 : Higher high water large tide 29 : Nearly highest high water 30 : Highest astronomical tide (HAT) | EN | 0,1 |
| Information |  |  | C | 0,* |
| Language |  | ISO 639-3 | (S) TE | 0,1 |
| Text | (INFORM) (NINFOM) |  | (S) TE | 1,1 |
| Scale minimum | (SCAMIN) | See clause X.X | IN | 0,1 |
| Textual description |  |  | C | 0,* |
| File reference | (TXTDSC) (NTXTDS) |  | (S) TE | 1,1 |
| Language |  | ISO 639-3 | (S) TE | 0,1 |
| Recording date | (RECDAT) | ISO 8601:1988 | DA | 0,1 |
| Recording indication | (RECIND) |  | TE | 0,1 |
| Source indication |  |  | C | 0,* |
| Authority |  |  | (S) TE | 1,1 |
| Nationality |  |  | (S) TE | 1,1 |
| ID code |  |  | (S) TE | 0,1 |
| Source |  |  | (S) TE | 0,1 |
| Source date | (SORDAT) | ISO 8601:1988 | (S) DA | 1,1 |
| INT 1 Reference: P 1-65 Directional lights (see S-4 – B-470) Directional (or direction) lights of several types are in use but all have in common a very narrow sector intended to mark a direction to be followed. The narrow sector may be flanked by: Unlit sectors or unintensified light. Sectors of different colour or character. Some direction lights are so precise that a complete colour change at a sector boundary occurs over an angle of less than 1 minute (0∙02°). This corresponds to a lateral distance of just 1 metre at a viewing distance of 3.5 km. In addition the intensity may be maintained right to the edge of the beam, and does not reduce the further the observer is away from the axis. A moiré effect mark (or variable arrow mark) is a short-range (normally up to 2 km) type of directional “light”. Sodium lighting gives a yellow background to a screen (up to 3 m square) on which a vertical black line will be seen by an observer on the centreline, or variable arrow marks when course alteration is needed. The system can be used by day and night. It can also be used as a stop line (seen abeam) for vessels berthing along quays. If it is required to encode a light with any sector having a directional function, it must be done using the feature Light Directional. This feature must be an equipment feature of a structure feature (see clause X.X), which may be another light feature at the same position (if it exists and there is no structure feature available), using a Structure/equipment feature association. Further guidance for encoding various types and characteristics of lights can be found in clauses X.X to X.X. Remarks: If it is required to encode a directional light sector that comprises a narrow (and sometimes intensified) sector, the sector must be encoded using the complex attribute sector limit, and the mandatory complex attribute orientation must be populated with an empty (null) value. The mandatory complex sub-attribute orientation must only be encoded to indicate the orientation, measured from seaward, of the leading line of the directional light sector when the complex attribute sector limit is not populated, and there is no Recommended Track or Navigation Line feature associated with the directional light. Where the directional sector has complex attribute sector limit, and/or there is an associated Recommended Track and/or Navigation Line, orientation (orientation value) for the light sector must be populated with an empty (null) value. For moiré effect lights, the attribute moiré effect must be set to True. If it is required to encode details of the lighting technology (e.g. neon), it must be done using the complex attribute information. The attribute vertical datum applies only to height; this value must only be encoded if it is different to the value encoded in the VDAT subfield of the “Coordinate Reference System Header field” [CRSH] field, or different to the value of vertical datum encoded on meta feature Vertical Datum of Data. Names of major lights are very important. If a light has a name which is unrelated to any other encoded feature, the name must be populated using the complex attribute feature name on at least the largest scale maximum display scale ENC data. If the name of a light is obviously that of the named feature on which the light stands, e.g. Saint Catherine’s Point, the name of the light need not be repeated for the light. If it is required to encode the recommended track and/or navigation line associated with a directional light, it must be done using the methods described in clause X.X. Distinction: Beacon, cardinal; beacon, isolated danger; beacon, lateral; beacon, safe water; beacon, special purpose/general; buoy, cardinal; buoy, installation; buoy, isolated danger; buoy, lateral; buoy, safe water; buoy, special purpose/general; light air obstruction; light all around; light float; light fog detector; light sectored; light vessel. |

# Comments

MD8 – 8.Cl.8 and 8.Co.11.

With light sector nested in rhythm of light there can be multiple sectors for a directional light.  Needs discussion.

TSMAD25.