# C:\Documents and Settings\julia.powell\My Documents\IHO TSMAD\S100-0 main\IHO S-100 Main Oct 1 2007.doc © ISO/IEC 2007 – All rights reservedISO-IEC_ 63Complementary elementIntroductory element — Main elementÉlément introductif — Élément central — Élément complémentaireIntroductory element — Main element — Complementary elementE2007-10-2 ISO/IECISO/IEC     2007 ISO/IEC ISO/IEC _(E).        2Heading 2Heading 1    02 STD Version 2.1c20   4             INTERNATIONAL HYDROGRAPHIC ORGANIZATION

IHO GEOSPATIAL STANDARD

# FOR HYDROGRAPHIC DATA

# Draft  0.0.1 – February 2010

# Special Publication No. 101

# Electronic Navigational Chart Product Specification

# Published by the

# International Hydrographic Bureau

# MONACO

Contents	Page

1	Overview	1

1.1	Introduction	1

1.2	References	1

1.3	Terms, definitions and abbreviations	1

1.3.1	Terms and Definitions	1

1.3.2	Abbreviations	1

1.4	S-101 General Data Product Description	1

1.5	Data product specification metadata	2

2	Specification Scopes	3

3	Data Set Identification	3

4	Data Content and structure	5

4.1	Application Schema	5

4.2	Feature Catalogue	7

4.3	Feature Types	8

4.3.1	Meta Feature Types (S-57 PS 3.4)	8

4.3.2	Geographic Feature Types	8

4.3.3	Theme Feature Types	8

4.3.4	Aggregated Feature Types (S-57 PS 3.9)	9

4.4	Time Varying Features (S-57 PS 3.7)	9

4.5	Attributes	9

4.5.1	Numeric Attribute Values (S-57 PS 3.5.4)	9

4.5.2	Text Attribute Values (S-57 PS 3.5.5)	9

4.5.3	Mandatory Attribute Values (S-57 PS 3.5.2)	9

4.6	ENC Data Set	10

4.7	Cells  (S-57 PS 2.2)	10

4.8	Feature Object Identifier (S-57 PS 3.1)	10

4.9	Geometry (S-57 PS 2.3 and 3.8)	11

4.9.1	Level 3a	12

5	Coordinate Reference Systems (CRS)	12

5.1	Introduction (S-57 PS 4.1)	12

5.2	Horizontal Coordinate Reference System (S-57 PS 4.1)	12

5.3	Vertical and Sounding Datum (S-57 PS 4.2)	13

5.3.1	Vertical Datum (S-57 UOC)	13

5.3.2	Sounding Datum (S-57 UOC)	13

5.4	Units of Measure (S-57 PS 4.4)	14

5.4.1	Positions (S-57 PS 4.4)	14

5.4.2	Depths (S-57 PS 4.4)	14

6	Data Quality (S-57 UOC)	14

6.1	Quality, Reliability and Accuracy of Bathymetric Data	15

6.1.1	Quality of bathymetric data	15

6.1.2	Survey reliability	15

6.1.3	Quality of sounding	15

6.1.4	Sounding accuracy	15

6.1.5	Technique of sounding measurement	15

6.2	Accuracy of non-bathymetric data	16

6.2.1	Quality of positions	16

6.2.2	Horizontal accuracy	16

6.2.3	Vertical accuracy	16

6.2.4	Source of bathymetric data	16

6.2.5	Source of other data	16

7	Data Capture and Classification	16

8	Data Maintenance	16

8.1	Introduction	16

9	Portrayal	17

10	Data Product format (encoding)	17

11	Data Product Delivery (S-57 PS 5.8? and 2.2)	17

11.1	Implementation (S-57 PS 5.1)	18

11.2	Feature and Portrayal Catalogue Delivery	18

11.3	Encoding	18

11.3.1	Data Sets (S-57 PS 5.5)	18

11.3.2	Data set file naming (S-57 PS 5.6.1)	19

11.3.3	ENC Cell files (S-57 PS 5.6.1)	19

11.3.4	New Editions and Updates(S-57 PS 5.7)	20

11.4	Data integrity (S-57 PS 5.9)	21

11.4.1	ENC data integrity measures	21

11.4.2	Implementation	21

11.4.3	Processing	22

12	Metadata	22

12.1	Language (S-57 PS 3.11)	24

12.1.1	Use of lexical level 2	24

ANNEX A Data Product format (encoding) (S-57 PS 6)	25

1	Introduction	25

1.1	Data set files	26

1.2	Records	27

1.3	Fields	27

1.4	Subfields	27

1.5	Base cell and update file structure	27

1.5.1	Data Set Identification field structure	30

1.5.2	Data Set Structure Information field structure	30

1.5.3	Attribute field structure	31

1.5.4	Data Set Coordinate Reference System record structure	32

1.5.5	Information Type Identifier field structure	34

1.5.6	Coordinate Control field structure	35

1.5.7	2-D Integer Coordinate field structure	35

1.5.8	3-D Integer Coordinate field structure	35

1.5.9	2-D Floating Point Coordinate field structure	36

1.5.10	3-D Floating Point Coordinate field structure	36

1.5.11	Feature Type Record Identifier field structure	42

1.5.12	Feature Object Identifier field structure	42

1.5.13	Spatial Association field structure	42

1.5.14	Feature Association field	43

1.5.15	Theme Association field	43

1.5.16	Masked Spatial Type field structure	44

2	ANNEX B (informative)	45

# Overview

## Introduction

## References

## Terms, definitions and abbreviations

### Terms and Definitions

Cell

A cell is a geographical area containing ENC data.

ENC

The latest version of official data carried by a vessel for the intended voyage.

ENC Product Specification

The set of specifications intended to enable Hydrographic Offices to produce a consistent ENC, and manufacturers to use that data efficiently in an ECDIS that satisfies the IMO Performance Standards for ECDIS. An ENC must be produced in accordance with the rules defined in this Specification and must be encoded using the rules described in the Data Capture and Classification Guide.

point

0-dimensional geometric primitive, representing a position

curve

1-dimensional geometric primitive, representing the continuous image of a line

NOTE: The boundary of a curve is the set of points at either end of the curve. If the curve is a cycle, the two ends are identical, and the curve (if topologically closed) is considered to not have a boundary. The first point is called the start point, and the last is the end point. Connectivity of the curve is guaranteed by the “continuous image of a line”

curve segment

1-dimensional geometric object used to represent a continuous component of a curve using homogeneous interpolation and definition methods

NOTE: The geometric set represented by a single curve segment is equivalent to a curve

### Abbreviations

IHO		International Hydrographic Organization

ENC		Electronic Navigational Chart

SENC		System Electronic Navigational Chart

## S-101 General Data Product Description

Note: This information contains general information about the data product.

Title:	Electronic Navigational Chart

Abstract: 		An Electronic Navigational Chart (ENC) is a vector chart produced on the authority of a government authorized Hydrographic Office. Its primary function is for use within an Electronic Chart Display and Information Systems (ECDIS) to meet International Maritime Organisation (IMO) and Safety Of Life At Sea (SOLAS) chart carriage requirements. The ENC contains an extraction of real world information necessary for the safe navigation of vessels.

Content: 	This Product Specification is a complete description of all the appropriate features, attributes and their relationships necessary to define an ENC data product. The precise content is documented within the Feature Catalogue and the relationships defined the Application Schema. Details of how these features should be symbolised are contained in the associated Portrayal Catalogue.

Spatial Extent:

Description: Areas specific to marine navigation.

East Bounding Longitude: 180

West Bounding Longitude: -180

North Bounding Latitude: 90

South Bounding Latitude -90

Purpose: 		The purpose of an ENC data set is to provide official navigational data to an Electronic Chart Display and Information System (ECDIS) for the safe passage of vessels between destinations.

## Data product specification metadata

Note: This information uniquely identifies this Product Specification and provides information about its creation and maintenance.

Title:		The International Hydrographic Organization Electronic Navigational Chart Product Specification

S-100 Version:	1.0.0

S-101 Version: 	0.0.1

Date:				January 31, 2010

Language: 		English

Classification: 	Unclassified

Contact: 			International Hydrographic Bureau (IHB)

4 Quai Antoine 1er

B.P. 445

MC 98011 MONACO CEDEX
Telephone: +377 93 10 81 00
Fax: + 377 93 10 81 40

URL: 				www.iho.int

Identifier: 		S-101

Maintenance:		Changes to the Product Specification S-101 are coordinated by Transfer Standards Maintenance and Applications Development Working Group (TSMAD) of the IHO and shall be made available via the IHO web site. Maintenance of the Product Specification shall conform to IHO Technical Resolution A1.21 (revised 2009).

# Specification Scopes

Scope ID: 		Root scope

Level:			Dataset

Level name:	ENC Dataset

Spatial Extent:

Description: Areas specific to marine navigation.

eastBoundLongitude: 180

westBoundLongitude: -180

northBoundLatitude: 90

southBoundLatitude -90

Vertical Extent:

minimumValue:

maximumValue:

unitOfMeasure:	meters

# Data Set Identification

A data set that conforms to this Product Specification will be identifiable by the discovery metadata that supports it.

Title: 									Electronic Navigational Chart

Alternate Title:						ENC

Abstract: 	When an S-101 ENC is produced it must be in accordance with the rules defined in the S-101 Product Specification. S-101 details specifications intended to enable Hydrographic Offices to produce a consistent ENC, and manufacturers to use that data efficiently in an ECDIS to satisfy IMO Performance Standards for ECDIS.

Topic Category:						Transportation

Geographic Description:	Areas specific to marine navigation.

Spatial Resolution:	Display scale will be the optimum intended viewing scale of the data within a cell. The display scale must be one of the scales listed in the table below.  The display scales for ENC have been aligned with the standard RADAR ranges and are as follows:

| Standard RADAR Ranges | Display Scale |
| --- | --- |
|  | >1:3,000,000 |
| 200 NM | 1:3,000,000 |
| 96 NM | 1:1,500,000 |
| 48 NM | 1:700,000 |
| 24NM | 1:350,000 |
| 12 NM | 1:180,000 |
| 6 NM | 1:90,000 |
| 3 NM | 1:45,000 |
| 1.5 NM | 1:22,000 |
| 0.75 NM | 1:12,000 |
| 0.5 NM | 1:8,000 |
| 0.25 NM | 1:4,000 |
|  | <=1:2,000 |

Table 1: Standard Display Scales

Purpose:	Electronic Navigational Chart for use in Electronic Chart Display Systems

Language: 							English

Classification: 						Unclassified

Spatial Representation Type: 	Vector

Point of Contact: 					Producing Hydrographic Office

Use Limitation: 						Not to be used for navigation on land.

# Data Content and structure

An S-101 ENC is a feature-based product.  This section contains the product Application Schema expressed in UML and an associated Feature Catalogue.  The Feature Catalogue provides a full description of each feature type including its attributes, attribute values and relationships in the data product.

## Application Schema

S-101 contains only a subset of the full application schema.  The sample UML diagrams based on the S-100 model in this section serve as a guide to how new elements such as complex attributes, information types, aggregations and associations may be used. It is not intended to provide exhaustive examples of each and every feature or attribute.

### Dataset Structure

ENC data will consist of scale dependant and scale independent S-101 datasets that combine to form the SENC.

Figure 1 – ENC Dataset structure.

### Simple Attributes

Simple attributes follow S-57 with a feature having multiple attributes which can be enumerations, codelists or simple types eg integer or characterstring.

Figure 2 – Feature with simple attributes.

Figure 3 – Feature with simple attributes.

### Complex Attributes

Complex attributes are properties of a feature which can be divided into multiple sub attributes. Complex attributes are used where objects have properties that better fit a hierarchical structure. In the example below a light with sectors can be captured as a single feature unlike in S-57 where each sector would have required a lights object. The complex attribute lightSector is used for each sector with a separate rythmOfLight complex attribute defining the light characteristics. SIGSEQ uses a list of lit and unlit segments to give the light sequence.

Figure 4 – Lights feature example using complex attributes.

Figure 5 – Seabed area example using a complex attribute.

### Aggregations

In order represent features that are related to each other the concept of aggregation is used to combine features into aggregate objects. In the example below an aggregate feature type of Traffic Separation Scheme has child feature types that make up the TSS and may include other related features such as buoys and beacons. In this case a deep water route is also associated to the aggregation but it is independent so would remain if the aggregate feature was deleted.

Figure 6 – An example of an aggregation.

Figure 7 – An example of an aggregation.

### Feature Associations

A feature association is a relationship that links instances of one feature type with instances of the same or a different feature type. In S-101 feature associations are utilized to represent master slave relationships. However specific feature associations will be defined in the feature catalogue providing the properties of the relationships between features. In the example below a buoy carries a light and a topmark. Two feature associations are therefore used to define these relationships. Each relationship has a name and two roles thus giving a more detailed representation of the real world relationships within the dataset.

Figure 8 – An example of feature associations and their properties.

### Themes

Theme objects are a special kind of aggregation objects. They do not define an object itself, but group other objects together. The reasons for the grouping are mostly thematic; other reasons are possible. Each feature object may belong to more than one theme. Themes are therefore not mutually exclusive. Since the kind of association from a theme object to its members (and vice versa) is not variable, the encoding of this type of association is different from the other feature associations. A separate field, the Theme Association field is used. The association is always encoded from the feature object that belongs to the theme to the theme object itself.

#### Skin of the earth feature types

Figure 9 – Use of a theme for TG1 objects in S-101

#### Data Type Themes

Themes are utilized to group like features together.  For example, the theme Navaids could be used to group navigational aids such as buoys and beacons together. A bathymetry theme might group together soundings, depth contours and depth areas. The idea of themes is more applicable to the non navigational use of ENC’s within commercial GIS environments.

Possible themes might include:

- Bathymetry

- Topography

- Routes, Areas and Limits

- Underwater Hazards

- Navaids and Services

- Tides and Currents

Figure 10 – Example Navaids theme,

NOTE:	the use of inheritance for specific buoy/beacon feature types. This simplifies the diagrams for features which share many common attributes.

### Information Types

An information type is a class of object which is defined in a feature catalogue. An instance of an information type is an identifiable unit of information in a data set. Information types have only thematic attribute properties. An instance of an information type may be associated with one or more feature instances or other instances of information type. The most common usage of an information type would be in place of a charted note that refers to multiple features possibly of different feature types.

Figure 11 – Example of an information type, its related features and a national language note as an associated information type.

NOTE:  UML diagrams detailing all new S-101 concepts, the Application Schema will form the backbone of the document. This is just a start it is not the complete Application Schema. The next section of this chapter will discuss each of the parts of the Application Schema in detail. It will be generic and will not tie us down to a specific encoding.

## Feature Catalogue

Only feature types, information types, attributes, attribute values, associations and roles which are defined in the IHO Feature Catalogue may be used in an ENC.

The Feature Catalogue will only be available as an XML schema and instance with an accompanying style sheet.

## Feature Types

### Meta Feature Types (S-57 PS 3.4)

Meta features contain information about other features within a data set. Information defined by meta features override the default metadata values defined by the data set descriptive records. All meta features are defined in the S-101 Feature Catalogue.

The maximum use must be made of meta features to reduce meta attribution on individual features.

In a base data set (EN Application profile), some meta features are mandatory:

Coverage (M_COVR)

QualityOfData (M_QUAL)

NavigationalSystemOfMarks (M_NSYS)

The Meta feature Coverage provides an exhaustive, non-overlapping coverage of the entire cell.

The Meta feature QualityOfData provides an exhaustive, non-overlapping coverage of any part of the cell containing depth or bathymetry.

The Meta feature NavigationSystemOfMarks with the attribute MARSYS provides an exhaustive, non-overlapping coverage of the part of the cell containing data.

### Geographic Feature Types

Geographic (geo) feature types form the principle content of the navigational product and are fully defined by their associated attributes and information types.

### Theme Feature Types

Theme features are a special kind of collection. They do not define a feature itself but group other features together. The reasons for the grouping are mostly thematic, other reasons are possible. Each feature may belong to more than one theme. Themes are therefore not mutually exclusive. Since the kind of association from a theme feature to its members (and vice versa) is not variable, the encoding of this type of association is different from the other feature associations.

#### Skin of the Earth Theme (S-57 PS 3.10.1)

Themes are normally defined in the Feature Catalogue however in this case there are constraints which have to be observed. Skin of the Earth features are a set of geo features of geometric type area that do not overlap each other and form a continuous surface named “Skin of the Earth”. The features listed below represent the only allowable features in this theme.

DepthArea (DEPARE)

DredgedArea (DRGARE)

LandArea (LNDARE)

UnsurveyedArea (UNSARE)

Each area covered by a meta feature Coverage with CATCOV = 1 must be totally covered by a set of geo features of type area that do not overlap each other (the Skin of the Earth).  The geometry of coincident boundaries between Skin of the Earth features must not be duplicated.

### Aggregated Feature Types (S-57 PS 3.9)

Features with a use type of aggregated can have multiple associations to other feature types.  They also are defined in the Feature Catalogue.

All association or aggregation relationships using collection features are assumed to be peer to peer. The “Relationship Indicator” [RIND] subfield of these collection feature records must be {3} = peer.

The use of these named aggregations is described in the Data Capture and Classification Guide.

#### Associations

Associations between features are established and carried in the Feature Catalogue.

EXAMPLE 	A light is associated with a landmark

#### Roles

Roles between features are established and carried in the Feature Catalogue.

EXAMPLE	A light is a slave to a buoy; buoy is the master of the light.  Where master and slave are the role between the buoy and the light.

## Time Varying Features (S-57 PS 3.7)

The ENC may contain information about magnetic variation, tides, tidal streams and currents.

## Attributes

### Numeric Attribute Values (S-57 PS 3.5.4)

Floating point or integer attribute values must not be padded by non-significant zeroes.

### Text Attribute Values (S-57 PS 3.5.5)

Character strings must be encoded using the character set defined in ISO 10646-1, in Unicode Transformation Format-8 (UTF-8).

### Mandatory Attribute Values (S-57 PS 3.5.2)

There are four reasons why attribute values may be considered mandatory:

- They determine whether a feature is in the display base,

- Certain features make no logical sense without specific attributes,

- Some attributes are necessary to determine which symbol is to be displayed,

- Some attributes are required for safety of navigation.

All mandatory attributes are identified in the Feature Catalogue.

### Unknown Attribute Values (S-57 PS 3.5.1)

In a base data set, when an attribute code is present but the attribute value is missing, it means that the producer wishes to indicate that this attribute value is unknown.

In a update data set, when an attribute code is present but the attribute value is missing it means:

- that the value of this attribute is to be replaced by an unknown value if it was present in the original data set,

- that an unknown value is to be inserted if the attribute was not present in the original data set.

## ENC Data Set

An ENC data set is a collection of geo-referenced cells containing geographic features that are used to fully describe the physical marine environment for the safe passage of vessels.

## Cells  (S-57 PS 2.2)

A cell is a grouping of features, attributes, geometry and metadata which form a data surface with a specific coverage.

Cells must be rectangular (i.e. defined by 2 meridians and 2 parallels). However the data contained within a cell does not have to be equal to the cell boundary.

Features with the geometric properties of point or line coincident with the border of two cells within the same layer and with the same display scale must be part of only one cell.

When a feature extends across cells at the same display scale its geometry must be split at the cell boundaries and its complete attribute description must be repeated in each cell.

In order to facilitate the efficient processing of ENC data the geographic coverage of a given usage must be split into cells. Each cell of data must be contained in a physically separate, uniquely identified file on the transfer medium, known as a data set file.

The coordinates of the borders of the cell are encoded in decimal degrees in the boundingBox field of the Catalogue file.

Each cell must be completely covered by meta feature(s) of class Coverage. The areas that contain data must be indicated by Coverage features with attribute CATCOV = 1. Any other areas that do not contain data must covered by Coverage features with CATCOV = 2.

Cells with the same navigational purpose may overlap. However, data within the cells must not overlap. Therefore, in the area of overlap only one cell may contain data, all other cells must have a meta feature Coverage with CATCOV = 2 covering the overlap area. This rule applies even if several producers are involved.

## Feature Object Identifier (S-57 PS 3.1)

Each real world feature and instances of information type within an ENC must have a unique universal Feature Object Identifier.

For ENC the Feature Object Identifier may be used to identify multiple instances of the same feature within a single cell or across multiple cells. For example, the same feature may appear in different display scales, or a feature may be split by the cell structure. In these circumstances each instance of this feature should have the same identifier.

Feature Object Identifier’s must not be reused, even when a feature has been deleted.

## Geometry (S-57 PS 2.3 and 3.8)

Figure ?:  S-100 Level 3a Geometry

Features contain descriptive attributes and do not contain any geometry (i.e. information about the shape and position of a real world entity). Spatial features may have descriptive attributes and must contain geometry. A feature is located by a relationship to one or more spatial features. Other feature types may exist without referencing a spatial feature, but each spatial feature must be referenced by another feature type.

The underlying geometry of an ENC will be constrained to S-100 level 3a which supports 0, 1 and 2 dimensional objects (points, curves and surfaces). The third dimension is expressed as an attribute of a feature.

ENC data must be encoded using chain-node topology. The Skin of the Earth Theme must be encoded using ?????

If there is a logical topological relationship between features, coincident linear geometry must not be duplicated.

Despite the saving in data volume offered by the use of arcs/curves, the disadvantages are such (e.g. during updating, generating warnings/alarms) that they must not be used for ENC.

Linear geometry between two explicit coordinates is defined as a loxodromic line on WGS84. Long lines may need to have additional explicit coordinates to cater for the effects of projection change.

In certain circumstances, the symbolisation of points, curves, and surfaces may need to be suppressed.  In order to suppress these spatial features the masked Spatial Type field structure is used.

### Level 3a

A set of point, curve and surface primitives with the following constraints:

- Each curve must reference a start and end point (they may be the same).

- Curves must not self intersect.

- Areas are represented by a closed loop of curves beginning and ending at a common point.

- In the case of areas with holes, all internal boundaries must be completely contained within the external boundary and the internal boundaries must not intersect each other or the external boundary. Internal boundaries may touch tangentially (i.e. at one point).

- The outer boundary of a surface must be in a clockwise direction (surface to the right of the curve) and the curve orientation positive. The inner boundary of a surface must be in a counter-clockwise direction (surface to the right of the curve) and the curve orientation negative.

- Coincident linear geometry must be avoided when there is a dependency between features.

For a complete description of the geometry in Figure ?? see S-100 Part 7 – Spatial Schema.

# Coordinate Reference Systems (CRS)

## Introduction (S-57 PS 4.1)

Due to the nature of hydrography it is common practice to separate the horizontal and vertical part of a position. This leads to 2D coordinate reference systems for the horizontal positions and 1D coordinate reference systems for the vertical positions. To describe 3D coordinates those coordinate reference systems must be combined to produce a compound reference system. An ENC data set must define at least one compound CRS. An ENC compound CRS is composed of a 2D geodetic CRS (WGS84) and a vertical CRS.

## Horizontal Coordinate Reference System (S-57 PS 4.1)

For ENC the geodetic datum of the horizontal CRS must be WGS 84.  No projection is to be used.  If the CRS WGS84 is not defined in the encoding by referencing then it must be fully defined, encoding all parameters and referenced to a geodetic Coordinate Reference System which incorporates an ellipsoidal coordinate system with axes graduated in degrees.

## Vertical and Sounding Datum (S-57 PS 4.2)

Although all coordinates in a data set must refer to the same horizontal CRS different Vertical Datums can be used for the height or depth component of a coordinate tuple. Therefore the vertical CRS can be repeated. For each Vertical CRS a unique identifier is defined. Those identifiers will be used to indicate which Vertical CRS is used.

No restriction is placed on the vertical or sounding CRSs that can be used to define height and depth reference systems within ENC.

The various levels which are used on paper charts for elevations and soundings must be used. The default values are encoded in Vertical Datum field structure (VDAT). In S-101 both heights and depths are represented by positive values i.e. positive values up for heights and positive values down for depths.

## Units of Measure (S-57 PS 4.4)

Units to be used in an ENC:

- Position: latitude and longitude in decimal degrees (converted into integer values).

- Depth: metres.

- Height: metres.

- Positional accuracy: metres.

- Distance: nautical miles or metres.

- Time: seconds.

- Bearings:  decimal degrees.

### Positions (S-57 PS 4.4)

Positions are in WGS84 and coordinates are held in the Data Set Structure Information field under coordinate multiplication factor for X, Y and Z coordinate.

Coordinates must be held in ENC production systems at a resolution of 0.0000001 (10-7) and the coordinate multiplication factor value should be set to 10000000 (107) for all cells.

EXAMPLE	A longitude = 34.5678E is converted into X = longitude * COMF = 34.5678 * 10000000 = 	345678000.

### Depths (S-57 PS 4.4)

Depths are converted from decimal meters to integers by means of the 3-D (Sounding) Multiplication Factor. Soundings are never encoded with a resolution greater than one decimetre, so the value of sounding multiplication factor must be 10.

For update cells, ‘Coordinate Multiplication Factor’ [X], [Y] and the ‘3-D (Sounding) Multiplication Factor’ [Z] will not be present. In this case, the values from the original base cell should be used.

# Data Quality (S-57 UOC)

Data quality comprises the following:

- source of data;

- accuracy of data;

- up-to-datedness of data.

Data quality is considered to be meta information. As such, it can be encoded at three different levels.

Data quality information is considered to be application specific. Therefore, rules for encoding data quality must be defined by the relevant product specification.

## Quality, Reliability and Accuracy of Bathymetric Data

Information about quality, reliability and accuracy of bathymetric data is given using:

- the meta feature QualityOfData for an assessment of the quality of bathymetric data,

- the meta feature SurveyReliability for additional information about the survey,

- the attributes QUASOU, SOUACC and TECSOU on groups of soundings or individual features,

- the attributes POSACC and QUAPOS on the spatial features.

For the mariner, QualityOfData provides the most useful information.  Therefore, the use of QualityOfData is mandatory for areas containing depth data or bathymetry.

More detailed information about a survey may be given using SurveyReliability.  For example, in incompletely surveyed areas, lines of passage soundings may be indicated as such using a linear SurveyReliability feature.  This information is more difficult for the mariner to interpret. Therefore, the use of SurveyReliability is optional.

For individual features (wrecks, obstructions etc), or small groups of soundings, QUASOU, SOUACC and TECSOU may be used to provide additional information about quality and accuracy.

### Quality of bathymetric data

The meta feature QualityOfData defines areas within which uniform assessment exists for the quality of bathymetric data, and must be used to provide an assessment of the overall quality of bathymetric data to the mariner.  Areas of a cell containing depth data or bathymetry must be covered by one or more QualityOfData, which must not overlap.

### Survey reliability

The survey reliability may be encoded using the meta feature SurveyReliability.

### Quality of sounding

If it is required to encode the quality of sounding, it must be done using the attribute QUASOU on either the meta feature SurveyReliability or on individual geo features (e.g. Sounding).

# The quality of sounding must not be encoded using QUASOU on the depth geo feature, unless it is different to the value of QUASOU populated on an encoded SurveyReliability feature covering the geo feature.

### Sounding accuracy

Sounding accuracy is encoded using the attribute CATZOC on the meta feature QualityOfData.  If it is required to encode additional sounding accuracy information, it must be done using the attribute SOUACC on either the meta feature QualityOfData or on individual geo features (e.g. Sounding).

# The accuracy of sounding must not be encoded using SOUACC on the depth geo feature, unless it is different to the value of SOUACC encoded on the covering QualityOfData feature.

### Technique of sounding measurement

If it is required to encode the technique of sounding measurement, it must be done using the attribute TECSOU on either the meta feature QualityOfData or on individual geo features (e.g. Sounding).

The technique of sounding measurement must not be encoded using TECSOU on the depth geo feature, unless it is different to the value of TECSOU encoded on the covering AccuracyOfPosition  feature.

## Accuracy of non-bathymetric data

### Quality of positions

The meta feature AccuracyOfPosition may be used to provide an overall accuracy of position for all non-bathymetric features.  It must not be used to provide the accuracy of bathymetric information.

The attributes QUAPOS and POSACC may be applied to any spatial feature, in order to qualify the location of a feature.

QUAPOS and POSACC must not be applied to the referenced spatial feature of any geo feature if they are identical to the QUAPOS and POSACC values of the underlying meta feature.

QUAPOS gives qualitative information, whereas POSACC gives quantitative information. POSACC on the AccuracyOfPosition applies to non bathymetric data situated within the area, while QUAPOS or POSACC on the associated spatial features, qualifies the location of the AccuracyOfPosition feature itself. Meta features AccuracyOfPosition and QualityOfData should not overlap.

### Horizontal accuracy

If it is required to encode the accuracy of a horizontal clearance (attribute HORCLR), it must be done using the attribute HORACC.

HORACC applies only to HORCLR.  There is no attribute to express the accuracy of the attributes HORLEN and HORWID.

### Vertical accuracy

If it is required to encode the accuracy of a vertical clearance (attributes VERCLR, VERCOP, VERCSA, VERCCL), it must be done using the attribute VERACC.

If several vertical clearances are given for one feature, the accuracy given must be that of the least accurate.

### Source of bathymetric data

Details of the source surveys used in compilation may be encoded using the meta feature SurveyReliability.

### Source of other data

The source of non-bathymetric information should be encoded using both the attributes SORIND and SORDAT on the individual features, but only if this information is considered to be useful to the mariner.

# Data Capture and Classification

The S-101 Data Capture and Classification guide will provide the information to map real world features into the data set.  This Guide is located in Appendix A.   Data collected as S-101 shall conform to the Data Classification and Capture Guide.

# Data Maintenance

## Introduction

Data shall be continually maintained and updated and checked against S-58.

| Item Name | Description | M/O | Card | type |
| --- | --- | --- | --- | --- |
| maintenanceAndUpdateFrequency | Frequency with which changes and additions are made to the data product (per update scope) | M | 1..* | continual |
| dataSource | Identification of the kinds of data sources usable to produce data sets | O | 1..* | LI_Source (ISO 19115) +description [0..1] : CharacterString |
| productionProcess | Textual description of the production process applicable to the data sets (per scope or data source) | O | 1..* | LI_ProcessStep (ISO 19115) +description [0..1] : CharacterString |

# Portrayal

S-101 shall include a portrayal catalogue.

| Item Name | Description | M/O | Card | type |
| --- | --- | --- | --- | --- |
| portrayalLibraryCitation | Bibliographic reference to the portrayal library | O | 0..1 | CI_Citation (ISO 19115) |

# Data Product format (encoding)

| formatName | S-100 part 10A |
| --- | --- |
| version | 1.0 |
| characterSet | UTF-8 |
| specification | S-100 profile of ISO/IEC 8211 |

See Annex A for a complete description of the data records, fields and subfields.

# Data Product Delivery (S-57 PS 5.8? and 2.2)

| Item Name | Description | type |
| --- | --- | --- |
| unitsOfDelivery | Cells - In order to facilitate the efficient processing of ENC data the geographic coverage of a given usage must be split into cells. | cells |
| transferSize | Estimated size of a unit | 5mb |
| mediumName | Name of the delivery medium | Digital data delivery |
| otherDeliveryInformation | Other information |  |

## Implementation (S-57 PS 5.1)

The binary implementation of S-101 must be used for ENC. Therefore, the “Implementation” [IMPL] subfield of the “Catalogue Directory” [CATD] field must be set to “BIN” for the data set files.

## Feature and Portrayal Catalogue Delivery

Revised Feature and Portrayal Catalogues will be made available on the IHO website.

## Encoding

The S-101 Product Specification defines an encoding which can be used as a default for transmission of data between parties. It is not suitable for commercial distribution of data and further encodings, which may draw on the standard encoding, will be defined for commercial distribution of data.

PHASE 2

The encoding encapsulates exchange set elements as follows:

- PHASE 2

- ENC cells – ISO 8211 binary encoding of features/attributes and their associated geometry and metadata. Defined further in XXXX

- Exchange Catalogue – ISO 8211 encoded representation of exchange set catalogue features [discovery metadata]. Includes an additional file level CRC check per cell.

- Useful information about the ENC dataset. This is contained within a README.TXT file.

- Supplementary files – These are contained within the exchange set as files and the map from the name included within the cell and the physical location on the media is defined within the Exchange Catalogue.

### Data Sets (S-57 PS 5.5)

Three kinds of ENC data set may be produced and contained within an exchange set:

- New data set: No ENC data has previously been produced for this area and for the same navigational purpose.

- Update: Changing some information in an existing data set.

- New edition of a data set: Including new information which has not been previously distributed by updates.  Each new edition of a data set must have the same name as the data set that it replaces.

Each new data set or new edition is called a base cell file. A data set containing updates to at least one base cell file is called an update cell file.

### Data set file naming (S-57 PS 5.6.1)

Within this encoding all cells are encapsulated as files as is the Exchange Catalogue. The entire exchange set is encapsulated therefore as a set of files which can be transmitted.

### ENC Cell files (S-57 PS 5.6.1)

In this encoding the ENC cells files are named according to the specifications given below:

CCSXXXXX.EEE

|   I	|    		|

|   	I	|    		| ----- EEE = update number – this is a ‘0’ padded 3 digit number identical to the cell’s

I   I     I	update number (see 11.3.4).

| 	|	|---------------- XXXXXXXX = individual cell code, up to eight characters.

| 	|--------------------- S = 1. Scale Independent - 2. Scale Dependant – 3. Complete.

|------------------------ CC = producer code.

The main part forms an identifier where:

- The first two characters identify the issuing agency.

- The third character indicates the cell type.

- The fourth to * characters are used for the cell code. This code can be used in any way by the producer to provide the unique file name. If characters other than numbers are used only uppercase letters are allowed the use of the underscore character in cell names is prohibited.

### New Editions and Updates(S-57 PS 5.7)

This section describes how the standard encoding defines updating methodologies for ENC cells. In order to ensure that feature type updates are incorporated into an ECDIS in the correct sequence without any omission, the file extension and a number of other parameters encoded in the data are used in the following way:

file extension	every new data set or new edition must have a .000 extension as per the translation from EDTN to the file extension. For update cell files the extension is the value of the UPDN field, ranging from .001 to .999. These numbers must be used sequentially, without omission. Number .001 is the first update after a new data set or a new edition.

edition number 	when a data set is initially created, the edition number 1 is assigned to it. The edition number is increased by 1 at each new edition.

update number 	update number 0 is assigned to a new data set. The first update cell file associated with this new data set must have update number 1. The update number must be increased by one for each consecutive update, until a new edition is released. The new edition must have update number 0. In the case of an update cell file the file extension is the same as the update number.

update comment	comment for describing the change introduced by an update.

issue date	date up to which the data producer has incorporated all applicable changes.

In order to cancel a data set, an update cell file is created for which the edition number must be set to 0. This message is only used to cancel a base cell file. Where a cell is cancelled and its name is re used at a later date, the issue date must be greater than the issue date of the cancelled cell.

Maintenance of support files is described in S-100.

Phase 2

When a feature pointing to a text, picture or application file is deleted or updated so that it no longer references the file, the ECDIS software should check to see whether any other feature referenced the same file, before that file is deleted.

An exchange set may contain base cell files and update cell files for the same cells. Under these circumstances the update cell files must follow on in the correct sequential order from the last update applied to the base cell file.

HA: Need to think about the sequences of things.  The ECDIS needs to control the sequence – they need to control the references before the file goes away.  Need to state that certain scenarios could occur.  If you issue an update that reference a support file, then the support file must be included in the update.

### Phase 3:

### Possibly use information types to like the update notice to the feature, package it with the update and then it would carry the information regarding the update, this becomes part of the data.

### HO would need to publish a list of ENC’s and what is updated and the ECDIS would have to compare that to the cells on board and create a report

### EK:  Two levels of information – generic information about the NTM – have that in the Metadata mechanism for maintenance.  However, there is no relation.  HO’s would have to issue a similar catalogue for comparison.  Some users want some specific information about the update.  Such as if the TSS was shifted, versus finding the NTM.

### HA:  Can link information types to the spatial.

### HB:  Needs to be more useful information available to the mariner.  Need to think more about the mechanism itself.  The information types are part of the dataset so that would be an update also.  The information type needs to have a link to a geographic position.  VPF has a separate layer that links the information to the geometric primitive.

### Handling deletes.

### FH:  Two ways you can look at deleted features.  The ECDIS could do it via a comparison.  Could introduce a deleted feature.

### Two issues:  the mariner needs to know what information is up-to-date, the port state needs to know how up-to-date the information is.

### EM:  There are several ways this can be done.  Get a needs statement on what needs to be done.  Ask the question to the stakeholders.

### Possible update theme

### The cancellation of a data file should use the same procedure as the cancellation of a support file.  (Whatever the procedure is)

## Data integrity (S-57 PS 5.9)

### ENC data integrity measures

Where there is a high impact on the integrity of data as a result of data corruption, such as to ENC data, there is a need for a mechanism within the ENC data itself to ensure it has not changed during transmission/delivery. The mechanism chosen for this assurance is a cyclic redundancy check. File integrity checks are based on the CRC-32 algorithm (a 32 bit Cyclic Redundancy Check algorithm) as defined in ANSI/IEEE Standard 802.3, the reference for which is given in clause 1.2.

### Implementation

The checksums for each data set are held in the “CRC” [CRCS] subfield of the “Catalogue Directory” [CATD] field. They allow the integrity of each file in the exchange set to be checked on receipt. The CRC value computed on the received file must the same as the CRC value transmitted.

The CRC values are recorded in ASCII as a hexadecimal number.

### Processing

Encoding is defined by the following generating polynomial:

G(x) = x 32 + x 26 + x 23 + x 22 + x 16 + x 12 + x 11 + x 10 + x 8 + x 7 + x 5 + x 4 + x 2 + x + 1

Processing is applied to relevant files as they appear in the exchange set.

The CRC value of the file is defined by the following process:

1.	The first 32 bits of the data are complemented.

2.	The n bits of the data are then considered to be the coefficients of a polynomial M(x) of degree n-1.

3.	M(x) is multiplied by x32 and divided by G(x), producing a remainder R(x) of degree <31.

4.	The coefficients of R(x) are considered to be a 32-bit sequence.

5.	The bit sequence is complemented and the result is the CRC.

The hexadecimal format of CRCs are converted to ASCII characters and stored in the “Catalogue Directory” [CATD] field.

An example of coding in C language is given in Annex.

# Metadata

Discovery metadata elements required for scale dependent and scale independent ENC cells.

| Name | Cardinality | Value | Type | Remarks |
| --- | --- | --- | --- | --- |
| DataSetDiscoveryMeta data | - |  | - | - |
| metadataFileIdentifier | 1 |  | CharacterString |  |
| metadataPointOfContact | 1 |  | CI_ResponsibleParty |  |
| metadataDateStamp | 1 |  | Date |  |
| metadataLanguage | 1 | English | CharacterString | All data sets conforming to S-101 PS must use English language |
| fileName | 1 |  | CharacterString | Dataset file name |
| filePath |  |  | CharacterString | Full path from the exchange set root directory |
| abstract | 1 |  | CharacterString | Short description of the area covered by dataset harbour or port name, between two named locations etc. |
| dataProtection | 1 | {1} to {2} | CharacterString | 1. Encrypted 2. Unprotected |
| purpose | 1 | {1} to {4} | CharacterString | 1. New 2. New Edition 3. Update 4.Cancellation |
| specificUsage | 1 | {1} to {3} | CharacterString | 1.Port Entry 2. 3. |
| editionNumber | 1 |  | CharacterString | when a data set is initially created, the edition number 1 is assigned to it. The edition number is increased by 1 at each new edition. Edition number remains the same for a re-issue. |
| updateNumber | 1 |  | CharacterString | Update number 0 is assigned to a new data set. |
| updateApplicationDate | 0..1 |  | Date |  |
| issueDate | 1 |  | Date |  |
| productSpecification | 1 |  | S-100_ ProductSpecification | This must be encoded as S-101 |
| producingAgency | 1 |  | CI_ResponsibleParty |  |
| displayScale | 1 | {1} to {12} | double | Display scale must be one of the 12 predefined scales detailed in Table 1. |
| horizontalDatum | 1 |  | CharacterString |  |
| verticalDatum | 1 |  | CharacterString |  |
| soundingDatum | 1 |  | CharacterString |  |
| dataType | 1 |  | S-100_DataFormat |  |
| otherDataTypeDescription | 0..1 |  | CharacterString |  |
| boundingBox | 1 |  | EX_GeographicBoundingBox |  |
| boundingPolygon | 1 |  | EX_BoundingPolygon |  |
| comment | 0..1 |  | CharacterString |  |
| cyclicRedundancyCheck | 1 |  | CharacterString NonNegativeInteger |  |
| layerId | 1..* |  | Double | Identifies the relationship to other layers that are required to view the complete data set. |

| Name | Path | Obligation |
| --- | --- | --- |
| Metadata file identifier | MD_Metadata.fileIdentifier | M |
| Metadata language | MD_Metadata.language | C ( documented if not defined by the encoding process) |
| Metadata character set | MD_Metadata.characterSet | C (documented if ISO 10646-1, is not used and not defined by the encoding process) |
| Metadata file parent identifier | MD_Metadata.parentIdentifier | C (documented if the hierarchy of a higher level exists) |
| Metadata hierarchy level | MD_Metadata.hierarchyLevel | O (assumed to be ‘dataset’ if MD_Metadata.hierarchyLevel is omitted) |
| Metadata hierarchy level name | MD_Metadata.hierarchyLevelName | O (assumed to be ‘dataset’ if MD_Metadata.hierarchyLevelName is omitted) |
| Metadata point of contact | MD_Metadata.contact > CI_ResponsibleParty | M |
| Metadata standard name | MD_Metadata.metadataStandardName | O |
| Metadata standard version | MD_Metadata.metadataStandardVersion | O |
| Metadata date stamp | MD_Metadata.dateStamp | M |
| Dataset title | MD_Metadata.identificationInfo > MD_DataIdentification.citation >CI_Citation.title | M |
| Dataset reference date | MD_Metadata.identificationInfo > MD_DataIdentification.citation > CI_Citation.date > CI_Date.date > MD_DataIdentification.citation > CI_Citation.date > CI_Date.date | M |
| Abstract describing the dataset | MD_Metadata.identificationInfo > MD_DataIdentification.abstract | M |
| Dataset point of contact | MD_Metadata.contact > CI_ResponsibleParty | O |
| Dataset spatial representation type | MD_Metadata.identificationInfo > MD_DataIdentification.spatialRepresentationType | O |
| Dataset spatial resolution | MD_Metadata.identificationInfo > MD_DataIdentification.spatialResolution > MD_Resolution.distance or MD_Resolution.equivalentScale | O |
| Dataset language | MD_Metadata.identificationInfo > MD_DataIdentification.language | M |
| Dataset character set | MD_Metadata.identificationInfo > MD_DataIdentification.characterSet | C (documented if ISO 10646-1 is not used) |
| Dataset topic category | MD_Metadata.identificationInfo > MD_DataIdentification.topicCategory | M |
| Geographic location of the dataset (by four coordinates or by description) | MD_Metadata.identificationInfo > MD_DataIdentification.extent > EX_Extent > EX_GeographicBoundingBox or EX_GeographicDescription | C |
| Temporal extent information for the dataset | MD_Metadata.identificationInfo > MD_DataIdentification.extent > EX_Extent.temporalElement | O |
| Vertical extent information for the dataset | MD_Metadata.identificationInfo > MD_DataIdentification.extent > EX_Extent.verticalElement > EX_VerticalExtent | O |
| Lineage | MD_Metadata.dataQualityInfo > DQ_DataQuality.lineage > LI_Lineage | O |
| Reference system | MD_Metadata.referenceSystemInfo > MD_ReferenceSystem.referenceSystemIdentifier > RS_Identifier | O |
| Distribution Format | MD_Metadata.distributionInfo > MD_Distribution > MD_Format | O |
| On-line resource | MD_Metadata.distributionInfo > MD_Distribution > MD_DigitalTransferOption.onLine > CI_OnlineResource | O |
| Dataset Identification Field |
| Record Name |  |  |
| Record Id |  |  |
| Exchange Purpose |  |  |
| Intended Usage |  |  |
| Dataset Name |  |  |
| Edition Number |  |  |
| Update Number |  |  |
| Update Application Date |  |  |
| Issue Date |  |  |
| Edition Number of S-57 |  |  |
| Product Specification |  |  |
| Product Specification Description |  |  |
| Product Specification Edition Number |  |  |
| Application Profile Identification |  |  |
| Producing Agency |  |  |
| Comment |  |  |
| Dataset Structure Information Field |
| Data Structure |  |  |
| ATTF Lexical Level |  |  |
| NATF Lexical Level |  |  |
| Number of Meta Records |  |  |
| Number of Cartographic Records |  |  |
| Number of Geo Records |  |  |
| Number of Collection Records |  |  |
| Number of Isolated Node Records |  |  |
| Number of Connected Node Records |  |  |
| Number of Edge Records |  |  |
| Number of Face Records |  |  |
| Dataset Parameter Field |
| Record Name |  |  |
| Record Id |  |  |
| Horizontal Geodetic Datum |  |  |
| Vertical Datum |  |  |
| Sounding Datum |  |  |
| Compilation Scale of Data |  |  |
| Units of Depth Measurement |  |  |
| Units of Height Measurement |  |  |
| Units of Positional Accuracy |  |  |
| Coordinate Units |  |  |
| Coordinate Multiplication Factor |  |  |
| 3-D (Sounding Multiplication Factor |  |  |
| Comment |  |  |

## Language (S-57 PS 3.11)

The exchange language must be English. Other languages may be used as a supplementary option.    In general, this means that when a national language is used in the textual national attributes the English translation must also exist in the textual international attributes. National geographic names can be left in their original national language in the international attributes, or transliterated or transcribed and used in the international attributes.

All national language attributes must be encoded in the “National Attribute” [NATF] field.

### Use of lexical level 2

If the national language cannot be expressed in lexical levels 0 or 1, the following rules apply:

- the exact spelling in the national language is encoded in the “National Attribute” [NATF] field using lexical level 2.

- translated text, including transliterated or transcribed national geographic names, is encoded in the “International Attributes” [ATTF] field using lexical level 0 or 1.

Where possible international standards should be used for the transliteration of non-Latin alphabets.

# ANNEX A

# Data Product format (encoding) (S-57 PS 6)

| formatName | ISO 8211 | M | 1..* | CharacterString |
| --- | --- | --- | --- | --- |
| version | Version of the format (date, number, etc.) | O | 0..1 | CharacterString |
| characterSet | Character coding standard used for the data set (western European requirement, Greek, Turkish, Cyrillic) | M | 1 | MD_CharacterSetCode (ISO 19115) |
| specification | Name of a subset, profile, or product specification of the format | O | 0..1 | CharacterString |
| fileStructure | Structure of delivery file | O | 0..1 | CharacterString |

# Introduction

This chapter defines the structure and content of the catalogue file and data set file in an exchange set.

The catalogue file is defined in XML schema language and the data set files are encoded as ISO/IEC 8211 data records, fields, and subfields.

Catalogue File (see associated S-101 Catalogue.xsd)

| Name | Cardinality | Value | Type | Remarks |
| --- | --- | --- | --- | --- |
| metadataFileIdentifier | 1 |  | CharacterString | Should this be changed from a mandatory in S-100 part 3 |
| metadataPointOfContact | 1 |  | CI_ResponsibleParty |  |
| metadataDateStamp | 1 |  | Date |  |
| metadataLanguage | 1 | English | CharacterString | All data sets conforming to S-101 PS must use English language |
| fileName | 1 |  | CharacterString |  |
| filePath |  |  | CharacterString |  |
| abstract | 1 |  | CharacterString | E.g. a harbour or port name, between two named locations etc. |
| purpose | 1 | {1} to {3} | CharacterString | 1. New, 2. New Edition, 3. Update |
| specificUsage | 1 | {1} to {3} | CharacterString | Navigation purpose 1. Ocean Passage, 2. Costal, 3. Port Entry |
| editionNumber | 1 |  | CharacterString | when a data set is initially created, the edition number 1 is assigned to it. The edition number is increased by 1 at each new edition. Edition number remains the same for a re-issue. |
| updateNumber | 1 |  | CharacterString | Update number 0 is assigned to a new data set. |
| updateApplicationDate | 0..1 |  | Date |  |
| issueDate | 1 |  | Date |  |
| productSpecificationEditionNumber | 1 |  |  |  |
| editionNumberS-100 | 1 |  |  |  |
| producingAgency | 1 |  | CI_ResponsibleParty |  |
| displayScale | 1 | {1} to {13} | double | Display scale must be one of the 13 predefined scales detailed in Clause 3. |
| horizontalGeodeticDatum | 1 |  | CharacterString |  |
| verticalDatum | 1 |  | CharacterString |  |
| soundingDatum | 1 |  | CharacterString |  |
| boundingBox | 1 |  | EX_GeographicBoundingBox |  |
| boundingPolygon | 1 |  | EX_BoundingPolygon |  |
| comment | 0..1 |  | CharacterString |  |
| cyclicRedundancyCheck | 1 |  | NonNegativeInteger |  |
| layerId | 1..* |  | Double | Identifies the relationship to other layers that are required to view the complete data set. |

## Data set files

The order of data in each base or update cell file is described below:

Data set file

Data set general information record

Data set structure information field structure

Data set Coordinate Reference System record structure

Information records

Information

Vector records

Point

Multi point

Curve

Composite Curve

Surface

Feature records

Meta features

Geo features (ordered from slave to master)

Aggregated features

Theme features

This order of records will enable the import software to check that the child record exists each time the parent record references it (i.e. it will already have read the child record so it will know if it exists or not).

## Records

Records and fields that do not appear in the following tree structure diagrams are prohibited. The order of records in the files must be the same as that described in these tree structure diagrams.

The combination of the file name and the “Name” of the record must provide a unique world-wide identifier of the record.

## Fields

For base cell files, some fields may be repeated (indicated by <R>) and all of their content may be repeated (indicated by *). In order to reduce the volume of data, the encoder should repeat the sequence of subfields, in preference to creating several fields.

## Subfields

Mandatory subfields must be filled by a non-null value.

Prohibited subfields must be encoded as missing subfields values. The exact meaning of missing attribute values is defined in clause ???

In the tables following the tree structure diagrams, mandatory subfields are shown by “M” in the “use” column and prohibited subfields by “P” in the same column. If there is nothing in this column, it means that the use of this subfield is optional. When a subfield value is prescribed, it is indicated in the “value” column. The “comment” column contains general comments and an indication of whether the subfield is ASCII or binary coded.

When encoding new base data sets the record update instruction (RUIN) is always set to insert. When encoding updates it can be set to insert, modify or delete.

## Base cell and update file structure

Base cell file

|

|--<1>--Data Set General Information record

| 	|

| 	|--0001 - ISO/IEC 8211 Record Identifier

| 		|

| 		|--<1>--DSID - Data Set Identification field

| 					|

| 					|--<1>--DSSI - Data Set Structure Information field

|					|

|					|--<R>-- ATTR – Attribute Field (Metadata)

|

|--<1>--Data Set Coordinate Reference System record

|	|

|	|--0001 - ISO/IEC 8211 Record Identifier

| 		|

|		|--<1>--CRID - Coordinate Reference System Record Identifier field

|					|

|					|--<1..2>--CRSH - Coordinate Reference System Header field

|					|

|					|--<1>--CSAX - Coordinate System Axes field

|					|

|					|--<1>-- PROJ - Projection field

|					|

|					*--GDAT - Geodetic Datum field

|					|

|					*--<R>--VDAT - Vertical Datum field

|--<R>--Information record

| 	|

| 	|--0001 - ISO/IEC 8211 Record Identifier

|		|

|		|--<R>-- ATTR – Attribute field

|					|

|					|--<R>-- INAS – Information Association field

|

|--<R>-- Point record

| 	|

| 	|--0001 - ISO/IEC 8211 Record Identifier

| 		|

| 		|--<1>--PRID – Point Record Identifier field

| 					|

| 					|--<R>--ATTR - Attribute field

| 					|

| 					|--<R>--INAS - Vector Record Pointer field

| 					|

| 					| alternate coordinate representations

| 					|

| 					*--C2DI (2): 2-D Integer Coordinate field

| 					|

| 					*--C3DI (4): 3-D Integer Coordinate field

| 					|

| 					*--C2DF (2): 2-D Floating Point Coordinate field

| 					|

| 					*--C3DF (4): 3-D Floating Point Coordinate field

|

|--<R>--Multi Point record

|	|

|	|--0001 - ISO/IEC 8211 Record Identifier

|		|

|		|--<1>--MRID - Multi Point Record Identifier field

|					|

|					|--<R>--ATTR - Attribute field

|					|

|					|--<R>--INAS - Information Association field

| 					|

| 					|--<1>--COCC - Coordinate Control field

|					|

| 					*--<R>--C2DI - 2-D Integer Coordinate field

| 					|

| 					*--<R>--C3DI - 3-D Integer Coordinate field

| 					|

| 					*--<R>--C2DF - 2-D Floating Point Coordinate field

| 					|

| 					*--<R>--C3DF - 3-D Floating Point Coordinate field

|

|--<R>-- Curve record

|	|

|	|--0001 - ISO/IEC 8211 Record Identifier

|		|

|		|--<1>--CRID - Curve Record Identifier field

|					|

|					|--<R>--ATTR - Attribute field

|					|

|					|--<R>--INAS - Information Association field

|					|

|					|--PTAS – Point Association field

|					|

|					|--SECC – Segment Header field

| 					|

| 					|--COCC - Coordinate Control field

|					|

|					| alternate coordinate representation

|					|

| 					*--<R>--C2DI - 2-D Integer Coordinate field

| 					|

| 					*--<R>--C3DI - 3-D Integer Coordinate field

| 					|

| 					*--<R>--C2DF - 2-D Floating Point Coordinate field

| 					|

| 					*--<R>--C3DF - 3-D Floating Point Coordinate field

|

|--<R>-- Composite Curve record

|	|

|	|--0001 - ISO/IEC 8211 Record Identifier

|		|

|		|--<1>--CCID – Composite Curve Record Identifier field

|					|

|					|--<R>--ATTR - Attribute field

|					|

|					|--<R>--INAS - Information Association field

|					|

| 					|--CCOC – Curve Component Control field

|					|

| 					|--<R>--CUCO – Curve Component field

|

|--<R>-- Surface record

|	|

|	|--0001 - ISO/IEC 8211 Record Identifier

|		|

|		|--<1>--SRID – Surface Record Identifier field

|					|

|					|--<R>--ATTR - Attribute field

|					|

|					|--<R>--INAS - Information Association field

|					|

| 					|--<R>--RIAS – Ring Association Field’

|

|--<R>-- Feature Type record

|	|

|	|--0001 - ISO/IEC 8211 Record Identifier

|		|

|		|--<1>--FRID - Feature Type Record Identifier field

|					|

|					|--FOID - Feature Object Identifier field

|					|

|					|--<R>--ATTR - Attribute field

|					|

|					|--<R>--INAS - Information Association field

|					|

|					|--<R>--SPAS - Spatial Association field

|					|

|					|--<R>--FEAS - Feature Association field

|					|

|					|--<R>--THAS - Theme Association field

|					|

|					|-<R>-MASK (*3): Masked Spatial Type field

Field Content

### Data Set Identification field structure

| Field Tag: DSID | Field Name: Data Set Identification |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Record name | RCNM | b11 | {10} - Data Set Identification |
| Record identification number | RCID | b14 | Range: 1 to 232-2 |
| Encoding specification | ENSP | A() | Encoding specification that defines the encoding |
| Encoding specification edition | ENED | A() | Edition of the encoding specification |
| Product identifier | PRSP | A() | Unique identifier for the data product as specified in the product specification |
| Product edition | PRED | A() | Edition of the product specification |
| Application profile | PROF | A() | Identifier that specifies a profile within the data product |
| Dataset file identifier | DSNM | A() | The file identifier of the dataset |
| Dataset title | DSTL | A() | The title of the dataset |
| Dataset reference date | DSRD | A(8) | The reference date of the dataset Format: YYYYMMDD according to ISO 8601 |
| Dataset language | DSLG | A() | The (primary) language used in this dataset |
| Dataset abstract | DSAB | A() | The abstract of the dataset |
| Dataset edition | DSED | A() | The edition of the dataset |
| Dataset topic category | *DSTC | b11 | A set of topic categories |

Data Descriptive Field

### Data Set Structure Information field structure

| Field Tag: DSSI | Field Name: Data Set Structure Information |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Dataset Coordinate Origin X | DCOX | b48 | Shift used to adjust x-coordinate before encoding |
| Dataset Coordinate Origin Y | DCOY | b48 | Shift used to adjust y-coordinate before encoding |
| Dataset Coordinate Origin Z | DCOZ | b48 | Shift used to adjust z-coordinate before encoding |
| Coordinate multiplication factor for x-coordinate | CMFX | b14 | Floating point to integer multiplication factor for the x-coordinate or longitude |
| Coordinate multiplication factor for y-coordinate | CMFY | b14 | Floating point to integer multiplication factor for the y-coordinate or latitude |
| Coordinate multiplication factor for z-coordinate | CMFZ | b14 | Floating point to integer multiplication factor for the z-coordinate or depths or height |
| Number of Information Type records | NOIR | b14 | Number of information records in the data set |
| Number of Point records | NOPN | b14 | Number of point records in the data set |
| Number of Multi Point records | NOMN | b14 | Number of multi point records in the data set |
| Number of Curve records | NOCN | b14 | Number of curve records in the data set |
| Number of Composite Curve records | NOXN | b14 | Number of composite curve records in the data set |
| Number of Surface records | NOSN | b14 | Number of surface records in the data set |
| Number of Feature Type records | NOFR | b14 | Number of feature records in the data set |

Data Descriptive Field

### Attribute field structure

| Field Tag: ATTR | Field Name: Attribute |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Attribute label/code | *ATLB | b12 | A valid attribute code |
| Attribute index | ATIX | b12 | Index (position) of the attribute in the sequence of attributes with the same code and the same parent (starting with 1). |
| Parent index | PAIX | b12 | Index (position) of the parent complex attribute within this ATTR field (starting with 1). If the attribute has no parent (top level attribute) the value is 0. |
| Attribute Instruction | ATIN | b11 | {1} - Insert {2} - Delete {3} - Modify |
| Attribute value | ATVL | A() | A string containing a valid value for the domain of the attribute specified by the subfields above. |

Layer ID

Data Descriptive Field

### Data Set Coordinate Reference System record structure

#### Coordinate Reference System Record Identifier field structure

| Field Tag: CRID | Field Name: Coordinate Reference System Record Identifier |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Record name | RCNM | b11 | {15} - Coordinate Reference System Identifier |
| Record identification number | RCID | b14 | Range: 1 to 232-2 |
| Number of CRS Components | NCRC | b11 | {1} - Single CRS {2} - Compound CRS (2 components) |

Data Descriptive Field

#### Coordinate Reference System Header field structure

| Field Tag: CRSH | Field Name: Coordinate Reference System Header |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| CRS Type | CRST | b11 | see table |
| Coordinate System Type | CSTY | b11 | {1} - Ellipsoidal CS {2} - Cartesian CS {3} - Vertical CS |
| CRS Name | CRNM | A() | Name of the Coordinate Reference System |
| CRS Identifier | CRSI | A() | Identifier of the CRS from an external source. Empty if not defined by reference |
| CRS Source | CRSS | b11 | {1} - IHO CRS Register {2} - EPSG {254} - Other Source {255} - Not Applicable |
| CRS Source Information | SCRI | A() | Information about the CRS source if CRSS = ‘Other Source’ |

Data Descriptive Field

#### Coordinate System Axes field structure

| Field Tag: CSAX | Field Name: Coordinate System Axes |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Axis Type | *AXTY | b11 | see table |
| Axis Unit of Measure | AXUM | b11 | {1} - Degree {2} - Grad {3} - Radian {4} - Metre {5} - International foot {6} - US survey foot |

Data Descriptive Field

#### Projection field structure

| Field Tag: PROJ | Field Name: Projection |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Projection Method | PROM | b11 | see table |
| Projection Parameter 1 | PRP1 | b48 | see table |
| Projection Parameter 2 | PRP2 | b48 | see table |
| Projection Parameter 3 | PRP3 | b48 | see table |
| Projection Parameter 4 | PRP4 | b48 | see table |
| Projection Parameter 5 | PRO5 | b48 | see table |
| False Easting | FEAS | b48 | False easting (Units of measurement according to the coordinate axis ‘Easting’ |
| False Northing | FNOR | b48 | False northing (Units of measurement according to the coordinate axis ‘Northing’ |

Data Descriptive Field

#### Geodetic Datum field structure

| Field Tag: GDAT | Field Name: Geodetic Datum |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Datum Name | DTNM | A() | Name of the geodetic datum |
| Ellipsoid Name | ELNM | A() | Name of the ellipsoid |
| Ellipsoid semi major axis | ESMA | b48 | Semi major axis of the ellipsoid in metre |
| Ellipsoid second parameter type | ESPT | b11 | {1} - Semi minor axis in metres {2} - Inverse Flattening |
| Ellipsoid second parameter | ESPM | b48 | The second defining parameter of the ellipsoid |
| Central Meridian Name | CMNM | A() | Name of the central meridian |
| Central Meridian Greenwich Longitude | CMGL | b48 | Greenwich longitude of the central meridian in degrees |

Data Descriptive Field

#### Vertical Datum field structure

| Field Tag: VDAT | Field Name: Vertical Datum |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Datum Index | DTIX | b11 | Internal identifier of the Vertical Datum |
| Datum Name | DTNM | A() | Name of the Vertical datum |
| Datum Identifier | DTID | A() | Identifier of the datum in an external source |
| Datum Source | DTSR | b11 | {1} - IHO CRS Register {2} - Feature Catalogue {3} - EPSG {254} - Other Source {255} - Not Applicable |
| Datum Source Information | SCRI | A() | Information about the CRS source if DTSR = ‘Other Source’ |

Data Descriptive Field

### Information Type Identifier field structure

| Field Tag: IRID | Field Name: Information Type Record Identifier |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Record name | RCNM | b11 | {150} - Information Type |
| Record identification number | RCID | b14 | Range: 1 to 232-2 |
| Object code | OBJC | b12 | A valid object code |
| Record version | RVER | b12 | RVER contains the serial number of the record edition |
| Record update instruction | RUIN | b11 | {1} - Insert {2} - Delete {3} - Modify |

Data Descriptive Field

### Coordinate Control field structure

| Field Tag: COCC [Upd] | Field Name: Coordinate Control |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Coordinate Update Instruction | COUI | b11 | {1} - Insert {2} - Delete {3} - Modify |
| Coordinate Index | COIX | b12 | Index (position) of the addressed coordinate tuple within the coordinate field(s) of the target record |
| Number of Coordinates | NCOR | b12 | Number of coordinate tuples in the coordinate field(s) of the update record |

Data Descriptive Field

### 2-D Integer Coordinate field structure

| Field Tag: C2DI | Field Name 2-D Integer Coordinate |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Coordinate in Y axis | *YCOO | b24 | Y-coordinate or latitude |
| Coordinate in X axis | XCOO | b24 | X-coordinate or longitude |

Data Descriptive Field

### 3-D Integer Coordinate field structure

| Field Tag: C3DI | Field Name: 3-DInteger Coordinate |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Vertical Datum Id | VDID | b11 | Internal identifier of the Vertical Datum |
| Coordinate in Y axis | *YCOO | b24 | Y- coordinate or latitude |
| Coordinate in X axis | XCOO | b24 | X- coordinate or longitude |
| Coordinate in Z axis | ZCOO | b24 | Z - coordinate (depth or height) |

Data Descriptive Field

### 2-D Floating Point Coordinate field structure

| Field Tag: C2DF | Field Name 2-D Floating Point Coordinate |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Coordinate in Y axis | *YCOO | b48 | Y-coordinate or latitude |
| Coordinate in X axis | XCOO | b48 | X-coordinate or longitude |

Data Descriptive Field

### 3-D Floating Point Coordinate field structure

| Field Tag: C3DF | Field Name: 3-D Floating Point Coordinate |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Vertical Datum Id | VDID | b11 | Internal identifier of the Vertical Datum |
| Coordinate in Y axis | *YCOO | b48 | Y- coordinate or latitude |
| Coordinate in X axis | XCOO | b48 | X- coordinate or longitude |
| Coordinate in Z axis | ZCOO | b48 | Z - coordinate (depth or height) |

Data Descriptive Field

#### Point Record Identifier field structure

| Field Tag: PRID | Field Name: Point Record Identifier |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Record name | RCNM | b11 | {110} - Point |
| Record identification number | RCID | b14 | Range: 1 to 232-2 |
| Record version | RVER | b12 | RVER contains the serial number of the record edition |
| Record update instruction | RUIN | b11 | {1} - Insert {2} - Delete {3} - Modify |

Data Descriptive Field

#### Multi Point Record Identifier field structure

| Field Tag: MRID | Field Name: Multi Point Record Identifier |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Record name | RCNM | b11 | {115} - Multi Point |
| Record identification number | RCID | b14 | Range: 1 to 232-2 |
| Record version | RVER | b12 | RVER contains the serial number of the record edition |
| Record update instruction | RUIN | b11 | {1} - Insert {2} - Delete {3} - Modify |

Data Descriptive Field

#### Curve Record Identifier field structure

| Field Tag: CRID | Field Name: Curve Record Identifier |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Record name | RCNM | b11 | {120} - Curve |
| Record identification number | RCID | b14 | Range: 1 to 232-2 |
| Record version | RVER | b12 | RVER contains the serial number of the record edition |
| Record update instruction | RUIN | b11 | {1} - Insert {2} - Delete {3} - Modify |

Data Descriptive Field

#### Point Association field structure

| Field Tag: PTAS | Field Name: Point Association |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Referenced Record name | *RRNM | b11 | Record name of the referenced record |
| Referenced Record identifier | RRID | b14 | Record identifier of the referenced record |
| Topology indicator | TOPI | b11 | {1} - Beginning point {2} - End point {3} - Beginning & End point |

Data Descriptive Field

#### Segment Control field structure

| Field Tag: SECC [Upd] | Field Name: Segment Control |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Segment update instruction | SEUI | b11 | {1} - Insert {2} - Delete {3} - Modify |
| Segment index | SEIX | b12 | Index (position) of the addressed segment in the target record |
| Number of segments | NSEG | b12 | Number of segments in the update record |

Data Descriptive Field

#### Segment Header field structure

| Field Tag: SEGH | Field Name: Segment Header |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Interpolation | INTP | b11 | {1} - Linear {2} - Arc3Points {3} - Geodetic {4} - Loxodromic |

Data Descriptive Field

#### Composite Curve Record Identifier field structure

| Field Tag: CCID | Field Name: Composite Curve Record Identifier |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Record name | RCNM | b11 | {125} - Composite Curve |
| Record identification number | RCID | b14 | Range: 1 to 232-2 |
| Record version | RVER | b12 | RVER contains the serial number of the record edition |
| Record update instruction | RUIN | b11 | {1} - Insert {2} - Delete {3} - Modify |

Data Descriptive Field

#### Curve Component Control field structure

| Field Tag: CRPC [Upd] | Field Name: Curve Component Control |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Curve Component update instruction | CCUI | b11 | {1} - Insert {2} - Delete {3} - Modify |
| Curve Component index | CCIX | b12 | Index (position) of the addressed Curve record pointer within the CRPT field(s) of the target record |
| Number of Curve Components | NCCO | b12 | Number of Curve record pointer in the CRPT field(s) of the update record |

Data Descriptive Field

#### Curve Component field structure

| Field Tag: CUCO | Field Name: Curve Component |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Referenced Record name | *RRNM | b11 | Record name of the referenced record |
| Referenced Record identifier | RRID | b14 | Record identifier of the referenced record |
| Orientation | ORNT | b11 | {1} - Forward {2} - Reverse |

Data Descriptive Field

#### Surface Record Identifier field structure

| Field Tag: SRID | Field Name: Surface Record Identifier |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Record name | RCNM | b11 | {130} - Surface |
| Record identification number | RCID | b14 | Range: 1 to 232-2 |
| Record version | RVER | b12 | RVER contains the serial number of the record edition |
| Record update instruction | RUIN | b11 | {1} - Insert {2} - Delete {3} - Modify |

Data Descriptive Field

#### Ring Association field structure

| Field Tag: RIAS | Field Name: Ring Association |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Referenced Record name | *RRNM | b11 | Record name of the referenced record |
| Referenced Record identifier | RRID | b14 | Record identifier of the referenced record |
| Orientation | ORNT | b11 | {1} - Forward {2} - Reverse |
| Usage indicator | USAG | b11 | {1} - Exterior {2} - Interior |
| Ring Association update instruction | RAUI | b11 | {1} - Insert {2} - Delete |

Data Descriptive Field

### Feature Type Record Identifier field structure

| Field Tag: FRID | Field Name: Feature Type Record Identifier |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Record name | RCNM | b11 | {100} - Feature type |
| Record identification number | RCID | b14 | Range: 1 to 232-2 |
| Object code | OBJC | b12 | A valid object code |
| Record version | RVER | b12 | RVER contains the serial number of the record edition |
| Record update instruction | RUIN | b11 | {1} - Insert {2} - Delete {3} - Modify |

Data Descriptive Field

### Feature Object Identifier field structure

| Field Tag: FOID | Field Name: Feature Object Identifier |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Producing agency | AGEN | b12 | Agency code |
| Feature identification number | FIDN | b14 | Range: 1 to 232-2 |
| Feature identification subdivision | FIDS | b12 | Range: 1 to 216-2 |

Data Descriptive Field

### Spatial Association field structure

| Field Tag: SPAS | Field Name: Spatial Association |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Referenced Record name | *RRNM | b11 | Record name of the referenced record |
| Referenced Record identifier | RRID | b14 | Record identifier of the referenced record |
| Orientation | ORNT | b11 | {1} Forward {2} Reverse {255} NULL (Not Applicable) |
| Scale Minimum | SMIN | b14 | Denominator of the largest scale for which the feature type can be depicted by the referenced spatial object. If the value is 0 it does not apply. |
| Scale Maximum | SMAX | b14 | Denominator of the smallest scale for which the feature type can be depicted by the referenced spatial object. If the value is 232-1 it does not apply. |
| Spatial Association Update Instruction | SAUI | b11 | {1} - Insert {2} - Delete |

Data Descriptive Field

### Feature Association field

| Field Tag: FEAS | Field Name: Feature Association |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Referenced Record name | *RRNM | b11 | Record name of the referenced record |
| Referenced Record identifier | RRID | b14 | Record identifier of the referenced record |
| Association Code | ASCD | b12 | A valid code for the association |
| Role Code | RLCD | b12 | A valid code for the role |
| Feature Association Update Instruction | FAUI | b11 | {1} - Insert {2} - Delete |

Data Descriptive Field

### Theme Association field

| Field Tag: THAS | Field Name: Theme Association |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Referenced Record name | *RRNM | b11 | Record name of the referenced record |
| Referenced Record identifier | RRID | b14 | Record identifier of the referenced record |
| Theme Association Update Instruction | TAUI | b11 | {1} - Insert {2} - Delete |

Data Descriptive Field

### Masked Spatial Type field structure

| Field Tag: MASK | Field Name: Masked Spatial Type |
| --- | --- |

| Subfield name | Label | Format | Subfield content and specification |
| --- | --- | --- | --- |
| Referenced Record name | *RRNM | b11 | Record name of the referenced record |
| Referenced Record identifier | RRID | b14 | Record identifier of the referenced record |
| Mask Update Instruction | MUIN | b11 | {1} - Insert {2} - Delete |

Data Descriptive Field

# ANNEX B (informative)

S-101 Maintenance - Change Proposal Form

| Organisation |  | Date |  |
| --- | --- | --- | --- |
| Contact |  | Email |  |

Change Proposal Type Select only one option

| 1.Clarification | 2.Correction | 3.Extension |
| --- | --- | --- |

Location Identify all change proposal locations

| S-100 Version No. | Part No. | Section No. | Proposal Summary |
| --- | --- | --- | --- |

Change Proposal

Please provide a detailed change proposal.

Change Proposal Justification

Please provide a suitable explanation for the change and where applicable supporting documentation.

Please send completed forms and supporting documentation to Thomas.Mellor@ukho.gov.uk.

Notes on ISO 8211 by Jonathan Prichard.

I have been thinking about iso8211 and ENC encodings in the context of S-101 for some time. We have been discussing the benefits of multiple encodings and the possibility of reconciling our integrity checks using a canonical form but this has led to a general discussion on the merits (or otherwise) of iso8211 encoding for ENC. iso8211 has been used ever since ENC was invented and is still the bottom layer of encoding within an ENC, i.e the data structures and records are encoded using iso8211's binary format. But how efficient is that format. Since the ENC cell is immutably associated with the file that contains the encoding it's where you should have the least "slack". The encoding of the ENC data has to be transferred via hard media or online transmission to every single customer so any inefficiencies which exist in the way the data is encoded are multiplied massively. I undertook a short survey on the amount of data compared with the amount of non-data within an ENC and the results are presented below:

Iso8211 structure.

The header.

Let's take a look at a typical ENC cell. It is a binary encoding of the ENC. iso8211 is a self describing binary format which uses a header/body structure to deliver its contents. Within a single iso8211 file there is a variable length header which describes all the records within the rest of the file and also their structure. Each record is made up of a number of subfields, each of which has a particular binary representation.

Data records

The header is then followed by a sequence of records. Each record follows the same structure.

1. A 5-byte length indicator for the entire record

2. A 24 byte leader which contains flags about how the record is constructed including an offset to the first byte of data.

3. A catalogue which describes each subfield, its length and offset (from the iso8211 header the reader knows then what sequence the data is in)

4. The data itself. Each record is standalone and contains no CRC values, record counts or other information. The structure of each record is laid down in the Se57 edition 3.1 ENC product specification. So, for example if we look at a simplified ENC update (I have used an update to illustrate the points made as it is a smaller file. A new edition is somewhat larger as we will see...).

Length Offset Name/Length

1. 01894 HEADER

2. 00301 00067 0001 00003 DSID 00195 DSSI 00036

3. 00069 00053 0001 00003 FRID 00013

4. 00069 00053 0001 00003 FRID 00013

5. 00069 00053 0001 00003 FRID 00013

6. 00069 00053 0001 00003 FRID 00013

7. 00069 00053 0001 00003 FRID 00013

8. 00181 00095 0001 00003 FRID 00013 FOID 00009 ATTF 00052 FSPT 00009

9. 00180 00095 0001 00003 FRID 00013 FOID 00009 ATTF 00051 FSPT 00009

10. 00177 00095 0001 00003 FRID 00013 FOID 00009 ATTF 00048 FSPT 00009

11. 00179 00095 0001 00003 FRID 00013 FOID 00009 ATTF 00050 FSPT 00009

12. 00230 00109 0001 00003 FRID 00013 FOID 00009 ATTF 00046 FFPT 00041 FSPT

00009

Finished. 11 records 3482 772

The above table shows a simple ENC update with just the data record and structure left behind. The header is 1894 bytes and then there are 11 data records with varying sizes and data offsets. you can see the update starts with a DSID & DSSI records and then continues with a number of feature related records. What's the point...? The point is the last line where it says "Finished". If you look in record (2) above, the first actual data record you will see that the whole record is 301 bytes long but the data doesn't start until byte 67. This is to allow enough space for the file to encode the DSSI and DSID catalogue entry before describing the data. So there are only 301-67 = 234 bytes of space being used to encode actual data. In fact, over the entire file there are 11 records which make up a file of 3,482 bytes, of which only 772 are used to encode real ENC data. The rest is header (1,894 bytes), record leaders and catalogue descriptors (in fact the "0001" records, of which there are one per record also take up 33 bytes). So, only 22% of the cell contains actual data... The rest is just iso8211 structure.

The point is... iso8211 is very good and very compact at storing data but it works best within a single file. Once you rely on multiple files you duplicate its self-describing overheads.

What does this mean for a base cell?

The example above is an update file. 90% of data which we distribute is actually new editions or new cells. In the case of a base cell the picture is slightly different. The size is not dominated by the 8211 header any more since the cell files are a lot larger. There are a large number of records though and in a lot of these the 8211 overhead of leader + catalogue is much larger than the data which it encompasses. I looked at some GB cells and, sparing the details of the actual records involved, found the following results (I've reproduced just the last line of the output from the previous example:

Cell Name Records Total size Data Size

GB203552.000 269 533152 378010

GB203593.000 1987 327800 214897

GB203596.000 4022 666528 437442

So you can see from the table above that 66-71% of the cell is data, the rest is record overhead!

It would be interesting to see what results could be gleaned from the current world ENC portfolio. I actually had a stab at this and got similar results. Of the 24,424 base and update cells which constituted the last UKHO AVCS base reissue about 8,000 of them were base cells. These on average contain 58% data. The remaining update cells contain about 23% data only. At the very bottom of the pile are updates with only one record. GB5A0052.002, a cancellation cell, contains 3% data only in a file containing 1,887 bytes. There are, however cells with the opposite effect GB200760.001 is 97% data. This is an update which added a small number of features with a high geographical content.

Conclusions:

1. It would seem we compress, encrypt and transport both in hard media and onlinedata but about 40% of it is actual ENC data

2. The rest is specific to the format we have chosen within the product specification to encode the data.

3. Although headers are likely to be highly compressible it does call into question iso8211's use in a world where cell numbers are in the 000s and vessel broadband technology still places a high value on good compression

4. Further analysis of where the choke points are and where the product specification leads to duplication of data could give valuable pointers for S-101 encoding development.

# Comments

NOTE:  some of these concepts will get implemented in later phases of S-101.

Phase 3 or 4.

ACTION:  Need to create a Skin of the Earth Theme and then add the features to that them and include the theme in the FC.

Is this an inconsistency?  The camelCase has been used for the feature class but has not been used for the attribute.  This needs to be addressed and if required applied to the entire document.  Also need to decide whether the same convention is going to be used in the DCCG.

ACTION: Holger  to re-write

ACTION: Need to explain how they will be modelled.  This would go in the application schema.

STAKEHOLDER QUESTION: The end state is to prevent the ? on the ECDIS.  How can we solve this issue.  New enumeration of unknown, presentation library.

AU Comment:  The “?” only needs to be shown if the feature does not symbolise in an intuitive way to the mariner.  Mariners need to pick-report features to find out everything about them anyway, so if the symbology is not compromised too badly, why should the “?” be displayed?

If the attribute is mandatory, how can it not be present in the original data set (the original data set would have failed validation).  Is this statement meant for mandatory attributes for new features inserted by Update?  Does it apply to adding a non-mandatory attribute to the data set (in which case the title of this clause is incorrect).  Why would anyone want to do this?

TSMAD DISCUSSSION NEEDED

I am not sure if I am mis-reading this, but this statement sounds more like a description of an Exchange Set or the SENC rather than an ENC data set.  This also seems to be inconsistent with Cause 11.3.1”Data Sets”, and other uses of the term “data set” throughout the document.

TSMAD DISCUSSION NEEDED

What does this mean?  Suggest remove “within the same layer and”.

TSMAD DISCUSSION NEEDED

Is this going to be defined somewhere?  I know this will  only be meta-data for the cell, but perhaps there needs to be a general statement as to what a “navigational purpose” or “usage band” is and how it applies to ENCs, and leave it up to HOs to determine what “optimum display scale” values they want to use for these bands.  If this is the case, all statements relating to features appearing in more than one cell, and allowable overlaps of data, will need to be standardised.  Otherwise, this could get messy!

JLP:  This should be removed because it is in conflict with the Display scales.

See comment above.

How will an ECDIS work this out if Nav Purpose is not in the cell name and different producers use different "display scales?

JLP:  This is a carryover from S-57, needs to be modified.

ACTION: Change curve interpolation loxodromic

Is this the case for soundings?  Refer 5.1 below.

This is the first time that I have heard about this.  Why does it have to be different from Chain-Node?

How does this fit in with the use of GM_Curve in the Figure and “curves” in the 2nd paragraph above?

JLP:  This needs to be re-written.  S-101 dos not say what cannot be used, but rather what is used.

What has happened to SDAT?

JLP:  It is now part of VDAT.

ACTION: Figure out where to put time and angular measure.  Barrie action.

ACTION:  Specify in the CMFX, CMFY, CMFZ fields that this is the multiplication factor, then remove.

ACTION:  same as positions.  Possibly take this section out and create a new section for coordinate multiplication factors for X,Y, and Z

ACTION: Look at S-100 data quality section.  Write something for Barrie to take to DQWG regarding this section , what should go into this section etc...

S-58 is a guide for validation software developers.  The data should be checked against the relevant Edition of the Product Specification and the DCCG.

JLP:  We need to sort out the checking process.  Is there two separate sets of checks. One for the data producers and one for the ECDIS to see if the data loads properly.

ACTION:  We really need to figure out how to incorporate the parts of S-52 into S-101.  We may end up with a very long product specification.

ACTION: Put in guidelines for producers about density of data and the interest of users.  Should not be a fixed rule.  Will ask the OEM’s.

AU:  Guidelines on density of data (0.3mm between coordinates at optimum intended display scale) has been included in the DCCG.

ACTION:  Where is this designation set?  Is it still needed.

Added to header information of the update file, consider also being in discovery meta data.

ACTION:  Modification to 8211?

Find specific section.

Updates to support files should be listed separate to the data file updates. Discussion for phase 2 or later.

JLP:  need to be clear what can happen with text and picture files.  You can have a scenario where one text file can reference multiple ENCs and that if you update a text and picture file outside of an ENC update then the ECDIS needs to know to replace all instances of that file. Consider XML structure for a super file of all text notes.

Section on updates of text and picture files (support files in general) should not contain much implementation direction, but contain what the plausible scenarios are and it will then be up to 61174 to contain testing scenarios to ensure ECDIS meet these requirements.

This would be covered by the update comment. Unless use case can be found.

Add to questionnaire

Find use case

This needs to be sorted out.

JLP:  Concur

How is the full CRS definition to be encoded?

How is the full CRS definition to be encoded ?

How is the full CRS definition to be encoded? The CRS section refers to the use of a compound CRS to define both horizontal and vertical components of CRS.

Do we need to provide both the bounding box and the polygon information.

ACTION: Holger to provide verbiage --- How are dealing with this for Phase one since lexical level is no longer valid?

This needs to be sorted out.

At present, it is intended that this go in the DCCG, therefore this reference should be to Appendix A.

Should this be a sub-heading (1.5.1) with update cell file being 1.5.2?  Or are the structures the same (there is no structure for an update in this document)?

See comment at 1.5 above.  These clauses need to be sorted out.

COMF

COMF

COMF

This seems out of place in the CRS header field. A coordinate system structure is needed. Some means of identifying which CS definition belongs to a CRS definition is needed. The coordinate system structure needs to list its axis(es) in order. This order is important because it defines the meaning of coordinate values in a tuple – the values follow the same order as the axis(es) – at least this is the ISO 19111 approach.

Missing axis orientation (eg up, down, east, west etc)

What is meant by axis type?

Section 11.5 outlaws projections

Why are False Easting and False Northing defined explicitly in addition to the projection parameters? They are themselves projection parameters.

Length of the semi-major axis of the ellipsoid [ISO 19111]

ISO 19111 also includes isSphere (Boolean) in the list of second defining parameters. If isSphere = true then a value for the second defining parameter is not needed since the sphere is defined by its radius which is specified by the Semi Major Axis.

The value of the second defining parameter (Scale if Inverse Flattening, Length if Semi Minor Axis)

Prefer the term Prime Meridian instead of central meridian in this context.

Longitude of the prime meridian measured from the Greenwich Meridian, positive eastward [ISO 19111]

# Text boxes

3600;&%/GData□Set□Identification▲RCNM!RCID!STRD!ENED!PRSP!PRED!PROF!DSNM!DSTL!DSRD!DSLG!DSAB!DSED\\*DSTC▲(b11,b14,7A,A(8),3A,b11)▼

1600;&□□□Data□Set□Structure□Information▲DCOX!DCOY!DCOZ!CMFX!CMFY!CMFZ!NOIR!NOPM!NOMN!NOCN!NOXN!NOSN!NOFR▲(3b48,10b14)▼

2600;&%/GAttribute▲*ATLB!ATIX!PAIX!ATIN!ATVL▲(3b12,b11,A)▼

1100;&□□□Coordinate□Reference□System□Record□Identifier▲RCNM!RCID!NCRC▲(b11,b14,b11)▼

1600;&%/GCoordinate□Reference□System□Header▲CRST!CSTY!CRNM!CRSI!CRSS!SRCI▲(2b11,2A,b11,A)▼

2100;&□□□Coordinate□System□Axes▲*AXTY!AXUM▲(2b11)▼

1600;&□□□Projection▲PROM!PRP1!PRP2!PRP3!PRP4!PRP5!FEAS!FNOR!▲(b11,7b48)▼

1600;&%/GGeodetic□Datum▲DTNM!ELNM!ESMA!ESPT!ESPM!CMNM!CMGL!▲(2A,b48,b11,b48,A,b48)▼

1600;&%/GVertical□Datum▲DTIX!DTNM!DTID!DTSR!SCRI!▲(b11,2A,b11,A)▼

1100;&□□□Information□Type□Record□Identifier▲RCNM!RCID!OBJC!RVER!RUIN▲(b11,b14,2b12,b11)▼

1100;&□□□Coordinate□Control▲COUI!COIX!NCOR▲(b11,2b12)▼

2100;&□□□2-D□Integer□Coordinate▲*YCOO!XCOO▲(2b24)▼

3100;&□□□3-D□Integer□Coordinate▲VDID\\*YCOO!XCOO!ZCOO▲(b11,3b24)▼

2200;&□□□2-D□Floating□Point□Coordinate▲*YCOO!XCOO▲(2b48)▼

3600;&□□□3-D□Floating□Point□Coordinate▲VDID\\*YCOO!XCOO!ZCOO▲(b11,3b48)▼

1100;&□□□Point□Record□Identifier▲RCNM!RCID!RVER!RUIN▲(b11,b14,b12,b11)▼

1100;&□□□Multi□Point□Record□Identifier▲RCNM!RCID!RVER!RUIN▲(b11,b14,b12,b11)▼

1100;&□□□Curve□Record□Identifier▲RCNM!RCID!RVER!RUIN▲(b11,b14,b12,b11)▼

2100;&□□□Point□Association▲*RRNM!RRID!TOPI▲(b11,b14,b11)▼

1100;&□□□Segment□Control▲SEUI!SEIX!NSEG▲(b11,2b12)▼

1100;&□□□Segment□Header▲INTP▲(b11)▼

1100;&□□□Composite□Curve□Record□Identifier▲RCNM!RCID!RVER!RUIN▲(b11,b14,b12,b11)▼

1100;&□□□Curve□Component□Control▲CCUI!CCIX!NCCO▲(b11,2b12)▼

2100;&□□□Curve□Component▲*RRNM!RRID!ORNT▲(b11,b14,b11)▼

1100;&□□□Surface□Record□Identifier▲RCNM!RCID!RVER!RUIN▲(b11,b14,b12,b11)▼

2100;&□□□Ring□Association▲RRNM!RRID!ORNT!USAG!RAUI▲(b11,b14,3b11)▼

1100;&□□□Feature□Type□Record□Identifier▲RCNM!RCID!OBJC!RVER!RUIN▲(b11,b14,2b12,b11)▼

1100;&□□□Feature□Object□Identifier▲AGEN!FIDN!FIDS▲(b12,b14,b12)▼

2100;&□□□Spatial□Association▲*RRNM!RRID!ORNT!SMIN!SMAX!SAUI!▲(b11,b14,b11,2b14,b11)▼

2100;&□□□Feature□Association▲*RRNM!RRID!ASCD!RLCD!APUI▲(b11,b14,2b12,b11)▼

2100;&□□□Theme□Association▲*RRNM!RRID!TAUI▲(b11,b14,b11)▼

2100;&□□□Masked□Spatial□Record▲*RRNM!RRID!MUIN▲(b11,b14,b11)▼