## Slide 1: 15th Meeting of the South West Pacific Hydrographic Commission Technical Workshop on Implementing Hydrographic Governance
IHO CB Strategy and importance of MSI
Basic steps for implementing MSI

## Slide 2
IHO CB Strategy
www.iho.int  Capacity Building  CB Strategy

## Slide 3
Introduction
IHO CB Strategy
Strategic aspect of MSI
What is MSI
Basic steps to implement MSI
Conclusion
Summary

## Slide 4
Capacity Building (CB) - Concept
CB is defined as the process by which the IHO assesses and assists in sustainable development and improvement of the States, to meet the objectives of the IHO and the obligations and recommendations related to hydrography, charting and maritime safety as described in SOLAS Chapter V, UNCLOS and other international instruments.
Introduction

## Slide 5
Capacity Building
Capacity Building is a strategic objective of the IHO.
Introduction

## Slide 6
Capacity Building Sub-Committee (CBSC)
The CBSC was established to coordinate the CB efforts, under the IRCC.
The CBSC is the guardian of the IHO CB Strategy.
Introduction

## Slide 7
Introduction
IHO CB Strategy
Strategic aspect of MSI
What is MSI
Basic steps to implement MSI
Conclusion
Summary

## Slide 8
Capacity building is a vital component of the efforts of intergovernmental technical organizations to support the development goals of the UN. The IHO is committed to matching its efforts to those of the IMO, the IOC, the IALA, the FIG and other organizations working in allied fields.
IHO CB Strategy

## Slide 9
Principles:
national needs should be assessed firmly against the 3 CB phases
capacity building projects should be coordinated regionally and through regional cooperation
the national administration of a State with developing hydrographic services must embrace and support the concept of CB as being in its national interest
IHO CB Strategy

## Slide 10
Principles:
funding of Non-MS is generally limited to technical visits and Phase 1 projects, awareness and technical assistance
IHO CB Strategy

## Slide 11
Phases of development of hydrographic surveying and nautical charting capability:
Phase 1: MSI
Phase 2: surveying
Phase 3: nautical charting
IHO CB Strategy

## Slide 12
Phase 1: MSI
IHO CB Strategy
Phases of Development | National Activity
Phase 1 Collection and circulation of nautical information, necessary to maintain existing charts and publications up to date | Form National Authority (NA) and/or National Hydrographic Coordinating Committee (NHCC). Create/improve current infrastructure to collect and circulate information Strengthen links with charting authority to enable updating of charts and publications Minimal training needed Strengthen links with NAVAREA Coordinator to enable the promulgation of safety information

## Slide 13
Phase 2: surveying
IHO CB Strategy
Phases of Development | National Activity
Phase 2 Creation of a surveying capability to conduct: Coastal projects Offshore projects | Establish capacity to enable surveys of ports and their approaches Maintain adequate aids to navigation Build capacity to enable surveys in support of coastal and offshore areas Build capacity to set up hydrographic databases to support the work of the NA/NHCC Provide basic geospatial data via MSDI Requires funding for training, advising & equipment or contract survey

## Slide 14
Phase 3: nautical charting
IHO CB Strategy
Phases of Development | National Activity
Phase 3 Produce paper charts, ENC and publications independently | The need shall be thoroughly assessed. Requires investment for production, distribution and updating Alternatively, bi-lateral agreements for charting can provide easier solutions in production and distribution (of ENC through RENCs) and rewards. Further development of MSDI

## Slide 15
Long term objectives:
• to enable all states with navigable waters to achieve Phase 1 and to develop a national plan to put in place appropriate elements of Phases 2 and 3 or alternative cooperative regional or bilateral arrangements.
IHO CB Strategy

## Slide 16
Long term objectives:
• in conjunction with the IMO’s Technical Cooperation Committee and IALA’s World Wide Academy a series of ‘country profiles’ will be developed to accurately measure the state of hydrography in every coastal State.
IHO CB Strategy

## Slide 17
The CB Process (the 4 As):
Degree of engagement (X = Low, XX = Medium-low, XXX = Medium-high, XXXX = High)
IHO CB Strategy
 | IHO | CBSC | RHC | Country
Awareness | XXX | XXXX | XX | X
Assessment | X | XXX | XXXX | XX
Analysis | XXXX | XXX | XX | X
Action | X | XX | XXX | XXXX

## Slide 18
Assessment of needs is done by:
high-level visits
technical visits
risk analysis
IHO CB Strategy

## Slide 19
CB annual cycle:
Assessment (RHC)
Planning (RHC)
Submission for support (RHC)
Preparation of the CB Plan (Secretariat)
Adoption of the CBWP (CBSC)
Implementation and impact assessment (RHC, Secretariat, CBSC, IRCC, Council)
IHO CB Strategy

## Slide 20
Introduction
IHO CB Strategy
Strategic aspect of MSI
What is MSI
Basic steps to implement MSI
Conclusion
Summary

## Slide 21
Why is MSI so important?
Maritime Safety Information is the fundamental piece of information that needs to be made available to the mariner to ensure safety of navigation!
Through the WWNWS the mariner will receive the elements to update the nautical charts and others.
Strategic aspects of MSI

## Slide 22
Why is MSI so important?
Without MSI, hydrographic services (SOLAS V/9) can’t be provided
Strategic aspects of MSI

## Slide 23
Introduction
IHO CB Strategy
Strategic aspect of MSI
What is MSI
Basic steps to implement MSI
Conclusion
Summary

## Slide 24
Reference:
IHO Publication S-53 Joint IMO/IHO/WMO Manual on Maritime Safety Information (January 2016)
What is MSI

## Slide 25
Maritime Safety Information (MSI) means navigational and meteorological warnings, meteorological forecasts and other urgent safety-related messages broadcast to ships.
What is MSI

## Slide 26
Maritime safety information service means the internationally and nationally coordinated network of broadcasts containing information which is necessary for safe navigation.
What is MSI

## Slide 27
Maritime safety information is grouped in:
Local warnings (ports)
Coastal warnings (national coordinator)
Sub-area warnings (Sub-area coordinator)
NAVAREA warnings (NAVAREA coordinator)
What is MSI

## Slide 28
Maritime safety information is promulgated by the Global Maritime Distress and Safety System (GMDSS) means the global communications service based upon automated systems, both satellite and terrestrial, to provide distress alerting and promulgation of maritime safety information for mariners.
What is MSI

## Slide 29
SafetyNET
GMDSS
NAVTEX
What is MSI

## Slide 30
NAVAREAS

## Slide 31
Introduction
IHO CB Strategy
Strategic aspect of MSI
What is MSI
Basic steps to implement MSI
Conclusion
Summary

## Slide 32
What do I need to put MSI in place?
A national coordinator
An email account
A telephone line
Access to the relevant information
The will to do it!
Basic steps to implement MSI

## Slide 33
Designate a National Coordinator
Train the National Coordinator
Establish a communication plan to access relevant information
Collect the relevant information
Draft the MSI messages
Send MSI messages to the NAVAREA Coordinator
Basic steps to implement MSI

## Slide 34
Examples of MSI message (1):
NAVAREA XIII 145/14
SEA OF OKHOTSK.
WESTERN PART.
CHART ________ (INT _______ ).
ISOLATED DANGER BUOY 54-49.9N 142-04.1E MISSING
Basic steps to implement MSI

## Slide 35
Examples of MSI message (2):
NAVAREA X 346/14
AUSTRALIA NORTH EAST COAST.
ARCHER POINT.
CHART ________ (INT _______ ).
LIGHT 15-35.6S 145-19.7E UNRELIABLE.
Basic steps to implement MSI

## Slide 36
Examples of MSI message (3):
NAVAREA VII 345/14
MOZAMBIQUE CHANNEL.
PORT OF MAPUTO.
CHART ________ (INT _______ ).
BAIXO RIBEIRO LIGHT 25-54.6S 032-48.1E UNLIT
Basic steps to implement MSI

## Slide 37
Examples of MSI message (4):
NAVAREA III 45/14
TUNISIA, EAST COAST.
RADE DE SFAX.
CHART ________ (INT _______ ).
WRECK REPORTED IN VICINITY 34-41.5N 010-54.0E.
Basic steps to implement MSI

## Slide 38
Examples of MSI message (5):
NAVAREA VI 16/14
ARGENTINA, EAST COAST.
VALDES PENINSULA.
CHART ________ (INT _______ ).
WRECK OF FISHING VESSEL REPORTED 42-05.75S 063-22.00W.
Basic steps to implement MSI

## Slide 39
Examples of MSI message (6):
NAVAREA IV 210/14
JAMAICA, SOUTHWARDS.
PEDRO BANK.
CHART 26050
SOUTHWEST ROCK LIGHT, FL (3) 10 SECONDS 7 METRES 5M ESTABLISHED 16-47.55N 078-11.48W.
Basic steps to implement MSI

## Slide 40
Examples of MSI message (7):
NAVAREA VII 58/14
SOUTH ATLANTIC OCEAN.
CHART ________ (INT _______ ).
TUG RIG DELIVERER WILL TOW VESSEL AGATE ISLAND FROM RECIFE, BRAZIL TO CAPE TOWN, COMMENCING 09 JUN 14, ETA CAPE TOWN 09 JUL 14. LENGTH OF TOW 550 METRES WIDE BERTH REQUESTED.
Basic steps to implement MSI

## Slide 41
Examples of MSI message (8):
NAVAREA II 78/14
PAZENN.
CHART ________ (INT _______ ).
1. SIX CONTAINERS ADRIFT IN VICINITY
47-37N 006-26W AT 262200 UTC JUL 14.
2. CANCEL THIS MSG 292200 UTC JUL 14
Basic steps to implement MSI

## Slide 42
Examples of MSI message (9):
NAVAREA I 112/14
CELTIC SEA.
CELTIC DEEP.
CHART ________ (INT _______ ).
1. DERELICT FISHING VESSEL REPORTED ADRIFT 51-25.5N 006-21.9W AT 132210 UTC NOV 14.
2. CANCEL THIS MSG 162210 UTC NOV 14.
Basic steps to implement MSI

## Slide 43
Examples of MSI message (10):
NAVAREA XIV 67/14
NEW ZEALAND.
COOK STRAIT.
CHART ________ (INT _______ ).
SAR OPERATION IN PROGRESS CENTRED ON 40-24.5S 173-57.6E. ALL VESSELS NOT UNDER INSTRUCTION OF THE SAR MISSION CONTROLLER RCCNZ ARE REQUESTED TO KEEP A WIDE BERTH.
Basic steps to implement MSI

## Slide 44
Examples of MSI message (11):
NAVAREA I 25/14
ENGLAND SOUTH COAST.
LYME BAY, BEER HEAD WESTWARDS.
CHART ________ (INT _______ ).
ANTIPOLLUTION OPERATIONS IN PROGRESS 50-40.0N 003-10.0W. A TEMPORARY EXCLUSION ZONE RADIUS TWO MILES HAS BEEN ESTABLISHED CENTRED ON THIS POSITION. SHIPS ARE PROHIBITED FROM ENTERING OR REMAINING WITHIN THIS ZONE.
Basic steps to implement MSI

## Slide 45
Examples of MSI message (12):
NAVAREA XII 222/14
COSTA RICA.
SOUTHWEST COAST.
CHART ________ (INT _______ ).
SHOALS LOCATED:
A. 28 METRES 08-17.1N 083-53.1W.
B. 13.5 METRES 08-19.2N 083-54.2W.
C. 27 METRES 08-21.8N 083-56.1W.
Basic steps to implement MSI

## Slide 46
Examples of MSI message (13):
NAVAREA IV 231/14
NORTH PACIFIC OCEAN.
JASPER SEAMOUNT.
CHART ________ (INT _______ ).
DISCOLOURED WATER WITH SUBMARINE VOLCANIC ACTIVITY REPORTED VICINITY 30-27N 122-40W AT 190110 UTC FEB 14
Basic steps to implement MSI

## Slide 47
Examples of MSI message (14):
NAVAREA VII 256/14
ATLANTIC OCEAN.
ANGOLA.
CHART ________ (INT _______ ).
M/V GECO EMERALD IS CONDUCTING SEISMIC SURVEY OPERATIONS AND TOWING SIX STREAMERS AT 8000 METRE LENGTH WITH ENDS MARKED WITH YELLOW BUOYS AND BLUE FLASHING LIGHTS IN AREA BOUNDED …
Basic steps to implement MSI

## Slide 48
Examples of MSI message (15):
NAVAREA XIII 55/14
TATARSKIY PROLIV.
PROLIV LAPERUZA.
CHART ________ (INT _______ ).
1. CABLE LAYING OPERATIONS IN PROGRESS BY SHIP SUBARU UNTIL 30 JUN 14 ALONG LINE JOINING 45–56.8N 140–00.7E, 46–36.5N 140–53.6E, 46-36.6N 141–29.0E, 46–38.9N 141–47.3E, 46–36.5N 141-49.8E. WIDE BERTH REQUESTED.
Basic steps to implement MSI

## Slide 49
Examples of MSI message (16):
NAVAREA VII 321/14
MADAGASCAR.
PORT OF MAJUNGA.
CHART ________ (INT _______ ).
TWO TIDE GAUGES AND A CURRENT METER MOORED IN AREA BOUNDED BY: 15-32.70S, 15-33.03S, 046-11.77E AND 046-11.53E.
Basic steps to implement MSI

## Slide 50
Examples of MSI message (17):
NAVAREA XI 95/14
HOKKAIDO, EAST COAST AND OKHOTSK COAST.
TSUNAMI WARNING.
TSUNAMI WARNING AT 130436 UTC JAN 14. DANGEROUS DRIFTING OBJECTS, CHANGE OF DEPTH AND DAMAGE OF HARBOUR FACILITIES OR NAVIGATIONAL AIDS MAY OCCUR.
Basic steps to implement MSI

## Slide 51
Examples of MSI message (18):
SUBAREA I 233/14
SOUTHERN BALTIC, THE BELTS, THE SOUND.
THE WATER LEVEL IS EXPECTED TO DROP 80 CM BELOW MSL AFTERNOON 20 AUG 14, RISING TO ABOUT MSL MORNING 21 AUG 14.
Basic steps to implement MSI

## Slide 52
Introduction
IHO CB Strategy
Strategic aspect of MSI
What is MSI
Basic steps to implement MSI
Conclusion
Summary

## Slide 53
It is much more inexpensive to send MSI than to remediate the damages caused by the lack of proper information and outdated charts.
Conclusion

## Slide 54: IHO Secretariat, here to help you! www.iho.int abri.kampfer@iho.int alberto.neves@iho.int