## Slide 1: SOUTH WEST PACIFIC
This story takes you on a journey to the South West Pacific, where in 2018, LINZ mapped the seafloor to update nautical charts. The expedition revealed, in unprecedented detail, beautiful atolls, coral reefs and underwater volcanoes!

## Slide 2
Much of Tongan waters have charts that have not been updated since the late 1800's. With fresh eyes and the latest in seafloor mapping technology, LINZ, EOMAP, GDS and iXblue, are mapping the seabed to make navigation safer and chart undocumented features on the seafloor.

## Slide 3: Pacific Regional Navigation Initiative LINZ HI 60, 61, 62 & 63
Multi-sensor Approach
  HS60 (Tonga) SDB, ALB, MBES
  HS61 (Cook Islands) SDB only
  HS62 (Niue) SDB and ALB
  HS63 (Tokelau) SDB only
  Tide gauge install & datum computations
  Requirement: LINZ-1 Standard (<40m), LINZ-2 (>40m)
  Survey Contractors: EOMAP, Geomatics Data Solutions and iXblue
Notes: iXBlue Project for LINZ

## Slide 4: Satellite Derived Bathymetry
Cost effective solution to obtain tightly georeferenced imagery, topography and shallow water bathymetry over large areas
Ideally suited to the SW Pacific where water clarity is high and the area is characterized by hundreds of small islands/atolls and reefs over a large area
Ideal tool to plan higher resolution/higher cost surveys. Has already been used by LINZ to reposition islands, atolls and reefs with SDB data
Notes: iXBlue Project for LINZ

## Slide 5: SDB coverage
Notes: iXBlue Project for LINZ

## Slide 6: Satellite-Derived Bathymetry Beveridge Reef Niue
RGB
SDB

## Slide 7: SDB Beveridge Reef Niue

## Slide 8: Airborne Lidar Bathymetry
Cost effective solution to obtain tightly georeferenced imagery, topography and shallow water bathymetry over large areas
Ideally suited to the SW Pacific where water clarity is high and the area is characterized by hundreds of small islands/atolls and reefs over a large area
Latest generation systems have sufficient data density to reliably meet the LINZ-1 feature detection requirement to 20m
Excellent sensor solution to remove a huge amount of navigational risk for any vessel mounted survey campaign
Provides a host of other valuable information that can be used for many purposes other than safety of navigation

## Slide 9: ALB/MBES planned coverage
Notes: iXBlue Project for LINZ

## Slide 10: Tides and Geodetics
Notes: iXBlue Project for LINZ

## Slide 12: TTechnical note:
GDS used the Shallow water, high resolution Leica Chiroptera system and chose not to also use the deeper water HawkeEye system.
Feature detection survey so whilst the bathymetry from the HawkeEye system might have been interesting, it would have been wasted time and money.
First time that the Leica Chiroptera 4x system had been used on a large commercial survey project. Unprecedented sounding density.

## Slide 13: Airborne LiDAR Bathymetry
Beveridge Reef, Niue

## Slide 14: Multi-beam Bathymetry
Multi-vessel solution
First time iXblue has used an unmanned survey vessel on a contract survey
MBES to be used in >18m water (due to ALB)
USV shows promise to reduce the time on task and cost of large area surveys
Notes: iXBlue Project for LINZ

## Slide 15: Vessel Mobilisation - NZ
Notes: iXBlue Project for LINZ

## Slide 16: Mothership – MV SILENT WINGS
Note: movie removed due to the size
Notes: iXBlue Project for LINZ

## Slide 17: DriX Survey System
INS iXblue PHINS C7
MBES Kongsberg Em2040C dual swath/FM Chirp
GNSS Trimble SPS855 & Septentrio AsterX-U
SVS Valeport miniSVS
CARIS Onboard
Notes: iXBlue Project for LINZ

## Slide 18: SILENT WINGS Survey System
INS iXblue ROVINS (x2)
MBES Kongsberg Em2040C dual swath/FM Chirp
SBES Odom 200/33 kHz
GNSS Fugro MarineStar 9205 (G2+)
SVS Valeport miniSVS, RapidSVT, SWIFT
Teledyne OceanScience SVP winch
QPS QINSy
CARIS HIPS
Notes: iXBlue Project for LINZ

## Slide 19: RESULTS
DriX acoustically quiet
45dB Stopped, engines off
(+1dB @12Kts)
Loss of seabed acoustic return
at 320m for SW
100% coverage at 380m for DriX
Improved bathymetric quality results
for backscatter interpretations and WC
analysis
Notes: iXBlue Project for LINZ

## Slide 20: RESULTS
Complimentary datasets
Average mean depth difference of 1.3cm
between SW and DriX on overlapping
surfaces
Complete merging of backscatter data
Notes: iXBlue Project for LINZ

## Slide 21: The case of the missing shipwreck
SDB: Dec 2017
ALB: May 2018

## Slide 22: Multibeam Data

## Slide 23: Reminder of the utility of hydrographic survey for safety of navigation. From 300m to 6m deep!

## Slide 25: Coral Reefs

## Slide 26: Underwater Volcanoes

## Slide 27
The optimal solution
Survey Summary | DriX | Silent Wings
Overall Line km | 7,450 | 
Line km | 2,360 | 5,090
% of total line km | 32% | 68%
Effective survey time (Hours) | 166 | 358
Total use (days) | 18 | 38
Average survey speed (knots) | 7.6 | 7.6
Average transit speed (knots) | 10 | 10
Endurance at average survey speed (days) | 5 | 7
Fuel consumption at average survey speed (Litres/day) | 50 | 3,600

## Slide 28: Update – What’s next?
The optimal solution ALB data final stages of cleaning
MBES data will be cleaned in the coming weeks
Merge ALB and MBES
Compile and render ROS (Q2 2019)
Analyse SDB, ALB and MBES datasets to better understand performance of each
Possibility to revisit the SDB data after it has been ground truthed to see if it can be further refined

## Slide 29: Project highlights:
Series of firsts:
First time in the world a multi-sensor survey of this scale had been attempted
First time the Chiroptera 4x ALB had been used on large area survey
First time iXblue DriX USV used on contract survey

## Slide 30: Multi-sensor Approach
The optimal solution The optimal solution for survey in SW Pacific SDB, ALB, USVs deliver data quicker cleaner cheaper
for a safer maritime environment

## Slide 31: We LOVE what we do!

## Slide 32: Acknowledgements:
Mr Adam Greenland (LINZ National Hydrographer)
Dr Magnus Wettel (EOMAP)
Ms Carol Lockhart (GDS)
Tongan Officials

## Slide 33: Acknowledgements:
SBES invented in 1913

## Slide 34
Thank You