# INTERNATIONAL HYDROGRAPHIC	ORGANISATION HYDROGRAPHIQUE

ORGANIZATION	INTERNATIONALE

NAUTICAL CARTOGRAPHY WORKING GROUP

(NCWG)

[A Working Group of the Hydrographic Services and Standards Committee (HSSC)]

| Chair: Jeff WOOTTON Australian Hydrographic Service 8 Station Street, Wollongong, NSW, 2500 Australia | Secretary: Andrew HEATH-COLEMAN United Kingdom Hydrographic Office Admiralty Way, Taunton, Somerset United Kingdom |
| --- | --- |
| Tel: +61 2 4223 6508 | Tel: +44 1823 337900 ext 3656 |
| Email: jeff.wootton@defence.gov.au | Email: andrew.coleman@ukho.gov.uk |

NCWG Letter: 15/2015

UKHO ref: HA317/010/031-12

AHS ref: fAA160756; fAA158960; fAA155722

Date 1 December 2015

Dear Colleagues

Subject: Covered Berths and Buildings In or Over the Water (follow-up to NCWG Letter 13/2015)

Thank you to the 21 Working Group members and ESRI who responded to NCWG Letter 13/2015. As usual, we have included a consolidated list of the responses, together with my responses to comments.

You will see that all respondents agreed with the revised versions of the specifications, and a clear majority preferred to use small dashes (C32/33) as the outer limit of the urban area.

We can now go ahead and include these specifications in the list of changes to be advised to IHO Member States prior to issuing S-4 Edition 4.6.0. There is no need to respond to this letter, unless you have further comments in response to the Chair comments at Annex A.

Yours sincerely,

Jeff Wootton,

Chair NCWG.

Annex A: Consolidated response to NCWG Letter 13/2015

Annex B: B-321.9 Covered Berths and B-370.9 Buildings In or Over the Water: Final versions.

Annex A to NCWG Letter 15/2015

Covered Berths and Buildings In or Over the Water

Consolidated Response Form

|  | Question | Yes | No |
| --- | --- | --- | --- |
| 1 | Do you agree with the revised structure, wording and graphics for the new paragraph B-321.9? | AU, BR, CA, DE, DK, ES, ESRI, FI, FR, GR, ID, IN, JP, LV, MX, NL, NO, SE, UA, UK, US, ZA |  |
| 2 | Do you agree with the revised new clause B-370.9 (noting further minor amendment may be required dependant on response to question 3 below)? | AU, BR, CA, DE, DK, ESRI, FI, FR, GR, ID, IN, JP, LV, MX, NL, NO, SE, UA, UK, US, ZA |  |
| 3 | What line style should be used for the outer boundary (apparent coastline) for an area of buildings above water (select a or b, not both): C32/33 |  |  |
|  |  | DK, BR, DE, DK, ESRI, FI, FR, GR, ID, IN, JP, LV, MX, NL, NO, SE, UA, UK, US, ZA |  |
|  | N1.1 | AU, CA, ES |  |

Further comments:

No further examples of graphics to support the textual guidance at B-370.9 were received.

Chairman: ID example C will be used in S-4 (after moving the settlement name within the extract, as would be expected to clarify that this is an urban area).

GERMANY

In the example A from Indonesia (hopefully we will get some more) the outer limit of the Houses above water area is a dashed coastline similar to C2 (a bold line according to B-310.1). In S-4 and INT 1 we have for C32/C33 examples with a medium and a bold line but not a fine line (line description according to B-127). I propose to delete “fine” from the last sentence of the paragraph.

Chairman: The dashes on the Indonesian examples are certainly shorter than would be expected for C2, although it is difficult to determine by eye whether the line is ‘fine’. The dashed line in S-4 at C32 and C33 is definitely a ‘fine’ line (visibly thinner that the coastline) as stated in S-4 B-312.2 and B-312.4. However, looking at the three official INT1s, the line at C32 is thinner than coastline. The line at C33 has longer dashes and may be the same thickness as the coastline (although in the small graphics it is difficult to be sure). It is a pity there is this inconsistency (which could be addressed at next editions of INT1, although unlikely to be an issue for the mariner). I think ‘fine’ should be retained in new B-370.9 to be consistent with the text at B-312.2 and B-312.4.

INDIA

B321.9 Covered berths: Example 1 in Annex B to NCWG Letter 13/15 is recommended.

Chairman: Agree, but is not an option for many offices.

INDONESIA

B-321.9 wording has given a complete choice in regards of the printing capabilities of HOs, and the graphic or profile diagram gives a thorough interpretation of the mariners to the berthing facility.

For B-370.9 would accommodate either single building or block building and their respective representation using urban tint and its explanatory text.

Chairman: Agree.

Annex B to NCWG Letter 15/2015

Covered Berths and Buildings In or Over the Water

(Final versions)

B-321.9 	A covered berth should be labelled by an appropriate descriptive legend or name, for example: ‘Covered wharf’; ‘Hull All-Weather Terminal’. Transparent urban tint (see B-370.4), representing the roof, may be inserted over the charted hydrography so that any shallow water tint shows through. The urban tint should be surrounded by a black line, finer than coastline. If a transparent urban tint is not possible, then the building should be charted in accordance with national practice for buildings (D1) with land tint and/or solid urban tint, associated legend and clearance height. If required, the depth of water at the berth should also be shown in parenthesis, for example (1.8m). A vertical clearance (see B-380.1-2) should be shown, if known. Examples:

A profile diagram may be included if considered useful (see B-390).

B-370.9 	Buildings in or over the water.  Buildings are sometimes erected in or over the water, beyond the coastline. These may be individual buildings, sometimes of a specialized nature, such as a fort, or an extension of urban areas on piles or stilts. In the latter case, it may be possible for small vessels to navigate amongst (or even under) the buildings, while it represents an impenetrable mass for larger vessels and appears to the eye or on radar images as apparent coastline. This is similar, in some respects, to the situation with mangroves, see B-312.4, and merits similar treatment.

In general, the same principles as for buildings on land should be followed. Individual buildings should be charted in outline with land tint if scale allows, or by symbols if the chart scale is too small (D5 or an appropriate selection from E). Urban areas (when the density of buildings is too close to show by symbols) should be charted in the same way as urban areas on land, depending on national practice: that is as building blocks with ‘shadow line’ or using urban tint (see B-370.4). If using building blocks, they should be filled with land tint. If using urban tint, if possible it should be ‘transparent’ so that the intertidal or shallow water tint remains visible. An explanatory legend such as ‘houses above water’, or equivalent, should be inserted. The high water line should be charted as coastline (C1 or C2, as appropriate) and the outer boundary (apparent coastline) of the urban area as a fine dashed line (similar to C32/33).

For example:

(Source: Dinas Hidro – Oseanografi (Dishidros), Indonesia)

For covered berths, see B-321.9. For houseboats, see B-330.