INTERnationAL HYDROGRAPHIC ORGANIZATION

S-101 ENC VALIDATION CHECKS

Published by the

International Hydrographic Bureau

MONACO

Page intentionally left blank

CONTENTS

1.	Introduction	1

2.	List of ENC Validation Checks	7

2.1.	Checks relating to S-101 Data Structure	7

2.2.	Checks relating to ENC Product Specification	22

2.3.	Exchange set Level checks……………………………………….…………………………..32

2.4.	Checks relating to Use of Object Catalogue for ENC	………... 34

2.5            Checks relating to allowable attribute values for particular feature classes…… 70

1. INTRODUCTION

This appendix specifies the minimum checks that producers of ENC validation tools should include in their validation software. This software must be used by hydrographic offices to help ensure that their ENC data are compliant with the S-101. The checklist has been compiled for the IHO from lists of checks provided by a number of hydrographic offices and software companies.

1.1 Document Layout

The validation checks are laid out as follows;

| 2.4 Checks relating to Use of the Object Catalogue for ENC |
| --- |
| No. | Check description | Check message | Check solution | Conformity to: | Cat |
| 1500 | For each LandArea feature of geometric primitive surface which OVERLAPS a CableArea or SeabedArea feature of geometric primitive surface. | CableArea or SeabedArea overlaps a LandArea feature. | Ensure CableArea or SeabedArea features do not overlap LandArea features | Logical consistency | W |
| 1501 | Check removed. |  |  |  |  |
| 1502 | For each spatial feature which contains the attribute HORDAT | HORDAT used in a spatial feature. | Remove HORDAT. | 2.1.1 | E |

Columns are as follows

1. Check number

2. Check description written in a defined syntax (wherever feasible) as defined in this document (1.4).

3. Check message to provide the user with meaningful information.

4. Check solution, suggested action to rectify a warning or error.

5. Conformity to, reference to the relevant location within the DCEG or PS

6. Check classification - Critical Error (C), Error (E), Warning (W) (see 1.2)

1.2 Check Classification

The check classification is intended to ensure that published ENC data is free of errors which would affect the use of an ENC in ECDIS. In some cases it has been necessary to diverge from the strength of wording used in the S-101 ENC Product Specification or the Data Classification and Encoding Guide for ENC. In such cases the impact on the user has been the overriding factor for consideration. The classifications have the following meanings;

| C | Critical Error | An error which would make an ENC unusable in ECDIS through not loading or causing an ECDIS to crash or presenting data upon which is unsafe for navigation. |
| --- | --- | --- |
| E | Error | An error which may degrade the quality of the ENC through appearance or usability but which will not pose a significant danger when used to support navigation. |
| W | Warning | An error which may be duplication or and inconsistency which will not noticeably degrade the usability of an ENC in ECDIS. |

At a minimum validation software must group validation reports using these categories. They may also support sub-grouping of related checks such as those relating to geometric validity or attribute consistency. Software may allow checks of type error or warning to be deselected completely or by such categories.

1.3 Minimum Check Standard

The intention is that Critical Errors will become mandatory once software conforming to S-58 5.0.0 is available and in use by ENC producers. In order to support this transition a test dataset and a mechanism to certify that the validation tools reflect the current standard will be developed. The implementation date of mandatory checks for ENC producers will be announced in due course by IHO circular letter at least two months in advance of the implementation date.

1.4 Guidecurves on the check syntax

In order to ensure that checks can be interpreted clearly and consistently a defined syntax has been used for the reworded checks wherever possible. Each check is a statement which generates a warning/error if the expression returns ‘true’.

In the below example the check would return true and give an error for each Berths feature which carries the attribute verticalDatum;

| No | Check description | Check Message | Check solution | Conformity to: | Cat |
| --- | --- | --- | --- | --- | --- |
| 1571 | For each Berths feature where verticalDatum is Present. | Prohibited attribute verticalDatum populated for a Berths feature. | Remove value of verticalDatum. | 4.6.2 | E |

The elements of the syntax are defined as follows;

1.4.1 Comparison and Logical Operators

The following comparison and logical operators are used;

Equal

Not equal

Less than

Less than or equal to

Greater than

Greater than or equal to

AND

OR (inclusive OR)

1.4.2 Spatial Operators

Within this document the following spatial operators (EQUALS, DISJOINT, TOUCHES, WITHIN, OVERLAPS, CROSSES, INTERSECTS, CONTAINS, and COINCIDENT) based on those laid out in the ISO standard 19125-1 are used to describe spatial relationships tested within the checks. They are described in annex A of this document.

For all spatial operators a default tolerance of 0.125mm at compilation scale should be applied in validation software.

1.4.3 Values

The following terms are used for types of values;

- Present – An attribute is present either with or without a value.

- Null – An attribute has a value of null (255)

- notNull – The attribute has been populated with a value.

1.4.4 Statements

The checks must be structured using the following statements;

- If – A conditional statement which determines whether a further statement should be executed.

- For – repeat a statement until a statement is met (evaluates to “true”). For the purposes of the checks the statement being met generates the error or warning specified.

Annex A

(In the diagrams within this annex LineString corresponds to the S-101 Line geometric primitive)

EQUALS – geometric feature 1 is exactly equal to geometric feature 2

The two geometries are the same.

Examples of the EQUALS relationship

DISJOINT – the geometries of feature 1 and geometric feature 2 do not touch or overlap.

(a)			       (b)				            (c)

Examples of the DISJOINT relationship

TOUCHES – geometric feature 1 shares one or more component (node) with geometric feature 2.

The two geometries have one or more common nodes.

Examples of the TOUCHES relationship.

WITHIN –geometric 1 feature is completely contained in geometric feature 2.

Examples of the WITHIN relationship — Polygon/Polygon (a), Polygon/LineString (b), LineString/LineString (c), and Polygon/Point (d)

OVERLAPS - the intersection of geometric feature 1 and geometric feature 2 returns a value which is not the same as geometric feature 1 or 2.

The geometries both cover a common curve or surface.

CROSSES -

INTERSECTS

The inverse of DISJOINT.

The two geometries cross or overlap.

CONTAINS

CONTAINS is identical in meaning to WITHIN.

COINCIDENT (not an ISO 19124 operator)

Two geometries share two or more consecutive nodes.

| 2.1 Checks relating to S-101 Data Structure |
| --- |
| No | Check description | Check message | Check solution | Conformity to: | Cat |
| 1 | For each edge which is COINCIDENT with another edge. | Partially duplicated edges. | Remove duplication, add nodes and edit edges as required. | 4.8.1 | E |
| 2 | For each edge which does not have a beginning or end node | VE edge missing beginning or end node. | Add nodes as required. | 4.8.1 | C |
| 3 | For each record where the record identifier NAME (concatenation of the RCNM & RCID subfields) is not unique within the file | Record identifier NAME is not unique. | Amend Record identifier NAME to be unique. | Part 3 (2.2) | C |
| 4 | For each RCNM where the value is not in table 2.2 S-101 | Invalid value of RCNM | Amend RCNM value | Part 3 (2.2.1) | C |
| 5 | For each RCID which is Less than 1 OR Greater than 232 (4294967294). | RCID is out of range. | Amend RCID value. | S-100 Part 10a-3.4 | C |
| 6 | Check removed |  |  |  |  |
| 7 | For each feature with invalid AGEN, FIDN or FIDS values. | Invalid values of AGEN, FIDN or FIDS. | Amend AGEN, FIDN or FIDS value. | B1.5.31 | C |
| 8 | For each feature where an attribute code is repeated. | Duplicate attribute code on an feature. | Remove or amend duplicate attribute code. | Part 3 (4.4), (4.5) and (5.1.2) | C |
| 9a | For each feature of geometric primitive curve where ORNT is Not equal to 1 (forward) OR 2 (reverse) | Invalid value of ORNT | Set value of ORNT to 1 (forward) or 2 (reverse). | B1.5.27 B1.6.20 | C |
| 9b | For each feature of geometric primitive curve where USAG is Not equal to Null. | Invalid value of USAG. | Set value of USAG to 255 (null). | 4.8.1 B1.5.29 B1.6.22 | C |
| 9c | For each feature of geometric primitive curve where MASK is Not equal to 1 (mask) OR 2 (show) OR 255 (masking is not relevant). | Invalid value of MASK. | Set MASK to 1 (mask), 2 (show) or 255 (masking is not relevant). | 4.8.2 B1.5.34 B1.6.27 | C |
| 10a | For each feature of geometric primitive point where ORNT is Not equal to 255 (direction is not relevant). | Invalid value of ORNT. | Set ORNT to 255 (direction is not relevant). | B1.5.32 B1.6.25 | E |
| 10b | For each feature of geometric primitive point where USAG is Not equal to 255 (null) | Invalid value of USAG. | Set USAG to 255 (null). | Part 3 (4.7.1) | E |
| 10c | For each feature of geometric primitive point where MASK is Not equal to 255 (masking is not relevant). | Invalid value of MASK. | Set MASK to 255 (masking is not relevant). | 4.8.2 B1.5.34 B1.6.27 | C |
| 11 | For each edge where USAG is Equal to 3 (exterior boundary truncated by the data limit) not referencing an DataCoverage meta feature. | Edge with USAG = 3 (exterior boundary truncated by the data limit) does not reference an DataCoverage feature. | Set USAG to 1(exterior) or 2(interior). | B1.5.29 B1.6.22 | E |
| 12 | For each feature (excluding C_AGGR and C_ASSO collection features) which does not have an FSPT. | Missing FSPT. | Add FSPT. | Part 3 (4.7) | C |
| 13a | For each feature of geometric primitive curve which references multiple edges where the vector records are not referenced sequentially. | Edges are not referenced sequentially. | Amend records to reference edges sequentially. | 4.8.1 | C |
| 13b | For each feature of geometric primitive curve which references multiple edges where the end node of a vector record is not identical to the beginning node of the following vector record. | Sequential edges do not have the same end and beginning nodes. | Ensure end and beginning nodes of sequential edges match. | B1.5.24 | C |
| 13c | For each feature of geometric primitive surface where a polygon ring references multiple edges where the vector records are not referenced sequentially. | Edges are not referenced sequentially. | Amend records to reference edges sequentially. | 4.8.1 | C |
| 13d | For each feature of geometric primitive surface which references multiple edges where the end node of a vector record is not identical to the beginning node of the following vector record. | Sequential edges do not have the same end and beginning nodes. | Ensure end and beginning nodes of sequential edges match. | 4.8.1 | C |
| 14 | For each feature of geometric primitive surface where the exterior boundary shares more than one node with an interior boundary. | Exterior and interior boundaries share more than one node. | Amend boundary to share at most one node. | 4.8.1 | C |
| 15 | For each feature of geometric primitive surface where the exterior boundary or an interior boundary is not closed | First and last edge of an surface boundary, do not meet at a common connected node. | Amend edges bounding the surface to meet at a common connected node. | 4.8.1 | C |
| 16 | For each feature of geometric primitive surface where the exterior boundary is not encoded clockwise. | Area exterior boundary not encoded clockwise. | Ensure surface exterior boundary is encoded clockwise. | 4.8.1 | C |
| 17 | For each feature of geometric primitive surface where an interior boundary is not encoded counter-clockwise. | Area interior boundary not encoded counter-clockwise. | Ensure surface interior boundary is encoded counter-clockwise. | 4.8.1 | C |
| 18a | For each feature of geometric primitive surface which does not have an exterior boundary OR has more than one exterior boundary. | Area feature without an exterior boundary or with several exterior boundaries. | Amend geometry so that surface feature has one exterior boundary. | 4.8.1 | C |
| 18b | For each feature of geometric primitive surface where the exterior boundary is not referenced first. | Area feature with exterior boundary which is not referenced first. | Amend geometry so that the exterior boundary is referenced first. | 4.8.1 | C |
| 18c | For each feature of geometric primitive surface with one or more interior boundaries where any boundary is not sequential OR includes invalid use of USAG. | Interior boundary is not closed or is not sequential or use of USAG is invalid. | Ensure interior boundary is closed and sequential. Ensure valid use of USAG. | 4.8.1 B1.5.29 B1.6.22 | C |
| 19 | For each edge which is COINCIDENT with the data limit borders (i.e. limits of DataCoverage with CATCOV is Equal to 1 (coverage available)) where USAG is Not equal to 3 (exterior boundary truncated by the data limit). | Edge coincides with the data limit and USAG does not equal 3 (exterior boundary truncated by the data limit). | Amend edge to USAG = 3 (exterior boundary truncated by the data limit). | 4.5.3 B1.5.29 B1.6.22 | E |
| 20a | For each feature where a geometric primitive is not one of those permitted. | Geometric primitive of this type is not permitted for this feature class. | Use alternative geometric primitive or alternative feature class as required. | S-101 Feature Catalogue | C |
| 20b | For each feature (excluding C_AGGR and C_ASSO) which does not reference a spatial record. | Feature feature without geometry. | Remove the feature or reference the feature to a spatial record of allowable geometric primitive. | Logical consistency S-101 Feature Catalogue | C |
| 20c | For each spatial record which is not referenced by a feature. | Orphaned geometry. | Remove orphaned geometry. | Logical consistency | C |
| 21 | For each VRPT field which is not pointed to by an edge vector record. | VRPT field not referenced by an edge vector record. | Ensure VRPT field is referenced by an edge vector record or delete. | Appendix B.1 (3.3), Part 3 (5.1.1) and Supplement No2 Ch.4 (3.3.1) | C |
| 22 | For each edge where the sequence of beginning and end nodes is incorrect. | Beginning and end nodes are not in the correct sequence. | Amend sequence of beginning and end nodes. | B1.5.24 B1.6.15 | C |
| 23 | For each coordinate which is not a SG2D or SG3D field. | Coordinate is not a SG2D or SG3D field. | Amend coordinate to valid field. | B1.5.18 B1.5.19 B1.6.8 B1.6.9 | C |
| 24 | For each Sounding feature which does not reference a SG3D field with X, Y and Z values. | Sounding does not reference a SG3D field. | Amend coordinate type or values for Sounding. | B1.5.19 B1.6.9 | C |
| 25a | For each edge where the beginning and end are not encoded as connected nodes. | Beginning or end nodes of an edge are not encoded as connected nodes. | Amend beginning or end nodes to be connected nodes. | 4.8.1 | C |
| 25b | Check removed |  |  |  |  |
| 25c | For each edge where the beginning or end node is not referenced using the vector record pointer. | Beginning or end nodes not referenced by the vector record pointer. | Amend edge to ensure beginning or end nodes are referenced. | 4.8.1 | C |
| 26a | For each subfield where the value is not within the range defined in the S-101 format description. | Subfield value does not conform to S-101 format specification. | Amend subfield value. | S-101 Appendix B | C |
| 26b | For each subfield value which is not within the legal range for attribute values (for attribute values of type "float", the resolution given in the format statement by the integer part (e.g. XX.X) must not be checked). | Subfield value outside of the permitted range for an attribute value. | Amend subfield value to permitted attribute value. | S-101 Appendix B S-101 Feature Catalogue | C |
| 27 | For each subfield which is not formatted in accordance with S-101. | Subfield not formatted in accordance with S-101. | Amend formatting of subfield value. | Part 3 (7.2.2.2) | C |
| 28 | If the count of records in the DSSI field is Not equal to the total number of records. | DSSI field record count incorrect. | Amend the DSSI field record count. | B1.5.3 B1.6.3 | E |
| 29 | For each of the following: FFPC-NFPT, FSPC-NSPT, SGCC-CCNC, and VRPC-NVPT subfields where the index position for updating is invalid. | Invalid index position for updating in the following FFPC-NFPT, FSPC-NSPT, SGCC-CCNC or VRPC-NVPT. | Amend to valid index position for updating. | Part 3 (7.6.5) (7.6.7), (7.7.1.5) and (7.7.1.3) | C |
| 30 | For each of the following: FFPC-FFIX, FSPC-FSIX, SGCC-CCIX, and VRPC-VPIX subfields where the index position for updating is invalid. | Invalid index position for updating in the following subfields FFPC-FFIX, FSPC-FSIX, SGCC-CCIX or VRPC-VPIX. | Amend to valid index position for updating. | Part 3 (7.7.1.5), (7.6.5), (7.6.7) and (7.7.1.3) | C |
| 31 | For each edge where SG2D coordinates are identical to the beginning or end node coordinates. | Edge where beginning or end node coordinates are the same as the SG2D coordinates. | Amend SG2D coordinates to differ from beginning and end node coordinates. | Part 3 (7.7.1.6) | C |
| 32 | For each record update which does not refer to a valid record NAME. | Record update does not refer to a valid record NAME. | Amend record update to refer to a valid record NAME. | Part 3 (8.3.2) | C |
| 33 | For each attribute update which does not refer to a valid record NAME and attribute label/code. | Attribute update does not refer to valid record NAME and attribute label/code. | Amend attribute update to refer to valid values. | Part 3 (8.3.3) | C |
| 34 | For each of the following fields FFPT, FSPT or VRPT where the update pointer index does not refer to a valid record NAME and index. | Update pointer index does not refer to a valid record NAME and index for FFPT, FSPT or VRPT. | Ensure update pointer index refers to a valid record NAME and index. | Part 3 (8.3.4) | C |
| 35 | For each feature where RVER is out of sequence. | RVER is out of sequence. | Ensure RVER is sequential. | S-101 Annex 2 | C |
| 36a | For each feature or vector update record which is DELETE and contains further fields. | DELETE update contains additional fields. | Remove additional fields from update record. | S-101 Annex 2 | C |
| 36b | For each feature or vector update record which is MODIFY/INSERT and contains no further fields. | MODIFY/INSERT update does not contain additional fields. | Add additional fields to update record. | S-101 Annex 2 | C |
| 37 | Check renumbered 1006 |  |  |  |  |
| 38 | For each update record which contains more than one of the following fields: FFPC, VRPC, FSPC or SGCC. | Update record contains more than one of the following fields: FFPC, VRPC, FSPC or SGCC. | Remove additional fields from update record. | Part 3 (8.4.2.3), (8.4.3.2b), (8.4.2.4) and (8.4.3.3) | C |
| 39 | Check removed. |  |  |  |  |
| 40 | For any pair feature features of geometric primitive curve where class and attribute values are identical AND all referenced edges have the same spatial attribute values AND which have one or two common connected nodes which is (are) a beginning node or an end node of each curvear feature AND each common connected node is not shared by more than two features which are not chained together. | Linear features with the same class, attribute values and spatial attribute values which are connected are not chained together. | Chain curvear features together. | Logical consistency | W |
| 41 | Check removed. |  |  |  |  |
| 42 | For each edge which is referenced by Skin of the Earth features and is not linked to feature features DataCoverage with CATCOV is Equal to 1 (coverage available) which does not appear twice with different ORNT values. | Skin of the Earth coverage is not correct, a hole or an overlap exists. | Amend Skin of the Earth coverage, to remove hole or overlap. | 4.3.2.1.1 4.5.3 | C |
| 43 | For each DepthContour feature which is not COINCIDENT with two Skin of the Earth feature features AND is not WITHIN an UnsurveyedArea or DredgedArea. | DepthContour does not coincide with two Skin of the Earth features. | Amend DepthContour or Skin of the Earth features as required. | 4.3.2.1.1 Logical consistency | W |
| 44 | For each depthRangeMinimumValue or depthRangeMaximumValue value (except the shallowest and the deepest found in the ENC) for a DepthArea feature of geometric primitive surface which is not Equal to a value of valueOfDepthContour on DepthContour feature features found in the ENC. | The value of depthRangeMinimumValue or depthRangeMaximumValue is different from one of the values of valueOfDepthContour found in the ENC. | Amend value of depthRangeMinimumValue or depthRangeMaximumValue so that it equals a value of valueOfDepthContour. | Logical consistency | W |
| 45a | For each feature (excluding Berths, CableOverhead, CableSubmarine, Conveyor, DeepWaterRouteCentercurve, FerryRoute, MarineFarmCulture, MooringFacility, NavigationLine, PipelineSubmarineOnLand, RecommendedRouteCentrecurve and RecommendedTrack) of geometric primitive curve which shares an edge with another feature of the same class and geometric primitive. | Coincident curvear features of the same class. | Remove coincident feature. | Logical consistency | W |
| 45b | For each Berths, CableOverhead, CableSubmarine, Conveyor, DeepWaterRouteCentercurve, FerryRoute, MarineFarmCulture, MooringFacility, NavigationLine, PipelineSubmarineOnLand, RecommendedRouteCentrecurve, or RecommendedTrack feature of geometric primitive curve which shares an edge with another feature of the same class AND geometric primitive AND the same attribute values. | Coincident curve features of the same class and attribute values. | Remove coincident feature. | Logical consistency | W |
| 46 | For each feature where dateEnd and dateStart are notNull AND dateEnd is Less than or equal to dateStart. | dateEnd less than dateStart. | Amend values of dateEnd or dateStart accordingly. | Logical consistency | E |
| 47a | For each LIGHTS or RadarTransponderBeacon feature where sectorLimitOne is notNull and sectorLimitTwo is Null OR is Equal to sectorLimitOne. (0 and 360 must be treated as the same value.) | sectorLimitTwo not populated with a valid value, must not be the same as sectorLimitOne. | Populate sectorLimitTwo with a valid value. | Logical consistency | E |
| 47b | For each LIGHTS or RadarTransponderBeacon feature where sectorLimitTwo is notNull and sectorLimitOne is Null OR is Equal to sectorLimitTwo. (0 and 360 must be treated as the same value.) | sectorLimitOne not populated with a valid value, must not be the same as sectorLimitTwo. | Populate sectorLimitOne with a valid value. | Logical consistency | E |
| 48 | For each QualityOfSurvey meta feature where scaleValueMaximum and scaleValueMimimum are notNull AND scaleValueMimimum is Less than scaleValueMaximum. | scaleValueMimimum is less than scaleValueMaximum. | Amend values of scaleValueMaximum or scaleValueMimimum accordingly. The value of scaleValueMimimum must be greater than scaleValueMaximum. | Logical consistency | E |
| 49 | For each feature where depthRangeMinimumValue AND depthRangeMaximumValue are notNull AND depthRangeMaximumValue is Less than depthRangeMinimumValue. | depthRangeMaximumValue is less than depthRangeMinimumValue, depthRangeMaximumValue must be greater than or equal to depthRangeMinimumValue. | Amend the values of depthRangeMinimumValue or depthRangeMaximumValue as required. | Logical consistency | E |
| 50 | For each RecommendedTrack feature of geometric primitive curve where categoryOfRecommendedTrack is Equal to 1 (based on a system of fixed marks) OR NavigationLine feature where its nodes/vertices do not lie on a straight curve. | RecommendedTrack where categoryOfRecommendedTrack = 1 (based on a system of fixed marks) or NavigationLine is not a straight curve. | Amend geometry to a straight curve. | Logical consistency | E |
| 51a | For each Coastline feature which is COINCIDENT with a ShorelineConstruction feature of geometric primitive curve. | Coastline and ShorelineConstruction features share an edge. | Amend features so that they do not share an edge. | Logical consistency | W |
| 51b | For each Coastline feature which is COINCIDENT with a ShorelineConstruction feature of geometric primitive surface where waterLevelEffect is Equal to 1 (partly submerged at high water) or 2 (always dry) that is WITHIN an LandArea feature of geometric primitive surface. | Coastline and ShorelineConstruction with illogical values of waterLevelEffect overlap. | Amend features so that they do not overlap or amend waterLevelEffect values. | Logical consistency | W |
| 52a | For each LandElevation feature of geometric primitive curve which is not WITHIN a LandArea feature of geometric primitive surface | Linear LandElevation feature covered by surface LandArea | Ensure curvear LandElevation feature is covered by a LandArea. | DCEG | E |
| 52b | For each LandElevation feature of geometric primitive point which is not WITHIN a LandArea feature of geometric primitive surface AND does not touch a LandArea feature of geometric primitive curve or point AND is not WITHIN a Wrecks feature of geometric primitive surface where waterLevelEffect is Equal to 1 (partly submerged at high water) or 2 (always dry). | LandElevation feature not covered by a LandArea or by a drying or partially submerged Wrecks feature. | Ensure LandElevation feature is covered by a LandArea or by a drying or partially submerged Wrecks feature. | DCEG | E |
| 53a | For each SlopingGround feature which is not WITHIN a LandArea feature of geometric primitive surface. | SlopingGround not covered by LandArea. | Amend LandArea or SlopingGround accordingly. | DCEG | E |
| 53b | For each SlopeTopline feature which is not WITHIN a LandArea feature of geometric primitive surface. | SlopeTopline not covered by LandArea. | Amend LandArea or SlopeTopline accordingly. | DCEG | E |
| 54a | For each FortifiedStructure, Landmark or SiloTank feature of geometric primitive surface which is not WITHIN a LandArea, BRIDGE, FloatingDock, OffshorePlatform or Pontoon feature of geometric primitive surface. | FortifiedStructure, Landmark or SiloTank not covered by a LandArea, BRIDGE, FloatingDock, OffshorePlatform or Pontoon. | Amend feature to ensure it is situated on a suitable feature. | Logical consistency | C |
| 54b | For each FortifiedStructure, Landmark, Daymark or SiloTank feature of geometric primitive point which is not WITHIN a LandArea, BRIDGE, FloatingDock, OffshorePlatform or Pontoon feature of geometric primitive surface OR does not EQUAL a LandArea, Pile, PylonBridgeSupport, OffshorePlatform, ShorelineConstruction or UnderwaterAwashRock feature of geometric primitive point OR is not COINCIDENT with a Coastline, Dam, BRIDGE, FloatingDock, LandArea, Pontoon or ShorelineConstruction feature of geometric primitive curve. | FortifiedStructure, Landmark, Daymark or SiloTank not covered by a suitable supporting feature. | Amend feature to ensure it is situated on a suitable feature. | Logical consistency | C |
| 54c | For each Building or Crane feature of geometric primitive surface which is not WITHIN a LandArea, BRIDGE, FloatingDock, HarbourFacility, OffshorePlatform, or Pontoon feature of geometric primitive surface OR for each Building feature of geometric primitive point which is not WITHIN a LandArea, BRIDGE, FloatingDock, OffshorePlatform or Pontoon feature of geometric primitive surface OR does not EQUAL a LandArea, Pile, PylonBridgeSupport, OffshorePlatform, ShorelineConstruction or UnderwaterAwashRock feature of geometric primitive point OR is not COINCIDENT with a Coastline, Dam, BRIDGE, FloatingDock, LandArea, Pontoon or ShorelineConstruction feature of geometric primitive curve. | Building or Crane not covered by a suitable supporting feature | Amend feature to ensure it is situated on a suitable feature. | Logical consistency | W |
| 55 | For each LandArea feature of geometric primitive point or curve which is WITHIN a LandArea feature of geometric primitive surface AND is not WITHIN a LakeArea, River, DockArea, LockBasin or Canal feature of geometric primitive surface. | Point LandArea lies on LandArea. | Amend point LandArea or surface LandArea accordingly. | Logical consistency | W |
| 56 | For each BuiltupArea feature not WITHIN a LandArea feature of geometric primitive surface OR which is COINCIDENT with a LandArea feature of geometric primitive point or curve. | BuiltupArea not located on LandArea. | Amend BuiltupArea so that it is covered by a LandArea. | Logical consistency | E |
| 57a | For each Coastline feature which is not COINCIDENT with a LandArea feature AND is not WITHIN a LandArea feature of geometric primitive surface. | Coastline feature not bounding LandArea | Ensure that Coastline coincides with LandArea boundary. | Logical consistency DCEG | E |
| 57b | For each Coastline feature which is WITHIN a LandArea feature of geometric primitive surface OR is COINCIDENT with LandArea feature features on both sides AND is COINCIDENT with a ShorelineConstruction or DryDock feature where condition is Not equal to 1(under construction) OR 3(under reclamation) OR 5(planned construction) | Coastline is within a LandArea or is coincident with a permanent ShorelineConstruction or DryDock feature. | Remove Coastline or amend condition values. | Logical consistency. DCEG | E |
| 57c | For each Coastline feature which is COINCIDENT with LandArea feature features on both sides where not one of them has condition is Equal to 1(under construction) OR 3(under reclamation) OR 5(planned construction) | Coastline is coincident with LandArea features on both sides | Remove Coastline or amend condition values. | Logical consistency. DCEG | E |
| 58 | For each SeabedArea feature of geometric primitive curve which is COINCIDENT with a SeabedArea feature of geometric primitive surface. | Line SeabedArea bounds an surface SeabedArea. | Remove curvear SeabedArea. | Logical consistency | W |
| 59 | For each Obstruction feature of geometric primitive curve which is COINCIDENT with an Obstruction feature of geometric primitive surface. | Line Obstruction bounds an surface Obstruction. | Amend or delete curvear Obstruction. | Logical consistency | W |
| 60 | For each CableSubmarine feature which INTERSECTS OR is WITHIN a LandArea feature of geometric primitive surface. | CableSubmarine covered by LandArea. | Amend CableSubmarine feature accordingly. | Logical consistency | W |
| 61a | For each feature of geometric primitive curve or surface where waterLevelEffect is Equal to 3 (always underwater/submerged) which OVERLAPS OR is WITHIN an inter-tidal surface (DepthArea feature where depthRangeMaximumValue is Less than or equal to 0) OR WITHIN a LandArea feature of geometric primitive surface. | Line or surface feature where waterLevelEffect = 3 (always underwater/submerged) is within or overlaps an inter-tidal surface (DepthArea with depthRangeMaximumValue ≤ 0) or LandArea. | Amend value of waterLevelEffect. | Logical consistency | E |
| 61b | For each feature of geometric primitive point where waterLevelEffect is Equal to 3 (always underwater/submerged) which is WITHIN an inter-tidal (DepthArea feature where depthRangeMaximumValue is Less than or equal to 0) surface OR is WITHIN a LandArea feature of geometric primitive surface OR EQUALS a LandArea feature of geometric primitive point OR is situated on a LandArea feature of geometric primitive curve. | Point feature where waterLevelEffect = 3 (always underwater/submerged) lies within an inter-tidal surface (DepthArea with depthRangeMaximumValue ≤ 0) or is within or coincident with a LandArea feature. | Amend value of waterLevelEffect. | Logical consistency | E |
| 62 | For each Pontoon, Hulk or FloatingDock feature of geometric primitive surface where any edge shares the geometry of a Coastline or ShorelineConstruction feature of geometric primitive curve AND the edge does not also share the geometry of a LandArea feature of geometric primitive surface. | Pontoon, Hulk or FloatingDock which shares an edge with a ShorelineConstruction or Coastline which is not on the edge of a LandArea. | Ensure all ShorelineConstruction or Coastline features are backed by LandArea features. | Logical consistency | W |
| 63 | For each RecommendedTrack feature which INTERSECTS LandArea, Pontoon, Hulk or FloatingDock feature features of geometric primitive curve or surface OR any feature where waterLevelEffect is Equal to 1 (partly submerged at high water) OR 2 (always dry). | RecommendedTrack intersects prohibited features. | Amend RecommendedTrack or other features to ensure RecommendedTrack is within navigable features. | Logical consistency | E |
| 64 | For each AnchorageArea feature of geometric primitive point or surface where categoryOfAnchorage is Not equal to 8 (small craft mooring surface) AND OVERLAPS another feature where restriction includes the value 1 (anchoring prohibited). | AnchorageArea feature within an surface with restriction = 1 (anchoring prohibited). | Amend AnchorageArea feature or feature carrying restriction = 1(anchoring prohibited). | Logical consistency | W |
| 65 | For each LIGHTS feature which EQUALS another LIGHTS feature AND status is Not equal to 4 (not in use) OR 6 (reserved) OR 11 (extinguished) where sectors overlap AND none of the values of the following attributes are different categoryOfLight, exhibitionConditionOfLight, lightCharacteristic, signalPeriod or signalGroup. | Coincident lights with overlapping sectors and the same characteristics. | Amend light sectors so that they do not overlap, or remove duplicated sectors. | Logical consistency | W |
| 66 | Check removed. |  |  |  |  |
| 67a | For each feature where the feature class, attribution and geometry is identical to another feature. | Duplicate feature exists. | Remove duplicate feature. | Data structure | E |
| 67b | For each collection feature which references identical feature features to another collection feature. | Duplicate collection feature exists. | Remove duplicate collection feature. | Data structure | E |
| 68 | Check renumbered 1007 |  |  |  |  |
| 69 | Check removed. |  |  |  |  |
| 70a | For each DepthArea feature of geometric primitive curve which does not EQUAL a Skin of the Earth boundary. | ‘Hanging' curvear depth surface. | Remove 'hanging' curvear DepthArea. | Logical consistency | E |
| 70b | For each DepthArea feature of geometric primitive curve. | Linear DepthArea present in the ENC | Remove curvear DepthArea. | Logical consistency | W |
| 71a | For each feature of geometric primitive surface that is not COINCIDENT with the DataCoverage boundary where all edges are masked (i.e. USAG is Equal to 3 (exterior boundary truncated by the data limit) OR MASK is Equal to 1 (mask)). | Area feature has all of its edges masked and is not the edge of the data coverage. | Remove masking. | Logical consistency | W |
| 71b | For each feature of geometric primitive curve which has any edges masked (i.e. MASK is Equal to 1 (mask)). | Line feature with masked edges. | Remove masking from curve feature, | Logical consistency | E |
| 72 | For each set of hierarchical relationships which form a loop (e.g. master feature is slave of its own slave). | Relationships form a loop. | Amend relationships to remove loop. | Logical consistency | E |
| 73a | For each attribute value which contains a leading or trailing space. | Attribute value contains leading or trailing spaces. | Remove leading or trailing spaces. | Logical consistency | W |
| 73b | For each attribute value of type list which contains spaces. | List attribute value contains spaces. | Remove spaces. | Logical consistency | W |
| 74 | For each DepthContour feature which does not share an edge with a Skin of the Earth feature AND is WITHIN a DepthArea feature of geometric primitive surface where depthRangeMinimumValue AND depthRangeMaximumValue are notNull AND valueOfDepthContour is Less than depthRangeMinimumValue OR Greater than depthRangeMaximumValue | Floating DepthContour within a DepthArea with valueOfDepthContour less than depthRangeMinimumValue or greater than depthRangeMaximumValue. | Amend floating contour valueOfDepthContour between depthRangeMinimumValue and depthRangeMaximumValue of the underlying DepthArea. | Logical consistency | C |
| 75 | For each DepthContour feature which does not share an edge with a Skin of the Earth feature AND is WITHIN a DredgedArea feature of geometric primitive surface where depthRangeMinimumValue is notNull AND valueOfDepthContour is Less than depthRangeMinimumValue. | Floating DepthContour within a DredgedArea with valueOfDepthContour less than depthRangeMinimumValue of the DredgedArea. | Amend floating contour valueOfDepthContour to be greater than the depthRangeMinimumValue of the underlying DredgedArea or amend depthRangeMinimumValue of the DredgedArea. | Logical consistency | C |
| 76 | For each DepthContour feature that INTERSECTS OR is WITHIN a FloatingDock, Hulk, LandArea or Pontoon feature of geometric primitive surface. | DepthContour intersects prohibited features. | Amend DepthContour to be within appropriate features. | Logical consistency. | E |
| 77 | For each DepthContour feature which CROSSES another DepthContour feature. | DepthContour features cross. | Amend DepthContour features so they do not cross. | Logical consistency | C |
| 78 | For each feature of geometric primitive surface where its boundary CROSSES itself. | Boundary of an surface feature crosses itself. | Amend boundary to remove part which crosses itself. | Logical consistency | C |
| 79 | For each feature of geometric primitive curve where a component edge CROSSES another component edge without a connected node at the crossing point. | Component edges of a curve feature cross without a connected node at the crossing point. | Insert connected node at crossing point. | Topology | E |
| 80a | For each feature of geometric primitive surface where an interior boundary is WITHIN an interior boundary. | Interior boundary within an interior boundary. | Amend boundaries so that interior boundary is not within another interior boundary. | Topology | C |
| 80b | For each feature of geometric primitive surface where an interior boundary is not WITHIN an exterior boundary. | Interior boundary outside of an exterior boundary. | Amend boundaries so that interior boundary is within exterior boundary. | Topology | C |
| 80c | For each feature of geometric primitive surface where an exterior boundary is WITHIN an interior boundary. | Exterior boundary within an interior boundary. | Amend boundaries so that exterior boundary is not within the interior boundary. | Topology | C |
| 81 | For each Sounding feature which is COINCIDENT with another Sounding feature. (COINCIDENT applies to the horizontal component only). | Sounding features are coincident. | Remove coincident sounding. | Topology | E |
| 82 | For each feature of geometric primitive curve or surface which references the same edge more than once. | Object references the same edge more than once. | Remove duplicate reference to the edge. | Topology | C |
| 83 | For each node which is COINCIDENT with another node (connected or isolated). | Nodes are coincident. | Removee or amend coincident node. | Topology | W |
| 84a | For each node which is physically isolated and is marked as connected. | Isolated node marked as connected. | Amend to isolated. | Part 3 (5.1.1) | C |
| 84b | For each node which is not physically isolated and is marked as isolated. | Connected node marked as isolated. | Amend to connected. | Part 3 (5.1.1) | C |
| 85 | Check renumbered 1008 |  |  |  |  |
| 86 | For each feature of geometric primitive point which references more than one vector record. | Point feature references more than one vector record. | Remove references to additional vector records. | B1.5.32 B1.6.25 | C |
| 87 | For each edge with COINCIDENT consecutive vertices. | Consecutive vertices are coincident. | Remove coincident vertices from edge. | B1.5.32 B1.6.25 | E |
| 88a | For each feature of geometric primitive surface where ORNT is Not equal to 1 (forward) OR 2 (reverse). | Invalid value of ORNT. | Set value of ORNT to 1 (forward) or 2 (reverse). | B1.5.32 B1.6.25 | C |
| 88b | For each feature of geometric primitive surface where USAG is Not equal to 1 (exterior) OR 2 (interior) OR 3 (exterior boundary truncated by the data limit) | Invalid value of USAG. | Set USAG to 1(exterior), 2(interior) or 3 (exterior boundary, truncated y the data limit). | B1.5.29 B1.6.22 | C |
| 88c | For each feature of geometric primitive surface where MASK is Not equal to 1 (mask) OR 2 (show) OR 255 (masking is not relevant). | Invalid value of MASK. | Set MASK to 1 (mask), 2 (show) or 255 (masking is not relevant). | S-101 Annex B | C |
| 89a | For each master feature which references the same slave more than once. | Master feature references the same slave more than once. | Remove duplicate reference to slave feature. | Part 3 (6.3); Appendix B.1 (3.9) & Appendix B.1 Annex A 12.1.2 | C |
| 89b | For each slave feature which is referenced by more than one master feature. | Slave feature has more than one master. | Remove incorrect master from slave feature. | Part 3 (6.3); Appendix B.1 (3.9) & Appendix B.1 Annex A 12.1.2 | C |
| 90a | Check renumbered 1009 |  |  |  |  |
| 90b | For an EN file where the DDR does not contain only the description of the base cell file structure. | Invalid DDR in EN file. | Amend DDR. | S-101 Annex B | W |
| 90c | For an ER file where the DDR does not contain only the description of the update cell file structure. | Invalid DDR in ER file. | Amend DDR. | S-101 Annex B | W |
| 91 | Check removed. |  |  |  |  |
| 92 | Check renumbered 1010 |  |  |  |  |
| 93a | For each feature of geometric primitive curve or surface where waterLevelEffect is Equal to 4 (covers and uncovers) OR 5 (awash) AND OVERLAPS a LandArea feature of geometric primitive surface. | Object with waterLevelEffect = 4 or 5 is within a LandArea feature. | Amend LandArea feature to ensure feature is within an inter-tidal surface. | Logical consistency | E |
| 93b | For each feature of geometric primitive point where waterLevelEffect is Equal to 4 (covers and uncovers) OR 5 (awash) which OVERLAPS a LandArea feature of geometric primitive surface OR EQUALS a LandArea feature of geometric primitive point OR is COINCIDENT with a LandArea feature of geometric primitive curve. | Object with waterLevelEffect = 4 or 5 on a LandArea feature. | Amend LandArea feature to ensure feature is within inter-tidal surface. | Logical consistency | E |
| 94 | For each ER file which contains instructions for the FSPC field to modify an FSPT field of a feature to a value it already contains. | ER file contains instructions to modify an FSPT field to a value it already contains. | Remove irrelevant FSPC field from ER file. | Logical consistency | E |
| 95 | If the COMT subfield of the DSID and DSPM fields contains text which is not lexical level (0). | COMT subfield contains text which is not lexical level (0). | Amend text to conform to lexical level (0). | Part 3 (2.4) | E |
| 96 | For each relationship which does not reference a C_ASSO or C_AGGR collection feature AND the RIND subfield of the FFPT field set to 3 (peer). | Invalid value of RIND. | Amend the relationship indicator to 1 (master) or 2 (slave) as appropriate. | Part 3 (6.2) and Appendix B.1 (3.9) | E |
| 97 | For each feature where SUREND and surveyDateRange are notNull AND SUREND is less than surveyDateRange. | SUREND less than surveyDateRange. | Amend values of SUREND or surveyDateRange accordingly. | Logical consistency | E |
| 98 | For each feature which has a relationship AND references an feature which does not exist. | Object references an feature that does not exist | Remove reference to non-existent feature | Logical consistency. | E |

| 2.2 Checks relating to ENC Product Specification |
| --- |
| No | Check description | Check message | Check solution | Conformity to: | Cat |
| 500 | For each feature where its geometry is not WITHIN an DataCoverage meta feature AND CATCOV is Equal to 1 (coverage available). | Objects fall outside the coverage feature. | Ensure features are not outside of the limits of the cell. | 4.5 | C |
| 501 | If the combined coverage of all DataCoverage meta features limits are not rectangular | Cell is not rectangular. | Ensure cell limits are rectangular. | 4.5 | E |
| 502 | If the cell file size is greater than 5 Megabytes. | The cell is larger than 10Mb in size. | Ensure that the cell is not larger than 10Mb. | 4.5 | E |
| 503 | For each feature where the FOID is not unique WITHIN the dataset. | Duplicate FOIDs exist within the dataset. | Ensure that no duplicate FOIDs exist. | 4.4 | W |
| 504 | For each CANBNK, LAKSHR, RIVBNK SQUARE, M_HDAT, M_PROD, M_UNIT, C_STAC, $AREAS, $LINES, $CSYMB,$COMPS, or $TEXTS feature. | Prohibited features exist within the dataset. | Remove prohibited features. |  | C |
| 505 | If any of the following meta features DataCoverage, NavigationalSystemOfMarks or QualityOfBathymetricSurvey do not exist within the data set. | Mandatory meta features are missing. | Include mandatory meta features DataCoverage, NavigationalSystemOfMarks and QualityOfBathymetricSurvey. |  | C |
| 506 | If mandatory subfields in EN and ER files are Null | Mandatory subfields do not contain a value. | Populate mandatory subfields. | 6.1.4 | C |
| 507 | If any mandatory attributes are not populated. | Mandatory attributes are not populated | Populate mandatory attributes. | S-101 Feature Catalogue | C |
| 508a | For each feature where more than one value of colour is encoded AND colourPattern does not contain a value OR is NULL | colour has multiple values without a value for colourPattern. | Ensure colourPattern has a value where multiple colour values are encoded. | Logical consistency S-101 Feature Catalogue | E |
| 508b | For each feature where colourPattern is notNull AND colour is Null OR only has one value. | colourPattern is populated without multiple colour values. | Ensure multiple colour values are populated or delete colourPattern value. | Logical consistency S-101 Feature Catalogue | E |
| 509 | For each feature listed below where the attribute stated is Null ArchipelagicSeaLaneArea: nation ArchipelagicSeaLaneAxis: nation ContiguousZone: nation ContinentalShelfArea: nation CautionArea: Information or TextualDescription CustomZone: nation DepthArea: depthRangeMinimumValue and depthRangeMaximumValue DepthContour: valueOfDepthContour DredgedArea: depthRangeMinimumValue DeepWaterRoutePart: orientation DeepWaterRouteCentercurve: orientation ExclusiveEconomicZone: nation FisheryZone: nation LandElevation: elevation DataCoverage: CATCOV M_CSCL: CSCALE NavigationalSystemOfMarks: marksNavigationalSystemOf or orientation QualityOfBathymetricSurvey: CATZOC SoundingDatum: verticalDatum VerticalDatumOfData: verticalDatum MagneticVariation: ValueOfMagneticVariation NEWOBJ: CLSDEF and CLSNAM RecommededTrafficLanePart: orientation RestrictedArea: categoryOfRestriction or restriction StraightTerritorialSeaBaseline: nation SweptArea: depthRangeMinimumValue TerritorialSeaArea: nation TidalStreamPanelData: TS_TSP | Mandatory attribute has not been populated with a value. | Populate mandatory attributes; in these cases the feature is meaningless without this value. | S-101 Feature Catalogue | E |
| 510 | Check removed. |  |  |  |  |
| 511 | For each feature where any of DUNITS, HUNITS, RECDAT, RECIND, SCAMAX, PUNITS or CATQUA is null OR notNull. | Prohibited attributes have been encoded. | Remove prohibited attributes. | 3.5.3 | C |
| 512 | For each feature with an attribute of type Float or Integer where the value contains zeroes before the first numerical digit or after the last numerical digit. | Values have been padded with non-significant zeroes. E.g. : For a signal period of 2.5 sec, the value of signalPeriod must be 2.5 and not 02.500 | Remove non-significant zeroes. | 10.1.3 | E |
| 513 | For each feature with an attribute value identical to a corresponding attribute of a meta feature it is WITHIN. | An attribute value of a meta feature is duplicated on a geo feature. | Remove duplicate value from geo feature. | S-101 Feature Catalogue | E |
| 514 | Check removed. |  |  |  |  |
| 515 | For each edge where USAG (Usage indicator) is Equal to 3 (exterior boundary, truncated by the data limit) AND MASK does not equal 255 (masking is not relevant). | Exterior edges truncated by the data limit are not masked. | MASK exterior edges truncated by the data limit. | 4.8.2 S-101 Annex B | W |
| 516a | For each master feature of geometric primitive point which does not share the geometry of the related slave features. | Master and slave point features do not share the same node. | Ensure master and slave point features share the same node. | 4.3 S-101 Feature Catalogue DCEG | E |
| 516b | For each master feature of geometric primitive curve where the slave feature does not OVERLAP the master feature. | Slave feature does not overlap the master curve feature | Ensure the master and slave features overlap. | 4.3 S-101 Feature Catalogue DCEG | E |
| 516c | For each master feature of geometric primitive surface where the slave feature is not WITHIN OR TOUCHING the master feature. | Slave feature does not touch or fall within the master surface feature. | Ensure the slave feature touches or lies within the master feature. | 4.3 S-101 Feature Catalogue DCEG | E |
| 517a | For each collection feature which does not reference at least two feature features. | Collection feature does not reference at least two feature features. | Remove collection feature or ensure that it references at least two feature features. | 4.3 S-101 Feature Catalogue DCEG | E |
| 517b | For each collection feature which references itself. | Collection feature references itself. | Remove circular reference. | 4.3 S-101 Feature Catalogue DCEG | E |
| 517c | For each collection feature where the subfield PRIM is not Equal to Null {255} (no geometry). | Invalid value of geometric primitive subfield. | Set PRIM subfield to Null {255} (no geometry). | 4.3 S-101 Annex B S-101 Feature Catalogue DCEG | E |
| 517d | Check removed. |  |  |  |  |
| 517e | For each collection feature where the RIND subfield is not 3 (peer) OR which references feature features where the subfield RIND is not 3 (peer). | Collection feature which is peer, references non-peer feature features. | Amend feature features to peer. | 34.3 S-101 Annex B S-101 Feature Catalogue DCEG | E |
| 517f | For each collection feature that references the same feature more than once | Collection feature contains multiple references to the same feature | Remove duplicated reference. | 4.3 S-101 Annex B S-101 Feature Catalogue DCEG | E |
| 518a | For each DredgedArea, LandArea, DepthArea or UnsurveyedArea, DockArea, LockBasin feature of geometric primitive surface where the GRUP subfield of the FRID is not equal to 1 (Skin of the Earth). | Skin of the earth features are not encoded as Skin of the Earth. | Ensure that the FRID subfield GRUP is set to 1 (Skin of the Earth) for all skin of the earth feature features. | 4.3.2.1.1 S-101 Annex B | C |
| 518 b | For each feature (excluding DredgedArea, LandArea, DepthArea or UnsurveyedArea, DockArea, LockBasin) of geometric primitive surface, where the GRUP subfield of the FRID is not equal to 2 (Group 2). | Group 2 features are not encoded as Group 2. | Ensure that the FRID subfield GRUP is set to 2 (Group 2) for all non skin of the earth feature features. | 4.3.2.1.1 S-101 Annex B | C |
| 519a | If the combined coverage of all DredgedArea, LandArea, DepthArea, UnsurveyedArea, DockArea, LockBasin feature features does Not EQUAL the combined coverage of all DataCoverage meta features with CATCOV Equal to 1(coverage available). | Skin of the earth (TG1) features do not cover the data coverage (DataCoverage=1) | Amend TG1 feature limits to match data coverage. | 4.3.2.1.1 S-101 Annex B | C |
| 519b | For each DredgedArea, LandArea, DepthArea DockArea, LockBasin OR UnsurveyedArea feature that OVERLAPS another DredgedArea, LandArea, DepthArea DockArea, LockBasin OR UnsurveyedArea a feature. | Skin of the earth (TG1) features overlap. | Ensure TG1 features do not overlap. | 4.3.2.1.1 S-101 Annex B | C |
| 520a | If the AALL subfield of the DSSI is not encoded with 0 OR 1. | Invalid value of AALL. | Set value of AALL to 0 or 1. | 3.11 and 3.5.5 | E |
| 520b | If the NALL subfield of the DSSI is not encoded with 0 OR 1 OR 2. | Invalid value of NALL. | Set value of NALL to 0, 1 or 2. | 3.11 and 3.5.5 | E |
| 520c | Check removed. |  |  |  |  |
| 520d | If lexical level 2 has been used anywhere other than the NATF field. | Lexical level 2 used outside of the NATF field. (Return character sets used and the sequence found.) | Amend text to remove lexical level 2 characters. | 3.11 and 3.5.5 | E |
| 520e | If any ATTF or NATF field contains characters of a lexical level greater than that in the DSSI -AALL/NALL subfields correspondingly. | Lexical level of characters in the attribute or encoding of DSSI-AALL/NALL is inconsistent. | Amend characters or the subfield encoding as required. | 3.11 and 3.5.5 | E |
| 520f | If the UT or FT is not encoded at the lexical level specified for that field. | The UT or FT is not of the correct lexical level. | Amend UT and FT to the correct lexical level. | Part 3 Annex B (B.2) | E |
| 520g | Check removed. |  |  |  |  |
| 520h | Check removed. |  |  |  |  |
| 521a | For each feature where featureName are notNull AND that they are EQUAL | Values for featureName are identical. | Ensure that national language attributes are populated with the correct values. | S-101 Feature Catalogue DCEG | W |
| 521b | For each feature where Information are notNull AND that they are EQUAL | Values for Information are identical. | Ensure that national language attributes are populated with the correct values. | S-101 Feature Catalogue DCEG | W |
| 521c | For each feature where PILDST and NPLDST are notNull AND that they are EQUAL | Values for PILDST and NPLDST are identical. | Ensure that national language attributes are populated with the correct values. | 3.11.1 | W |
| 521d | For each feature where TextualDescription are notNull AND that they are EQUAL | Values for TextualDescription are identical. | Ensure that national language attributes are populated with the correct values. | S-101 Feature Catalogue DCEG | W |
| 522 | For each feature where NOBJNM is notNull AND FeatureName is Null OR not Present | NOBJNM is populated without FeatureName. | Populate Object name. | S-101 Feature Catalogue DCEG | E |
| 523 | Where the HDAT subfield of the DSPM field is Not equal to 2 (WGS 84). | HDAT does not equal 2 (WGS 84). | Set the HDAT subfield to 2 (WGS 84). | S-101 Annex B | C |
| 524 | Where the DUNI subfield of the DSPM field is Not equal to 1 (metres). | DUNI does not equal 1 (metres). | Set the DUNI subfield to 1 (metres). | S-101 Annex B | C |
| 525 | Where the PUNI subfield of the DSPM is Not equal to 1 (metres). | PUNI does not equal 1 (metres). | Set the PUNI subfield to 1 (metres). | S-101 Annex B | C |
| 526 | Where the COUN subfield of the DSPM field is Not equal to 1 (latitude/longitude). | COUN does not equal 1 latitude/longitude. | Set the COUN subfield to 1 (latitude/longitude). | S-101 Annex B | C |
| 527 | Check renumbered 1011 |  |  |  |  |
| 528 | Check renumbered 1012 |  |  |  |  |
| 529 | Check renumbered 1013 |  |  |  |  |
| 530 | Check renumbered 1014 |  |  |  |  |
| 531 | If the file names are not in accordance with the ENC Product Specification. | File names are not in accordance with the ENC Product Specification. | Amend file names. | 11.3.2 | C |
| 532 | Check renumbered 1015 |  |  |  |  |
| 533 | If the UADT subfield of the DSID field is used in an ER file. | DSID-UADT subfield populated in an ER file. | Remove value of DSID-UADT subfield. | S-101 Annex B | C |
| 534 | If a delete cell message contains anything other than the DSID field AND EDTN is Equal to 0 | Incorrect delete cell message. | Remove additional information from delete cell message. | S-101 Annex B | C |
| 535 | Check renumbered 1016 |  |  |  |  |
| 536 | If a field without a repetition factor repeats. | Field without a repetition factor repeats. | Remove repeating value. | S-101 Annex B | C |
| 537 | Check renumbered 1017 |  |  |  |  |
| 538 | Check renumbered 1018 |  |  |  |  |
| 539 | If DSID-PROF is Not equal to 1 (EN) OR 2 (ER). | Invalid value of DSID-PROF. | Set DSID-PROF to either 1 (EN) or 2 (ER). | B1.5.2 B1.6.2 B1.7.2 | C |
| 540a | If mandatory records fields and subfields are not Present OR are Null. | Mandatory records, fields or subfields are not used. | Add mandatory records/values. | S-101 Annex B | C |
| 540b | If data set file contains prohibited records, fields or subfields. | Prohibited records, fields or subfields used. | Remove prohibited records/values. | S-101 Annex B | C |
| 541a | Check removed. |  |  |  |  |
| 541b | Check removed. |  |  |  |  |
| 542 | For each LIGHTS feature where categoryOfLight is Not equal to 1 (fixed) AND where signalGroup does not start and finish with a bracket. | signalGroup is not formatted correctly. | Amend the formatting of signalGroup. | S-101 Feature Catalogue DCEG | E |
| 543 | For each TS_TSP attribute value that does not conform to the correct structure, (i.e. values not separated by commas). | TS_TSP value not formatted correctly. | Amend the formatting of TS_TSP value. | Appendix A Ch.2 (code 159) | E |
| 544 | For each feature that OVERLAPS OR is WITHIN an surface of DataCoverage where CATCOV is Equal to 2 (no coverage available). | Feature within an surface of no coverage. | Remove feature or amend coverage. | 4.5.3 | C |
| 545 | For each feature which does not have a valid feature class label/code as defined by the Object Catalogue and S-101 Supplement No 2. | Object has invalid feature class code. | Amend feature class code. | 3.2 and Supplement No2 Ch.2 | C |
| 546 | For each attribute which does not have a valid attribute label/code as defined by the Object Catalogue and S-101 Supplements No 2. | Attribute has invalid attribute label/code. | Amend attribute label/code. | 3.2 and Supplement No2 Ch.3 | C |
| 547 | For each feature which contains attributes outside the list of permissible attributes for the feature (as defined in the S-101 Feature Catalogue). | Attribute not permitted on feature class. | Remove attribute. | S-101 Feature Catalogue | C |
| 548 | If the combined coverage of DataCoverage meta features is Not equal to the cell extents. | Cell not entirely covered by DataCoverage features. | Edit DataCoverage coverage to match cell extents. | 4.5.3 | C |
| 549 | For each DepthArea or DredgedArea feature which is not WITHIN the combined coverage of QualityOfBathymetricSurvey meta features. | DepthArea or DredgedArea features not covered by an QualityOfBathymetricSurvey feature. | Ensure full coverage of QualityOfBathymetricSurvey features over DepthArea or DredgedArea features. | DCEG | E |
| 550 | For each UnsurveyedArea feature which CONTAINS OR OVERLAPS the following features DepthContour, Obstruction, Sounding, UnderwaterAwashRock or Wrecks and which is not WITHIN the combined coverage of QualityOfBathymetricSurvey meta features. | UnsurveyedArea containing bathymetric features not completely covered by QualityOfBathymetricSurvey. | Ensure QualityOfBathymetricSurvey features completely cover UnsurveyedArea features | DCEG | E |
| 551a | If text attribute values use (C0) characters (C0 as defined in S-57 Part 3, Annex B). | C0 characters used in text attribute values. | Amend text attribute values. | 3.5.5 & Part 3 Annex B | E |
| 551b | If the delete character is used outside of the update mechanism, (i.e. in records where RUIN is Equal to 3 (modify)). | Delete character used outside of the update mechanism. | Only use delete within the update mechanism. | 3.5.5 | E |
| 552 | Check removed. |  |  |  |  |
| 553 | For each Skin of the Earth feature where any of dateStart, dateEnd, periodStart or periodEnd is Present and notNull. | Attributes dateStart, dateEnd, periodStart or periodEnd are encoded on Skin of the Earth features. | Remove these attributes from Skin of the Earth features. | S-101 Feature Catalogue DCEG | C |
| 554 | For each edge referenced by only one DataCoverage meta feature where CATCOV is Equal to 1 (coverage available), AND is also shared by more than one Skin of the Earth feature. | Edge of DataCoverage (coverage available) referenced by more than one Skin of the Earth feature. | Ensure edges on the edge of data coverage only reference one Skin of the Earth feature. | 4.3.2.1.1 | C |
| 555 | If the order of the data in a base or update file is not correct. | Incorrect data order. | Amend data order. | S-101 Annex B | C |
| 556a | Check renumbered 1024a |  |  |  |  |
| 556b | Check renumbered 1024b |  |  |  |  |
| 557 | For each signalSequence attribute value which does not conform to the correct structure (i.e. string content is not in accordance with format specification). | signalSequence attribute not formatted correctly. | Amend formatting of signalSequence attribute value. | S-101 Feature Catalogue DCEG | E |
| 558 | For each feature where signalSequence is notNull and signalPeriod is Not equal to the sum of the intervals of lit and eclipse given in signalSequence. | signalPeriod does not correspond to signalSequence. | Ensure signalPeriod corresponds to the sum of the intervals of lit and eclipse given in signalSequence. | S-101 Feature Catalogue DCEG logical consistency | E |
| 559a | For each feature where status includes the value 1 (permanent) in combination with at least one of, 2 (occasional), 5 (periodic/intermittent) or 7 (temporary). | Illogical combination of status values. | Amend values for status. | S-101 Feature Catalogue DCEG logical consistency | E |
| 559b | For each feature where status includes the value 3 (recommended) in combination with at least one of 4 (not in use) or 11 (extinguished). | Illogical combination of status values. | Amend values for status. | S-101 Feature Catalogue DCEG logical consistency | E |
| 559c | For each feature where status includes the value 4 (not in use) in combination with at least one of 5 (periodic/intermittent), 9 (mandatory). | Illogical combination of status values. | Amend values for status. | S-101 Feature Catalogue DCEG logical consistency | E |
| 559d | For each feature where status includes the value 5 (periodic/intermittent) in combination with 11 (extinguished). | Illogical combination of status values. | Amend values for status. | S-101 Feature Catalogue DCEG logical consistency | E |
| 559e | For each feature where status includes the value 9 (mandatory) in combination with 11 (extinguished). | Illogical combination of status values. | Amend values for status. | S-101 Feature Catalogue DCEG logical consistency | E |
| 559f | For each feature where status includes the value16 (watched) in combination with 17 (un-watched). | Illogical combination of status values. | Amend values for status. | S-101 Feature Catalogue DCEG logical consistency | E |
| 559g | For each feature where status includes the value 8 (private) in combination with 14 (public). | Illogical combination of status values. | Amend values for status. | S-101 Feature Catalogue DCEG logical consistency | E |
| 560a | For all feature features with the same FOID where the feature class and attribute values are not identical. | Objects with the same FOID do not have the same feature encoding | Ensure features with the same FOID have the same feature class and attribute values. | 4.4 | C |
| 560b | For all feature features with the same FOID where the geometric primitives are Point OR are not of the same geometric primitive. | Objects with the same FOID are of geometric primitive point or have different geometric primitives. | Ensure point features do not have the same FOID and that curve and surface features which share FOIDs have the same geometric primitive. | 4.4 | C |
| 561 | Check removed. |  |  |  |  |
| 562 | For each NEWOBJ feature where Information or TextualDescription does not commence with the CLSNAM of the feature. | The text in Information or TextualDescription does not commence with the CLSNAM of the NEWOBJ feature. | Ensure that the text in Information or TextualDescription commences with the CLSNAM of the NEWOBJ feature. | Supplement No2 Ch.4 (3.3.1) and Appendix B1, Annex A (16) | C |
| 563 | Check removed. |  |  |  |  |
| 564 | Check removed. |  |  |  |  |
| 565 | Check removed. |  |  |  |  |

| 566 | For each NEWOBJ feature with the attributes CLSDEF, CLSNAM and SYMINS not populated with exactly one of the following combinations: | Invalid use of NEWOBJ | Amend to reflect TSMAD guidance. | EB 54 | E |
| --- | --- | --- | --- | --- | --- |
|  | CLSDEF | CLSNAM | SYMINS |  |
|  | A Virtual feature which indicates navigable water lies northwards | Virtual AtoN, North Cardinal | SY(BRTHNO01);SY(BeaconCardinal01); TX('V-AIS',3,2,2,'15110',2,0,CHMGD,11) |  |
|  | A Virtual feature which indicates navigable water lies eastwards | Virtual AtoN, East Cardinal | SY(BRTHNO01);SY(BeaconCardinal02); TX('V-AIS',3,2,2,'15110',2,0,CHMGD,11) |  |
|  | A Virtual feature which indicates navigable water lies southwards | Virtual AtoN, South Cardinal | SY(BRTHNO01);SY(BeaconCardinal03); TX('V-AIS',3,2,2,'15110',2,0,CHMGD,11) |  |
|  | A Virtual feature which indicates navigable water lies westwards | Virtual AtoN, West Cardinal | SY(BRTHNO01);SY(BeaconCardinal04); TX('V-AIS',3,2,2,'15110',2,0,CHMGD,11) |  |
|  | A Virtual feature marking the port side of a channel | Virtual AtoN, Port Lateral | SY(BRTHNO01);SY(BuoyLateral24); TX('V-AIS',3,2,2,'15110',2,0,CHMGD,11) |  |
|  | A Virtual feature marking the starboard side of a channel | Virtual AtoN, Starboard Lateral | SY(BRTHNO01);SY(BuoyLateral13); TX('V-AIS',3,2,2,'15110',2,0,CHMGD,11) |  |
|  | A Virtual feature marking the port side of a channel | Virtual AtoN, Port Lateral | SY(BRTHNO01);SY(BuoyLateral23); TX('V-AIS',3,2,2,'15110',2,0,CHMGD,11) |  |
|  | A Virtual feature marking the starboard side of a channel | Virtual AtoN, Starboard Lateral | SY(BRTHNO01);SY(BuoyLateral14); TX('V-AIS',3,2,2,'15110',2,0,CHMGD,11) |  |
|  | A Virtual feature marking an isolated danger | Virtual AtoN, Isolated Danger | SY(BRTHNO01);SY(BeaconIsolatedDanger21); TX('V-AIS',3,2,2,'15110',2,0,CHMGD,11) |  |
|  | A Virtual feature marking safe water | Virtual AtoN, Safe Water | SY(BRTHNO01);SY(BuoySafeWater12); TX('V-AIS',3,2,2,'15110',2,0,CHMGD,11) |  |
|  | A Virtual feature used to mark an surface or feature referred to in nautical documents | Virtual AtoN, Special Purpose | SY(BRTHNO01);SY(BuoySpecialPurpose11); TX('V-AIS',3,2,2,'15110',2,0,CHMGD,11) |  |
|  | A Virtual feature marking a wreck | Virtual AtoN, Wreck Marking | SY(BRTHNO01);SY(BuoySpecialPurpose11); TX('V-AIS',3,2,2,'15110',2,0,CHMGD,11) |  |
| 567 | For each attribute of type ‘list’ (excluding colour, natureOfSurfaceQualifyingTerms and natureOfSurface) with more than one instance of the same value. | List attribute contains the same value more than once. | Remove unnecessary attribute value. | Logical consistency | E |
| 568 | For each feature where periodStart and periodEnd are notNull AND their values are identical. | Object has identical values of periodStart and periodEnd. | Ensure values of periodStart and periodEnd are logical. | Logical consistency | E |
| 569 | For each feature where periodStart is notNull AND periodEnd is Null OR not Present. | Object has periodStart without a value of periodEnd. | Populate periodEnd or remove periodStart. | Logical consistency | E |
| 570 | For each feature where periodEnd is notNull AND periodStart is Null OR not Present. | Object has periodEnd without a value of periodStart. | Populate periodStart or remove periodEnd. | Logical consistency | E |
| 571 | For each edge which contains vertices at a density Greater than 0.3mm at compilation scale. | Vertex density exceeds the allowable tolerance. | Generalise edge(s). | 4.8.1 | W |
| 572 | For each feature where NINFOM is notNull AND Information is Null OR not Present. | NINFOM is populated without Information. | Populate Information. | 3.11.1 | E |
| 573 | For each feature where NPLDST is notNull AND PILDST is Null OR not Present. | NPLDST is populated without PILDST. | Populate Pilot district. | 3.11.1 | E |
| 574 | For each feature where NTXTDS is notNull AND TextualDescription is Null OR not Present. | NTXTDS is populated without TextualDescription. | Populate TextualDescription and include relevant Text file | 3.11.1 | E |

| 2.3 Exchange Set Level Checks |
| --- |
| No | Check description | Check message | Check solution | Conformity to: | Cat |
| 1000 | Check removed |  |  |  |  |
| 1001 | Check removed |  |  |  |  |
| 1002 | Check removed |  |  |  |  |
| 1003 | Check removed |  |  |  |  |
| 1004 | Check removed |  |  |  |  |
| 1005 | Check removed |  |  |  |  |
| 1006 | If an update and its base cell do not have the same lexical level. | Update and base cell do not have the same lexical level. | Amend the lexical level of the update. | Part 3 (8.4.2.2a) | C |
| 1007 | For each feature which references a text/picture file and the text/picture file is not Present in the exchange set. | Text or picture file referenced by a feature is not present in the exchange set. | Add referenced text or picture files to exchange set. | 11.4 | C |
| 1008 | For each ER (update) file where an AGEN subfield value of the DSID field OR FOID field is not identical to the AGEN subfield values in the EN (base) file. | AGEN subfield values do not agree between ER (update) and EN (base) files. | Amend AGEN subfield values to agree. | B1.5.31 B1.6.24 | C |
| 1009 | For a catalogue file where the DDR does not contain only the description of the catalogue file structure. | Invalid DDR in catalogue file. | Amend DDR. | 11 12 | W |
| 1010 | For each FRID field in an ER (update) file where RUIN is Equal to 3 (modify) AND the FOID for the modified feature is not identical in the EN (base) and ER (update) files. | FOID for the modified feature is not identical in the EN (base) and ER (update) files. | Amend FOIDs to be identical or make separate insert and delete updates. | B1.5.30 B1.6.23 | C |
| 1011 | For each TextualDescription, PictoralRepresentation attribute which is ‘notNull’ and references a file that does not exist or their names do not conform to the ENC Product Specification. | Referenced files are missing or their names are non-conformant. | Ensure referenced files exist and are named correctly. | 11.2 11.4 | C |
| 1012 | If a catalogue file does not exist. | No catalogue file exists. | Create a catalogue file. | 11 12 | C |
| 1013 | If volume name is not in accordance with the ENC Product Specification. | Volume name is not in accordance with the ENC Product Specification. | Amend the volume name. | Appendix B.1 5.4.2 | C |
| 1014 | If the directory structure for physical media is not in accordance with the ENC Product Specification. | The directory structure for physical media is not in accordance with the ENC Product Specification. | Amend the directory structure of the physical media. | 12 | C |
| 1015 | If the text and picture file names are not unique, OR not with extension (e.g. .TXT and .TIF). | Text and picture file names have incorrect format/name. | Use correctly formatted and named text and picture files. | 11.4 | C |
| 1016 | If the calculated CRC value of a file is Not equal to that stated in the catalogue file. | CRC values do not match. | Amend CRC value. | 11.6 | C |
| 1017 | If the format of the catalogue file is not correct. | Catalogue file format not correct. | Amend format of the catalogue file. | 11.5 12 | C |
| 1018 | If the IMPL subfield of the CATD field is Not equal to “BIN” | CATD-IMPL is not equal to “BIN” | Amend CATD-IMPL. | Appendix B.1 6.2.2 | E |
| 1019 | For each feature where TextualDescription are notNull AND the files referenced are identical or empty. | Files referenced by TextualDescription are the same or empty. | Ensure files are different. | Logical consistency | W |
| 1020 | If the value of the EDTN subfield of the DSID field is incorrect. | Incorrect value of Edition Number. | Amend Edition Number. | Appendix B.1 Annex A 2.2.2 | C |
| 1021a | If the data set is not a re-issue AND the UPDN subfield of the DSID field is incorrect OR it is not equivalent to the extension of the data set file name. | Update number is incorrect or not equivalent to the data set file name extension. | Amend Update number subfield. | Appendix B.1 Annex A 2.2.2 | C |
| 1021b | If the data set is a re-issue AND UPDN subfield of the DSID field is not equal to the last issued update number. | Re-issue data set where Update number is not equal to the last issued update number. | Amend Update number subfield to the value of the last issued update number. | Appendix B.1 Annex A 2.2.2 | C |
| 1022 | For each text file forming part of the exchange set which is not an ASCII file AND is not referenced by the attribute NTXTDS when the NALL subfield of the DSSI is set to 2. | Non ASCII text file included in the exchange set. | Include as an ASCII file or ensure referenced by NTXTDS and that the NALL (NATF lexical level) subfield of the DSSI (Data Set Structure Information) field is set to 2. | Appendix B.1 Annex A 2.3 | C |
| 1023 | For each picture file which is not in the TIFF format. | Picture file not in Tiff format. | Replace picture file with Tiff format version. | 11.4 | C |
| 1024a | For a base cell file if the limits contained in the subfields SLAT, WLON, NLAT, and ELON of the CATD field of the catalogue file are Not equal to the furthest coordinates of the DataCoverage meta feature in the corresponding base cell file. | Limits in catalogue do not correspond to DataCoverage limits for a base cell file. | Amend limits in catalogue or base cell file DataCoverage feature to agree. | 12 logical consistency | C |
| 1024b | For an update cell file if the limits are not identical to the limits of the base cell to which they apply. | Update with limits different to that of the base cell. | Amend limits of update file. | 4.5.2 logical consistency | C |

| 2.4 Checks relating to Data Classification and Encoding Guide (DCEG) |
| --- |
| No | Check description | Check message | Check solution | Conformity to: | Cat |
| 1500 | For each LandArea feature of geometric primitive surface which OVERLAPS a CableArea or SeabedArea feature of geometric primitive surface. | CableArea or SeabedArea overlaps a LandArea feature. | Amend features to remove overlap. | Logical consistency | W |
| 1501 | Check removed. |  |  |  |  |
| 1502 | For each spatial feature which contains the attribute HORDAT. | HORDAT used in a spatial feature. | Remove HORDAT. | 2.1.1 | E |
| 1503 | For each feature (excluding VerticalDatumOfData and SoundingDatum) where verticalDatum is notNull AND all of the following attributes are Null elevation, height, verticalClearanceClosed, verticalClearance, verticalClearanceOpen and verticalClearanceSafe. | Value of verticalDatum without corresponding vertical distance value. | Remove verticalDatum or populate vertical distance attribute. | DCEG | E |
| 1504 | If the value of the VDAT subfield of the DPSM field is Null. | VDAT is not populated. | Populate the VDAT subfield with the vertical datum of the cell. |  | C |
| 1505 | For each VerticalDatumOfData meta feature where verticalDatum is notNull AND is Equal to the value of verticalDatum in the VDAT subfield of the DSPM field. | Value of verticalDatum replicates that in the VDAT subfield of the DPSM field. | Remove unnecessary value of verticalDatum. | DCEG | E |
| 1506 | For each feature where any of elevation, height, verticalClearanceClosed, verticalClearance, verticalClearanceOpen or verticalClearanceSafe is notNull AND which OVERLAPS more than one VerticalDatumOfData meta feature. | Object with height value not split at boundary of VerticalDatumOfData feature. | Split feature at boundary of VerticalDatumOfData feature. | DCEG (3.7) | E |
| 1507 | For each VerticalDatumOfData meta feature which OVERLAPS another VerticalDatumOfData meta feature. | VerticalDatumOfData features overlap. | Amend features to remove the overlap. | DCEG (3.7) | E |
| 1508 | For each SoundingDatum meta feature which OVERLAPS another SoundingDatum meta feature. | SoundingDatum features overlap. | Amend features to remove the overlap. | DCEG (3.6) | E |
| 1509 | Check removed. |  |  |  |  |
| 1510 | If the SDAT subfield of the DPSM field is Null. | SDAT is not populated. | Populate the SDAT subfield with the sounding datum of the cell. | 2.1.3 | C |
| 1511 | For each SoundingDatum meta feature where verticalDatum is Equal to the value of SDAT subfield of the DSPM field. | SoundingDatum feature has the same verticalDatum as in the SDAT subfield of the DSPM. | Remove SoundingDatum feature or amend value of verticalDatum. | 2.1.3 | E |
| 1512a | For each Sounding feature which OVERLAPS more than one SoundingDatum meta feature. | Sounding feature overlaps multiple SoundingDatum features. | Split Sounding feature at boundary of SoundingDatum features. | DCEG (3.6) | E |
| 1512b | For each feature where any of valueOfSounding, valueOfDepthContour, waterLevelEffect, expositionOfSounding, depthRangeMinimumValue or depthRangeMaximumValue is notNull AND which OVERLAPS more than one SoundingDatum meta feature. | Object with depth information overlaps multiple SoundingDatum features. | Split feature at boundary of SoundingDatum features. | DCEG (3.6) | E |
| 1513 | If the value of the HUNI subfield of the DSPM field is Not equal to 1 (metres). | HUNI subfield is not equal to 1 (metres). | Set value of HUNI to 1 (metres). | 2.1.4 | C |
| 1514 | Check removed. |  |  |  |  |
| 1515a | For each feature where a value of dateEnd, dateStart, periodEnd or periodStart, does not conform to the formatting defined in ISO 8601:1988. | Date attribute not formatted according to ISO 8601:1988. | Amend formatting to conform to ISO 8601:1988. | DCEG (2.4.2) | C |
| 1515b | For each feature where a value of SORDAT, SUREND or surveyDateRange does not conform to the formatting defined in ISO 8601:1988. | Date attribute not formatted according to ISO 8601:1988. | Amend formatting to conform to ISO 8601:1988. | DCEG (2.4.2) | E |
| 1516 | For each Group 2 feature with allowable attributes status, periodStart and periodEnd, where status is Equal to 5 (periodic/intermittent) AND periodStart or periodEnd are Null OR not Present. | periodStart or periodEnd not populated where status = 5. | Populate periodStart or periodEnd with values or remove status = 5 (periodic/intermittent) | DCEG (2.4.8.1) | W |
| 1517 | For each feature where TIMSTA or TIMEND is notNull AND their values do not conform to the format defined in Chapter 2 of S-101 Appendix A. | TIMEND or TIMSTA are not formatted correctly. | Amend the formatting of TIMEND or TIMSTA. | 2.1.6 | E |
| 1518a | If the AGEN subfield of the DSID field is not one of the values listed in S-62 sections I and II. | Producing Agency code is not a valid S-62 value. | Amend AGEN subfield to a valid S-62 value. | 2.2.1 | C |
| 1518b | If the first 2 characters of the data set file name do not correspond to the value of the AGEN subfield of the DSID field. | Data set file name does not begin with the agency code corresponding to that set in the AGEN subfield of the DSID field. | Amend the first 2 characters of the data set file name. | 11.3.2 | C |
| 1519 | Check removed. |  |  |  |  |
| 1520 | Check renumbered 1020 |  |  |  |  |
| 1521a | Check renumbered 1021a |  |  |  |  |
| 1521b | Check renumbered 1021b |  |  |  |  |
| 1522a | Check removed. |  |  |  |  |
| 1522b | If the file extension is not “.000” AND the UADT subfield of the DSID field is notNull. | Update application date is notNull for an update. | Set Update application date Null. | S-101 Annex B | C |
| 1523a | Check removed. |  |  |  |  |
| 1523b | If the data set file name extension is Equal to “.000” AND the ISDT subfield of the DSID field is Less than the value of the UADT subfield. | The ISDT of a base cell file precedes the UADT. | Amend UADT or ISDT accordingly. | S-101 Annex B | C |
| 1524 | For each QualityOfBathymetricSurvey meta feature which is not completely WITHIN a SweptArea feature AND where depthRangeMinimumValue is notNull. | QualityOfBathymetricSurvey which is not covered by a SweptArea feature contains depthRangeMinimumValue. | Remove value of depthRangeMinimumValue. | DCEG | E |
| 1525 | For each QualityOfBathymetricSurvey meta feature where positionalUncertainty is notNull AND depthRangeMinimumValue is notNull. | QualityOfBathymetricSurvey feature with both depthRangeMinimumValue and positionalUncertainty populated. | Remove positionalUncertainty from QualityOfBathymetricSurvey feature. | DCEG | E |
| 1526 | Check removed. |  |  |  |  |
| 1527 | Check removed. |  |  |  |  |
| 1528 | Check removed. |  |  |  |  |
| 1529 | For each feature WITHIN a QualityOfBathymetricSurvey meta feature where techniqueOfVerticalMeasurement is notNull AND the value of techniqueOfVerticalMeasurement is Equal to the techniqueOfVerticalMeasurement of the QualityOfBathymetricSurvey meta feature. | techniqueOfVerticalMeasurement value of a feature is equal to value for the QualityOfBathymetricSurvey it lies within. | Remove unnecessary value of techniqueOfVerticalMeasurement. | DCEG | E |
| 1530 | For each feature WITHIN a QualityOfBathymetricSurvey meta feature where verticalUncertainty is notNull AND the value of verticalUncertainty is Equal to the verticalUncertainty OR is equivalent to the CATZOC values of the QualityOfBathymetricSurvey meta feature. | verticalUncertainty value of a feature is equal to the verticalUncertainty value or equivalent to the value of CATZOC of the QualityOfBathymetricSurvey it lies within. | Remove unnecessary value of verticalUncertainty. | DCEG | E |
| 1531 | For each QualityOfBathymetricSurvey meta feature where the value of positionalUncertainty, verticalUncertainty or techniqueOfVerticalMeasurement is notNull AND is equivalent to or degrades the accuracy indicated by the value of CATZOC. | Value of positionalUncertainty, verticalUncertainty, or techniqueOfVerticalMeasurement conflicts with the accuracy indicated by the value of CATZOC. | Amend CATZOC value or remove inappropriate value of positionalUncertainty, verticalUncertainty or techniqueOfVerticalMeasurement. | DCEG | E |
| 1532 | For each QualityOfBathymetricSurvey meta feature where surveyDateRange is Not equal to the smallest (oldest) value of surveyDateRange of the QualityOfSurvey meta features WITHIN the QualityOfBathymetricSurvey meta feature. | surveyDateRange of a QualityOfBathymetricSurvey feature is not equal to the oldest survey within the QualityOfBathymetricSurvey feature. | Amend the surveyDateRange value of QualityOfBathymetricSurvey to reflect the oldest survey within it. | DCEG | E |
| 1533 | For each DredgedArea feature where verticalUncertainty is notNull AND it is equivalent to or degrades the CATZOC value of the QualityOfBathymetricSurvey meta feature it is WITHIN. | verticalUncertainty of a DredgedArea feature is equivalent to or degrades the CATZOC value of the underlying QualityOfBathymetricSurvey feature. | Amend the CATZOC value of QualityOfBathymetricSurvey. | DCEG | E |
| 1534 | For each UnderwaterAwashRock feature where verticalUncertainty is notNull AND is equivalent to or degrades the CATZOC value of the QualityOfBathymetricSurvey meta feature it is WITHIN. | verticalUncertainty of an UnderwaterAwashRock feature is equivalent to or degrades the CATZOC value of the underlying QualityOfBathymetricSurvey feature. | Amend CATZOC value of QualityOfBathymetricSurvey. | DCEG | E |
| 1535 | For each UnderwaterAwashRock feature where verticalUncertainty is notNull AND is Equal to or degrades the verticalUncertainty value of the QualityOfBathymetricSurvey meta feature it is WITHIN. | verticalUncertainty of an UnderwaterAwashRock feature is equal to or degrades the verticalUncertainty value of the underlying QualityOfBathymetricSurvey feature. | Delete or amend the verticalUncertainty value of QualityOfBathymetricSurvey. | DCEG | E |
| 1536 | For each Wrecks feature where verticalUncertainty is notNull AND is equivalent to or degrades the CATZOC value of the QualityOfBathymetricSurvey meta feature it is WITHIN. | verticalUncertainty of a Wrecks feature is equal to or degrades the CATZOC value of the underlying QualityOfBathymetricSurvey feature. | Amend the CATZOC value of QualityOfBathymetricSurvey. | DCEG | E |
| 1537 | For each Wrecks feature where verticalUncertainty is notNull AND is equal to or degrades the verticalUncertainty value of the QualityOfBathymetricSurvey meta feature it is WITHIN. | verticalUncertainty of a Wrecks is equal to or degrades the verticalUncertainty value of the underlying QualityOfBathymetricSurvey feature. | Amend the verticalUncertainty value of QualityOfBathymetricSurvey or Wrecks as appropriate. | DCEG | E |
| 1538 | For each Obstruction feature where verticalUncertainty is notNull AND is equivalent to or degrades the CATZOC value of the QualityOfBathymetricSurvey meta feature it is WITHIN. | verticalUncertainty of an Obstruction feature is equivalent to or degrades the CATZOC value of the underlying QualityOfBathymetricSurvey feature. | Amend the verticalUncertainty value of QualityOfBathymetricSurvey or Obstruction as appropriate. | DCEG | E |
| 1539 | For each Obstruction feature where verticalUncertainty is notNull AND it is Equal to or degrades the verticalUncertainty value of the QualityOfBathymetricSurvey meta feature it is WITHIN. | verticalUncertainty of an Obstruction is equal to or degrades the verticalUncertainty value of the underlying QualityOfBathymetricSurvey feature. | Remove or amend the verticalUncertainty value of QualityOfBathymetricSurvey or Obstruction as appropriate. | DCEG | E |
| 1540 | Check removed. |  |  |  |  |
| 1541 | For each single sounding where the value of qualityOfSounding of the Sounding feature is Equal to the qualityOfSounding value of the QualityOfSurvey meta feature it lies WITHIN. | qualityOfSounding of a Sounding feature is equal to the qualityOfSounding value of the underlying QualityOfSurvey feature. | Remove qualityOfSounding from Sounding feature. | DCEG | E |
| 1542 | For each feature where the value of positionalUncertainty is Equal to the positionalUncertainty value of the QualityOfNonBathymetricData meta feature it is WITHIN. | positionalUncertainty of an feature is equal to the positionalUncertainty value of the underlying QualityOfNonBathymetricData feature. | Remove unnecessary positionalUncertainty value. | DCEG | E |
| 1543 | Check removed. |  |  |  |  |
| 1544 | For each QualityOfNonBathymetricData meta feature where horizontalDistanceUncertainty, verticalUncertainty or verticalUncertainty are Present. | QualityOfNonBathymetricData feature includes horizontalDistanceUncertainty, verticalUncertainty or verticalUncertainty. | Remove horizontalDistanceUncertainty, verticalUncertainty or verticalUncertainty. | DCEG | E |
| 1545 | For each feature where horizontalDistanceUncertainty is notNull AND HORCLR is Null OR not Present. | Value for horizontalDistanceUncertainty without a value of HORCLR. | Add HORCLR value or remove horizontalDistanceUncertainty. | DCEG | E |
| 1546 | For each feature where verticalUncertainty is notNull AND verticalClearance, verticalClearanceOpen, verticalClearanceSafe and verticalClearanceClosed are Null OR not Present. | Value for verticalUncertainty without value of verticalClearance, verticalClearanceOpen, verticalClearanceSafe or verticalClearanceClosed. | Remove verticalUncertainty or populate vertical clearance value. | DCEG | E |
| 1547 | Check removed. |  |  |  |  |
| 1548 | For each feature (excluding Sounding, DepthContour, DepthArea, DredgedArea and Obstruction) where SORIND is notNull AND SORDAT is Null OR not Present. | Value of SORIND without a value of SORDAT for a non-bathymetric feature. | Populate SORDAT with an appropriate value. | 2.2.5.2 | W |
| 1549 | If the value of CSCL subfield of the DPSM field is Null. | CSCL is not populated with a value. | Populate CSCL with an appropriate value. | 2.2.6 | C |
| 1550 | For each M_CSCL meta feature where CSCALE is Equal to the value of CSCL subfield in the DPSM field. | CSCALE of M_CSCL is equal to the value given CSCL subfield of the DSPM field. | Remove unnecessary M_CSCL feature. | 2.2.6 | E |
| 1551 | For each M_CSCL meta feature which OVERLAPS another M_CSCL meta feature. | M_CSCL features overlap. | Amend M_CSCL features so that they do not overlap. | 2.2.6 | E |
| 1552 | Check removed. |  |  |  |  |
| 1553 | For each value of scaleMinimum which is Less than or equal to the compilation scale of the data for the surface. | scaleMinimum value less than or equal to compilation scale. | Amend scaleMinimum value accordingly. | DCEG (2.5.12) | E |
| 1554a | For each Skin of the Earth feature where scaleMinimum is Present. | scaleMinimum present for a Skin of the Earth feature. | Remove scaleMinimum. | DCEG (2.5.12) | C |
| 1554b | For each meta feature where scaleMinimum is Present. | scaleMinimum present for a meta feature. | Remove scaleMinimum. | DCEG (2.5.12) | C |
| 1555 | Check removed. |  |  |  |  |
| 1556 | Check renumbered 1022 |  |  |  |  |
| 1557 | For each T_HMON feature where T_MTOD is Not equal to 1 (simplified harmonic method of tidal prediction) OR 2 (full harmonic method of tidal prediction). | Invalid value of T_MTOD for T_MTOD feature. | Set value of T_MTOD to 1(simplified harmonic method of tidal prediction) or 2(full harmonic method of tidal prediction). | 3.2.2 | E |
| 1558 | For each T_NHMN feature where T_MTOD is Not equal to 3 (time and height difference non-harmonic method). | Invalid value of T_MTOD for T_NHNM feature. | Set value of T_MTOD to 3(time and height difference non-harmonic method). | 3.2.3 | E |
| 1559 | For each T_NHMN feature which is not associated (using the C_ASSO collection feature) with a T_TIMS or T_HMON feature. | T_NHMN which is not associated with a T_TIMS or a T_HMON feature. | Associate T_NHNM with a T_TIMS or T_HMON feature. | 3.2.3 | E |
| 1560 | For each TS_PRH feature where T_MTOD is Not equal to 1 (simplified harmonic method of tidal prediction) OR 2 (full harmonic method of tidal prediction). | Invalid value of T_MTOD for TS_PRH feature. | Set value of T_MTOD to 1(simplified harmonic method of tidal prediction) or 2(full harmonic method of tidal prediction). | 3.3.3 | E |
| 1561 | For each TS_PNH feature where T_MTOD is Not equal to 3 (time and height difference non-harmonic method). | Invalid value of T_MTOD for TS_PNH feature. | Set value of T_MTOD to 3(time and height difference non-harmonic method). | 3.3.4 | E |
| 1562 | For each TS_PNH feature which is not associated (using the C_ASSO collection feature) with a TS_TIS OR TS_PRH feature. | TS_PNH feature which is not associated with a TS_TIS or TS_PRH feature. | Associate TS_PNH with a TS_TIS or TS_PRH feature using C_ASSO. | 3.3.4 | E |
| 1563 | For each River, Canal, LakeArea, DockArea or LockBasin feature which is not WITHIN a LandArea or UnsurveyedArea feature of geometric primitive surface. | Non navigable water features not covered by UnsurveyedArea or LandArea. | Amend LandArea or UnsurveyedArea to cover non navigable water features. | DCEG (5.4 and 11.9) | W |
| 1564 | For each CTRPNT feature where verticalUncertainty or verticalDatum are Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a CTRPNT feature. | Remove verticalUncertainty or verticalDatum. | 4.3 | E |
| 1565 | For each edge of a LandArea feature of geometric primitive surface which is not COINCIDENT with one of the following feature features; a) Coastline, ShorelineConstruction, Gate or Dam of geometric primitive curve. OR b) DataCoverage, Gate, Dam, River, Tunnel, DryDock, Canal, LakeArea, LockBasin, DockArea or LandArea of geometric primitive surface. OR c) Causeway, ShorelineConstruction, MooringFacility, Wrecks, Obstruction or PylonBridgeSupport where waterLevelEffect is Equal to 1 (partly submerged at high water) OR 2 (always dry) OR 6 (subject to inundation or flooding). | LandArea not enclosed by appropriate curvear or surface feature. | Ensure LandArea is enclosed by an appropriate feature. | DCEG (5.4) | E |
| 1566 | For each edge of a Coastline or ShorelineConstruction feature of geometric primitive curve which is COINCIDENT with a River, Canal, LakeArea, DockArea, DryDock or LockBasin feature AND is not COINCIDENT with a DepthArea, DredgedArea, UnsurveyedArea, Pontoon, FloatingDock or Hulk feature. | Coastline or ShorelineConstruction used as the boundary of features on LAND. | Remove Coastline or ShorelineConstruction feature. | DCEG (5.3 and 8.6) | E |
| 1567 | For each Coastline feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a Coastline feature. | Remove values of verticalUncertainty or verticalDatum. | DCEG (5.3) | E |
| 1568 | For each ShorelineConstruction feature of geometric primitive surface which is not WITHIN a LandArea, DepthArea or UnsurveyedArea of geometric primitive surface. | Area ShorelineConstruction feature not covered by a appropriate Skin of the Earth feature. | Amend appropriate Skin of the Earth feature to cover ShorelineConstruction feature. | DCEG (8.6) | E |
| 1569 | For each ShorelineConstruction feature of geometric primitive surface where waterLevelEffect is Equal to 3 (always under water/submerged) OR 4 (covers and uncovers) OR 5 (awash) AND which is not WITHIN a DepthArea and/or UnsurveyedArea of type surface. | Area ShorelineConstruction feature not covered by an appropriate Skin of the Earth feature. | Amend appropriate Skin of the Earth feature to cover ShorelineConstruction feature. | DCEG (8.6) | E |
| 1570 | For each ShorelineConstruction feature where VERCCA or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a ShorelineConstruction feature. | Remove values of verticalUncertainty or verticalDatum. | DCEG (8.6) | E |
| 1571 | For each Berths feature where verticalDatum is Present. | Prohibited attribute verticalDatum populated for a Berths feature. | Remove value of verticalDatum. | DCEG (8.13) | E |
| 1572 | For each DryDock feature where verticalDatum is Present. | Prohibited attribute verticalDatum populated for a DryDock feature. | Remove value of verticalDatum. | DCEG (8.15) | E |
| 1573 | For each DryDock feature which is not WITHIN a LandArea feature of geometric primitive surface. | DryDock not covered by LandArea. | Amend LandArea or DryDock as required. | DCEG (8.15) | E |
| 1574 | Check removed. |  |  |  |  |
| 1575 | For each FloatingDock feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a FloatingDock feature. | Remove values of verticalUncertainty or verticalDatum. | DCEG (8.16) | E |
| 1576 | Check removed. |  |  |  |  |
| 1577 | For each DockArea feature where the geometric primitive EQUALS a SeaArea feature. | DockArea overlaps SeaArea. | Amend or delete SeaArea as required. | DCEG (8.18) | W |
| 1578 | For each Gate feature where verticalDatum is notNull AND verticalClearance is not Present. | verticalDatum populated without verticalClearance being present. | Remove verticalDatum or populate verticalClearance. | DCEG (8.10) | E |
| 1579 | Check removed. |  |  |  |  |
| 1580 | For each Gate feature which is not WITHIN a DepthArea, DredgedArea, UnsurveyedArea or LandArea of geometric primitive surface. | Gate not covered by DepthArea, DredgedArea, UnsurveyedArea or LandArea. | Amend features to ensure Gate is covered by DepthArea, DredgedArea, UnsurveyedArea or LandArea. | DCEG (8.10) | E |
| 1581 | For each LockBasin feature where its geometric primitive EQUALS a SeaArea feature. | LockBasin overlaps SeaArea. | Amend or delete SeaArea as required. | DCEG (8.20) | W |
| 1582 | For each Gridiron feature where horizontalDistanceUncertainty or verticalUncertainty is Present. | Prohibited attribute verticalUncertainty or horizontalDistanceUncertainty populated for a Gridiron feature. | Remove HORDAT or verticalUncertainty. | DCEG (8.19) | E |
| 1583 | For each MooringFacility feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a MooringFacility feature. | Remove values of verticalUncertainty or verticalDatum. | DCEG (8.14) | E |
| 1584 | For each MooringFacility feature where waterLevelEffect is Equal to 1 (partly submerged at high water) OR 2 (always dry) OR 6 (subject to inundation or flooding) which is not WITHIN a LandArea feature of geometric primitive surface. | MooringFacility with waterLevelEffect=1, 2 or 6 not covered by LandArea. | Amend MooringFacility or LandArea as required. | DCEG (8.14) | E |
| 1585 | For each Pile feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a Pile feature. | Remove verticalUncertainty or verticalDatum. | DCEG (8.4) | E |
| 1586 | For each Pontoon feature where verticalUncertainty is Present. | Prohibited attribute populated for a Pontoon feature. | Remove verticalUncertainty. | DCEG (8.17) | E |
| 1587 | For each Hulk feature where horizontalDistanceUncertainty or verticalUncertainty is Present. | Prohibited attribute horizontalDistanceUncertainty or verticalUncertainty populated for a Hulk feature. | Remove horizontalDistanceUncertainty or verticalUncertainty. | DCEG (8.3) | E |
| 1588 | Check removed. |  |  |  |  |
| 1589 | For each feature where condition is Equal to 1 (under construction), OR 3 (under reclamation) OR 5 (planned construction) AND SORDAT is Null OR not Present. | Object with condition = 1, 3 or 5 without a value for SORDAT. | Populate SORDAT. | DCEG | W |
| 1590 | For each LandRegion feature which is not WITHIN OR does not TOUCH a LandArea feature. | LandRegion not covered by LandArea feature. | Ensure LandRegion is covered by or contains a LandArea feature. | DCEG (5.10) | W |
| 1591 | For each LandElevation feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a LandElevation feature. | Remove verticalUncertainty or verticalDatum. | DCEG (5.5) | E |
| 1592 | For each Coastline feature which is COINCIDENT with a LandRegion feature where categoryOfLandRegion is Equal to 2 (marsh) AND categoryOfCoastline for the Coastline feature is Not equal to 8 (marshy shore) OR qualityOfPosition is Not equal to 4(approximate). | Invalid value of qualityOfPosition or categoryOfCoastline for a Coastline feature adjacent to a LandRegion where categoryOfLandRegion = 2. | Amend value of categoryOfCoastline or qualityOfPosition as required. | DCEG (5.3) | W |
| 1593 | For each SlopingGround feature where natureOfConstruction or natureOfSurfaceQualifyingTerms is Present. | Prohibited attribute natureOfConstruction or natureOfSurfaceQualifyingTerms populated for a SlopingGround feature. | Remove natureOfConstruction or natureOfSurfaceQualifyingTerms. | DCEG (5.13) | E |
| 1594 | For each SlopeTopline feature where natureOfConstruction, natureOfSurfaceQualifyingTerms, verticalUncertainty or verticalDatum is Present. | Prohibited attribute natureOfConstruction, natureOfSurfaceQualifyingTerms, verticalUncertainty or verticalDatum populated for a SlopeTopline feature. | Remove unnecessary values of natureOfConstruction, natureOfSurfaceQualifyingTerms, verticalUncertainty or verticalDatum. | DCEG (5.14) | E |
| 1595 | For each SlopeTopline feature where categoryOfSlope is Equal to 6(cliff) AND is COINCIDENT with a Coastline feature. | SlopeTopline feature where categoryOfSlope = 6 coincides with a Coastline feature. | Remove SlopeTopline feature. Only Coastline with categoryOfCoastline = 1(steep coast) should be encoded. | DCEG (5.14) | W |
| 1596 | Check removed. |  |  |  |  |
| 1597 | For each River feature where its geometric primitive EQUALS a SeaArea feature. | River feature overlaps a SeaArea feature. | Amend SeaArea feature. | DCEG (5.6) | E |
| 1598 | For each Rapids feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for a Rapids feature. | Remove verticalUncertainty. | DCEG (5.7) | E |
| 1599a | For each Rapids or Waterfall feature which is not WITHIN OR COINICIDENT with a River feature. | Rapids or Waterfall not within or touching a River feature. | Ensure Rapids or Waterfall feature is within or touching a River feature. | DCEG (5.7 and 5.8) | W |
| 1599b | For each Rapids or Waterfall feature which is not WITHIN a LandArea or UnsurveyedArea feature. | Rapids or Waterfall not within LandArea or UnsurveyedArea. | Ensure Rapids or Waterfall feature is covered by LandArea or UnsurveyedArea feature. | DCEG (5.7 and 5.8) | W |
| 1600 | For each Waterfall feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for a Waterfall feature. | Remove verticalUncertainty. | DCEG (5.8) | E |
| 1601 | For each LakeArea feature where verticalUncertainty OR verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a LakeArea feature. | Remove values of verticalUncertainty and verticalDatum. | DCEG (5.9) | E |
| 1602 | For each LakeArea feature where its geometric primitive EQUALS a SeaArea feature. | LakeArea overlaps SeaArea feature. | Amend features to remove overlap. | DCEG (5.9) | W |
| 1603 | Check removed. |  |  |  |  |
| 1604 | For each Coastline feature which is COINCIDENT with a LandRegion feature where categoryOfLandRegion is Equal to 15 (salt pan) AND categoryOfCoastline for the Coastline feature is Not equal to 2 (flat coast). | Coastline feature adjacent to LandRegion with categoryOfLandRegion = 15 does not have categoryOfCoastline = 2. | Amend the categoryOfCoastline of Coastline feature to (2) (flat coast). | DCEG (5.3) | W |
| 1605 | For each IceArea feature which is not WITHIN a LandArea or UnsurveyedArea or DepthArea feature of geometric primitive surface. | IceArea not covered by appropriate TG1 features. | Amend features to ensure TG1 features cover. | DCEG (5.12) | E |
| 1606 | For each Coastline feature where categoryOfCoastline is Not equal to 6 (glacier (seaward end)) AND which is COINCIDENT with an IceArea feature where categoryOfIce is Equal to 5 (glacier). | Coastline without categoryOfCoastline = 6 touching an IceArea with categoryOfIce = 5. | Populate categoryOfCoastline = 6 (glacier (seaward end)) for the Coastline feature. | DCEG (5.3) | W |
| 1607a | For each Coastline feature where categoryOfCoastline is Not equal to 7 (mangrove) AND is COINCIDENT with a Vegetation feature where categoryOfVegetation is Equal to 7 (mangroves). | Coastline with categoryOfCoastline not equal to 7 is coincident with a Vegetation feature with categoryOfVegetation = 7. | Populate categoryOfCoastline = 7 (mangrove) for the Coastline feature. | DCEG (5.3) | W |
| 1607b | For each Vegetation feature where categoryOfVegetation is Equal to 7 (mangroves) AND the qualityOfPosition of the spatial feature is Not equal to 4 (approximate). | Vegetation feature where categoryOfVegetation = 7 without qualityOfPosition = 4. | Populate qualityOfPosition = 4 (approximate). | DCEG (5.11) | W |
| 1608 | For each Vegetation feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a Vegetation feature. | Remove verticalUncertainty or verticalDatum. | DCEG (5.11) | E |
| 1609 | For each Canal feature where the geometric primitive EQUALS a SeaArea feature. | Canal overlaps SeaArea feature. | Remove SeaArea or amend features to remove overlap. | DCEG (8.8) | W |
| 1610 | For each Railway feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for a Railway feature. | Remove verticalUncertainty. | DCEG (6.12) | E |
| 1611 | For each Tunnel feature where buriedDepth is Present. | Prohibited attribute buriedDepth populated for a TunnelS feature. | Remove buriedDepth. | DCEG (6.14) | E |
| 1612 | Check removed. |  |  |  |  |
| 1613 | For each Tunnel feature which CONTAINS a Canal feature AND where any of HORCLR, verticalUncertainty or verticalClearance is notNull. | Tunnel which covers a Canal feature has values of HORCLR, verticalUncertainty or verticalClearance. | Remove HORCLR, verticalUncertainty or verticalClearance. | DCEG (6.14) | E |
| 1614 | For Tunnel feature which CONTAINS any non-hydrographic feature. (for this check hydrographic features are DepthArea, DepthContour, DredgedArea and LandArea) | Tunnel contains non Hydrographic feature. | Remove features within Tunnel which are unnecessary. | DCEG (6.14) | W |
| 1615 | Check removed. |  |  |  |  |
| 1616 | For each Dam feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for Dam feature. | Remove verticalUncertainty or verticalDatum. | DCEG (8.11) | E |
| 1617 | For each Dam feature of geometric primitive surface which is not WITHIN a LandArea feature of geometric primitive surface. | Dam not covered by LandArea. | Ensure Dam is covered by LandArea. | DCEG (8.11) | C |
| 1618 | For each Dyke feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for Dyke feature. | Remove verticalUncertainty or verticalDatum. | DCEG (8.5) | E |
| 1619 | For each Dyke feature of geometric primitive surface which is not WITHIN a LandArea feature of geometric primitive surface. | Dyke not covered by LandArea. | Ensure Dyke is covered by LandArea. | DCEG (8.5) | E |
| 1620 | For each edge of a Dyke feature which is COINCIDENT with both a LandArea feature AND a DepthArea or DredgedArea or UnsurveyedArea feature of geometric primitive surface AND is not COINCIDENT with an ShorelineConstruction of geometric primitive curve where categoryOfShorelineConstruction is not Present. | Dyke not enclosed by ShorelineConstruction feature where it forms the boundary between water and land. | Add ShorelineConstruction to ensure boundary between land and water is shown. | DCEG (8.5) | E |
| 1621 | Check removed. |  |  |  |  |
| 1622 | Check removed. |  |  |  |  |
| 1623 | For each BRIDGE feature which OVERLAPS a DepthArea or DredgedArea feature AND the supports are not encoded with PylonBridgeSupport feature features where categoryOfPylon is Equal to 4 (bridge pylon/tower) OR 5 (bridge pier). | BRIDGE over navigable water with supports not encoded using a valid PylonBridgeSupport feature/attribute combination. | Ensure bridge supports are encoded using PylonBridgeSupport with categoryOfPylon = 4 (bridge pylon/tower) or 5 (bridge pier). | DCEG | E |
| 1624 | Check removed. |  |  |  |  |
| 1625 | For each AirportAirfield or Runway feature associated using a C_AGGR collection feature. | AirportAirfield or Runway or associated using C_AGGR. | Encode association using C_ASSO not C_AGGR. | DCEG (6.3 and 6.4) | W |
| 1626 | For each AirportAirfield feature where VisuallyConspicuous is Present. | Prohibited attribute VisuallyConspicuous populated for AirportAirfield feature. | Remove VisuallyConspicuous. | DCEG (6.3 and 6.4) | E |
| 1627 | For each Runway feature where VisuallyConspicuous is Present. | Prohibited attribute VisuallyConspicuous populated for Runway feature. | Remove VisuallyConspicuous. | DCEG (6.4) | E |
| 1628 | For each ProductionStorageArea feature where verticalUncertainty OR verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for ProductionStorageArea feature. | Remove verticalUncertainty or verticalDatum. | DCEG (7.5) | E |
| 1629 | For each BuiltupArea feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a BuiltupArea feature. | Remove verticalUncertainty or verticalDatum. | DCEG (6.1) | E |
| 1630 | For each River, LockBasin, DockArea, LakeArea or Canal feature of geometric primitive surface which OVERLAPS a BuiltupArea feature. | Area River, LockBasin, DockArea, LakeArea or Canal feature overlaps a BuiltupArea feature. | Amend BuiltupArea feature to remove overlap. | DCEG (6.1) | W |
| 1631 | For each Building feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a Building feature. | Remove values of verticalUncertainty or verticalDatum. | DCEG (6.2) | E |
| 1632 | For each SiloTank feature where verticalUncertainty OR verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for SiloTank feature. | Remove verticalUncertainty or verticalDatum. | DCEG (7.3) | E |
| 1633 | For each Landmark feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for Landmark feature. | Remove verticalUncertainty or verticalDatum. | DCEG (7.2) | E |
| 1634 | For each FenceWall feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for FenceWall feature. | Remove verticalUncertainty or verticalDatum. | DCEG (6.11) | E |
| 1635 | For each FortifiedStructure feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for FortifiedStructure feature. | Remove verticalUncertainty or verticalDatum. | DCEG (7.4) | E |
| 1636 | For each PylonBridgeSupport feature where verticalUncertainty or verticalDatum are Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for PylonBridgeSupport feature. | Remove verticalDatum or verticalUncertainty. | DCEG (6.10) | E |
| 1637 | For each PylonBridgeSupport feature of geometric primitive surface where waterLevelEffect is Equal to 1 (partly submerged at high water) OR 2 (always dry) OR 6 (subject to inundation or flooding) which is not WITHIN a LandArea feature of geometric primitive surface. | PylonBridgeSupport feature with waterLevelEffect = 1, 2 or 6 not covered by a LandArea feature. | Ensure PylonBridgeSupport is covered by LandArea. | DCEG (6.10) | E |
| 1638 | Check renumbered to 1023 |  |  |  |  |
| 1639 | For each DepthContour feature where verticalDatum is Present. | Prohibited attribute verticalDatum populated for DepthContour feature. | Remove verticalDatum. | DCEG (11.6) | E |
| 1640 | For each Sounding feature where verticalDatum is Present. | Prohibited attribute verticalDatum populated for Sounding feature. | Remove verticalDatum. | DCEG (11.3) | E |
| 1641 | For each UnderwaterAwashRock feature which is COINCIDENT with a Sounding feature. (COINCIDENT applies to the horizontal component only). | UnderwaterAwashRock feature coincident with Sounding feature. | Remove feature which is not required. | DCEG (13.4) | E |
| 1642 | For each DepthArea feature where verticalDatum or verticalUncertainty is Present. | Prohibited attribute verticalDatum or verticalUncertainty populated for a DepthArea feature. | Remove verticalDatum or verticalUncertainty. | DCEG (11.7) | E |
| 1643 | Check removed. |  |  |  |  |
| 1644 | For each edge bounding a DepthArea feature which is COINCIDENT with a DataCoverage meta feature AND is COINCIDENT with a curvear geo feature. | DepthArea feature on the edge of data coverage not bounded by curvear spatial features without geo features. | Ensure DepthArea features at the edge of the dataset only have spatial features without geo features as their outer boundary. | DCEG (11.7) | W |
| 1645 | Check removed. |  |  |  |  |
| 1646 | For each DredgedArea feature where depthRangeMaximumValue is notNull AND is Equal to the value of depthRangeMinimumValue | depthRangeMinimumValue and depthRangeMaximumValue have the same value for a DredgedArea feature. | Amend values or remove value of depthRangeMaximumValue. | DCEG (11.4) | W |
| 1647 | For each DredgedArea feature where verticalDatum is Present. | Prohibited attribute verticalDatum populated for a DredgedArea feature. | Remove verticalDatum. | DCEG (11.4) | E |
| 1648 | For each DredgedArea feature where qualityOfSounding is notNull AND its value is Not equal to 10 (maintained depth) OR 11 (not regularly maintained). | Invalid value of qualityOfSounding for DredgedArea. | Remove invalid value of qualityOfSounding. | DCEG (11.4) | E |
| 1649 | For each DredgedArea feature where verticalUncertainty is notNull AND is Less than or equal to the value of verticalUncertainty of the QualityOfBathymetricSurvey meta feature it lies WITHIN. has an Equal OR Less than value of verticalUncertainty. | Value of verticalUncertainty on DredgedArea is equivalent to or degrades the value on the underlying QualityOfBathymetricSurvey. | Amend or remove value of verticalUncertainty as appropriate. | DCEG (11.4) | E |
| 1650 | For each SweptArea feature where verticalDatum is Present. | Prohibited attribute verticalDatum populated for a SweptArea feature. | Remove verticalDatum. | DCEG (11.5) | E |
| 1651 | For each SweptArea feature which does not OVERLAP DepthArea and/or DredgedArea feature features of geometric primitive surface. | SweptArea not covered by DredgedArea or DepthArea features. | Amend limits of SweptArea or edit DepthArea and/or DredgedArea features. | DCEG (11.5) | C |
| 1652 | For each SweptArea feature which EQUALS an QualityOfBathymetricSurvey meta feature AND the depthRangeMinimumValue values of the two feature features are Not equal. | SweptArea feature sharing geometry of QualityOfBathymetricSurvey feature where depthRangeMinimumValue values are not equal. | Amend value of depthRangeMinimumValue. | DCEG (11.5) | E |
| 1653 | For each SweptArea feature where verticalUncertainty is notNull AND is Not equal to verticalUncertainty value of the QualityOfBathymetricSurvey meta feature it is WITHIN. | verticalUncertainty of a SweptArea feature is not equal to the verticalUncertainty of the QualityOfBathymetricSurvey meta feature it is within. | Remove or amend or the verticalUncertainty value of the QualityOfBathymetricSurvey feature. | DCEG (11.5) | E |
| 1654 | For each SweptArea feature where techniqueOfVerticalMeasurement is notNull AND is Not equal to 6 (swept by wire-drag) OR 8 (swept by vertical acoustic system) OR 13 (swept by side-scan sonar). | Prohibited value of techniqueOfVerticalMeasurement for a SweptArea feature | Set value of techniqueOfVerticalMeasurement to 6 (swept by wire-drag), 8 (swept by vertical acoustic system) or 13 (swept by side-scan sonar). | DCEG (11.5) | E |
| 1655 | For each SweptArea feature which EQUALS an QualityOfBathymetricSurvey meta feature where positionalUncertainty AND verticalUncertainty are notNull. | positionalUncertainty and verticalUncertainty encoded on QualityOfBathymetricSurvey feature which covers a SweptArea feature. | Remove positionalUncertainty. | DCEG (11.5) | E |
| 1656 | For each UnderwaterAwashRock feature where verticalDatum is Present. | Prohibited attribute verticalDatum populated for UnderwaterAwashRock feature. | Remove verticalDatum. | DCEG (13.4) | E |
| 1657 | For each UnderwaterAwashRock feature where the values of valueOfSounding, qualityOfSounding, waterLevelEffect, techniqueOfVerticalMeasurement and verticalUncertainty are not as defined in the table below (additional values may be encoded). | Illogical attribute values for UnderwaterAwashRock feature. | Amend to logical combination. | DCEG (13.4) | W |
|  | valueOfSounding | qualityOfSounding | waterLevelEffect | techniqueOfVerticalMeasurement |  |
|  |  |  |  | verticalUncertainty |  |
|  | unknown | 2 OR not Present | 3, 4 OR 5 | Not Present |  |
|  |  | 2 OR not Present | unknown | Not Present |  |
|  | < 0 | 1, 3, 4, 6, 8, 9 OR not Present | 4 | notNull |  |
|  |  | 7 | 4 | Not Present |  |
|  | 0 | 1, 3, 4, 6, 8, 9 OR not Present | 5 | notNull |  |
|  |  | 7 | 5 | Not Present |  |
|  | > 0 | 1, 3, 4, 6, 8 OR 9 OR not Present | 3 | notNull |  |
|  |  | 7 | 3 | Not Present |  |
| 1658 | For each Wrecks feature where verticalUncertainty, verticalDatum or verticalLength are Present. | Prohibited attribute verticalDatum, verticalUncertainty or verticalLength populated for Wrecks feature. | Remove verticalDatum, verticalUncertainty or verticalLength. | DCEG (13.5) | E |
| 1659a | For each Wrecks feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 1 (within the range of depth of the surrounding depth surface) OR is not Present AND valueOfSounding is Less than or equal to the depthRangeMinimumValue OR Greater than depthRangeMaximumValue of the DepthArea feature it is WITHIN. | valueOfSounding for Wrecks feature with expositionOfSounding = 1 or not present is outside of the range of the underlying DepthArea. | Populate an appropriate value of expositionOfSounding. | DCEG (13.5) | E |
| 1659b | For each Wrecks feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 1 (within the range of depth of the surrounding depth surface) OR is not Present AND valueOfSounding is Less than or equal to the depthRangeMinimumValue OR Greater than depthRangeMaximumValue of the DredgedArea feature it is WITHIN AND depthRangeMaximumValue is notNull AND Not equal to depthRangeMinimumValue. | valueOfSounding for Wrecks feature with expositionOfSounding = 1 or not present is outside of the range of the underlying DredgedArea. | Populate an appropriate value of expositionOfSounding. | DCEG (13.5) | E |
| 1660 | For each Wrecks feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 2 (shoaler than the range of depth of the surrounding depth surface) AND valueOfSounding is Greater than the depthRangeMinimumValue of the DepthArea or DredgedArea feature it is WITHIN AND depthRangeMinimumValue is notNull. | Wrecks feature where expositionOfSounding = 2 but with a valueOfSounding greater than the depthRangeMinimumValue of the underlying DepthArea/DredgedArea. | Populate an appropriate value of expositionOfSounding. | DCEG (13.5) | E |
| 1661a | For each Wrecks feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 3 (deeper than the range of depth of the surrounding depth surface) AND valueOfSounding is Less than or equal to depthRangeMaximumValue of the DepthArea feature it is WITHIN AND depthRangeMaximumValue is notNull. | Wrecks feature where expositionOfSounding = 3 and valueOfSounding is less than depthRangeMaximumValue of the underlying DepthArea. | Amend value of expositionOfSounding to a logical value. | DCEG (13.5) | E |
| 1661b | For each Wrecks feature where expositionOfSounding is Equal to 3 (deeper than the range of depth of the surrounding depth surface) AND valueOfSounding is Less than or equal to the depthRangeMaximumValue of the DredgedArea feature it is WITHIN where depthRangeMinimumValue AND depthRangeMaximumValue are notNull. | Wrecks feature where expositionOfSounding = 3 and valueOfSounding is less than depthRangeMaximumValue of the underlying DredgedArea. | Amend value of expositionOfSounding to a logical value. | DCEG (13.5) | E |
| 1661c | For each Wrecks feature where expositionOfSounding is Equal to 3 (deeper than the range of depth of the surrounding depth surface) AND valueOfSounding is Less than or is equal to the depthRangeMinimumValue of the DredgedArea feature it is WITHIN where depthRangeMaximumValue is not Present. | Wrecks with expositionOfSounding= 3 but with a valueOfSounding less than depthRangeMinimumValue of the underlying DredgedArea when only depthRangeMinimumValue is populated. | Amend value of expositionOfSounding to a logical value. | DCEG (13.5) | E |
| 1662 | For each Wrecks or Obstruction feature of geometric primitive surface which is not WITHIN a DepthArea, LandArea or UnsurveyedArea feature of geometric primitive surface. | Area Wrecks or Obstruction feature not within a DepthArea, LandArea or UnsurveyedArea feature. | Amend to ensure appropriate Skin of the Earth feature is the underlying feature. | DCEG (13.5 and 13.6) | E |
| 1663 | For each Wrecks feature where the attribute values do not correspond to the table below. | Wrecks feature with illogical attribute combination. | Amend attributes in accordance with the logical values defined in the table. | DCEG (13.5) | W |
|  | valueOfSounding | waterLevelEffect | categoryOfWreck | qualityOfSounding | height | techniqueOfVerticalMeasurement verticalUncertainty |  |
|  | Undefined | 3 OR unknown | 1, 2, 3 OR unknown | 2 OR undefined | Undefined | Undefined |  |
|  |  | 4 OR 5 | Any value | 2 OR undefined | Undefined | Undefined |  |
|  |  | 1 OR 2 | 4, 5 OR unknown | Undefined | Any value | Undefined |  |
|  | Unknown | 3 OR unknown | 1, 2, 3 OR undefined | 2 OR undefined | Undefined | Undefined |  |
|  |  | 4 OR 5 | Any value | 2 OR undefined | Undefined | Undefined |  |
|  |  | 1 OR 2 |  | Undefined | Any value | Undefined |  |
|  | < 0 | 4 | Any value | 7 | Undefined | Undefined |  |
|  |  | 4 | Any value | 1, 3, 4, 6, 8, 9 OR undefined | Undefined | Any value |  |
|  | 0 | 5 | 1, 2, 3 OR undefined | 7 | Undefined | Undefined |  |
|  |  | 5 | Any value | 1, 3, 4, 6, 8, 9 OR undefined | Undefined | Any value |  |
|  | > 0 | 3 | 1, 2, 3 OR undefined | 7 | Undefined | Undefined |  |
|  |  | 3 | 1, 2, 3 OR undefined | 1, 3, 4, 6, 8, 9 OR undefined | Undefined | Any value |  |
| 1664 | For each Obstruction feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for an Obstruction feature. | Remove verticalUncertainty or verticalDatum. | DCEG (13.6) | E |
| 1665a | For each Obstruction feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 1 (within the range of depth of the surrounding depth surface) OR not Present AND valueOfSounding is Less than or equal to depthRangeMinimumValue OR Greater than depthRangeMaximumValue of the DepthArea feature it is WITHIN. | valueOfSounding for Obstruction feature with expositionOfSounding = 1 or not present is outside of the range of the underlying DepthArea. | Populate an appropriate value of expositionOfSounding. | DCEG (13.6) | E |
| 1665b | For each Obstruction feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 1 (within the range of depth of the surrounding depth surface) OR not Present AND valueOfSounding is Less than or equal to depthRangeMinimumValue OR Greater than depthRangeMaximumValue of the DredgedArea feature it is WITHIN AND depthRangeMaximumValue is notNull AND Not equal to depthRangeMinimumValue. | valueOfSounding for Obstruction feature with expositionOfSounding = 1 or not present is outside of the range of the underlying DredgedArea. | Populate an appropriate value of expositionOfSounding. | DCEG (13.6) | E |
| 1666 | For each Obstruction feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 2 (shoaler than the range of depth of the surrounding depth surface) AND valueOfSounding is Greater than the depthRangeMinimumValue of the DepthArea or DredgedArea feature it is WITHIN AND depthRangeMinimumValue is notNull. | Obstruction feature where expositionOfSounding = 2 with a valueOfSounding greater than the depthRangeMinimumValue of the underlying DepthArea/DredgedArea. | Populate an appropriate value of expositionOfSounding. | DCEG (13.6) | E |
| 1667a | For each Obstruction feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 3 (deeper than the range of depth of the surrounding depth surface) AND valueOfSounding is Less than or equal to depthRangeMaximumValue of the DepthArea feature it is WITHIN AND depthRangeMaximumValue is notNull. | Obstruction feature where expositionOfSounding = 3 and a valueOfSounding is less than the depthRangeMaximumValue of the underlying DepthArea. | Amend value of expositionOfSounding to a logical value. | DCEG (13.6) | E |
| 1667b | For each Obstruction feature where expositionOfSounding is Equal to 3 (deeper than the range of depth of the surrounding depth surface) AND valueOfSounding is Less than or equal to the depthRangeMaximumValue of the DredgedArea feature it is WITHIN AND depthRangeMinimumValue AND depthRangeMaximumValue are notNull. | Obstruction feature where expositionOfSounding = 3 and a valueOfSounding is less than the depthRangeMaximumValue of the underlying DredgedArea. | Amend value of expositionOfSounding to a logical value. | DCEG (13.6) | E |
| 1667c | For each Obstruction feature where expositionOfSounding is Equal to 3 (deeper than the range of depth of the surrounding depth surface)AND valueOfSounding is Less than or equal to the depthRangeMinimumValue of the DredgedArea feature it is WITHIN AND depthRangeMaximumValue is not Present. | Obstruction feature where expositionOfSounding = 3 and valueOfSounding is less than depthRangeMinimumValue of the underlying DredgedArea where only depthRangeMinimumValue is populated. | Amend value of expositionOfSounding to a logical value. | DCEG (13.6) | E |
| 1668 | For each Obstruction feature where product is Present AND categoryOfObstruction is Not equal to 2 (wellhead) OR 3 (diffuser). | Obstruction feature with a value for product without a logical value of categoryOfObstruction. | Remove value of product or populate logical value of categoryOfObstruction. | Logical consistency | W |
| 1669 | For each Obstruction feature where the attribute values do not correspond to the table below; | Obstruction feature with illogical attribute value combinations. | Populate logical attribute value combinations. | DCEG (13.6) | E |
|  | valueOfSounding | waterLevelEffect | qualityOfSounding | techniqueOfVerticalMeasurement verticalUncertainty | height |  |
|  | Unknown | 3, 4, 5 OR unknown | 2 OR undefined | Undefined | Undefined |  |
|  |  | 1 OR 2 | Undefined | Undefined | Any value |  |
|  |  | 7 | Undefined | Undefined | Undefined |  |
|  | < 0 | 4 | 1, 3, 4, 6, 8, 9 OR undefined | Any value | Undefined |  |
|  |  | 4 | 7 | Undefined | Undefined |  |
|  | 0 | 5 | 1, 3, 4, 6, 8, 9 OR undefined | Any value | Undefined |  |
|  | > 0 | 3 | 1, 3, 4, 6, 8, 9 OR undefined | Any value | Undefined |  |
|  |  | 3 | 7 | Undefined | Undefined |  |
| 1670 | For each Wrecks or Obstruction feature of geometric primitive surface which CONTAINS Wrecks or Obstruction feature of geometric primitive point AND the values of expositionOfSounding, qualityOfSounding, verticalUncertainty, valueOfSounding and waterLevelEffect of the surface feature are Not equal to the values of the shallowest point feature. | Point Wrecks or Obstruction within surface Wrecks or Obstruction have attribute values not reflected for the surface feature. | Ensure surface Wrecks or Obstruction feature attribute values reflect the shallowest point feature. | DCEG (13.5 and 13.6) | W |
| 1671 | For each feature of geometric primitive curve which is COINCIDENT with an surface feature of the same feature class and attribute values except attributes SORIND, SORDAT and scaleMinimum. | Line feature touching feature with the same attribute values except SORIND, SORDAT and scaleMinimum. | Remove unnecessary feature. | Logical consistency | W |
| 1672 | For each feature of geometric primitive point which is WITHIN a feature of the same class of geometric primitive surface AND which has the same attribute values AND is not a LandArea, Obstruction or Wrecks feature. | Object with the same attributes within an identical feature. | Remove duplicate feature or amend attributes accordingly. | Logical consistency | E |
| 1673a | For each SeabedArea feature where natureOfSurface values are not separated by a comma or slash (without spaces). | natureOfSurface values not separated by a comma or slash. | Insert comma or slash as required. | DCEG (12.1) | E |
| 1673b | For each SeabedArea feature where natureOfSurface starts or ends with a comma or slash. | natureOfSurface starts or ends with a comma or slash. | Remove unnecessary comma or slash. | DCEG (12.1) | E |
| 1673c | For each SeabedArea feature where natureOfSurface contains ‘,,’ OR ‘//’. | Consecutive comma or slash within natureOfSurface. | Remove unnecessary comma or slash. | DCEG (12.1) | E |
| 1673d | For each SeabedArea feature where the natureOfSurfaceQualifyingTerms and natureOfSurface attributes do not contain an Equal number of commas or slashes. | natureOfSurfaceQualifyingTerms and natureOfSurface have different numbers of commas or slashes. | Ensure appropriate commas or slashes are used to separate values. | DCEG (12.1) | E |
| 1673e | For each SeabedArea feature where natureOfSurface contains ‘ 9/ ‘. | natureOfSurface contains ‘9/ ‘. (Rock is encoded as the surface layer, it should be underlying). | Remove inappropriate natureOfSurface contents. | DCEG (12.1) | E |
| 1674 | For each SeabedArea feature of geometric primitive surface WITHIN a DepthArea where depthRangeMinimumValue is Less than 0 AND waterLevelEffect is Not equal to 4 (covers and uncovers). | SeabedArea feature in an inter-tidal surface without waterLevelEffect = 4. | Set value of waterLevelEffect to 4 (covers and uncovers). | DCEG (12.1) | W |
| 1675 | For each Sandwave feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for a Sandwave feature. | Remove verticalUncertainty. | DCEG (12.3) | E |
| 1676 | Check removed. |  |  |  |  |
| 1677 | For each MooringFacility feature where bouyShape is Present AND categoryOfMooringWarpingFacility is Not equal to 7 (mooring buoy). | MooringFacility with bouyShape without categoryOfMooringWarpingFacility = 7. | Set value of categoryOfMooringWarpingFacility to 7(mooring buoy) or remove bouyShape. | DCEG (8.14) | E |
| 1678 | For each RecommendedTrack feature where depthRangeMaximumValue or verticalDatum is Present. | Prohibited attributes depthRangeMaximumValue or verticalDatum populated for RecommendedTrack feature. | Remove depthRangeMaximumValue or verticalDatum. | DCEG (15.5) | E |
| 1679 | For each feature where attributes of the following types enumerated ('E'), float ('F'), integer ('I') or code string ('A') have more than one value. | More than one value present for attributes of the following types; enumerated ('E'), float ('F'), integer ('I') or code string ('A'). | Remove unnecessary values. | DCEG | C |
| 1680 | Check removed. |  |  |  |  |
| 1681 | For each RecommendedTrack feature of geometric primitive curve where orientation is notNull AND traffic is Equal to 1 (inbound) OR 2 (outbound) OR 3 (one-way) AND the bearing of the curve is more than 5 degrees Greater than OR Less than the value of orientation. | RecommendedTrack where orientation does not correspond to the bearing of the curve. | Populate an appropriate value of orientation consistent with the geometry of the feature. | DCEG (15.5) | C |
| 1682 | For each RecommendedTrack or NavigationLine feature which is not part of a C_AGGR collection feature AND is not a RecommendedTrack feature with categoryOfRecommendedTrack is Equal to 2 (not based on a system of fixed marks). | RecommendedTrack or NavigationLine feature is not part of a C_AGGR collection feature. | Add to C_AGGR collection feature. | DCEG (15.5 and 15.4) | W |
| 1683 | For each C_AGGR collection feature with a single instance of both NavigationLine and RecommendedTrack AND their orientation values are Not equal OR reciprocal. | RecommendedTrack and NavigationLine as part of a C_AGGR do not have consistent values of orientation. | Amend values of orientation to agree. | DCEG (15.5 and 15.4) | C |
| 1684 | For each group of feature features forming a measured distance where the beacons and transit curves are not aggregated into a C_AGGR collection feature AND the C_AGGR collection features are not aggregated into another C_AGGR collection feature including the track to be followed. | Measured distance not grouped using C_AGGR collection features. | Encode C_AGGR features and relate as appropriate. |  | E |
| 1685 | For each TrafficSeparationSchemeBoundary feature that is not COINCIDENT with the outer limit of a TrafficSeparationSchemeRoundabout, TrafficSeparationSchemeLanePart or TSSZNE. | TrafficSeparationSchemeBoundary not on the outer limit of an appropriate TSS feature. | Amend TrafficSeparationSchemeBoundary or other TSS features so that it forms the outer limit. | DCEG (15) | E |
| 1686 | For each TrafficSeparationLine feature which is not COINCIDENT with two TrafficSeparationSchemeLanePart feature features OR one TrafficSeparationSchemeLanePart feature and one InshoreTrafficZone feature. | TrafficSeparationLine does not separate TrafficSeparationSchemeLanePart features or TSSPLT and InshoreTrafficZone features. | Amend TSELNE to ensure it separates appropriate features. | DCEG (15) | E |
| 1687 | For each TrafficSeparationZone feature which is not COINCIDENT with two or more TrafficSeparationSchemeLanePart feature features OR at least one TrafficSeparationSchemeLanePart feature and one InshoreTrafficZone feature OR COINCIDENT with a TrafficSeparationSchemeRoundabout feature. | TrafficSeparationZone does not separate appropriate TSS features. | Amend TSSZNE to separate appropriate features. | DCEG (15) | E |
| 1688 | For each TrafficSeparationSchemeCrossing feature which does not touch Greater than 3 TrafficSeparationSchemeLanePart or TwowayRoutePart feature features. | TrafficSeparationSchemeCrossing feature does not encode a crossing of 4 or more lanes. | Encode all lane parts or use another feature. | DCEG (15) | E |
| 1689 | For each TrafficSeparationSchemeCrossing feature which OVERLAPS a TrafficSeparationZone feature. | TrafficSeparationSchemeCrossing feature overlaps TrafficSeparationZone feature. | Amend features to remove overlap. | DCEG (15) | E |
| 1690 | For each TrafficSeparationSchemeRoundabout feature which OVERLAPS a TrafficSeparationZone feature. | TrafficSeparationSchemeRoundabout feature overlaps TrafficSeparationZone feature. | Amend features to remove overlap. | DCEG (15) | E |
| 1691 | For each DeepWaterRoutePart feature wheredepthRangeMaximumValue or verticalDatum is Present. | Prohibited attribute depthRangeMaximumValue or verticalDatum populated for DeepWaterRoutePart feature. | Remove depthRangeMaximumValue or verticalDatum. | DCEG (15) | E |
| 1692 | For each DeepWaterRoutePart feature which is not WITHIN the combined coverage of DepthArea AND DredgedArea feature features. | DeepWaterRoutePart feature not covered by DepthArea or DredgedArea feature. | Encode appropriate DepthArea or DredgedArea features. | DCEG (15) | E |
| 1693 | For each DeepWaterRoutePart or DeepWaterRouteCentercurve feature where FeatureName is notNull AND is aggregated in a collection feature. | DeepWaterRoutePart or DeepWaterRouteCentercurve feature with FeatureName form part of a collection feature. | Encode the name using the C_AGGR collection feature or create a SEARRE. Remove name from DeepWaterRoutePart and/or DeepWaterRouteCentercurve. | DCEG (15) | W |
| 1694 | For each DeepWaterRouteCentercurve feature where orientation is notNull AND traffic is Equal to 1 (inbound) OR 2 (outbound) OR 3 (one-way) AND the bearing of the curve is more than 5 degrees Greater than OR Less than the value of orientation. | One way DeepWaterRouteCentercurve where orientation does not correspond to the bearing of the curve. | Populate an appropriate value of orientation consistent with the geometry of the feature. | DCEG (15) | C |
| 1695 | For each DeepWaterRouteCentercurve feature where verticalDatum or depthRangeMaximumValue is Present. | Prohibited attribute depthRangeMaximumValue or verticalDatum populated for DeepWaterRouteCentercurve feature. | Remove depthRangeMaximumValue or verticalDatum. | DCEG (15) | E |
| 1696 | For each RecommendedRouteCentrecurve feature where traffic is Equal to 1 (inbound) OR, 2 (outbound) OR 3 (one-way) AND the bearing of the curve is more than 5 degrees Greater than OR Less than the value of orientation. | One-way RecommendedRouteCentrecurve where orientation does not correspond to the bearing of the curve. | Populate an appropriate value of orientation consistent with the geometry of the feature. | DCEG (15) | C |
| 1697 | For each RecommendedRouteCentrecurve feature where depthRangeMaximumValue or verticalDatum is Present. | Prohibited attribute depthRangeMaximumValue or verticalDatum populated for RecommendedRouteCentrecurve feature. | Remove depthRangeMaximumValue or verticalDatum. | DCEG (15) | E |
| 1698 | For each TwowayRoutePart feature where depthRangeMaximumValue or verticalDatum is Present. | Prohibited attribute drval2 or verticalDatum populated for TwowayRoutePart feature. | Remove depthRangeMaximumValue or verticalDatum. | DCEG (15) | E |
| 1699 | For each Fairway feature where verticalDatum is Present. | Prohibited attribute verticalDatum populated for a Fairway feature. | Remove verticalDatum. | DCEG (15.6) | E |
| 1700 | For each TerritorialSeaArea feature which OVERLAPS an ExclusiveEconomicZone feature. | TerritorialSeaArea feature overlaps ExclusiveEconomicZone feature. | Amend limits to remove overlap. | DCEG (16.24) | E |
| 1701 | For each CableSubmarine feature where verticalDatum is Present. | Prohibited attribute verticalDatum populated for a CableSubmarine feature. | Remove verticalDatum. | DCEG (14.3) | E |
| 1702 | For each CableSubmarine feature where status is Equal to 4 (not in use) AND categoryOfCable is notNull. | CableSubmarine feature where status = 4 and categoryOfCable is populated. | Amend categoryOfCable or status. | DCEG (14.3) | W |
| 1703 | For each CableSubmarine feature where categoryOfCable is Equal to 3 (transmission curve). | CableSubmarine feature where categoryOfCable = 3. | Remove prohibited value of categoryOfCable. | DCEG (14.3) | E |
| 1704 | For each CableOverhead feature where verticalDatum is Present AND verticalClearance and verticalClearanceSafe are not Present. | verticalDatum populated for CableOverhead feature without value of verticalClearance or verticalClearanceSafe. | Remove verticalDatum or populate verticalClearance or verticalClearanceSafe. | DCEG (6.8) | E |
| 1705 | Check removed. |  |  |  |  |
| 1706 | For each CableOverhead, CableSubmarine, PipelineSubmarineOnLand or PipelineOverhead feature where condition is notNull AND is Not equal to 1 (under construction) OR 5 (planned construction). | CableOverhead, CableSubmarine, PipelineSubmarineOnLand or PipelineOverhead feature where condition does not equal 1 or 5. | Amend value of condition accordingly. | DCEG | E |
| 1707 | For each CableArea feature where categoryOfCable is Equal to 3 (transmission curve) OR 6 (mooring cable/chain), | CableArea has an inappropriate value of categoryOfCable. | Amend to appropriate value of categoryOfCable or remove. | DCEG (14.4) | E |
| 1708 | For each PipelineSubmarineOnLand feature where verticalUncertainty or verticalDatum is Present. | Prohibited attributes verticalUncertainty or verticalDatum populated for PipelineSubmarineOnLand feature. | Remove verticalUncertainty or verticalDatum. | DCEG (14.5) | E |
| 1709 | For each PipelineSubmarineOnLand feature where status is Equal to 4 (not in use) AND categoryOfPipelinePipe is Present. | PipelineSubmarineOnLand subject where status =4 and categoryOfPipelinePipe is populated. | Remove value of categoryOfPipelinePipe if status equals 4 (not in use). | DCEG (14.5) | W |
| 1710 | Check removed. |  |  |  |  |
| 1711 | Check removed. |  |  |  |  |
| 1712 | For each PipelineOverhead feature where status is Equal to 4 (not in use) AND categoryOfPipelinePipe OR product is Present. | PipelineOverhead has status =4 and has a value for categoryOfPipelinePipe or product. | Remove values of categoryOfPipelinePipe or product if status equals 4 (not in use). | DCEG (6.9) | W |
| 1713 | For each SubmarinePipelineArea feature where condition is Present. | Prohibited attribute condition populated for SubmarinePipelineArea feature. | Remove condition. | DCEG (14.5) | E |
| 1714 | Check removed. |  |  |  |  |
| 1715 | For each OffshorePlatform feature where verticalUncertainty or verticalDatum is Present. | Prohibited attributes verticalUncertainty or verticalDatum populated for a OffshorePlatform feature. | Remove verticalUncertainty or verticalDatum. | DCEG (14.2.1) | E |
| 1716 | For each OffshoreProductionArea feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for a OffshoreProductionArea feature. | Remove verticalUncertainty | DCEG (14.7) | E |
| 1717 | For each FishingFacility feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for FishingFacility feature. | Remove verticalUncertainty | DCEG (13.9) | E |
| 1718 | For each MarineFarmCulture feature where verticalDatum is Present. | Prohibited attribute verticalDatum populated for a MarineFarmCulture feature. | Remove verticalDatum. | DCEG (13.10) | E |
| 1719 | For each MarineFarmCulture feature where the attribute values do not correspond to the table below. For each specific case, when qualityOfSounding (attribute of type List) is encoded, it should contain one or more values selected from the list of allowed values given in the table. In addition, other attributes which do not appear in the table may be encoded. | Illogical attribute combination for MarineFarmCulture. | Amend attribute values to reflect a logical scenario. | DCEG (13.10) | W |
|  | waterLevelEffect | valueOfSounding | qualityOfSounding |  |
|  | 1, 2, 5 OR 7 | Undefined | Undefined |  |
|  | 4 | < 0 | 1, 3, 4, 6, 7, 8, 9 OR undefined |  |
|  |  | Undefined OR unknown | 2 OR undefined |  |
|  | 5 | 0 | 1, 3, 4, 6, 8, 9 OR undefined |  |
|  |  | Undefined OR unknown | 2 OR undefined |  |
|  | 3 | > 0 | 1, 3, 4, 6, 7, 8, 9 OR undefined |  |
|  |  | Unknown | 2 OR undefined |  |
|  | Unknown | Unknown | 2 OR undefined |  |
| 1720 | For each IceArea feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for IceArea feature. | Remove verticalUncertainty or verticalDatum. | DCEG (5.12) | E |
| 1721 | For each RadarReflector feature which is associated with a navigational aid (BCNXXX, BOYXXX, LightFloat, LightVessel feature features). | RadarReflector encoded on a navigational aid. | Remove RadarReflector and set the value of RadarConspicuous to 3 (radar conspicuous has radar reflector) for the navigational aid feature. | DCEG (19.17) | E |
| 1722a | For each navigational aid equipment feature which is not a slave to a navigational aid structure feature OR another navigational aid equipment feature. NOTE: Crane, FloatingDock, FortifiedStructure, FishingFacility, Hulk, Obstruction, Pontoon, PylonBridgeSupport, SiloTank and Wrecks feature features must be considered as possible structure features, in addition to the list given in Annex A (12.1.1). | Equipment feature which is not a slave of a structure or another equipment feature. | Amend equipment feature to slave. | DCEG | W |
| 1722b | For each Daymark feature that EQUALS another structure feature AND is not marked as an equipment feature NOTE: Crane, FloatingDock, FortifiedStructure, FishingFacility, Hulk, Obstruction, Pontoon, PylonBridgeSupport, SiloTank and Wrecks feature features must be considered as possible structure features, in addition to the list given in Annex A (12.1.1). | Daymark marked as structure feature where another exists. | Amend Daymark to slave. | DCEG | W |
| 1723 | For each feature of geometric primitive point forming the same navigational aid which does not reference the same spatial feature. | Object forming a navigational aid does not point to the same spatial feature. | Ensure all components point to the same spatial feature. | DCEG | C |
| 1724 | For each navigational aid equipment feature where FeatureName is Equal to the FeatureName of the master feature. | FeatureName on navigational aid equipment feature repeats that of the master feature. | Remove repeated FeatureName value. | DCEG | W |
| 1725 | For each master to slave relationship where all component feature features (master and slaves) are of the classes Daymark, FogSignal, LIGHTS, RadarStation, RadioStation, Retroreflector, RadarTransponderBeacon, SignalStationTraffic, SignalStationWarning and/or TOPMAR AND where at least one feature Daymark or LIGHTS is in the list AND where a Daymark or a LIGHTS feature is not the master feature. | Equipment feature does not have coincident Daymark or LIGHTS feature as a master. | Amend relationship so that the equipment feature is slave to the LIGHTS or Daymark feature. | DCEG | W |
| 1726 | If the DataCoverage meta feature where CATCOV is Equal to 1 AND is Not equal to the combined coverage of NavigationalSystemOfMarks meta features where marksNavigationalSystemOf is notNull. | Data coverage not completely covered by NavigationalSystemOfMarks features with a value for marksNavigationalSystemOf. | Ensure complete coverage of NavigationalSystemOfMarks features with marksNavigationalSystemOf populated. | DCEG (3.3) | C |
| 1727 | For each NavigationalSystemOfMarks meta feature where marksNavigationalSystemOf is notNull which OVERLAPS another meta NavigationalSystemOfMarks feature where marksNavigationalSystemOf is notNull. | NavigationalSystemOfMarks features with marksNavigationalSystemOf values overlap. | Amend limits of NavigationalSystemOfMarks features to remove overlap. | DCEG (3.3) | C |
| 1728 | For each NavigationalSystemOfMarks meta feature where orientation is notNull which OVERLAPS another meta NavigationalSystemOfMarks feature where orientation is notNull. | NavigationalSystemOfMarks features with orientation values overlap. | Amend limits of NavigationalSystemOfMarks features to remove overlap. | DCEG (3.3) | E |
| 1729 | For each feature forming part of a BCNXX or BOYXX feature AND marksNavigationalSystemOf is Not equal to 9 (no system) OR 10 (other system) where the attributes for structure, topmark and lights do not conform to the value of marksNavigationalSystemOf of the feature or the NavigationalSystemOfMarks meta feature it is WITHIN. | Component of an aid to navigation does not conform to the IALA system defined by the marksNavigationalSystemOf attribute of the underlying NavigationalSystemOfMarks feature. | Ensure attributes conform to the IALA system encoded in marksNavigationalSystemOf. | DCEG (17) | E |
| 1730 | For each BeaconCardinal feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a BeaconCardinal feature. | Remove verticalUncertainty or verticalDatum. | DCEG (17) | E |
| 1731 | For each BeaconIsolatedDanger feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a BeaconIsolatedDanger feature. | Remove verticalUncertainty or verticalDatum. | DCEG (17) | E |
| 1732 | For each BeaconLateral feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a BeaconLateral feature. | Remove verticalUncertainty or verticalDatum. | DCEG (17) | E |
| 1733 | For each BeaconSafeWater feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a BeaconSafeWater feature. | Remove verticalUncertainty or verticalDatum. | DCEG (17) | E |
| 1734 | For each BeaconSpecialPurpose feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a BeaconSpecialPurpose feature. | Remove verticalUncertainty or verticalDatum. | DCEG (17) | E |
| 1735 | For each BCNXXX or BOYXXX feature where marksNavigationalSystemOf is Present AND is Equal to the value of marksNavigationalSystemOf on the NavigationalSystemOfMarks meta feature it is WITHIN. | Value of marksNavigationalSystemOf on BCNXXX or BOYXXX feature is the same as the value on NavigationalSystemOfMarks feature. | Remove marksNavigationalSystemOf from BCNXXX or BOYXXX. | DCEG (17) | E |
| 1736 | For each Daymark feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for Daymark feature. | Remove verticalUncertainty or verticalDatum. | DCEG (17) | E |
| 1737 | For each BuoyCardinal feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for a BuoyCardinal feature. | Remove verticalUncertainty. | DCEG (17) | E |
| 1738 | For each BuoyInstallation feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for a BuoyInstallation feature. | Remove verticalUncertainty. | DCEG (17) | E |
| 1739 | For each BuoyIsolatedDanger feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for a BuoyIsolatedDanger feature. | Remove verticalUncertainty. | DCEG (17) | E |
| 1740 | For each BuoyLateral feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for a BuoyLateral feature. | Remove verticalUncertainty. | DCEG (17) | E |
| 1741 | For each BuoySpecialPurpose feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for a BuoySpecialPurpose feature. | Remove verticalUncertainty. | DCEG (17) | E |
| 1742 | For each BuoySafeWater feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for a BuoySafeWater feature. | Remove verticalUncertainty. | DCEG (17) | E |
| 1743 | Check removed. |  |  |  |  |
| 1744 | For each LightVessel feature where horizontalDistanceUncertainty OR verticalUncertainty is Present. | Prohibited attribute horizontalDistanceUncertainty or verticalUncertainty populated for LightVessel feature. | Remove horizontalDistanceUncertainty or verticalUncertainty. | DCEG (17) | E |
| 1745 | For each LightFloat feature where horizontalDistanceUncertainty or verticalUncertainty are Present. | Prohibited attribute horizontalDistanceUncertainty or verticalUncertainty populated for LightFloat feature. | Remove horizontalDistanceUncertainty or verticalUncertainty. | DCEG (17) | E |
| 1746 | For each TOPMAR feature where verticalUncertainty, verticalDatum, verticalLength, height or marksNavigationalSystemOf is Present. | Prohibited attribute verticalUncertainty, verticalDatum, verticalLength, height or marksNavigationalSystemOf populated for TOPMAR feature. | Remove verticalUncertainty, verticalDatum, verticalLength, height or marksNavigationalSystemOf. | DCEG (17) | E |
| 1747 | For each Retroreflector feature where marksNavigationalSystemOf, verticalUncertainty or verticalDatum is Present. | Prohibited attribute marksNavigationalSystemOf, verticalUncertainty or verticalDatum populated for Retroreflector feature. | Remove marksNavigationalSystemOf, verticalUncertainty or verticalDatum. | DCEG (17) | E |
| 1748 | Check removed. |  |  |  |  |
| 1749 | For each LIGHTS feature where verticalUncertainty is Present. | Prohibited attribute verticalUncertainty populated for a LIGHTS feature. | Remove verticalUncertainty. | DCEG (17) | E |
| 1750 | For each LIGHTS feature which is a slave to a BOYXXX feature AND height is Present. | height populated for a LIGHTS feature which is slave to a BOYXXX feature. | Remove height. | DCEG (17) | E |
| 1751 | For each LIGHTS feature where orientation is Present AND categoryOfLight is Not equal to 1 (directional function) OR 16 (moiré effect). | orientation populated without categoryOfLight = 1 or 16. | Populate appropriate value of categoryOfLight or remove orientation. | DCEG (17) | E |
| 1752 | For each LIGHTS feature where lightCharacteristic is Equal to 1 (fixed) AND signalGroup, signalPeriod or signalSequence is Present. | signalGroup, signalPeriod or signalSequence populated for LIGHTS feature where lightCharacteristic = 1. | Remove signalGroup, signalPeriod or SEGSEQ, not applicable to fixed lights. | DCEG (17) | E |
| 1753 | Check removed. |  |  |  |  |
| 1754 | For each LIGHTS feature where verticalDatum is notNull AND is Equal to the value of verticalDatum on the VerticalDatumOfData meta feature it is WITHIN. | LIGHTS feature with verticalDatum which is identical to that on the underlying VerticalDatumOfData feature. | Remove unnecessary value of verticalDatum from the LIGHTS feature. | DCEG (17) | E |
| 1755 | For each LIGHTS feature where verticalDatum is notNull AND is Equal to the value of verticalDatum in the VDAT subfield of the DPSM field. | LIGHTS feature with verticalDatum which is identical to that in the VDAT subfield of the DPSM field. | Remove unnecessary value of verticalDatum. | DCEG (17) | E |
| 1756 | For each LIGHTS feature where categoryOfLight is Equal to 4 (leading light) AND categoryOfLight is Not equal to 1 (directional function) AND orientation is Present. | orientation present for non-directional leading light LIGHTS feature. | Remove value of orientation. | DCEG (17) | E |
| 1757 | For each LIGHTS feature where categoryOfLight is Equal to 19 (horizontally disposed) OR 20 (vertically disposed) AND multiplicityOfFeatures does not contain a value Greater than 1. | LIGHTS feature where categoryOfLight = 19 or 20 without a value of multiplicityOfFeatures. | Populate the value of multiplicityOfFeatures. | DCEG (17) | E |
| 1758 | For each LIGHTS feature where categoryOfLight is Equal to 17 (emergency) AND is not COINCIDENT with another LIGHTS feature. | LIGHTS feature isolated and with categoryOfLight = 17 (emergency). | Encode primary LIGHTS feature. | DCEG (17) | E |
| 1759 | For each RadioStation feature where orientation is notNull AND categoryOfRadioStation is Not equal to 2 (directional radiobeacon). | RadioStation with orientation without categoryOfRadioStation = 2. | Set the value of categoryOfRadioStation to 2 (directional radiobeacon). | DCEG (17) | E |
| 1760 | For each RadarStation feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a RadarStation feature. | Remove verticalUncertainty or verticalDatum. | DCEG (17) | E |
| 1761 | For each RadarReflector feature where verticalUncertainty or verticalDatum is Present. | Prohibited attribute verticalUncertainty or verticalDatum populated for a RadarReflector feature. | Remove verticalUncertainty or verticalDatum. | DCEG (17) | E |
| 1762 | For each RadarReflector feature which TOUCHES an feature of geometric primitive surface or point having RadarConspicuous as an allowable attribute. | Unnecessary RadarReflector encoded. | Remove RadarReflector and set the value of RadarConspicuous to 3 (radar conspicuous has radar reflector) on the associated feature. | DCEG (17) | E |
| 1763 | Check removed. |  |  |  |  |
| 1764 | For each feature where status is Equal to 1 (permanent) AND periodStart or periodEnd is Present. | periodStart or periodEnd is populated for an feature with status = 1. | Remove periodStart/periodEnd if value of status is valid. | DCEG | E |
| 1765a | If the cell contains both QualityOfBathymetricSurvey and QualityOfNonBathymetricData meta features AND their combined coverage is Not equal to the DataCoverage features where CATCOV is Equal to 1 (coverage available). | QualityOfBathymetricSurvey or QualityOfNonBathymetricData do not provide full coverage. | Amend features to provide full coverage. | DCEG | W |
| 1765b | If meta features QualityOfBathymetricSurvey and QualityOfNonBathymetricData OVERLAP. | QualityOfBathymetricSurvey and QualityOfNonBathymetricData features overlap. | Amend features to remove overlap. | DCEG | W |
| 1766 | For each PictoralRepresentation, TextualDescription and NTXTDS attribute that contains more than one file name. | PictoralRepresentation, TextualDescription or NTXTDS contains more than one file name. | Amend value to only contain a single file name. | DCEG | E |
| 1767 | For each edge which is COINCIDENT with a SeabedArea feature of geometric primitive surface where waterLevelEffect is Equal to 4 (covers and uncovers) AND is COINCIDENT with a DepthArea or DredgedArea feature of geometric primitive surface where depthRangeMaximumValue is Less than or equal to 0 AND is COINCIDENT with a DepthArea or DredgedArea feature of geometric primitive surface where depthRangeMinimumValue is Greater than or equal to 0 OR an UnsurveyedArea feature AND is not COINCIDENT with a Dam, Gate, ShorelineConstruction or LandArea feature AND is not COINCIDENT with a DepthContour feature where valueOfDepthContour is Equal to 0. | Missing zero metre DepthContour. | Capture an appropriate zero metre DepthContour. | DCEG (11.6) | W |
| 1768 | For each Sounding feature where the depth value is Less than or equal to the depthRangeMinimumValue of the DepthArea or DredgedArea it lies WITHIN AND depthRangeMinimumValue of that feature is notNull. | Sounding feature with depth less than or equal to the depthRangeMinimumValue value of the underlying DepthArea. | Amend depthRangeMinimumValue value of depth features accordingly. | DCEG (11.3) | E |
| 1769 | For each Sounding feature where expositionOfSounding is Not equal to 3 (deeper than the range of the depth of the surrounding depth surface) AND the depth value is Greater than the depthRangeMaximumValue of the underlying DepthArea feature AND depthRangeMaximumValue is notNull. | Sounding feature deeper than the depthRangeMaximumValue value of the underlying DepthArea without expositionOfSounding = 3. | Populate appropriate value of expositionOfSounding. | DCEG (11.3) | E |
| 1770a | For each Sounding feature where expositionOfSounding is Equal to 3(deeper than the range of depth of the surrounding depth surface) AND the depth value is Less than or equal to depthRangeMaximumValue of the DepthArea it is WITHIN AND depthRangeMaximumValue is notNull. | Sounding feature with expositionOfSounding = 3 and a depth value less than or equal to the depthRangeMaximumValue of the underlying DepthArea. | Amend value of expositionOfSounding to a logical value. | DCEG (11.3) | W |
| 1770b | For each Sounding feature where expositionOfSounding is Equal to 3 (deeper than the range of depth of the surrounding depth surface) AND the depth value is Less than or equal to the depthRangeMaximumValue of the DredgedArea it is WITHIN where depthRangeMinimumValue AND depthRangeMaximumValue are notNull. | Sounding feature with expositionOfSounding = 3 and a depth value less than the depthRangeMaximumValue of the underlying DredgedArea. | Amend value of expositionOfSounding to a logical value. | DCEG (11.3) | W |
| 1770c | For each Sounding feature where expositionOfSounding is Equal to 3 (deeper than the range of depth of the surrounding depth surface) where the depth value is Less than or equal to the depthRangeMinimumValue of the DredgedArea feature it is WITHIN where depthRangeMaximumValue is not Present. | Sounding with expositionOfSounding= 3 and a depth value less than the depthRangeMinimumValue of the underlying DredgedArea when only depthRangeMinimumValue is populated. | Amend value of expositionOfSounding to a logical value. | DCEG (11.3) | W |
| 1771 | For each edge which is COINCIDENT with a DepthContour feature AND DepthArea feature features AND valueOfDepthContour is Less than the minimum depthRangeMinimumValue OR Greater than the maximum depthRangeMaximumValue. | Illogical value of valueOfDepthContour of a DepthContour between two DepthArea features. | Amend valueOfDepthContour to a logical value. | DCEG (11.6) | E |
| 1772a | For each UnderwaterAwashRock feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 1 (within the range of depth of the surrounding depth surface) OR not Present AND valueOfSounding is Less than or equal to depthRangeMinimumValue OR Greater than depthRangeMaximumValue of the DepthArea feature it is WITHIN.. | valueOfSounding for UnderwaterAwashRock feature with expositionOfSounding =1 or not present is outside the range of the underlying DepthArea. | Populate appropriate value of expositionOfSounding. | DCEG (13.4) | E |
| 1772b | For each UnderwaterAwashRock feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 1 (within the range of depth of the surrounding depth surface) OR not Present AND valueOfSounding is Less than or equal to depthRangeMinimumValue OR Greater than depthRangeMaximumValue of the DredgedArea feature it is WITHIN AND depthRangeMaximumValue is notNull AND Not equal to depthRangeMinimumValue. | valueOfSounding for UnderwaterAwashRock feature with expositionOfSounding = 1 or not present is outside of the range of the underlying DredgedArea. | Populate an appropriate value of expositionOfSounding. | DCEG (13.4) | E |
| 1773 | For each UnderwaterAwashRock feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 2 (shoaler than the range of depth of the surrounding depth surface) AND valueOfSounding is Greater than the value of depthRangeMinimumValue of the DepthArea or DredgedArea feature it is WITHIN AND depthRangeMinimumValue is notNull. | UnderwaterAwashRock with expositionOfSounding = 2 and a valueOfSounding value deeper than the depthRangeMinimumValue of the underlying DepthArea or DredgedArea. | Amend expositionOfSounding to a logical value. | DCEG (13.4) | W |
| 1774a | For each UnderwaterAwashRock feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 3 AND the valueOfSounding is Less than or equal to depthRangeMaximumValue of the DepthArea it is WITHIN where depthRangeMaximumValue is not unknown. | UnderwaterAwashRock with expositionOfSounding = 3 and a valueOfSounding value less than or equal to the depthRangeMaximumValue value of the underlying DepthArea. | Amend value of expositionOfSounding to a logical value. | DCEG (13.4) | E |
| 1774b | For each UnderwaterAwashRock feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 3(deeper than the range of depth of the surrounding depth surface) AND valueOfSounding is Less than or equal to the depthRangeMaximumValue of the DredgedArea it is WITHIN where depthRangeMinimumValue AND depthRangeMaximumValue are notNull. | UnderwaterAwashRock with expositionOfSounding = 3 and a valueOfSounding less than depthRangeMaximumValue of the underlying DredgedArea. | Amend value of expositionOfSounding to a logical value. | DCEG (13.4) | E |
| 1774c | For each UnderwaterAwashRock feature where valueOfSounding is notNull AND expositionOfSounding is Equal to 3(deeper than the range of depth of the surrounding depth surface) AND valueOfSounding is Less than or equal to the depthRangeMinimumValue of the DredgedArea feature it is within where depthRangeMaximumValue is not Present. | UnderwaterAwashRock feature with expositionOfSounding= 3 and with a valueOfSounding value less than or equal to the depthRangeMinimumValue of the underlying DredgedArea when only depthRangeMinimumValue is populated. | Amend value of expositionOfSounding to a logical value. | DCEG (13.4) | E |
| 1775 | For each equipment feature (UOC 12.1.1) which is WITHIN a DepthArea, DredgedArea or UnsurveyedArea AND does not have a navigational aid structure as a master, the geometry of which does not Equal a BeaconSpecialPurpose, Hulk LandArea, Pile or PylonBridgeSupport feature of geometric primitive point OR does not TOUCH a CableOverhead, Conveyor, Coastline, Dam (with categoryOfDam Equal to 3 (flood barrage)), BRIDGE, FloatingDock, LandArea, MooringFacility, PipelineOverhead, Pontoon or ShorelineConstruction feature of geometric primitive curve OR does not TOUCH Conveyor or BRIDGE feature of geometric primitive curve. | Equipment feature within DepthArea, DredgedArea or UnsurveyedArea without an appropriate supporting structure feature or underlying feature. | Ensure equipment feature is encoded with an appropriate structure feature or underlying feature. | DCEG | C |
| 1776 | For each LIGHTS feature where the value of lightCharacteristic and signalGroup are not Null AND the combination of values is not as listed in the table below. | Values of lightCharacteristic and signalGroup are not consistent. | Amend values to be consistent. | DCEG (17) | W |
|  | lightCharacteristic | signalGroup |  |  |  |  |
|  | 6 | (1) |  |  |  |  |
|  | 7 | (1) |  |  |  |  |
|  | 9 | () |  |  |  |  |
|  | 10 | () |  |  |  |  |
|  | 11 | () |  |  |  |  |
|  | 28 | () |  |  |  |  |
| 1777 | For each collection feature which references feature features which do not exist in the cell. | Collection feature references features which do not exist within the cell. | Remove invalid references. | DCEG | E |
| 1778 | For each LIGHTS feature where categoryOfLight is Equal to 1 (directional function) AND the value of the angle between sectorLimitOne – sectorLimitTwo is Greater than 10. | LIGHTS feature with categoryOfLight = 1 with a sector arc greater than 10 degrees. | Amend sectorLimitOne or sectorLimitTwo values, or remove categoryOfLight = 1 (directional function). | DCEG (17) | E |
| 1779 | For each DepthArea feature where depthRangeMinimumValue is Equal to depthRangeMaximumValue. | depthRangeMinimumValue is equal to depthRangeMaximumValue of a DepthArea feature. | Amend depthRangeMinimumValue or depthRangeMaximumValue to logical values. | DCEG (11.7) logical consistency | C |
| 1780 | For each SeabedArea feature where natureOfSurface AND natureOfSurfaceQualifyingTerms are notNull AND the combination of values are not as listed in the table below; | Illogical combination of natureOfSurface and natureOfSurfaceQualifyingTerms. | Amend natureOfSurface and natureOfSurfaceQualifyingTerms to logical combinations. | Logical consistency | W |
|  | natureOfSurfaceQualifyingTerms | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 |  |
|  | natureOfSurface |  |  |  |  |  |  |  |  |  |  |  |
|  | 1 |  |  |  |  | x | x | x | x | x | x |  |
|  | 2 |  |  |  |  | x | x | x |  |  | x |  |
|  | 3 | x | x | x |  | x | x | x |  |  | x |  |
|  | 4 | x | x | x |  |  | x |  | x | x | x |  |
|  | 5 | x | x | x |  |  |  |  | x | x |  |  |
|  | 6 | x | x | x |  |  |  |  | x | x |  |  |
|  | 7 | x | x | x |  |  |  |  | x | x |  |  |
|  | 8 |  |  |  |  |  |  |  | x | x |  |  |
|  | 9 |  |  |  |  |  |  |  | x | x |  |  |
|  | 11 |  |  |  |  |  |  |  | x |  |  |  |
|  | 14 |  |  |  | x |  |  |  |  |  |  |  |
|  | 17 | x | x | x | x |  |  |  |  | x |  |  |
|  | 18 |  |  |  |  |  |  |  | x | x |  |  |
| 1781 | For each Building or Landmark feature which is part of a master to slave relationship AND references a LIGHTS feature as slave AND categoryOfLight is Not equal to 6 (air obstruction light) OR 8 (flood light) OR 9(strip light) AND function does not contain value 33 (light support). | Building or Landmark feature with a slave LIGHTS feature without function = 33. | Set value of function to 33 (light support). | DCEG (7.2 and 6.2) | W |
| 1782 | For each SweptArea feature which OVERLAPS another SweptArea feature. | SweptArea features overlap. | Amend features to remove overlap. | Logical consistency | E |
| 1783a | For each feature of geometric primitive surface where waterLevelEffect is Equal to 4 (covers and uncovers) AND OVERLAPS a DepthArea feature where depthRangeMinimumValue is Greater than or equal to 0. | Area feature with illogical waterLevelEffect value which is shoaler than the depthRangeMinimumValue value of the underlying DepthArea. | Populate appropriate value of waterLevelEffect. | Logical consistency | E |
| 1783b | For each feature of geometric primitive surface where waterLevelEffect is Equal to 5 (awash) AND OVERLAPS a DepthArea feature where depthRangeMinimumValue is Greater than 0. | Area feature with illogical value of waterLevelEffect which is shoaler than the depthRangeMinimumValue value of the DepthArea feature. | Populate appropriate value of waterLevelEffect. | Logical consistency | E |
| 1784 | For each spatial feature where the value of HORDAT, positionalUncertainty or qualityOfPosition is Null. | HORDAT, positionalUncertainty or qualityOfPosition populated with an unknown value. | Remove attribute or populate with a known value. | Logical consistency | W |
| 1785 | For each feature where condition is Equal to 4 (wingless) AND categoryOfLandmark is Not equal to 18 (windmill) OR 19 (windmotor) | Object other than windmill or windmotor with condition = 4. | Remove value of condition or use Landmark feature. | Logical consistency. | E |
| 1786 | For each feature of geometric primitive surface where waterLevelEffect is Equal to 2 (always dry) AND is not WITHIN a LandArea feature of geometric primitive surface. | Area feature with waterLevelEffect = 2 not covered by a LandArea feature. | Amend waterLevelEffect value or ensure feature is on land. | Logical consistency | E |
| 1787 | For NavigationLine and RecommendedTrack feature features which are COINCIDENT AND have values of orientation which are Not equal OR reciprocal. | orientation values for NavigationLine and RecommendedTrack features sharing an edge are not equal or reciprocal. | Ensure values of orientation agree or are reciprocal. | Logical consistency | E |
| 1788 | For each NavigationLine feature which is COINCIDENT with a RecommendedTrack feature AND is not part of the same C_AGGR collection feature. | NavigationLine and RecommendedTrack features share an edge but are not aggregated using C_AGGR. | Aggregate features using C_AGGR feature. | 10.1.2 | W |
| 1789 | For each DeepWaterRouteCentercurve, NavigationLine, RecommendedTrack and RecommendedRouteCentrecurve feature of geometric primitive curve where orientation is notNull AND traffic is Equal to 4 (two-way) AND the bearing of the curve is more than 5 degrees, Greater than OR Less than the value (or reciprocal value) of orientation. | DeepWaterRouteCentercurve, NavigationLine, RecommendedTrack or RecommendedRouteCentrecurve where the orientation of the geometry is not consistent with the value of orientation. | Populate an appropriate value of orientation consistent with the geometry of the feature. | Logical consistency | C |
| 1790a | For each LIGHTS feature where orientation is notNull AND sectorLimitOne OR sectorLimitTwo is notNull. | LIGHTS feature where orientation and sectorLimitOne or sectorLimitTwo is populated. | Remove values of sectorLimitOne and sectorLimitTwo or orientation. | DCEG (17) | E |
| 1790b | For each LIGHTS feature where orientation is notNull AND it is aggregated to a RecommendedTrack or NavigationLine in a C_AGGR collection feature. | LIGHTS feature where orientation is populated and is aggregated with a NavigationLine or RecommendedTrack within a C_AGGR collection feature. | Set orientation to Null | DCEG (17) | E |
| 1790c | For each LIGHTS feature where orientation is notNull AND the structure feature of this LIGHTS feature is aggregated to a RecommendedTrack or NavigationLine in a collection feature C_AGGR. | LIGHTS feature where orientation is populated and the master structure feature is aggregated with a NavigationLine or RecommendedTrack within a C_AGGR collection feature. | Set orientation to Null | DCEG (17) | E |
| 1791 | For each NavigationLine feature where categoryOfNavigationLine is Equal to 3(leading curve bearing a recommended track) which is not COINCIDENT with a RecommendedTrack where categoryOfRecommendedTrack is Equal to 1(based on a system of fixed marks). | NavigationLine with categoryOfNavigationLine =3 does not share the curvear geometry of a RecommendedTrack with categoryOfRecommendedTrack = 1. | Ensure NavigationLine with categoryOfNavigationLine = 3 has a coincident RecommendedTrack with categoryOfRecommendedTrack = 1. | Logical consistency | E |
| 1792 | If the cell OVERLAPS the 180° meridian. | Cell overlaps 180° meridian. | Amend cell limits accordingly. | 4.5.2 | C |
| 1793 | For each master/slave relationship which references more than one LIGHTS feature AND all of the LIGHTS feature features are encoded with lightVisibility is Equal to 6 (visibility deliberately restricted) OR 7(obscured). | Group of LIGHTS where all are lightVisibility = 6 or 7. | Confirm values of lightVisibility or encode primary light. | Logical consistency | E |
| 1794 | For each LIGHTS feature where categoryOfLight is equal to 1(directional function) AND is a slave in a master to slave relationship AND the master feature is any of BOYXXX, LightVessel or LightFloat. | Directional light a slave to BOYXXX, LightVessel or LightFloat master feature. | Amend master to a logical feature or remove value of categoryOfLight. | Logical consistency | E |
| 1795 | For each feature which is a master in a master to slave relationship AND where dateEnd, dateStart, periodEnd or periodStart attributes are notNull AND the values of dateEnd, dateStart, periodEnd or periodStart are not identical to those on the slave features. | Temporal attributes on a master feature do not match those on slave features. | Populate appropriate temporal attributes on slave features. | Logical consistency | C |
| 1796 | Check removed. |  |  |  |  |

| 1797 | For each of the feature class, geometry and attribute combinations in the table below; | Object, geometry and attribute combinations which do not display in ECDIS. | Delete features which do not display in ECDIS or use alternative encoding. | S-101 Feature Catalogue | E |
| --- | --- | --- | --- | --- | --- |
|  | Object | Geom | Attributes |  |  |
|  | BRIDGE | P | - |  |  |
|  | Dam | P | categoryOfDam ≠ 3 |  |  |
|  | Gridiron | P |  |  |  |
|  | PipelineSubmarineOnLand | P |  |  |  |
|  | ProductionStorageArea | P | CATPRA = not Present |  |  |
|  | Rapids | P |  |  |  |
|  | Roadway | P |  |  |  |
|  | Runway | P |  |  |  |
|  | SlopingGround | A | categoryOfSlope = 1,2,3,4,5,7 AND RadarConspicuous ≠ 1, OR categoryOfSlope = not Present |  |  |
|  | Tunnel | P |  |  |  |
|  | Vegetation | P,S | categoryOfVegetation = 1, 10, 11, 12 OR not Present |  |  |
|  | Waterfall | P |  |  |  |
| 1798 | For each value of Information OR NINFOM which contains Greater than 300 characters. | Information or NINFOM contains more than 300 characters. | Amend value of Information or NINFOM. Use TextualDescription or NTXTDS if appropriate. | DCEG | E |
| 1799 | For each BRIDGE feature where verticalClearanceClosed or verticalClearanceOpen are notNull AND categoryOfBridge is Not equal to 2 (opening bridge) OR 3 (swing bridge) OR 4 (lifting bridge) OR 5 (bascule bridge) OR 7 (draw bridge) OR 8 (transporter bridge). | BRIDGE feature has values of verticalClearanceClosed or verticalClearanceOpen without appropriate value of categoryOfBridge. | Ensure appropriate value of categoryOfBridge is populated. | Logical consistency | W |
| 1800 | For each BRIDGE feature where verticalClearance is notNull AND categoryOfBridge is Equal to 2 (opening bridge) OR 3 (swing bridge) OR 4 (lifting bridge) OR 5 (bascule bridge) OR 7 (draw bridge) OR 8 (transporter bridge). | verticalClearance populated without an appropriate value of categoryOfBridge. | Ensure appropriate value of categoryOfBridge is populated. | Logical consistency | W |
| 1801 | For each L (List) type attribute, (excluding colour, natureOfSurfaceQualifyingTerms and natureOfSurface) that contains more than one instance of the same value. | Value repeated for a list attribute where not permitted. | Remove duplicate value. | Logical consistency | W |
| 1802 | Check removed. |  |  |  |  |
| 1803 | For each Master to Slave relationship where referenced feature features have been populated with different values of scaleMinimum. | Objects which are in a master slave relationship with different values of scaleMinimum. | Amend values of scaleMinimum to agree. | Logical consistency | W |
| 1804 | For each Obstruction, UnderwaterAwashRock or Wrecks feature of geometric primitive point which is COINCIDENT with the geometry of a DepthArea, DredgedArea or UnsurveyedArea. | Point feature coincides with the edge between Skin of the Earth features. | Amend Skin of the Earthfeature geometry so that it is not coincident with the point feature. | DCEG (13) | C |
| 1805 | For each SmallCraftFacility feature of geometric primitive surface which overlaps a DepthArea, DredgedArea or UnsurveyedArea of geometric primitive surface. | Area SmallCraftFacility feature is within a water feature. | Amend feature to remove overlap with all water features. | DCEG (21.8) | W |
| 1806 | For each CautionArea feature of geometric primitive surface which is COINCIDENT with a DepthContour feature. | Area CautionArea feature shares geometry with DepthContour. | Edit the CautionArea limits clear of the DepthContour. | DCEG (16.10) | W |

| 2.5 Checks relating to allowable attribute values for particular feature classes |
| --- |
| No | Check description | Check message | Check solution | Conformity to: | Cat |
| 2000 | For each feature where an attribute of type "L" (list) or type "E" (enumerated) contains an attribute value that is not listed in the table below for the given feature class. - x-y-z allowable values (alone or in a list); * all the pre-defined attribute values as listed in S-101 3.1 Appendix A, Chapter 2 are allowed.; # the attribute is mandatory, and the missing value (Unknown) is allowed. (#) the attribute is mandatory, but the missing value (Unknown) is prohibited (no logical sense). | Attribute value which is not permitted on an feature. | Remove disallowed attribute value. | Logical consistency | E |
| Attribute |  | Code | Allowable attribute values |
| BCNSHP |  | 2 |  |
|  | BeaconCardinal | 5 | * # |
|  | BeaconIsolatedDanger | 6 | * # |
|  | BeaconLateral | 7 | * # |
|  | BeaconSafeWater | 8 | * # |
|  | BeaconSpecialPurpose | 9 | * # |
| BUISHP |  | 3 |  |
|  | Building | 12 | * |
|  | SiloTank | 125 | * |
| bouyShape |  | 4 |  |
|  | BuoyCardinal | 14 | * # |
|  | BuoyInstallation | 15 | * # |
|  | BuoyIsolatedDanger | 16 | * # |
|  | BuoyLateral | 17 | * # |
|  | BuoySafeWater | 18 | * # |
|  | BuoySpecialPurpose | 19 | * # |
|  | MooringFacility | 84 | * |
| CATAIR |  | 7 |  |
|  | AirportAirfield | 2 | * |

| categoryOfAnchorage |  | 8 |  |
| --- | --- | --- | --- |
|  | ACHBRT | 3 | * |
|  | AnchorageArea | 4 | * |
| categoryOfBridge |  | 9 |  |
|  | BRIDGE | 11 | * # |
| CATBUA |  | 10 |  |
|  | BuiltupArea | 13 | * |
| categoryOfCable |  | 11 |  |
|  | CableArea | 20 | 1-4-5 (see check 1707) |
|  | CableOverhead | 21 | 1-3-4-5 |
|  | CableSubmarine | 22 | 1-4-5-6 (see check 1703) |
| CATCAN |  | 12 |  |
|  | Canal | 23 | * |
| CATCAM |  | 13 |  |
|  | BeaconCardinal | 5 | * # |
|  | BuoyCardinal | 14 | * # |
| CATCHP |  | 14 |  |
|  | CHKPNT | 28 | * |
| categoryOfCoastline |  | 15 |  |
|  | Coastline | 30 | * |
| CATCTR |  | 16 |  |
|  | CTRPNT | 33 | * |
| CATCON |  | 17 |  |
|  | Conveyor | 34 | * |
| CATCOV |  | 18 |  |
|  | DataCoverage | 302 | * (#) |
| CATCRN |  | 19 |  |
|  | Crane | 35 | * |

| categoryOfDam |  | 20 |  |
| --- | --- | --- | --- |
|  | Dam | 38 | * |
| CATDIS |  | 21 |  |
|  | DISMAR | 44 | * |
| CATDOC |  | 22 |  |
|  | DockArea | 45 | * |
| CATDPG |  | 23 |  |
|  | DMPGRD | 48 | * |
| CATFNC |  | 24 |  |
|  | FenceWall | 52 | * |
| CATFRY |  | 25 |  |
|  | FerryRoute | 53 | * # |
| CATFIF |  | 26 |  |
|  | FishingFacility | 55 | * |
| CATFOG |  | 27 |  |
|  | FogSignal | 58 | * # |
| CATFOR |  | 28 |  |
|  | FortifiedStructure | 59 | * |
| CATGAT |  | 29 |  |
|  | Gate | 61 | * |
| CATHAF |  | 30 |  |
|  | HarbourFacility | 64 | * # |
| CATHLK |  | 31 |  |
|  | Hulk | 65 | * |
| categoryOfIce |  | 32 |  |
|  | IceArea | 66 | * # |
| CATINB |  | 33 |  |
|  | BuoyInstallation | 15 | * |

| categoryOfLandRegion |  | 34 |  |
| --- | --- | --- | --- |
|  | LandRegion | 73 | * # |
| categoryOfLandmark |  | 35 |  |
|  | Landmark | 74 | * # |
| CATLAM |  | 36 |  |
|  | BeaconLateral | 7 | * # |
|  | BuoyLateral | 17 | * # |
| categoryOfLight |  | 37 |  |
|  | LIGHTS | 75 | * # |
| CATMFA |  | 38 |  |
|  | MarineFarmCulture | 82 | * |
| CATMPA |  | 39 |  |
|  | MIPARE | 83 | * |
| categoryOfMooringWarpingFacility |  | 40 |  |
|  | MooringFacility | 84 | * # |
| categoryOfNavigationLine |  | 41 |  |
|  | NavigationLine | 85 | * # |
| categoryOfObstruction |  | 42 |  |
|  | Obstruction | 86 | * |
| CATOFP |  | 43 |  |
|  | OffshorePlatform | 87 | * |
| CATOLB |  | 44 |  |
|  | OILBAR | 89 | * |
| CATPLE |  | 45 |  |
|  | Pile | 90 | * |
| CATPIL |  | 46 |  |
|  | PILBOP | 91 | * |

| categoryOfPipelinePipe |  | 47 |  |
| --- | --- | --- | --- |
|  | SubmarinePipelineArea | 92 | * |
|  | PipelineOverhead | 93 | 2-3-4-6 |
|  | PipelineSubmarineOnLand | 94 | * |
| CATPRA |  | 48 |  |
|  | OffshoreProductionArea | 88 | 1-2-5-8-9 |
|  | ProductionStorageArea | 97 | * # |
| categoryOfPylon |  | 49 |  |
|  | PylonBridgeSupport | 98 | * # |
| CATRAS |  | 51 |  |
|  | RadarStation | 102 | * |
| CATRTB |  | 52 |  |
|  | RadarTransponderBeacon | 103 | * # |
| categoryOfRadioStation |  | 53 |  |
|  | RadioStation | 105 | * |
| categoryOfRecommendedTrack |  | 54 |  |
|  | DeepWaterRouteCentercurve | 40 | * # |
|  | RecommendedRouteCentrecurve | 108 | * # |
|  | RecommendedTrack | 109 | * # |
|  | TwowayRoutePart | 152 | * |
| CATRSC |  | 55 |  |
|  | RSCSTA | 111 | * |
| categoryOfRestriction |  | 56 |  |
|  | RestrictedArea | 112 | * # |
| CATROD |  | 57 |  |
|  | Roadway | 116 | 1-2-3-4-5-6 (replaces check 1621) |
| CATRUN |  | 58 |  |
|  | Runway | 117 | * |
| CATSEA |  | 59 |  |
|  | SeaArea | 119 | * # |

| categoryOfShorelineConstruction |  | 60 |  |
| --- | --- | --- | --- |
|  | ShorelineConstruction | 122 | * |
| CATSIT |  | 61 |  |
|  | SignalStationTraffic | 123 | * # |
| CATSIW |  | 62 |  |
|  | SignalStationWarning | 124 | * # |
| CATSIL |  | 63 |  |
|  | SiloTank | 125 | * |
| categoryOfSlope |  | 64 |  |
|  | SlopeTopline | 126 | * |
|  | SlopingGround | 127 | * |
| CATSCF |  | 65 |  |
|  | SmallCraftFacility | 128 | * # |
| CATSPM |  | 66 |  |
|  | BeaconSpecialPurpose | 9 | * # |
|  | BuoySpecialPurpose | 19 | * # |
|  | Daymark | 39 | * |
| CAT_TS |  | 188 |  |
|  | TS_FEB | 160 | * # |
| CATTSS |  | 67 |  |
|  | InshoreTrafficZone | 68 | * |
|  | TSELNE | 145 | * |
|  | TrafficSeparationSchemeBoundary | 146 | * |
|  | TrafficSeparationSchemeCrossing | 147 | * |
|  | TrafficSeparationSchemeLanePart | 148 | * |
|  | TrafficSeparationSchemeRoundabout | 149 | * |
|  | TrafficSeparationZone | 150 | * |
| categoryOfVegetation |  | 68 |  |
|  | Vegetation | 155 | * # |
| CATWAT |  | 69 |  |
|  | WATTUR | 156 | * # |

| CATWED |  | 70 |  |
| --- | --- | --- | --- |
|  | WEDKLP | 158 | * |
| categoryOfWreck |  | 71 |  |
|  | Wrecks | 159 | * # |
| CATZOC |  | 72 |  |
|  | QualityOfBathymetricSurvey | 308 | * (#) |
| colour |  | 75 |  |
|  | BeaconCardinal | 5 | * # |
|  | BeaconIsolatedDanger | 6 | * # |
|  | BeaconLateral | 7 | * # |
|  | BeaconSafeWater | 8 | * # |
|  | BeaconSpecialPurpose | 9 | * # |
|  | BRIDGE | 11 | * |
|  | Building | 12 | * |
|  | BuoyCardinal | 14 | * # |
|  | BuoyInstallation | 15 | * # |
|  | BuoyIsolatedDanger | 16 | * # |
|  | BuoyLateral | 17 | * # |
|  | BuoySafeWater | 18 | * # |
|  | BuoySpecialPurpose | 19 | * # |
|  | Coastline | 30 | * |
|  | Conveyor | 34 | * |
|  | Crane | 35 | * |
|  | Dam | 38 | * |
|  | Daymark | 39 | * # |
|  | FenceWall | 52 | * |
|  | FloatingDock | 57 | * |
|  | Hulk | 65 | * |
|  | Landmark | 74 | * |
|  | LIGHTS | 75 | 1-3-4-5-6-9-10-11 # |
|  | LightFloat | 76 | * # |
|  | LightVessel | 77 | * # |
|  | MooringFacility | 84 | * |
|  | NEWOBJ | 163 | * |
|  | OffshorePlatform | 87 | * |
|  | Pile | 90 | * |
|  | PylonBridgeSupport | 98 | * |
|  | Retroreflector | 113 | 1-3-4-5-6-7-8-9-10-11-12-13 |
|  | SeabedArea | 121 | * |
|  | ShorelineConstruction | 122 | * |
|  | SiloTank | 125 | * |
|  | SlopeTopline | 126 | * |
|  | SlopingGround | 127 | * |
|  | TOPMAR | 144 | * |
| colourPattern |  | 76 |  |
|  | BeaconCardinal | 5 | * # |
|  | BeaconIsolatedDanger | 6 | * # |
|  | BeaconLateral | 7 | * # |
|  | BeaconSafeWater | 8 | * # |
|  | BeaconSpecialPurpose | 9 | * # |
|  | BRIDGE | 11 | * # |
|  | Building | 12 | * # |
|  | BuoyCardinal | 14 | * # |
|  | BuoyInstallation | 15 | * # |
|  | BuoyIsolatedDanger | 16 | * # |
|  | BuoyLateral | 17 | * # |
|  | BuoySafeWater | 18 | * # |
|  | BuoySpecialPurpose | 19 | * # |
|  | Conveyor | 34 | * # |
|  | Crane | 35 | * # |
|  | Dam | 38 | * # |
|  | Daymark | 39 | * # |
|  | FenceWall | 52 | * # |
|  | FloatingDock | 57 | * # |
|  | Hulk | 65 | * # |
|  | Landmark | 74 | * # |
|  | LightFloat | 76 | * # |
|  | LightVessel | 77 | * # |
|  | MooringFacility | 84 | * # |
|  | NEWOBJ | 163 | * # |
|  | OffshorePlatform | 87 | * # |
|  | Pile | 90 | * # |
|  | PylonBridgeSupport | 98 | * # |
|  | Retroreflector | 113 | * # |
|  | ShorelineConstruction | 122 | * # |
|  | SiloTank | 125 | * # |
|  | TOPMAR | 144 | * # |
| condition |  | 81 |  |
|  | AirportAirfield | 2 | 1-2-3-5 |
|  | BeaconCardinal | 5 | 1-2-5 |
|  | BeaconIsolatedDanger | 6 | 1-2-5 |
|  | BeaconLateral | 7 | 1-2-5 |
|  | BeaconSafeWater | 8 | 1-2-5 |
|  | BeaconSpecialPurpose | 9 | 1-2-5 |
|  | BRIDGE | 11 | 1-2-5 |
|  | Building | 12 | 1-2-5 |
|  | BuiltupArea | 13 | 1-2-5 |
|  | CableOverhead | 21 | 1-5 (see check 1706) |
|  | CableSubmarine | 22 | 1-5 (see check 1706) |
|  | Canal | 23 | 1-2-3-5 |
|  | Causeway | 26 | 1-2-3-5 |
|  | Conveyor | 34 | 1-2-5 |
|  | Crane | 35 | 1-2-5 |
|  | Dam | 38 | 1-2-3-5 |
|  | DockArea | 45 | 1-2-3-5 |
|  | DryDock | 47 | 1-2-3-5 |
|  | Dyke | 49 | 1-2-3-5 |
|  | FenceWall | 52 | 1-2-5 |
|  | FloatingDock | 57 | 1-2-3-5 |
|  | FortifiedStructure | 59 | 1-2-5 |
|  | Gate | 61 | 1-2-5 |
|  | HarbourFacility | 64 | 1-2-3-5 |
|  | Hulk | 65 | 1-2-5 |
|  | LandArea | 71 | 1-3-5 |
|  | Landmark | 74 | 1-2-4-5 |
|  | MooringFacility | 84 | 1-2-5 |
|  | NEWOBJ | 163 | * |
|  | Obstruction | 86 | 1-2-5 |
|  | OffshorePlatform | 87 | 1-2-5 |
|  | OffshoreProductionArea | 88 | 1-2-3-5 |
|  | OILBAR | 89 | 1-2-5 |
|  | Pile | 90 | 1-2-5 |
|  | PipelineOverhead | 93 | 1-5 (see check 1706) |
|  | PipelineSubmarineOnLand | 94 | 1-5 (see check 1706) |
|  | Pontoon | 95 | 1-2-5 |
|  | ProductionStorageArea | 97 | 1-2-3-5 |
|  | PylonBridgeSupport | 98 | 1-2-5 |
|  | Railway | 106 | 1-3-5 |
|  | Roadway | 116 | 1-2-3-5 |
|  | Runway | 117 | 1-2-3-5 |
|  | ShorelineConstruction | 122 | 1-2-3-5 |
|  | SiloTank | 125 | 1-2-5 |
|  | Tunnel | 151 | 1-2-3-5 |
| RadarConspicuous |  | 82 |  |
|  | BeaconCardinal | 5 | * |
|  | BeaconIsolatedDanger | 6 | * |
|  | BeaconLateral | 7 | * |
|  | BeaconSafeWater | 8 | * |
|  | BeaconSpecialPurpose | 9 | * |
|  | BRIDGE | 11 | * |
|  | Building | 12 | * |
|  | BuiltupArea | 13 | * |
|  | BuoyCardinal | 14 | * |
|  | BuoyInstallation | 15 | * |
|  | BuoyIsolatedDanger | 16 | * |
|  | BuoyLateral | 17 | * |
|  | BuoySafeWater | 18 | * |
|  | BuoySpecialPurpose | 19 | * |
|  | CableOverhead | 21 | * |
|  | Coastline | 30 | * |
|  | Conveyor | 34 | * |
|  | Crane | 35 | * |
|  | Dam | 38 | * |
|  | Dyke | 49 | * |
|  | FenceWall | 52 | * |
|  | FloatingDock | 57 | * |
|  | FortifiedStructure | 59 | * |
|  | Hulk | 65 | * |
|  | Landmark | 74 | * |
|  | LightFloat | 76 | * |
|  | LightVessel | 77 | * |
|  | MooringFacility | 84 | * |
|  | NEWOBJ | 163 | * |
|  | OffshorePlatform | 87 | * |
|  | OffshoreProductionArea | 88 | * |
|  | PipelineOverhead | 93 | * |
|  | Pontoon | 95 | * |
|  | ProductionStorageArea | 97 | * |
|  | PylonBridgeSupport | 98 | * |
|  | ShorelineConstruction | 122 | * |
|  | SiloTank | 125 | * |
|  | SlopeTopline | 126 | * |
|  | SlopingGround | 127 | * |
|  | Wrecks | 159 | * |

| VisuallyConspicuous |  | 83 |  |
| --- | --- | --- | --- |
|  | BeaconCardinal | 5 | * |
|  | BeaconIsolatedDanger | 6 | * |
|  | BeaconLateral | 7 | * |
|  | BeaconSafeWater | 8 | * |
|  | BeaconSpecialPurpose | 9 | * |
|  | BRIDGE | 11 | * |
|  | Building | 12 | * |
|  | BuiltupArea | 13 | * |
|  | CableOverhead | 21 | * |
|  | Coastline | 30 | * |
|  | Conveyor | 34 | * |
|  | Crane | 35 | * |
|  | Dam | 38 | * |
|  | FenceWall | 52 | * |
|  | FloatingDock | 57 | * |
|  | FortifiedStructure | 59 | * |
|  | Hulk | 65 | * |
|  | IceArea | 66 | * |
|  | LandElevation | 72 | * |
|  | Landmark | 74 | * # |
|  | LightFloat | 76 | * |
|  | LightVessel | 77 | * |
|  | MooringFacility | 84 | * |
|  | NEWOBJ | 163 | * |
|  | OffshorePlatform | 87 | * |
|  | OffshoreProductionArea | 88 | * |
|  | Pile | 90 | * |
|  | PipelineOverhead | 93 | * |
|  | Pontoon | 95 | * |
|  | ProductionStorageArea | 97 | * |
|  | PylonBridgeSupport | 98 | * |
|  | ShorelineConstruction | 122 | * |
|  | SiloTank | 125 | * |
|  | SlopeTopline | 126 | * |
|  | SlopingGround | 127 | * |
|  | Vegetation | 155 | * |
|  | Waterfall | 157 | * |
|  | Wrecks | 159 | * |

| exhibitionConditionOfLight |  | 92 |  |
| --- | --- | --- | --- |
|  | LIGHTS | 75 | * |
| expositionOfSounding |  | 93 |  |
|  | MarineFarmCulture | 82 | * |
|  | Obstruction | 86 | * |
|  | Sounding | 129 | * |
|  | UnderwaterAwashRock | 153 | * |
|  | Wrecks | 159 | * |
| function |  | 94 |  |
|  | Building | 12 | * |
|  | Landmark | 74 | * |
| JRSDTN |  | 103 |  |
|  | ADMARE | 1 | * # |
| lightCharacteristic |  | 107 |  |
|  | LIGHTS | 75 | * # |
| lightVisibility |  | 108 |  |
|  | LIGHTS | 75 | * |
| marksNavigationalSystemOf |  | 109 |  |
|  | BeaconCardinal | 5 | * |
|  | BeaconIsolatedDanger | 6 | * |
|  | BeaconLateral | 7 | * |
|  | BeaconSafeWater | 8 | * |
|  | BeaconSpecialPurpose | 9 | * |
|  | BuoyCardinal | 14 | * |
|  | BuoyInstallation | 15 | * |
|  | BuoyIsolatedDanger | 16 | * |
|  | BuoyLateral | 17 | * |
|  | BuoySafeWater | 18 | * |
|  | BuoySpecialPurpose | 19 | * |
|  | LIGHTS | 75 | * |
|  | NavigationalSystemOfMarks | 306 | * # |
| natureOfConstruction |  | 112 |  |
|  | BeaconCardinal | 5 | 1-2-6-7-8-9 |
|  | BeaconIsolatedDanger | 6 | 1-2-6-7-8-9 |
|  | BeaconLateral | 7 | 1-2-6-7-8-9 |
|  | BeaconSafeWater | 8 | 1-2-6-7-8-9 |
|  | BeaconSpecialPurpose | 9 | 1-2-6-7-8-9 |
|  | BRIDGE | 11 | 1-2-4-5-6-7-8-9 |
|  | Building | 12 | 1-2-6-7-8-9 |
|  | BuoyCardinal | 14 | 6-7-8-9 |
|  | BuoyInstallation | 15 | 6-7-8-9 |
|  | BuoyIsolatedDanger | 16 | 6-7-8-9 |
|  | BuoyLateral | 17 | 6-7-8-9 |
|  | BuoySafeWater | 18 | 6-7-8-9 |
|  | BuoySpecialPurpose | 19 | 6-7-8-9 |
|  | Causeway | 26 | 1-2-3-4-5-6-7 |
|  | Dam | 38 | 1-2-3-4-5-6-7-9 |
|  | Daymark | 39 | 1-2-4-6-7-8-9 |
|  | Dyke | 49 | 1-2-3-4-5-6-7-9 |
|  | FenceWall | 52 | 1-2-3-6-7-9 |
|  | FortifiedStructure | 59 | 1-2-3-6-7-9 |
|  | Gate | 61 | 1-2-6-7-9 |
|  | Gridiron | 62 | 1-2-6-7-9 |
|  | HarbourFacility | 64 | 1-2-3-6-7-9 |
|  | Landmark | 74 | 1-2-3-6-7-8-9 |
|  | LightFloat | 76 | 6-7-9 |
|  | LightVessel | 77 | 6-7-9 |
|  | MooringFacility | 84 | 1-2-6-7-9 |
|  | Obstruction | 86 | 1-2-3-6-7-9 |
|  | OffshorePlatform | 87 | 1-2-6-7-9 |
|  | Pontoon | 95 | 1-2-6-7-9 |
|  | PylonBridgeSupport | 98 | 1-2-6-7-9 |
|  | Roadway | 116 | 1-2-4-5-6-9 |
|  | Runway | 117 | 1-2-4-5-6-7-9 |
|  | ShorelineConstruction | 122 | * |
|  | SiloTank | 125 | 1-2-6-7-8-9 |
| natureOfSurface |  | 113 |  |
|  | LandRegion | 73 | * |
|  | Obstruction | 86 | * |
|  | SeabedArea | 121 | * # |
|  | SlopeTopline | 126 | * |
|  | SlopingGround | 127 | * |
|  | UnderwaterAwashRock | 153 | 9-14-18 |
| natureOfSurfaceQualifyingTerms |  | 114 |  |
|  | LandRegion | 73 | * |
|  | Obstruction | 86 | * |
|  | SeabedArea | 121 | * # |
|  | UnderwaterAwashRock | 153 | 4-8-9-10 |
| product |  | 123 |  |
|  | BuoyInstallation | 15 | 1-2-18-19 |
|  | Conveyor | 34 | 4-5-6-7-10-11-12-13-14-15-16-17-21-22 |
|  | Obstruction | 86 | 1-2-3-8 |
|  | OffshorePlatform | 87 | 1-2 |
|  | OffshoreProductionArea | 88 | 1-2-4-6-10-14 |
|  | SubmarinePipelineArea | 92 | 1-2-3-7-8-18-19-20 |
|  | PipelineOverhead | 93 | 1-2-3-7-8-9-18-19-20-22 |
|  | PipelineSubmarineOnLand | 94 | 1-2-3-7-8-9-18-19-20-22 |
|  | ProductionStorageArea | 97 | * |
|  | SiloTank | 125 | 1-2-3-7-8-9-14-18-19-20-21-22 |
| qualityOfSounding |  | 125 |  |
|  | Berths | 10 | 1-2-3-4 |
|  | DeepWaterRouteCentercurve | 40 | 1-2-3-4 |
|  | DeepWaterRoutePart | 41 | 1-2-3-4 |
|  | DepthArea | 42 | 1-2-3-4 |
|  | DredgedArea | 46 | 10-11 (replaces check 1648) |
|  | DryDock | 47 | 2-3-4-6-7-8-9 |
|  | Fairway | 51 | 1-2-3-4 |
|  | Gate | 61 | 2-3-4-6-7 |
|  | MarineFarmCulture | 82 | 1-2-3-4-6-7-8-9 |
|  | Obstruction | 86 | 1-2-3-4-6-7-8-9 |
|  | RecommendedRouteCentrecurve | 108 | 1-2-3-4 |
|  | RecommendedTrack | 109 | 1-2-3-4-6 |
|  | Sounding | 129 | 1-3-4-5-8-9-10-11 |
|  | SweptArea | 134 | 1-3-4-5-8-9-10-11 |
|  | TwowayRoutePart | 152 | 1-2-3-4 |
|  | UnderwaterAwashRock | 153 | 1-2-3-4-6-7-8-9 |
|  | Wrecks | 159 | 1-2-3-4-6-7-8-9 |
|  | QualityOfSurvey | 310 | 1-2-3-4-5-6-7-8-9-10-11 |
| restriction |  | 131 |  |
|  | AnchorageArea | 4 | 2-3-4-5-6-8-9-10-11-12-13-15-16-17-18-19-20-21-23-24-27 |
|  | CableArea | 20 | 1-2-3-4-5-6-7-8-9-10-11-12-13-16-17-18-19-20-21-22-23-24-25-27 |
|  | DeepWaterRoutePart | 41 | 1-2-3-4-5-6-8-9-10-11-12-13-16-17-18-19-20-21-22-23-24-25-27 |
|  | DredgedArea | 46 | 1-2-3-4-5-6-7-8-11-12-13-16-17-18-19-20-21-22-23-25-27 |
|  | DMPGRD | 48 | 1-2-3-4-5-6-7-8-9-10-11-12-13-16-17-18-19-20-21-22-23-24-25-27 |
|  | Fairway | 51 | 1-2-3-4-5-6-8-9-10-11-12-13-15-16-17-18-19-20-21-22-23-24-25-27 |
|  | ICNARE | 67 | 1-2-3-4-5-6-7-8-9-10-11-12-13-16-17-18-19-20-21-22-23-24-25-27 |
|  | InshoreTrafficZone | 68 | 1-2-3-4-5-6-8-9-10-11-12-13-18-19-20-21-22-23-24-25-27 |
|  | MarineFarmCulture | 82 | 1-2-3-4-5-6-8-9-10-11-12-13-15-16-17-18-19-20-21-22-23-24-25-27 |
|  | MIPARE | 83 | 1-2-3-4-5-6-8-9-10-11-12-13-15-16-17-18-19-20-21-22-23-24-25-27 |
|  | NEWOBJ | 163 | * |
|  | OffshoreProductionArea | 88 | 1-2-3-4-5-6-7-8-9-10-11-12-13-15-16-17-18-19-20-21-22-23-24-25-27 |
|  | SubmarinePipelineArea | 92 | 1-2-3-4-5-6-7-8-9-10-11-12-13-15-16-17-18-19-20-21-22-23-24-25-27 |
|  | PRCARE | 96 | 1-2-3-4-5-6-8-9-10-11-12-13-16-17-18-19-20-21-22-23-24-25-27 |
|  | RestrictedArea | 112 | *# |
|  | SPLARE | 120 | 1-2-3-4-5-6-7-8-9-10-11-12-13-15-16-17-18-19-20-21-22-23-24-25-27 |
|  | SUBTLN | 133 | 1-2-3-4-5-6-7-8-9-10-11-12-13-16-17-18-19-20-21-22-23-24-25-27 |
|  | TerritorialSeaArea | 135 | 1-2-3-4-5-6-7-8-9-10-11-12-13-16-17-18-19-20-21-22-23-24-25-26-27 |
|  | TrafficSeparationSchemeCrossing | 147 | 1-2-3-4-5-6-8-9-10-11-12-13-16-17-18-19-20-21-22-23-24-25-27 |
|  | TrafficSeparationSchemeLanePart | 148 | 1-2-3-4-5-6-8-9-10-11-12-13-16-17-18-19-20-21-22-23-24-25-27 |
|  | TrafficSeparationSchemeRoundabout | 149 | 1-2-3-4-5-6-8-9-10-11-12-13-16-17-18-19-20-21-22-23-24-25-27 |
| SIGGEN |  | 140 |  |
|  | FogSignal | 58 | * |
| status |  | 149 |  |
|  | AirportAirfield | 2 | 1-2-4-5-6-7-8-12-14-16-17 |
|  | ACHBRT | 3 | 1-2-3-4-5-6-7-8-9-14 |
|  | AnchorageArea | 4 | 1-2-3-5-6-7-8-9-14 |
|  | BeaconCardinal | 5 | 1-2-4-5-7-8-12-18 |
|  | BeaconIsolatedDanger | 6 | 1-2-4-5-7-8-12-18 |
|  | BeaconLateral | 7 | 1-2-4-5-7-8-12-18 |
|  | BeaconSafeWater | 8 | 1-2-4-5-7-8-12-18 |
|  | BeaconSpecialPurpose | 9 | 1-2-4-5-7-8-12-18 |
|  | Berths | 10 | 1-2-3-5-6-7-8-9-12-14 |
|  | Building | 12 | 1-4-6-7-8-12-13-14-16-17 |
|  | BuoyCardinal | 14 | 1-2-5-7-8-18 |
|  | BuoyInstallation | 15 | 1-2-4-5-7-8-18 |
|  | BuoyIsolatedDanger | 16 | 1-2-5-7-8-18 |
|  | BuoyLateral | 17 | 1-2-5-7-8-18 |
|  | BuoySafeWater | 18 | 1-2-5-7-8-18 |
|  | BuoySpecialPurpose | 19 | 1-2-5-7-8-18 |
|  | CableArea | 20 | 1-7-13 |
|  | CableOverhead | 21 | 1-4-5-7-12 |
|  | CableSubmarine | 22 | 1-4-13 |
|  | Canal | 23 | 1-3-4-5-6-8-14 |
|  | CTSARE | 25 | 1-2-3-5-6-7-9 |
|  | Causeway | 26 | 1-8-12-14 |
|  | CHKPNT | 28 | 1-2-5-7-9-12-16-17 |
|  | CGUSTA | 29 | 1-4-5-16-17 |
|  | ContiguousZone | 31 | 1 |
|  | Conveyor | 34 | 1-4-6-12 |
|  | Crane | 35 | 1-4-6-12 |
|  | Daymark | 39 | 1-4-5-7-8-12 |
|  | DeepWaterRouteCentercurve | 40 | 1-3-6-9 |
|  | DeepWaterRoutePart | 41 | 1-3-6-9 |
|  | DockArea | 45 | 1-4-6-8-14 |
|  | DryDock | 47 | 1-4-6-8-12-14 |
|  | DMPGRD | 48 | 1-2-4-6-7 |
|  | Fairway | 51 | 1-3-6-7-9 |
|  | FenceWall | 52 | 1-12 |
|  | FerryRoute | 53 | 1-2-4-5-6-7-8-9 |
|  | FisheryZone | 54 | 1-5-6-7 |
|  | FishingFacility | 55 | 1-4-5-6-7-8-12-16-17 |
|  | FSHGRD | 56 | 1-5-6-7-8-14-16-17 |
|  | FloatingDock | 57 | 1-4-6-7-8-12 |
|  | FogSignal | 58 | 1-2-4-5-7-8-15 |
|  | FRPARE | 60 | 1-6-8-14 |
|  | Gate | 61 | 1-4-6-16-17 |
|  | Gridiron | 62 | 1-4-6-8-14-16-17 |
|  | HRBARE | 63 | 1-4-6-8-14-16-17 |
|  | HarbourFacility | 64 | 1-4-5-6-7-8-9-12-13-14-16-17 |
|  | IceArea | 66 | 1-2-5-16-17 |
|  | ICNARE | 67 | 1-2-5-6-7-16-17 |
|  | InshoreTrafficZone | 68 | 1-3-6-9-16-17 |
|  | LandArea | 71 | 6-7-8-12-14-16-17-18 |
|  | Landmark | 74 | 1-2-4-5-7-8-12-13-14-16-17 |
|  | LIGHTS | 75 | 1-2-4-5-6-7-8-11-14-15-16-17 |
|  | LightFloat | 76 | 1-2-4-5-7-8-14-16-17 |
|  | LightVessel | 77 | 1-2-4-5-7-8-14-16-17 |
|  | LockBasin | 79 | 1-4-6-8-13-14-16-17 |
|  | LOGPON | 80 | 1-2-4-5-6-7-8 |
|  | MarineFarmCulture | 82 | 1-2-4-5-6-7-8-14-16-17 |
|  | MIPARE | 83 | 1-2-5-6-7-16-17 |
|  | MooringFacility | 84 | 1-2-3-4-5-6-7-8-9-12-14-18 |
|  | NavigationLine | 85 | 1-2-5-7-8-14 |
|  | NEWOBJ | 163 | * |
|  | Obstruction | 86 | 1-4-5-7-8-13-18 |
|  | OffshorePlatform | 87 | 1-2-4-7-8-12-16-17 |
|  | OffshoreProductionArea | 88 | 1-4-7-8-12 |
|  | OILBAR | 89 | 1-2-4-7-8 |
|  | PILBOP | 91 | 1-2-3-5-6-9-16-17 |
|  | SubmarinePipelineArea | 92 | 1-4-7 |
|  | PipelineOverhead | 93 | 1-4-7-12 |
|  | PipelineSubmarineOnLand | 94 | 1-4-7-12 |
|  | Pontoon | 95 | 1-2-4-5-6-7-8-12-14 |
|  | PRCARE | 96 | 1-9 |
|  | ProductionStorageArea | 97 | 1-4-8 |
|  | RADLNE | 99 | 1-2-4-7 |
|  | RADRNG | 100 | 1-2-4-7 |
|  | RadarReflector | 101 | 1-4-8 |
|  | RadarStation | 102 | 1-2-4-7-8 |
|  | RadarTransponderBeacon | 103 | 1-2-4-5-7-8 |
|  | RDOCAL | 104 | 1-3-4-5-6-7-9 |
|  | RadioStation | 105 | 1-2-4-5-7-8 |
|  | Railway | 106 | 1-4-6-12 |
|  | RecommendedRouteCentrecurve | 108 | 1-5-6-9 |
|  | RecommendedTrack | 109 | 1-2-5-6-8-9-14 (replaces check 1680) |
|  | RecommededTrafficLanePart | 110 | 1-6-9 |
|  | RSCSTA | 111 | 1-2-4-5-7-8-14-16-17 |
|  | RestrictedArea | 112 | 1-2-3-4-5-6-7-9-18 |
|  | Retroreflector | 113 | 1-4-8 |
|  | River | 114 | 1-2-5-8-14 |
|  | Roadway | 116 | 1-2-4-6-8-12-14 |
|  | Runway | 117 | 1-2-4-5-6-8-12-14 |
|  | SPLARE | 120 | 1-2-3-4-5-6-7-8-9-14 |
|  | ShorelineConstruction | 122 | 1-2-3-4-6-7-8-9-12-14-16-17 |
|  | SignalStationTraffic | 123 | 1-2-4-5-7-8-12-14-15-16-17 |
|  | SignalStationWarning | 124 | 1-2-4-5-7-8-12-14-15-16-17 |
|  | SiloTank | 125 | 1-4-12 |
|  | SmallCraftFacility | 128 | 1-2-3-4-5-6-7-8-9-12-14-16-17 |
|  | Sounding | 129 | 18 |
|  | TS_PRH | 136 | 1-2-5-7-18 |
|  | TS_PNH | 137 | 1-2-5-7-18 |
|  | TS_TIS | 139 | 1-2-5-7-18 |
|  | T_HMON | 140 | 5 |
|  | T_NHMN | 141 | 5 |
|  | T_TIMS | 142 | 5 |
|  | TOPMAR | 144 | 1-5-7-8-12-14 |
|  | TSELNE | 145 | 1-3-9 |
|  | TrafficSeparationSchemeBoundary | 146 | 1-3-9 |
|  | TrafficSeparationSchemeCrossing | 147 | 1-3-6-9 |
|  | TrafficSeparationSchemeLanePart | 148 | 1-3-6-9 |
|  | TrafficSeparationSchemeRoundabout | 149 | 1-3-6-9 |
|  | TrafficSeparationZone | 150 | 1-3-9 |
|  | Tunnel | 151 | 1-3-4-6-8-14-16-17 |
|  | TwowayRoutePart | 152 | 1-3-6-9 |
|  | UnderwaterAwashRock | 153 | 13-18 |
|  | Wrecks | 159 | 7-13-18 |
| SURTYP |  | 153 |  |
|  | QualityOfSurvey | 310 | * |
| techniqueOfVerticalMeasurement |  | 156 |  |
|  | DeepWaterRouteCentercurve | 40 | 1-2-3-6-7-8-9-11-13 |
|  | DeepWaterRoutePart | 41 | 1-2-3-6-7-8-9-11-13 |
|  | DredgedArea | 46 | 1-2-3-6-7-8-9-11-13 |
|  | Obstruction | 86 | 1-2-3-4-5-6-7-8-9-10-11-12-13 |
|  | RecommendedRouteCentrecurve | 108 | 1-2-3-6-7-8-9-11-13 |
|  | RecommendedTrack | 109 | 1-2-3-6-7-8-9-11-13 |
|  | Sounding | 129 | * |
|  | SweptArea | 134 | 6-8-13 (see check 1654) |
|  | TwowayRoutePart | 152 | 1-2-3-6-7-8-9-10-11-13 |
|  | UnderwaterAwashRock | 153 | 1-2-3-4-5-6-7-8-9-10-11-12-13 |
|  | Wrecks | 159 | 1-2-3-4-5-6-7-8-9-10-11-12-13 |
|  | QualityOfBathymetricSurvey | 308 | * |
| T_ACWL |  | 161 |  |
|  | TS_TIS | 139 | * |
|  | T_HMON | 140 | * |
|  | T_NHMN | 141 | * |
| T_MTOD |  | 163 |  |
|  | TS_PRH | 136 | 1-2 # (see check 1560) |
|  | TS_PNH | 137 | 3 (#) (see check 1561) |
|  | T_HMON | 140 | 1-2 # (see check 1557) |
|  | T_NHMN | 141 | 3 (#) (see check 1558) |
| TOPSHP |  | 171 |  |
|  | Daymark | 39 | * # |
|  | TOPMAR | 144 | * # |
| traffic |  | 172 |  |
|  | DeepWaterRouteCentercurve | 40 | * # |
|  | DeepWaterRoutePart | 41 | * # |
|  | Fairway | 51 | * |
|  | RDOCAL | 104 | * # |
|  | RecommendedRouteCentrecurve | 108 | * |
|  | RecommendedTrack | 109 | * # |
|  | TwowayRoutePart | 152 | * # |
| verticalDatum |  | 185 |  |
|  | BRIDGE | 11 | * |
|  | CableOverhead | 21 | * |
|  | Conveyor | 34 | * |
|  | Crane | 35 | * |
|  | Gate | 61 | * |
|  | LIGHTS | 75 | * |
|  | PipelineOverhead | 93 | * |
|  | SoundingDatum | 309 | * (#) |
|  | VerticalDatumOfData | 312 | * (#) |
| waterLevelEffect |  | 187 |  |
|  | Causeway | 26 | 1-2-3-4-5-6 |
|  | Gridiron | 62 | 1-2-3-4-5 |
|  | LandRegion | 73 | 1-2-4-6 |
|  | MarineFarmCulture | 82 | 1-2-3-4-5-7 # |
|  | MooringFacility | 84 | * 1-2-3-4-5-6 |
|  | NEWOBJ | 163 | * |
|  | Obstruction | 86 | 1-2-3-4-5-7 # |
|  | PylonBridgeSupport | 98 | 1-2-3-4-5-6 |
|  | SeabedArea | 121 | 3-4-5 |
|  | ShorelineConstruction | 122 | * |
|  | UnderwaterAwashRock | 153 | 3-4-5 # |
|  | Wrecks | 159 | 1-2-3-4-5 # |
| HORDAT |  | 400 |  |
|  | M_HOPA | 304 | * # |
| qualityOfPosition |  | 402 |  |
|  | QualityOfSurvey | 310 | * |

# Comments

As far as I can tell HORDAT is not used in S-101.

Remove Clause.  This is already handled in the main PS

NOTE:  If there is an S-100 in front of the clause number it means that it conforms to an S-100 clause, if not then it is S-101

Wierdly there is no reference to creating a NAME within S-101.

This table no longer exists in S-100 – Delete Check

Cannot find a reference to not allowing Attribute codes be repeated

In the 8211 this is on the Ring Association field

255 is not a value anymore

USAG is not carried on point anymore

255 is not a value anymore

Change to associations, aggregations and compositions

FSPT does not exist anymore

The concept of CATCOV has been removed

Change to associations, aggregations and compositions

There is no VRPT.  I think it is now SPAS

I think it is C2IT and C3IT – coordinate tuple field structure

C3IT

Would this be the List Field Structure – C2IL and C3IL

This table is not in S-100 or S-101.

Need to figure out the new 8211 fields.

Need to figure out the new 8211 fields

C2IT or C2IL?

The NAME field is not defined in S-100/S-101.

The NAME field is not defined in S-100/S-101

Need to find the new 8211 equivelents

Need to find the new 8211 reference

Concept has changed

Needs to be redone as lights have been remodeled

Need to account for the fact that these are sub attributes of the complex attribute of Sector Limit

Need to be redone as the model has changed

Bridge has been remodeled

BRIDGE has been remodeled

Do we need to name each type of aggregation, association, composition

This has changed.  The RCNM does not refer to isolated

This has changed. The RCNM does not refer to connected

This does not exist

Needs to be researched.

Remove Check in favour of specific checks regarding associations, aggregations and compositions.

Remove Check in favour of specific checks regarding associations, aggregations and compositions.

COMT does not exist nor does DSPM

Need to research

Now a complex called survey date range

Need to fix as CATCOV does not exist

Remove check….  Should validate against the feature catalogue.

We haven’t defined mandatory meta features.

This statement is not in S-101

Additional Information

remodeled

Eliminated for DataCoverage

remodeled

Removed

Station Name, number and values

Remove Check

Needs to be reworked

Needs to be reworked

Needs to be reworked

Needs to be reworked

Needs to be reworked

Needs to be reworked. No PRIM subfield

Needs to be reworked

Needs to be reworked

GRUP no longer exists

GRUP no longer exists

This needs to be fixed

This needs to be researched

This needs to be researched

Does not exist

Does not exist

Does not exist anymore.

Does not exist anymore

Does not exist anymore

Does not exist

Needs amending

These are part of a complex or a aggregations.

Needs amending

Needs to be fixed.  DSPM does not exist.  I think that this is now in the CRSH field

Needs to be fixed.  DUNI and DSPM does not exist anymore

No DSPM

No DSPM

UADT does not exist

EDTN does not exist

Is not specified specifically in S-101

Lights have been remodeled

Needs some work.  I think these are now attribute values

Needs to be fixed

Delete

Delete – not sure if codes are still in use.

This isn’t defined in S-101.

Delete characters are not defined in S-101

Needs to be reworded

Remove

Remove.  Add check for the correct feature

Remove Check

Remove Check

Remove Check

Delete Check.  Not in S-101

DDR does not exist and catalogue files are different

Delete

No CRC’s it is digital signatures

Does not exist in S-101

EDTN does not exist need the new mapping

UPDN does not exist need the new mapping

UPDN does not exist need new mapping

Does not exist in S-101 need new mapping

Rewrite.  This is in the metadata catalogue

Remove

DPSM does not exist in S-101

Need new mapping

DPSM does not exist in S-101

DPSM does not exist in S-101

Does not exist in S-101

SORDAT has been removed.  Check the other dates like survey date.

Time range complex attributre.

Is this a DCEG check????

Need to find the new mapping in S211

Need to find the new mapping

Get DQWG to write this check.

Write new check for Dredged Date

Removed

Remove check

dataCoverage

DataCoverage

feature removed

feature removed

Featrues removed or remodeld

Featrues removed or remodeld

Featrues removed or remodeld

Features Removed

Removed

SORDAT is now longer in S-101

Bridge has been remodeled

I don’t think this exists

Need to fix

Need to fix

Concept has changed

Not a feature

Change to named aggregation

Change to named aggregation

No Longer a feature

Change to new methodology

Not a feature but an attribute

Need to update to new modelling

Need to fix

Need to update the model

Modelling