© ISO/IEC 2007 – All rights reservedISO-IEC_ 63Complementary elementIntroductory element — Main elementÉlément introductif — Élément central — Élément complémentaireIntroductory element — Main element — Complementary elementE2007-10-2 ISO/IECISO/IEC     2007 ISO/IEC ISO/IEC _(E).        2Heading 2Heading 1    02 STD Version 2.1c20   4            INTERNATIONAL HYDROGRAPHIC ORGANIZATION

IHO GEOSPATIAL STANDARD

FOR MARINE PROTECTED AREAS

Draft  0.0.2 – February 2012

Special Publication No. 10X

Marine Protected Areas - Product Specification

Published by the

International Hydrographic Bureau

MONACO

Record of Document Maintenance

Changes to this Product Specification are coordinated by the IHO Standardization of Nautical Publications Working Group (SNPWG). New editions will be made available via the IHO web site. Maintenance of the Product Specification shall conform to IHO Technical Resolution 2/2007 (revised 2010).

| Date | Description | Authority | Version |
| --- | --- | --- | --- |

Content

Page

1	Introduction	6

2	Data Product Specification Metadata	6

3	Overview	7

3.1	Informal Description	7

4	References	7

5	Terms, definitions and abbreviations	7

5.1	Terms and Definitions	7

6	Abbreviations	9

7	Specification Scope	9

8	MPA Data Product Identification	9

9	Data Content and Structure	10

10	Application Schema	11

10.1	Feature Catalogue	12

10.2	Reference Systems	12

11	Geometric representation	13

12	Quality	13

13	Maintenance	13

14	Data Encoding	14

15	Data Product Delivery Information	14

15.1	Data product delivery information.	14

16	Exchange Set	15

16.1	Support Files	15

16.2	Support File Naming	15

17	Metadata	15

17.1	Dataset Metadata	16

17.1.1	Information about the documented metadata (if provided as a separate resource)	16

17.2	Exchange Set Metadata	17

17.2.1	Exchange Catalogue File Metadata.	18

18	Portrayal	19

ANNEX A – Feature Catalogue	20

A.1	Feature Types (Classes)	20

A.1.1	Geo Object Class: Marine Protected Area	20

A.2	Information Types	21

A.2.1	Applicability	21

A.2.2	AUTORI	23

A.2.3	Contact Details	24

A.2.4	Nautical Information	25

A.2.5	Non-standard working day	26

A.2.6	Recommendations	27

A.2.7	Regulations	28

A.2.8	Restrictions	29

A.2.9	Service hours	30

A.2.10	IMO Ship Report	31

A.3	Feature Attributes	32

A3.1	Date end	32

A.3.2	Date start	32

A.3.3	Periodic date start	32

A.3.4	Periodic date end	33

A.3.5	Category of restricted area	34

A.3.6	IUCN* Categories	36

A.3.7	Category of authority	38

A.3.8	Status	39

A.3.9	Category of IMO ship report	40

A.3.10	Category of Cargo	41

A.3.11	Category of dangerous or hazardous cargo, or ballast	42

A.3.12	Category of Relationship	44

A.3.13	Day of Week	45

A.3.14	Jurisdiction	46

A.3.15	Operation	47

A.3.16	Restriction	48

A.3.17	Logical Connectives	50

A.3.18	Comparison Operator	51

A.3.19	Category of Vessel Registry	52

A.3.20	Category Of Vessel	53

A.3.21	Vessels Characteristics	54

A.3.22	Time Reference	55

A.4	Complex Attributes	56

A.4.1	Day of the Week Range	56

A.4.2	Information	57

A.4.3	Notice Time	58

A.4.4	Object Name	59

A.4.5	Textual Description	60

A.4.6	Under Keel Clearance	61

A.4.7	Vessels Measurements	62

A.4.8	Working Hours Of Day	63

A.4.9	Working Schedule	64

# Introduction

This document has been produced by the IHO Standardisation of Nautical Publications Working Group in response to a requirement to produce a data product that can be used as a Nautical Information Publication Overlay (NPIO) within an Electronic Chart Display and Information Systems. It is based on the IHO S-100 framework specification and the ISO 19100 series of standards. It is a vector product specification that is primarily intended for encoding the extent and nature of Marine Protected Areas, for navigational purposes.

The United Nations Convention on the Law of the Sea (UNCLOS) identifies certain categories of Marine Protected Areas which may require higher standards of environmental protection. Article 194(5) places an obligation on parties to take measures necessary to protect and preserve rare or fragile ecosystems. Part IX of UNCLOS identifies enclosed or semi-enclosed areas, such as a gulf, bay, basin or sea between two or more countries, as places where countries shall endeavour to coordinate the management of environmental protection activities. In respect of Particularly Sensitive Sea Areas (PSSA), Article 211(6)(a) UNCLOS makes provision for a State to submit to the “competent international organization” (IMO for shipping), special mandatory measures concerning the protection from vessel sourced pollution.

UNCLOS thus creates an overall structure for the protection and preservation of the marine environment and places a general obligation on States to implement global conventions addressing particular forms of pollution protection and regional agreements tailored to the requirements of discrete sea areas.

# Data Product Specification Metadata

This section provides metadata about the creation of this data product specification.

Title:				IHO S-10X Marine Protected Areas – Data Product Specification

S-100 Version:	1.0.0 (January 2010)

MPA Version:		0.0.1 Draft

Date:				April 2011

Language:			English

Classification:	Unclassified

Contact:			International Hydrographic Bureau

4 Quai Antoine 1er
B.P. 445
MC 98011 MONACO CEDEX
Telephone: + 377 93 10 81 40
Fax: +377 93 10 81 40
URL:		www.iho-ohi.net

Document Identifier: IHO Publication S-10X

Maintenance:	This document is maintained by the IHO Standardization of Nautical Publications Working Group (SNPWG).  New editions will be published as determined by the Hydrographic Standards and Services Committee (HSSC) (in conformance with IHO Technical Resolution 2/2007 - revised 2010), and will be made available for download from the IHO web site (www.IHO.int)

# Overview

## Informal Description

A Marine Protected Area (MPA) is a protected area whose boundaries include an area of ocean. They include areas of the intertidal or sub-tidal terrain, together with their overlying water and associated flora, fauna, historical and cultural features, which have been reserved by law or other effective means to protect part or all of, the enclosed environment. For example, MPA’s may be established to protect fish species, rare habitat area, or entire ecosystems.

MPAs can range from, simple declarations to protect a resource, to areas that are extensively regulated. The degree to which environmental regulations affect shipping varies according to whether MPA’s are located in territorial waters, exclusive economic zones, or high seas. These limits are regulated by the law of the sea.  Most MPAs are located in the territorial waters of coastal states, where enforcement can be ensured. MPAs can also however be established in a state's exclusive economic zone and even within international waters. For example in 1999, Italy, France and Monaco jointly established a cetacean sanctuary in the Ligurian Sea named the Pelagos Sanctuary for Mediterranean Marine Mammals. This sanctuary includes both national and international waters.

# References

The following normative documents contain provisions that, through reference in this text, constitute provisions of this document.

IHO S.100 IHO Universal Hydrographic Data Model

ISO 19101-2:2008 Geographic Information - Rules for Application Schema

ISO/TS 19103:2005 Geographic information - Conceptual schema language

ISO 19106:2004 Geographic Information - Profiles

ISO 19109:2005 Geographic Information - Rules for Application Schema

ISO 19111:2003 Geographic information - Spatial referencing by coordinates

ISO 19115:2003 Geographic information - Metadata

ISO 19115-2:2009 Geographic information - Metadata: Extensions for imagery and gridded data

ISO 19123:2005 Geographic information - Schema for coverage geometry and functions

ISO 19129:2009 Geographic information - Imagery gridded and coverage data framework

ISO 19131:2007 Geographic information - Data product specifications

# Terms, definitions and abbreviations

## Terms and Definitions

application

manipulation and processing of data in support of user requirements (ISO 19101)

application schema

conceptual schema for data required by one or more applications (ISO 19101]

conceptual model

model that defines concepts of a universe of discourse (ISO 19101]

conceptual schema

formal description of a conceptual model (ISO 19101]

coverage

feature that acts as a function to return values from its range for any direct position within its spatial, temporal or spatiotemporal domain (ISO 19123]

EXAMPLE Raster image, polygon overlay, digital elevation matrix.

data product

dataset or dataset series that conforms to a data product specification

data product specification

detailed description of a dataset or dataset series together with additional information that will enable it to be created, supplied to and used by another party

NOTE A data product specification provides a description of the universe of discourse and a specification for mapping the universe of discourse to a dataset. It may be used for production, sales, end-use or other purpose.

dataset

identifiable collection of data (ISO 19115]

NOTE A dataset may be a smaller grouping of data which, though limited by some constraint such as spatial extent or feature type, is located physically within a larger dataset. Theoretically, a dataset may be as small as a single feature or feature attribute contained within a larger dataset. A hardcopy map or chart may be considered a dataset.

dataset series

collection of datasets sharing the same product specification (ISO 19115]

domain

well-defined set (ISO/TS 19103]

NOTE Well-defined means that the definition is both necessary and sufficient, as everything that satisfies the definition is in the set and everything that does not satisfy the definition is necessarily outside the set.

feature

abstraction of real world phenomena (ISO 19101]

NOTE A feature may occur as a type or an instance. Feature type or feature instance shall be used when only one is meant.

feature association

relationship that links instances of one feature type with instances of the same or a different feature type (ISO19110]

NOTE 1 A feature association may occur as a type or an instance. Feature association type or feature association instance is used when only one is meant.

NOTE 2 Feature associations include aggregation of features.

feature attribute

characteristic of a feature (ISO 19101]

NOTE 1 A feature attribute may occur as a type or an instance. Feature attribute type or feature attribute instance is used when only one is meant.

NOTE 2 A feature attribute type has a name, a data type and a domain associated to it. A feature attribute for a feature instance has an attribute value taken from the domain.

geographic data

data with implicit or explicit reference to a location relative to the Earth (ISO 19109]

NOTE Geographic information is also used as a term for information concerning phenomena implicitly or explicitly associated with a location relative to the Earth.

metadata

data about data (ISO 19115]

model

abstraction of some aspects of reality (ISO 19109]

portrayal

presentation of information to humans (ISO 19117]

quality

totality of characteristics of a product that bear on its ability to satisfy stated and implied needs (ISO 19101]

universe of discourse

view of the real or hypothetical world that includes everything of interest (ISO 19101]

# Abbreviations

ASCII 	American Standard Code for Information Interchange
ENC	Electronic Navigational Chart
GML	Geography Markup Language
IHO	International Hydrographic Organization
IOC	International Oceanographic Commission
ISO	International Organization for Standardization
MPA	Marine Protected Area
MIO	Marine Information Overlay
NPIO 	Nautical Publication Information Overlay
UML	Unified Modelling Language
URI	Uniformed Resource Identifier
URL 	Uniform Resource Locator
WMS	Web Map Service
WFS	Web Feature Service
www 	World Wide Web
WGS	World Geodetic System
XML	Extensible Markup Language
XSLT	eXtensible Stylesheet Language Transformations

# Specification Scope

Unlike S-100 ENCs which may have “scalable” and “non-scalable” variants, Marine Protected Areas data products are homogeneous (i.e. have common properties) their format or structure do not vary. This product specification describes one data product and therefore requires only one scope which is described below;

Scope ID:  	Marine Protected Areas datasets.

Hierarchical level: 	005 – (from 19115 - MD_ScopeCode)

Hierarchical level name: 	dataset

Level description:	information applies to the dataset

Extent:	EX_GeographicExtent  - Global coverage of maritime areas.
EX_TemporalExtent and EX_VerticalExtent are not defined for this product specification.

# MPA Data Product Identification

The following information is intended to describe the MPA data product.

Title: 	Nautical Information Overlay - Marine Protected Areas

Abstract: 	Data product describing Marine Protected Areas that are of significance to mariners and others operating within the maritime domain.

Purpose: 	A data product for encoding and transferring MPA information for use as an NIO, within electronic navigational systems such as ECDIS.

Topic category: 	environment, oceans, boundaries (see 19115 MD_TopicCategoryCode)

Content: 	A conformant data set contains features defined by the MPA Feature Catalogue and described in the application schema as shown in Figure 2.

Description:  	An S-100 compliant rendering of MPA information.

Spatial Extent:	East Bounding Longitude:	 180
West Bounding Longitude: 	-180
North Bounding Latitude: 	   90
South Bounding Latitude:	  -90

Specific Purpose: 	MPA datasets provide information regarding the location and nature of various national and international marine protected areas for navigational purposes.

Spatial representation type: vector

# Data Content and Structure

The MPA product is based on the S-100 General Feature Model (GFM).  A General Feature Model is a Metamodel of feature types. A feature may have properties that may be operations, attributes or associations. Any feature may have a number of attributes, some of which may be geometric and spatial. A feature is not defined in terms of a single geometry, but rather as a conceptually meaningful object within a particular domain of discourse, one or more of whose properties may be geometric. The 'Feature' is the fundamental unit of geospatial information, so the Feature Model is the fundamental meta-model used for developing an Application Schema.

This section contains the MPA Application Schema expressed in UML and an associated Feature Catalogue.  The Feature Catalogue included at Annex A, provides a full description of each feature type including its attributes, attribute values and relationships in the data product.

MPAs are encoded as vector entities which are derived from the geometry element GM_Object as per S-100 Version 1.0.0 Figure 7-3.

Figure 1 - Domain Model Overview

# Application Schema

The UML model shown in Figure 2 below illustrates a simplified version of the MPA application schema.  It includes a general description of elements used to construct the application schema, and the relationships between them. These elements include features types, information types, simple attributes, complex attributes, aggregations and associations.  A brief description of these is provided below and the full description is in the feature catalogue.

A feature is an abstraction of real world phenomena. GF_FeatureType is a metaclass that is instantiated as classes that represent individual feature types. A certain feature type is the class used for all instances of that feature type. The instance of a class that represents an individual feature type is called feature instances.  In object-oriented modelling, feature types are equivalent to classes and feature instances are equivalent to objects.

An information type is an identifiable object that can be associated with features in order to carry information pertaining to the associated features. S100_GF_InformationType is the class intended for information types within S-100.  A primary object carrying a Chart Note for example, may contain text in English and an associated supplementary information object may be used to carry the same text in another language.

Simple attributes can be enumerations, codelists or simple types (e.g. integer or character string).

Complex attributes are properties of a feature which can be divided into multiple sub attributes and are used where objects have properties that better fit a hierarchical structure.  They provide a better construct for encoding list attributes on objects such as light sectors.

An association is a relationship that links instances of one feature or information type with instances of the same or different feature and information types. Each relationship has a name and two roles thus giving a more detailed representation of the real world relationships within the dataset.  The MPA application schema is presented as a UML model in figure 3.

[Note – need to look at the diagram to ensure that there are roles on both ends of associations].

Figure 2 – MPA Application Schema.

## Feature Catalogue

The Feature Catalogue describes the feature types, information types, attributes, attribute values, associations and roles which may be used in an MPA. The Feature Catalogue is available from the IHO website as an XML document which conforms to the S-100 XML Feature Catalogue Schema.

## Reference Systems

The CRS used for this product specification is World Geodetic System (WGS) 84 which is defined by the the European Petroleum Survey Group (EPSG) code 4326, (or similar - North American Datum 1983 / Canadian Spatial Reference System).

Spatial data are expressed as latitude (φ) and longitude (λ) geographic coordinates. Longitude values are stored as a negative number to represent a position west of the Prime Meridian (0°). Latitude values are stored as a negative number to represent a position south of the Equator (0°). Coordinates are expressed as real value, degree / degree decimal format. Datasets conforming to this product specification are not projected.

Spatial reference system: 					Horizontal coordinate reference system: WGS 84

Projection: 									None

Vertical coordinate reference system: 		WGS 84

Temporal reference system: 				Gregorian calendar

Coordinate reference system registry: 		EPSG Geodetic Parameter Registry

Date type (according to ISO 19115):  		002 - publication

Responsible party:  							International Organisation of Oil and Gas Producers (OGP)

URL:  http://www.ogp.org.uk/

Coordinate reference system identifier (CRSID):  4326 (or 4617 for NAD 83)

Code space: OGP – OGP

# Geometric representation

Geometric representation is the digital description of the spatial component of an object as described in S-100 and ISO 19107. This product specification uses three types of geometries: GM_Point, GM_Curve, and GM_Polygon (GM_Surface).

Figure 3 - Geometric Primitives

# Quality

Spatial data quality

Completeness of information 
How current the data is

# Maintenance

Maintenance and Update Frequency: Datasets are maintained as needed and must include mechanisms for MPA updating.

Data Source: Data Producers must use applicable sources to maintain and update data and provide a brief description of the sources that were used to produce the dataset in the appropriate metadata field.

# Data Encoding

The principal encoding will be the Open Geospatial Consortium (OGC), Geography Markup Language (GML) format. GML is an XML grammar designed to express geographical features. It serves as a modeling language for geographic systems as well as an open interchange format for geographic transactions.

Note: ENC data cells are delivered in either the ISO 8211 format, or a proprietary internal System ENC (SENC) format.  These are binary formats that are machine readable, but are not human readable. Although this product specification, specifies GML as the primary encoding format, it does not preclude the use of other encoding formats.

# Data Product Delivery Information

This data product specification defines GML as the primary format in which MPA data product are to be delivered. Information concerning the delivery medium should also be included. If a data product is to be delivered in different formats, then the appropriate information for each shall be given.

The delivery format information should include the following items (from ISO/DIS 19131:2005 with some changes of obligation):  format name, version, language, character set.

Delivery format information may also include (from ISO/DIS 19131:2005): specification, file structure.

Delivery medium information may include (from ISO/DIS 19131:2005): units of delivery.

## Data product delivery information.

| Name | ISO 19131 Elements | Value |
| --- | --- | --- |
| Format name | DPS_DeliveryInformation.deliveryFormat > DPS_DeliveryFormat.formatName | GML |
| Version | DPS_DeliveryInformation.deliveryFormat > DPS_DeliveryFormat.version | 3.2.1 |
| Specification description | DPS_DeliveryInformation.deliveryFormat > DPS_DeliveryFormat.specification | See * below |
| Language | DPS_DeliveryInformation.deliveryFormat > DPS_DeliveryFormat.language | English English |
| Character set | DPS_DeliveryInformation.deliveryFormat > DPS_DeliveryFormat.characterSet > MD_CharacterSetCode | 004 – utf8 |

Table 1

* GML is an XML encoding for the transport and storage of geographic information, including both the geometry and the properties of geographic features, between distributed systems. The XML Schema for the GML application schema is provided in a single schema document MPA.xsd. (http://www.iho.int/schemas/MPA …). Feature instance shall validate against MPA.xsd and conform to all other requirements specified in this data product specification including all constraints not captured in the XML Schema document.

# Exchange Set

An exchange set will consist of one or more MPA datasets.  An exchange set may also include one or more support files containing supplementary information encoded in separate files. These are linked to the MPA dataset features, using the attributes described below. Each exchange set will include a single (XML) catalogue file containing discovery metadata for each MPA data as well all support files that will be included in the exchange set. MPA attributes that reference external support files are listed below.

textualDescription (TXTDSC)  (see complex attribute textualDescription)

nationalTextualDescription - NTXTDS (not included - is the a need to include national textual description?)

pictorialRepresentation (PICREP) (see abstract feature type)

## Support Files

Support files contain ancillary textual or graphic information in separate (linked) files. Textual information may be encoded in an unstructured (TXT) or structured (XML / HTML 4) format.

Picture files must be encoded in one of the following W3C graphics formats;

Portable Network Graphics (PNG) [Edition 2.0] must be used for picture (raster) files and;

Scalable Vector Graphics (SVG) [Edition 1.1] must be used for vector diagrams.

PNG is an extensible file format designed for lossless, portable storage of raster images. It provides a patent-free replacement for the GIF format and also replicates many common uses of TIFF. The PNG edition 2 format has been adopted as an ISO standard, (ISO/IEC 15948:2003).  SVG is a language for describing two-dimensional graphics in XML [XML10]. SVG allows for three types of graphic objects: vector graphic shapes (e.g., paths consisting of straight lines and curves), images and text.

## Support File Naming

All support files will have unique world-wide file identifiers. The file identifier of support information should not be used to describe the physical content of the file. The support file metadata that accompanies the file will inform the user of the name and purpose of the file (i.e. new, replacement and deletion).

In this encoding the support files are named according to the specifications given below:

CCXXXXXXXX.E00

The main part forms an identifier where:

- the first two characters identify the issuing agency.

- the third to tenth characters can be used in any way by the producer to provide the unique file name. The following characters are allowed in the dataset name, A to Z, 0 to 9 and the special character _ (underscore).

- .E00 – support file extension.

# Metadata

The MPA metadata description is based on the S-100 metadata document section, which is a profile of the ISO 19115 standard. These documents provide a structure for describing digital geographic data and define metadata elements, a common set of metadata terminology, definitions and extension procedures.

Two main types of metadata are described in this product specification; dataset metadata and exchange set metadata.

Figure 4 – Metadata

## Dataset Metadata

Dataset metadata is intended to describe information about a dataset or data resource. It facilitates the management and exploitation of data and is an important requirement for understanding the characteristics of a dataset (and or data resource). Whereas dataset metadata is usually fairly comprehensive, there is also a requirement for a constrained subset of metadata elements that are usually required for discovery purposes. Discovery metadata are often used for building web catalogues, and can help users to determine whether a product or service is fit for purpose and how/where they can be accessed.

### Information about the documented metadata (if provided as a separate resource)

| Name | Cardinality | Value | Type | Remarks |
| --- | --- | --- | --- | --- |
| DataSetDiscoveryMetadata |  |  |  |  |
| metadataFileIdentifier | 1 |  | CharacterString |  |
| metadataPointOfContact | 1 |  | CI_ResponsibleParty | Contact information for the vessel or authority |
| metadataDateStamp | 1 |  | Date | When the dataset was created |
| metadataLanguage | 1 | English, French | CharacterString | All data sets conforming to this PS must use English or French language |
| fileName | 1 |  | CharacterString | Dataset file name |
| filePath | 1 |  | CharacterString | Full path from the exchange set root directory |
| description | 1 |  | CharacterString |  |
|  |  |  |  | NATIONAL LANGUAGE enabled |
| dataProtection | 1 | {1} to {2} | CharacterString | 1. Unencrypted 2. Unencrypted |
| purpose |  | {1} to {2} | CharacterString | 1. New dataset 2. Update |
| specificUsage |  | {1} to {2} | Integer | 1, Notices of Arrival: A dataset containing a new or updated notice of arrival as required by local or national regulations |
|  |  |  |  | 2. A new or updated request for making pilotage arrangements |
| editionNumber | 1 | {1} | Integer | The dataset edition. Required for s100 but not applicable to MPA, therefore it is set to 1 for all datasets. |
| updateNumber | 1 |  | CharacterString | Update number 0 is assigned to a new request or notice. Subsequent updates or supplements are assigned numbers 1, 2, 3… |
| issueDate | 1 |  | Date | Date on which the dataset was generated. |
| productSpecification | 1 | MPA version 1.0.0 | S100_ProductSpecification | This must be encoded as MPA |
| producingAgency | 1 |  | CI_ResponsibleParty | Party responsible for generating the dataset. |
| horizontalDatum | 1 | WGS84 | CharacterString | The datum for latitude/longitude. EPSG:4326 |
| verticalDatum | 1 | {1} to {30} | Integer | Mean low water springs (29 other values) |
| soundingDatum | 1 | {1} to {30} | Integer | Mean low water springs (29 other values) |
| dataType | 1 | other | S-100_DataFormat | GML. Or other possible S-100 defined formats. |
| otherDataTypeDescription | 0..1 |  | CharacterString |  |
| boundingBox | 0..1 |  | EX_GeographicBoundingBox | Either boundingBox or geographicDescription must be given. |
| boundingPolygon | 0..* |  | EX_BoundingPolygon |  |
| geographicDescription | 0..1 | Norway | EX_GeographicDescription | Descriotion of the location for notices or requests, in the form of the country of the national authority. Either boundingBox or geographicDescription must be given. |
| comment | 0..1 |  | CharacterString | Any additional Information |
| cyclicRedundancyCheck | 1 | NonNegativeInteger |  | Check value for the dataset |
| layerId | 1 | {1} | integer | Identifies the relationship to other S100 information on a graphical display. 1.Scale Independent 2. Scale Independent |

Table 2

Note: Types with CI_, EX_, and MD_ prefixes are from packages defined in ISO 19115 and adapted by S-100. Types with S100_ prefix are from packages defined in S-100.

## Exchange Set Metadata

Frequently datasets are packaged and distributed as composite exchange sets by third party vendors. An exchange set could contain many different types of datasets, sourced from different data producers. For example an exchange set may contain numerous dataset files, ancillary data files, discovery metadata files and others.  Exchange set metadata contains metadata about the contents of the exchange set and metadata about the data distributor.

Figure 5 Exchange Set Metadata

### Exchange Catalogue File Metadata.

All MPA Catalogue metadata files must contain at least the following metadata elements.

| Name | Cardinality | Value | Type | Remarks |
| --- | --- | --- | --- | --- |
| metadataFileIdentifier | 1 |  | CharacterString |  |
| metadataPointOfContact | 1 |  | CI_ResponsibleParty |  |
| metadataDateStamp | 1 |  | Date |  |
| metadataLanguage | 1 | English | CharacterString | All data sets conforming to this PS must use English language. The catalogue file must be in English. |
| name | 1 | CATALOG.MPA | CharacterString | Catalogue filename |
| abstract | 1 | CharacterString |  | Description of what the exchange catalogue contains |
| productSpecification | 1 | e.g. 1.0.0 |  | Product specification Version Number |
| comment | 0..1 | CharacterString |  | Any additional Information |

Table 2

# Portrayal

Needs to be completed – further information required.

See attribute category of restricted area CATREA enumerations: (i.e. offshore safety zone, nature reserve, bird sanctuary, game reserve, seal sanctuary ….)

Should we include the portrayal documentation provided by David here ?

ANNEX A – Feature Catalogue

This annex contains the geographic objects (feature types) and information objects (information types) in the feature catalogue.

A.1	Feature Types (Classes)

A.1.1	Geo Object Class: Marine Protected Area

Alpha code: MPAREA

Camel case: MarineProtectedArea 			Abstract type: False

Definition: An area where restrictions apply to protect the environment. References: INT 1 (still to be defined)

Remarks: No remarks. 						Spatial Objects: Point (GM_Point); Area (GM_Polygon) 
Distinction: None.

| Attribute | Camel Case Name | Alpha Code | Cardinality | Sequential |
| --- | --- | --- | --- | --- |
| C Information | cInformation | CINFOM | 0..* |  |
| C object name | cObjectName | COBNAM | 1..* |  |
| C Text Description | cTextualDescription | CTXDSC | 1..* |  |
| Category of restricted area | categoryOfRestrictedArea | CATRES | 1..* |  |
| Category of IUCN | categoryOfIUCN | CIUCNO | 0..1 |  |
| Source indication | sourceIndication | SORIND | 0..* |  |
| Period start | periodStart | PERSTA | 0..1 |  |
| Period end | periodEnd | PEREND | 0..1 |  |
| Date start | dateStart | DATSTA | 0..1 |  |
| Date end | dateEnd | DATEND | 0..1 |  |
| Source date | sourceDate | SORDAT | 0..* |  |
| Jurisdiction | jurisdiction | JRSDTN | 0..1 |  |
| Status | status | STATUS | 0..* |  |
| Scale minimum | scaleMinimum | SCAMAX | 0..1 |  |
| Scale maximum | scaleMaximum | SCAMIN | 0..1 |  |
| Restriction | restriction | RESTRN | 1..* |  |
| Pictorial Representation | pictorialRepresentation | PICREP | 0..* |  |

A.2	Information Types

A.2.1	Applicability

Alpha code: APPLIC

Camel Case: Applicability							 	Abstract type: False

Definition: Describes the relationship between vessel characteristics and: (i) the applicability of an associated information object or feature to the vessel; or, (ii) the use of a facility, place, or service by the vessel; or, (iii) passage of the vessel through an area.

References: Unspecified.

Remarks: No remarks.

Distinction: None

| Attribute | Camel Case Name | Alpha Code | Cardinality | Sequential |
| --- | --- | --- | --- | --- |
| Start date | dateStart | DATSTA | 0..1 |  |
| End date | dateEnd | DATEND | 0..1 |  |
| Period start | periodDateEnd | PEREND | 0..1 |  |
| Period end | periodStart | PERSTA | 0..1 |  |
| Recording date | recordingDate | RECDAT | 0..1 |  |
| Recording Indication | recordingIndication | RECIND | 0..1 |  |
| Source date | sourceDate | SORDAT | 0..1 |  |
| Source indication | sourceIndication | SORIND | 0..1 |  |
| C Information | cInformation | CINFOM | 0..* |  |
| C Text description | cTextualDescription | CTXDSC | 0..* |  |
| C Object name | cObjectName | COBNAM | 0..* |  |
| Category of vessel | categoryOfVessel | CATVES | 0..1 |  |
| Category of cargo | categoryOfCargo | CATCAR | 0..1 |  |
| Category of dangerous or hazardous cargo | categoryOfDangerousOrHazardousCargo | CATDCO | 0..1 |  |
| Category of relationship | categoryOfRelationship | CATREL | 0..1 |  |
| category of vessel registry | categoryOfVesselRegistry | CATVSR | 0..1 |  |
| Logical Connectives | logicalConnectives | LOGCON | 0..1 |  |
| Thickness of ice Capability | thicknessOfIceCapability | ICETHK | 0..1 |  |
| Vessel performance | vesselPerformance | VESPER | 0..1 |  |
| Vessels measurements | vesselsMeasurements | VESMSR | 0..* |  |

Relationships

| Multiplicity | Association |
| --- | --- |
| 0..* 0..* | Regulations . Applicability .Applicability |
| 0..* 0..* | Restrictions . Applicability .Applicability |
| 0..* | vesselsMeasurements . Applicability . |
| 0..* 0..* | NauticalInformation Applicability .Applicability |  |
| 0..* 0..* | ShipReport.managementAuthority Applicability .Applicability |  |
| 0..* 0..* | Recommendations . Applicability .Applicability |  |
|  | Applicability . InformationType. |  |
| 0..1 | underKeelClearance . Applicability . |  |

A.2.2	AUTORI

Camel Case: Authority							 	Abstract type: False

Definition: A person or organisation having political or administrative power and control. (Oxford Dictionary of English)

References: Unspecified.
 
Remarks: No remarks.
 
Distinctions: natinf; rcmdts; resdes;

| Attribute | Camel Case Name | Alpha Code | Cardinality | Sequential |
| --- | --- | --- | --- | --- |
| Start date | sourceIndication | SORIND | 0..* |  |
| End date | categoryOfAuthority | CATAUT | 0..1 |  |
| Period start | periodStart | PERSTA | 0..1 |  |
| Source date | sourceDate | SORDAT | 0..* |  |
| Recording date | dateStart | DATSTA | 0..1 |  |
| Recording Indication | periodDateEnd | PEREND | 0..1 |  |
| Source date | dateEnd | SATEND | 0..1 |  |
| Source indication | recordingDate | RECDAT | 0..1 |  |
|  | recordingIndication | RECIND | 0..1 |  |
| C Information | cInformation | CINFO | 0..* |  |
| C Text description | cTextualDescription | CTXDSC | 0..* |  |
| C Object name | cObjectName | COBNAM | 0..* |  |

Relationships

| Multiplicity | Association |
| --- | --- |
| 0..* 0..* | Authority.managementAuthority ServiceHours .ServiceHours |
| 0..* 0..* | Authority.issuingAuthority ShipReport.shipReport |
| 0..* 0..* | Authority.managementAuthority ContactDetails .ContactDetails |
| 0..* 0..* | MarineProtectedArea . Authority.Authority |
|  | Authority. InformationType. |

A.2.3	Contact Details

Alpha code: CONDET

Camel Case: ContactDetails						Abstract type: False

Definition: Information on how to reach a person or organisation by postal, internet, telephone, telex and radio systems.

References: Unspecified.

Remarks: None.

Distinctions: None

| Attribute | Camel Case Name | Alpha Code | Cardinality | Sequential |
| --- | --- | --- | --- | --- |
| source Indication | sourceIndication |  | 0..* |  |
| source Date | sourceDate |  | 0..* |  |
| period Start | periodStart |  | 0..1 |  |
| periodDateEnd | periodDateEnd |  | 0..1 |  |
| dateEnd | dateEnd |  | 1,0 |  |
| dateStart | dateStart |  | 0..1 |  |
| callSign | callSign |  | 1 |  |
| callName | callName |  | 0..1 |  |
| adminstrativeDivision | adminstrativeDivision |  | 0..1 |  |
| cInformation | cInformation |  | 0..* |  |
| cTextualDescription | cTextualDescription |  | 0..* |  |
| cObjectName | cObjectName |  | 0..* |  |
| internetAddress | internetAddress |  | 0..1 |  |
| cityName | cityName |  | 0..1 |  |
| communicationChannel | communicationChannel |  | 0..1 |  |
| country | country |  | 0..1 |  |
| recordingDate | recordingDate |  | 0..1 |  |
| recordingIndication | recordingIndication |  | 0..1 |  |
| deliveryPoint | deliveryPoint |  | 0..1 |  |
| maritimeMobileServiceIdentityCode | maritimeMobileServiceIdentityCode |  | 0..1 |  |
| telephoneNumber | telephoneNumber |  | 1 |  |
| emailAddress | emailAddress |  | 1 |  |
| telephoneNumberOutsideWorkingHours | telephoneNumberOutsideWorkingHours |  | 1 |  |
| faxNumber | faxNumber |  | 1 |  |
| postalCode | postalCode |  | 1 |  |

Relationship

| Multiplicity | Association |
| --- | --- |
| 0..* 0..* | Authority.managementAuthority ContactDetails .ContactDetails |
|  | ContactDetails InformationType. |

A.2.4	Nautical Information

Alpha code: NATINF

Camel Case: NauticalInformation	Abstract type: False

Definition: Nautical information about a related area or facility.

References: INT 1: M-3: Chapter C 2.2.1, C 2.7, C 2.8, Chater 3 Section C, Chapter 3 Section E, M-4:

Remarks: None.
 
Distinctions: None

| Attribute | Camel Case Name | Alpha Code | Cardinality | Sequential |
| --- | --- | --- | --- | --- |
| Category of authority | categoryOfAuthority | CATAUT | 1 |  |
| Start date | dateStart | DATSTA | 0..1 |  |
| End date | dateEnd | DATEND | 0..1 |  |
| Period start | periodDateEnd | PEREND | 0..1 |  |
| Period end | periodStart | PERSTA | 0..1 |  |
| Recording date | recordingDate | RECDAT | 0..1 |  |
| Recording Indication | recordingIndication | RECIND | 0..1 |  |
| Source date | sourceDate | SORDAT | 0..1 |  |
| Source indication | sourceIndication | SORIND | 0..1 |  |
| C Information | cInformation | CINFOM | 0..* |  |
| C Text description | cTextualDescription | CTXDSC | 0..* |  |
| C Object name | cObjectName | COBNAM | 0..* |  |

Relationships

| Multiplicity | Association |
| --- | --- |
| 0..* 0..* | NauticalInformation . Applicability .Applicability |
| 0..* 0..* | MarineProtectedArea . NauticalInformation .Information |
|  | NauticalInformation . Information. |

A.2.5	Non-standard working day

Alpha code: NWKDAY

Camel Case: NonStdWkgDay	Abstract type: False

Definition: Days when many services are not available. Often days of festivity or recreation when normal working hours are limited, esp. a national or religious festival, etc.

References: INT 1: M-3: M-4:

Remarks: None.
 
Distinctions: None

| Attribute | Camel Case Name | Alpha Code | Cardinality | Sequential |
| --- | --- | --- | --- | --- |
| Fixed date | fixedDate | FIXDAT | 0..* |  |
| Variable date | variableDate | VARDAT | 0..* |  |
| Start date | dateStart | DATSTA | 0..1 |  |
| End date | dateEnd | DATEND | 0..1 |  |
| Period start | periodDateEnd | PEREND | 0..1 |  |
| Period end | periodStart | PERSTA | 0..1 |  |
| Recording date | recordingDate | RECDAT | 0..1 |  |
| Recording Indication | recordingIndication | RECIND | 0..1 |  |
| Source date | sourceDate | SORDAT | 0..1 |  |
| Source indication | sourceIndication | SORIND | 0..1 |  |
| C Information | cInformation | CINFOM | 0..* |  |
| C Text description | cTextualDescription | CTXDSC | 0..* |  |
| C Object name | cObjectName | COBNAM | 0..* |  |

Relationships

| Multiplicity | Association |
| --- | --- |
|  | NonStandardWorkingDay. InformationType. |
| 0..* 0..* | NonStandardWorkingDay.information ServiceHours .informationFor |

A.2.6	Recommendations

Alpha code: RCMDTS

Camel Case: Recommendations	Abstract type: False

Definition: Recommendations for a related area or facility

References: INT 1: M-3: Chapter C 2.2.1, C 2.7, C 2.8, C 3.19, C 3.21 M-4:

Remarks: None.

Distinctions: None

| Attribute | Camel Case Name | Alpha Code | Cardinality | Sequential |
| --- | --- | --- | --- | --- |
| Category of authority | categoryOfAuthority | CATAUT | 0..1 |  |
| Start date | dateStart | DATSTA | 0..1 |  |
| End date | dateEnd | DATEND | 0..1 |  |
| Period start | periodDateEnd | PEREND | 0..1 |  |
| Period end | periodStart | PERSTA | 0..1 |  |
| Recording date | recordingDate | RECDAT | 0..1 |  |
| Recording Indication | recordingIndication | RECIND | 0..1 |  |
| Source date | sourceDate | SORDAT | 0..1 |  |
| Source indication | sourceIndication | SORIND | 0..1 |  |
| C Information | cInformation | CINFOM | 0..* |  |
| C Text description | cTextualDescription | CTXDSC | 0..* |  |
| C Object name | cObjectName | COBNAM | 0..* |  |

Relationships

| Multiplicity | Association |
| --- | --- |
| 0..* 0..* | MarineProtectedArea . Recommendations .Recommendations |
| 0..* 0..* | Recommendations . Applicability .Applicability |
|  | Recommendations . InformationType. |

A.2.7	Regulations

Alpha code: REGLTS

Camel Case: Regulations									Abstract type: False

Definition: Regulations for a related area or facility.

References: INT 1: M-3: Chapter C 2.2.1, C 2.7, C 2.8, C 3.19, C 3.21 M-4:

Remarks: None.

Distinctions: None

| Attribute | Camel Case Name | Alpha Code | Cardinality | Sequential |
| --- | --- | --- | --- | --- |
| Category of authority | categoryOfAuthority | CATAUT | 0..1 |  |
| Start date | dateStart | DATSTA | 0..1 |  |
| End date | dateEnd | DATEND | 0..1 |  |
| Period start | periodDateEnd | PEREND | 0..1 |  |
| Period end | periodStart | PERSTA | 0..1 |  |
| Recording date | recordingDate | RECDAT | 0..1 |  |
| Recording Indication | recordingIndication | RECIND | 0..1 |  |
| Source date | sourceDate | SORDAT | 0..1 |  |
| Source indication | sourceIndication | SORIND | 0..1 |  |
| C Information | cInformation | CINFOM | 0..* |  |
| C Text description | cTextualDescription | CTXDSC | 0..* |  |
| C Object name | cObjectName | COBNAM | 0..* |  |

Relationships

| Multiplicity | Association |
| --- | --- |
| 0..* 0..* | Regulations . Applicability .Applicability |
| 0..* . 0..* | MarineProtectedArea . Regulations .Regulations |
|  | Regulations . InformationType. |

A.2.8	Restrictions

Alpha code: RESDES

Camel Case: Restrictions	Abstract type: False

Definition: Restrictions for a related area or facility.

References:  INT 1: M-3: Chapter C 2.2.1, C 2.7, C 2.8, C 3.19, C 3.21 M-4

Remarks: None.

Distinctions: None

| Attribute | Camel Case Name | Alpha Code | Cardinality | Sequential |
| --- | --- | --- | --- | --- |
| Category of authority | categoryOfAuthority | CATAUT | 0..1 |  |
| Start date | dateStart | DATSTA | 0..1 |  |
| End date | dateEnd | DATEND | 0..1 |  |
| Period start | periodDateEnd | PEREND | 0..1 |  |
| Period end | periodStart | PERSTA | 0..1 |  |
| Recording date | recordingDate | RECDAT | 0..1 |  |
| Recording Indication | recordingIndication | RECIND | 0..1 |  |
| Source date | sourceDate | SORDAT | 0..1 |  |
| Source indication | sourceIndication | SORIND | 0..1 |  |
| C Information | cInformation | CINFOM | 0..* |  |
| C Text description | cTextualDescription | CTXDSC | 0..* |  |
| C Object name | cObjectName | COBNAM | 0..* |  |

Relationships

| Multiplicity | Association |
| --- | --- |
| 0..* 0..* | Restrictions . Applicability .Applicability |
| 0..*. 0..* | MarineProtectedArea . Restrictions .Restrictions |
|  | Restrictions . InformationType. |

A.2.9	Service hours

Alpha code: SRVHRS

Camel Case: ServiceHours	Abstract type: False

Definition: The time when a service is available and known exceptions

References:

Remarks: None.

Distinctions: None

| Attribute | Camel Case Name | Alpha Code | Cardinality | Sequential |
| --- | --- | --- | --- | --- |
| Working schedule | workingSchedule | WRKSCH | 1 |  |
| Notice time | noticeTime | NOTCTM | 1 |  |
| Start date | dateStart | DATSTA | 0..1 |  |
| End date | dateEnd | DATEND | 0..1 |  |
| Period start | periodDateEnd | PEREND | 0..1 |  |
| Period end | periodStart | PERSTA | 0..1 |  |
| Recording date | recordingDate | RECDAT | 0..1 |  |
| Recording Indication | recordingIndication | RECIND | 0..1 |  |
| Source date | sourceDate | SORDAT | 0..1 |  |
| Source indication | sourceIndication | SORIND | 0..1 |  |
| C Information | cInformation | CINFOM | 0..* |  |
| C Text description | cTextualDescription | CTXDSC | 0..* |  |
| C Object name | cObjectName | COBNAM | 0..* |  |

| Multiplicity | Association |
| --- | --- |
| 1..* | noticeTime . ServiceHours . |
| 0..* 0..* | Authority.managementAuthority ServiceHours .ServiceHours |
| 1..*. | workingSchedule. ServiceHours . |
| 0..* 0..* | NonStandardWorkingDay.information ServiceHours .informationFor |
|  | ServiceHours . InformationType. |

A.2.10	IMO Ship Report

Alpha code: SHPREP

Camel Case: ImoShipReport								Abstract type: False 

Definition: This describes how a ship should report to a maritime authority, including when to report, what to report and whether the format conforms to the IMO standard.

References: IMO Resolution A 851(20) adopted 27 November 1997.

Remarks: TXTDSC and NTXTDS are used to describe non-standard ship reports. The Associated Information Object chalim indicates characteristics of vessels which use this report.
Distinctions: None

| Attribute | Camel Case Name | Alpha Code | Cardinality | Sequential |
| --- | --- | --- | --- | --- |
| Category of ship report | categoryOfShipReport | CATREP | 1 |  |
| IMO format for reporting | imoFormatForReporting | IMOREP | 1 |  |
| Start date | dateStart | DATSTA | 0..1 |  |
| End date | dateEnd | DATEND | 0..1 |  |
| Period start | periodDateEnd | PEREND | 0..1 |  |
| Period end | periodStart | PERSTA | 0..1 |  |
| Recording date | recordingDate | RECDAT | 0..1 |  |
| Recording Indication | recordingIndication | RECIND | 0..1 |  |
| Source date | sourceDate | SORDAT | 0..1 |  |
| Source indication | sourceIndication | SORIND | 0..1 |  |
| C Information | cInformation | CINFOM | 0..* |  |
| C Text description | cTextualDescription | CTXDSC | 0..* |  |
| C Object name | cObjectName | COBNAM | 0..* |  |

Relationships

| Multiplicity | Association |
| --- | --- |
| 0..* 0..* | ShipReport.managementAuthority Applicability .Applicability |
| 0..* 0..* | Authority.issuingAuthority ShipReport.shipReport |
|  | ShipReport. InformationType. |

A.3	Feature Attributes

A3.1	Date end

Alpha code: DATEND

Attribute type: Simple

Camel case: dateEnd Data 				Type: Date

Definition: The attribute “date end” indicates the latest date on which an object (e.g. a buoy) will be present.

Constraints:

CCYYMMDD, consisting of 4 digits for the calendar year (CCYY), 2 digits for the month (MM) (e.g. April = 04) and 2 digits for the day (DD), according to ISO 8601:1988.

A.3.2	Date start

Alpha code: DATSTA

Attribute type: Simple

Camel case: dateStart 						Data Type: Date

Definition: The attribute “date, start” indicates the earliest date on which an object (e.g. a buoy) will be present.

Constraints:

CCYYMMDD, consisting of 4 digits for the calendar year (CCYY), 2 digits for the month (MM) (e.g. April = 04) and 2 digits for the day (DD), according to ISO 8601:1988.

A.3.3	Periodic date start

Alpha code: PERSTA

Attribute type: Simple

Camel case: periodicDateStart 				Data Type: Date

Definition: The start of the active period for a seasonal object (e.g. a buoy). See also “date start”.

Constraints:

Structure objects: The value should be encoded using 4 digits for the calendar year (CCYY), 2 digits for the month (MM) (e.g. April = 04) and 2 digits for the day (DD).   CCYYMMDD (full date); --MMDD (same day each year); --MM (same month each year). This conforms to ISO 8601:1988.

Other objects: If an object has either of its PERSTA/PEREND attribute values non-null, the other must also be non-null.

A.3.4	Periodic date end

Alpha code: PEREND

Attribute type: Simple

Camel case: periodicDateEnd 			Data Type: Date

Definition: The end of the active period for a seasonal object (e.g. a buoy). See also “date end”.

Constraints:

Structure objects: The value should be encoded using 4 digits for the calendar year (CCYY), 2 digits for the month (MM) (e.g. April = 04) and 2 digits for the day (DD).   CCYYMMDD (full date); --MMDD (same day each year); --MM (same month each year) This conforms to ISO 8601:1988.

Other objects: If an object has either of its PERSTA/PEREND attribute values non-null, the other must also be non-null.

A.3.5	Category of restricted area

Alpha code: CATREA

Attribute type: Simple

Camel case: categoryOfRestrictedArea							Data Type: Enumeration

Definition:  The official legal status of each kind of restricted area defines the kind of restriction(s), e.g., the restriction for a "game preserve" may be "entering prohibited", the restriction for an "anchoring prohibition area" is "anchoring prohibited".

Values:

| Code | Name | Definition |
| --- | --- | --- |
| 4 | nature reserve | a tract of land managed so as to preserve its flora, fauna, physical features, etc |
| 5 | bird sanctuary | a place where birds are bred and protected. |
| 6 | game reserve | a place where wild animals or birds hunted for sport or food are kept undisturbed for private use. |
| 7 | seal sanctuary | a place where seals are protected. |
| 10 | historic wreck area | an area around certain wrecks of historical importance to protect the wrecks from unauthorized interference by diving, salvage or deposition (including anchoring). (IHO Chart Specifications, S-4) |
| 20 | research area | an area where marine research takes place. |
| 22 | fish sanctuary | a place where fish are protected |
| 23 | ecological reserve: | a tract of land managed so as to preserve the relation of plants and living creatures to each other and to their surroundings. |

References:

Remarks:

The official legal status of each kind of restricted area defines the kind of restriction(s), e.g. the restriction for a ‘game reserve’ may be ‘entering prohibited’.  The following two categories of restricted areas are of particular relevance to Marine Protected Areas;

Environmentally Sensitive Sea Areas pertain specifically to shipping and are described in the IHO S-4 publication as Environmentally Sensitive Sea Areas (ESSA) which is a generic term used to describe a wide range of areas. These include Particularly Sensitive Sea Areas (PSSAs), Special Area designation, Emission Control Area Designation, Areas to be Avoided, No Anchoring Areas, and Mandatory Ship Reporting Systems. The IMO is the only international body responsible for designating Particularly Sensitive Sea Areas and adopting associated protective measures and submissions for their designation may only be made by Member Governments of the IMO.

There are two broad types of Environmentally Sensitive Sea Areas (ESSA):

a. those established to protect specific types of nature from disturbance (usually close inshore and established under national legislation); see S-4 section B-437.3;

b. those specifically designated in response to wider environmental considerations, potentially ‘the total environment’ (usually including some degree of risk from shipping, possibly covering extensive sea areas, and established under state, national or international legislation); see S-4 sections B- 437.4, B-437.5, B-437.6, B-437.7, B-437.9.

The relationships between the different types of ESSA and the relevant paragraphs in S-4, B-437 are tabulated as follows:

Legal basis for PSSA’s - The United Nations Convention on the Law of the Sea (UNCLOS) identifies certain categories of areas which may require higher standards of environmental protection. Article 194(5) places an obligation on parties to take measures necessary to protect and preserve rare or fragile ecosystems. Part IX of UNCLOS identifies enclosed or semi-enclosed areas, such as a gulf, bay, basin, or sea between two or more countries, as places where countries shall endeavour to coordinate management and environmental protection. Most importantly in respect of PSSA’s, however, is Article 211(6)(a) which makes provision for a State to submit to the “competent international organization” (IMO for shipping) for its approval proposals for special mandatory measures within their exclusive economic zones which require extra protection from vessel sourced pollution for recognized technical reasons.

UNCLOS thus creates an overall structure for the protection and preservation of the marine environment and a general obligation for States to implement and elaborate upon this structure through both global conventions addressing particular forms of pollution and regional agreements tailored to the requirements of discrete sea areas.

A.3.6	IUCN* Categories

Alpha code: IUCNCD

Attribute type: Simple

Camel case: categoryOfIUCN							Data Type: Enumeration

Definition:  A clearly defined geographical space, recognised, dedicated and managed, through legal or other effective means, to achieve the long-term conservation of nature with associated ecosystem services and cultural values.

Values:

| Code | Name | Definition |
| --- | --- | --- |
| 1 | Category Ia | Strict Nature Reserve |
| 2 | Category Ib | Wilderness Area |
| 3 | Category II | National Park |
| 4 | Category III | Natural Monument |
| 5 | Category IV | Habitat/Species |
| 6 | Category IV | Protected Landscape/Seascape |
| 7 | Category IV | Managed Resource Protected Area |

*International Union for Conservation of Nature and Natural Resources (IUCN) Categories

References: International Union for Conservation of Nature and Natural Resources (http://www.unep-wcmc.org/protected_areas/categories/index.html)

Remarks: Protected Area Management Categories. IUCN has defined a series of six protected area management categories, based on primary management objective. In summary, these are:

Ia. Strict Nature Reserve: protected area managed mainly for science Area of land and/or sea possessing some outstanding or representative ecosystems, geological or physiological features and/or species, available primarily for scientific research and/or environmental monitoring.

Ib. Wilderness Area: protected area managed mainly for wilderness protection Large area of unmodified or slightly modified land, and/or sea, retaining its natural character and influence, without permanent or significant habitation, which is protected and managed so as to preserve its natural condition.

II. National Park: protected area managed mainly for ecosystem protection and recreation Natural area of land and/or sea, designated to (a) protect the ecological integrity of one or more ecosystems for present and future generations, (b) exclude exploitation or occupation inimical to the purposes of designation of the area and (c) provide a foundation for spiritual, scientific, educational, recreational and visitor opportunities, all of which must be environmentally and culturally compatible.

III. Natural Monument: protected area managed mainly for conservation of specific natural feature Area containing one, or more, specific natural or natural/cultural feature which is of outstanding or unique value because of its inherent rarity, representative or aesthetic qualities or cultural significance.

IV. Habitat/Species Management Area: protected area managed mainly for conservation through management intervention Area of land and/or sea subject to active intervention for management purposes so as to ensure the maintenance of habitats and/or to meet the requirements of specific species.

V. Protected Landscape/Seascape: protected area managed mainly for landscape/seascape conservation and recreation Area of land, with coast and sea as appropriate, where the interaction of people and nature over time has produced an area of distinct character with significant aesthetic, ecological and/or cultural value, and often with high biological diversity. Safeguarding the integrity of this traditional interaction is vital to the protection, maintenance and evolution of such an area.

VI. Managed Resource Protected Area: protected area managed mainly for the sustainable use of natural ecosystems Area containing predominantly unmodified natural systems, managed to ensure long term protection and maintenance of biological diversity, while providing at the same time a sustainable flow of natural products and services to meet community needs.

A.3.7	Category of authority

Alpha code: CATAUT

Attribute type: Simple

Camel case: categoryOfAuthority						Data Type: Enumeration

Definition: the persons or the body exercising power or command; as, the local authorities of the States; the military authorities.

Values:

| Code | Name | Definition |
| --- | --- | --- |
| 1 | customs | The agency or establishment for collecting duties, tolls. (Merriam-Websters online Dictionary 23rd February 2006, amended). |
| 2 | border control | The administration to prevent or detect and prosecute violations of rules and regulations at international boundaries (adapted from Merriam-Websters online Dictionary 23rd February 2006). |
| 3 | police | The department of government, or civil force, charged with maintaining public order. (Adapted from OED) |
| 4 | port | Person or corporation, owners of, or entrusted with or invested with the power of managing a port. May be called a Harbour Board, Port Trust, Port Commission, Harbour Commission, Marine Department (NP 100 8th Edition 14 Oct 2004) |
| 5 | immigration | The authority controlling people entering a country. |
| 6 | health | The authority with responsibility for checking the validity of the health declaration of a vessel and for declaring free pratique. |
| 7 | coast guard | Organisation keeping watch on shipping and coastal waters according to governmental law; normally the authority with responsibility for search and rescue. |
| 8 | agricultural | The authority with responsibility for preventing infection of the agriculture of a country and for the protection of the agricultural interests of a country |
| 9 | military | A military authority which provides control of access to or approval for transit through designated areas or airspace. |
| 10 | private company | a private or publicly owned company or commercial enterprise which exercises control of facilities, for example a calibration area. |
| 11 | maritime police | a governmental or military force with jurisdiction in territorial waters. Examples could include Gendarmerie Maritime, Carabinierie, and Guardia Civil. |
| 12 | environmental | an authority with responsibility for the protection of the environment. |
| 13 | maritime | a national or regional authority charged with administration of maritime affairs. |

References: INT 1: unspecified; M-4: unspecified;

Remarks: No remarks.

A.3.8	Status

Alpha code: STATUS

Attribute type: Simple

Camel case: status	Data Type: Enumeration

Definition:  A state or condition with respect to prevailing circumstances. (modified from Merriam-Webster dictionary).

Values:

| Code | Label | Definition | References |
| --- | --- | --- | --- |
| 1 | permanent | intended to last or function indefinitely. (The Concise Oxford Dictionary, 7th Edition) |  |
| 2 | occasional | acting on special occasions; happening irregularly. (The Concise Oxford Dictionary, 7th Edition) | INT 1: IP 50; M-4: 473.2; |
| 3 | recommended | presented as worthy of confidence, acceptance, use, etc. (The Macquarie Dictionary, 1988) | INT 1: IN 10; M-4: 431.1; |
| 4 | not in use | no longer used for the purpose intended; disused. | INT 1: IL 14, 44; M-4: 444.7; |
| 5 | periodic/intermittent | recurring at intervals. (The Concise Oxford Dictionary, 7th Edition) | INT 1: IC 21; IQ 71; M-4: 353.3; 460.5; |
| 6 | reserved | set apart for some specific use. (adapted from The Concise Oxford Dictionary, 7th Edition) | INT 1: IN 12.9; |
| 7 | temporary | meant to last only for a time. (The Concise Oxford Dictionary) | INT 1: IP 54; |
| 8 | private | not in public ownership or operation. | INT 1: IQ 70; |
| 9 | mandatory | compulsory; enforced. (The Concise Oxford Dictionary, 7th Edition) |  |
| 11 | extinguished | no longer lit |  |
| 12 | illuminated | lit by floodlights, strip lights, etc. |  |
| 13 | historic | famous in history; of historical interest. (The Concise Oxford Dictionary, 7th Edition) |  |
| 14 | public | belonging to, available to, used or shared by, the community as a whole and not restricted to private use. (adapted from The New Shorter Oxford English Dictionary, 1993) |  |
| 15 | synchronized | occur at a time, coincide in point of time, be contemporary or simultaneous. (The New Shorter Oxford English Dictionary, 1993) |  |
| 16 | watched | looked at or observed over a period of time especially so as to be aware of any movement or change. (adapted from The New Shorter Oxford English Dictionary, 1993) |  |
| 17 | un-watched | usually automatic in operation, without any permanently-stationed personnel to superintend it. (adapted from IHO Dictionary, S-32, 5th Edition, 2814) |  |

A.3.9	Category of IMO ship report

Alpha code: CATREP

Attribute type: Simple

Camel case: categoryOfImoShipReport					Data Type: Enumeration

Definition: This describes how a ship should report to a maritime authority, including when to report, what to report and whether the format conforms to the IMO standard.

Values:

| Code | Name | Definition |
| --- | --- | --- |
| 1 | sailing plan | before or as near as possible to the time of departure from a port within a system or when entering the area covered by a system [for instance A, B, J, X etc] |
| 2 | position report | when necessary to ensure effective operation of the system |
| 3 | deviation report | when the ship’s position varies significantly from the position that would have been predicted from previous reports, when changing the reported route, or as decided by the master |
| 4 | final report | on arrival at the destination or on leaving the area covered by the system |
| 5 | dangerous goods report | when an incident takes place involving the loss or likely loss overboard of packaged dangerous goods, including those in freight containers, portable tanks, road and rail vehicles and shipborne barges, into the sea |
| 6 | harmful substances report | when an incident takes place involving the discharge or probable discharge of oil (Annex I of MARPOL 73/78) or noxious liquid substances in bulk (Annex II of MARPOL 73/78) |
| 7 | marine pollutants report | in the case of the loss or likely loss overboard of harmful substances in packaged form, including those in freight containers, portable tanks, road and rail vehicles and shipborne barges identified in the International Maritime Goods Code as marine pollutants (Annex III of MARPOL 73/78). |
| 8 | any other report | any other report should be made in accordance with the system procedures as notified in accordance with paragraph 9 of the general principles |

References: Appendix to IMO Resolution A.851(20) GENERAL PRINCIPLES FOR SHIP REPORTING SYSTEMS AND SHIP REPORTING REQUIREMENTS, INCLUDING GUIDELINES FOR REPORTING INCIDENTS INVOLVING DANGEROUS GOODS, HARMFUL SUBSTANCES AND/OR MARINE POLLUTANTS. (URL: http://www.imo.org/includes/blastDataOnly.asp/data_id%3D22635/A851(20).pdf)

Remarks: Through Resolution A.851(20), the IMO encourages authorities to require standard formats and procedures for ship reporting specified at 1 to 7 above but recognises that some authorities require amended formats and these cases are covered by 8 above.

A.3.10	Category of Cargo

Alpha code: CATCGO

Attribute type: Simple

Camel case: categoryOfCargo	Data Type: Enumeration

Definition: Types of cargo that may need to be handled differently.

Values:

| Code | Name | Definition |
| --- | --- | --- |
| 1 | bulk | Normally dry cargo which is transported to and from the vessel on conveyors or grabs |
| 2 | container | One of a number of standard sized cargo carrying units, secured using standard corner attachments and bars |
| 3 | general | Break bulk cargo normally loaded by crane |
| 4 | liquid | Any cargo loaded by pipeline |
| 5 | passenger | A fee paying traveller |
| 6 | livestock | Live animals carried in bulk |
| 7 | dangerous or hazardous | Dangerous or hazardous cargo as described by the IMO International Maritime Dangerous Goods code |

References: INT 1: unspecified; M-4: unspecified.

Remark: If item 7 is used, the nature of dangerous or hazardous cargoes can be amplified with category of dangerous or hazardous cargo.

A.3.11	Category of dangerous or hazardous cargo, or ballast

Alpha code: CATDHC

Attribute type: Simple

Camel case: categoryOfDangerousOrHazardousCargo    Data Type: Enumeration

Definition: Categories of cargo that are dangerous or hazardous to transport as defined by the International Maritime Dangerous Goods (IMDG) Code.

Values:

Remarks: Substances (including mixtures and solutions) and articles subject to the provisions of the International Maritime Dangerous Goods (IMDG) Code are assigned to one of the classes 1-9 according to the hazard or the most predominant of the hazards they present. Some of these classes are subdivided into divisions. These classes or divisions are as listed in IDs 1 : 20 above. (Adapted from IMDG code www.imo.org).

| Code | Name | Description |
| --- | --- | --- |
| 1 | Class 1; Division 1.1 | Explosives, Division 1: substances and articles which have a mass explosion hazard |
| 2 | Class 1; Division 1.2 | Explosives, Division 2: substances and articles which have a projection hazard but not a mass explosion hazard |
| 3 | Class 1; Division 1.3 | Explosives, Division 3: substances and articles which have a fire hazard and either a minor blast hazard or a minor projection hazard or both, but not a mass explosion hazard |
| 4 | Class 1; Division 1.4 | Explosives, Division 4: substances and articles which present no significant hazard |
| 5 | Class 1; Division 1.5 | Explosives, Division 5: very insensitive substances which have a mass explosion hazard |
| 6 | Class 1; Division 1.6 | Explosives, Division 6: extremely insensitive articles which do not have a mass explosion hazard |
| 7 | Class 2.1 | Gases, flammable gases |
| 8 | Class 2.2 | Gases, non-flammable, non-toxic gases |
| 9 | Class 2.3 | Gases, toxic gases |
| 10 | Class 3 | flammable liquids |
| 11 | Class 4.1 | flammable solids, self-reactive substances and desensitized explosives |
| 12 | Class 4.2 | substances liable to spontaneous combustion |
| 13 | Class 4.3 | substances which, in contact with water, emit flammable gases |
| 14 | Class 5.1 | oxidizing substances |
| 15 | Class 5.2 | organic peroxides |
| 16 | Class 6.1 | toxic substances |
| 17 | Class 6.2 | infectious substances |
| 18 | Class 7 | Radioactive material |
| 19 | Class 8 | Corrosive substances |
| 20 | Class 9 | Miscellaneous dangerous substances and articles |
| 21 | Harmful Substances in packaged form | Harmful substances are those substances which are identified as marine pollutants in the International Maritime Dangerous Goods Code (IMDG Code). Packaged form is defined as the forms of containment specified for harmful substances in the IMDG Code. (MARPOL (73/78) Annex III) |

A.3.12	Category of Relationship

Alpha code: CATREL

Attribute type: Simple

Camel case: categoryOfRelationship	Data Type: Enumeration

Definition: This attribute describes the interpretation of an “APPLIC” information object in the context of the object(s) with which it is associated.  (FC definition: This attribute expresses the level of insistence for or against a course of action)

Alternative definition: This attribute describes how the information object "APPLICABILITY" controls the relationship between other objects.

| Code | Name | Description |
| --- | --- | --- |
| 1 | prohibited | use of facility (boarding place, etc.) by vessels satisfying the conditions is prohibited |
| 2 | not recommended | use of facility (boarding place, etc.) by vessels satisfying the conditions is not recommended |
| 3 | permitted | use of facility (boarding place, etc.) by vessels satisfying the conditions is permitted but not required |
| 4 | recommended | use of facility (boarding place, etc.) by vessels satisfying the conditions is recommended |
| 5 | required | use of facility (boarding place, etc.) by vessels satisfying the conditions is required |
| 6 | included | associated information object applies to vessels satisfying the conditions |
| 7 | excepted | associated information object does not apply to vessels satisfying the conditions |

Remarks: (The conditions under which the limitation operates are those expressed by the “CHALIM” object to which this attribute is bound. - Original remark for LIMTYP to be deleted).

(The conditions under which the relationship operates are those expressed by the "APPLIC" information object to which this attribute is bound. - simple transposition of words - hard to understand)

Proposed Alternative remarks: APPLICABILTY, to which this attribute is bound, expresses the relationship between two other objects ?features?. For example it could be used to express the combined impact on a vessel of an area, to which regulations apply, and attributes like the vessel's tonnage, length or nation of registration.

Distinction: No distinctions.

A.3.13	Day of Week

Alpha code: DAYOWK

Attribute type: Simple

Camel case: dayOfWeek 	Data Type: Enumeration

Definition: Sequential day of the week.

Values:

| Code | Name | Description |
| --- | --- | --- |
| 1 | monday | monday - the day of the week before Tuesday and following Sunday |
| 2 | tuesday | tuesday - the day of the week before Wednesday and following Monday |
| 3 | wednesday | wednesday - the day of the week before Thursday and following Tuesday |
| 4 | thursday | thursday - the day of the week before Friday and following Wednesday |
| 5 | friday | friday - the day of the week before Saturday and following Thursday |
| 6 | saturday | saturday - the day of the week before Sunday and following Friday (together with Sunday forming part of the weekend) |
| 7 | sunday | sunday - the day of the week before Monday and following Saturday (together with Saturday forms part of the weekend) |

A.3.14	Jurisdiction

Alpha code: JRSDCN

Attribute type: Simple

Camel case: jurisdiction 	Data Type: Enumeration

Definition: The power, right, or authority to interpret and apply the law. (FC definition: “The jurisdiction applicable to an administrative area”).

Values:

| Code | Name | Description |
| --- | --- | --- |
| 1 | international | involving more than one country; covering more than one national area. |
| 2 | national | an area administered or controlled by a single nation. |
| 3 | national sub-division | an area smaller than the nation in which it lies. |

A.3.15	Operation

Alpha code: OPERAT

Attribute type: Simple

Camel case: operation	Data Type: Enumeration

Definition: Operations are constructs used to retrieve or set attributes. Needs to be checked

Values:

OPERAT is intended to be used in conjunction with other attributes (or sub-attributes of a complex attribute) to indicate how their values must be combined in order to describe a condition. Null attributes are ignored.

Example:
Complex attribute UKCLRN with sub-attributes UKCFIX=2.5, UKCVAR=10.00, OPERAT=1 indicates that the under-keel clearance required is the greater of 2.5 metres or 10% of the ship's draught.

| Code | Name | Description |
| --- | --- | --- |
| 1 | largest value | The largest value computed from the applicable attributes or sub-attributes |
| 2 | smallest value | The smallest value computed from the applicable attributes or sub-attributes |

A.3.16	Restriction

Alpha code: RESTRN

Attribute type: Simple

Camel case: restriction	Data Type: Enumeration

Definition: The official legal statute of each kind of restricted area.

Alternative definition: The official legal statue of each kind of restricted area defines the kind of restriction(s), e.g. the restriction for ' a game preserve' may be 'entry prohibited', the restriction for an 'anchoring prohibition' is 'anchoring prohibited'.

| Code | Name | Description |
| --- | --- | --- |
| 1 | anchoring prohibited | an area within which anchoring is not permitted. |
| 2 | anchoring restricted | a specified area designated by appropriate authority, within which anchoring is restricted in accordance with certain specified conditions. |
| 3 | fishing prohibited | an area within which fishing is not permitted. |
| 4 | fishing restricted | a specified area designated by appropriate authority, within which fishing is restricted in accordance with certain specified conditions. |
| 5 | trawling prohibited | an area within which trawling is not permitted. |
| 6 | trawling restricted | a specified area designated by appropriate authority, within which trawling is restricted in accordance with certain specified conditions. |
| 7 | entry prohibited | an area within which navigation and/or anchoring is prohibited. (adapted from IHO Dictionary, S-32, 5th Edition, 4044) |
| 8 | entry restricted | a specified area designated by appropriate authority, within which navigation is restricted in accordance with certain specified conditions. (adapted from IHO Dictionary, S-32, 5th Edition, 4366) |
| 9 | dredging prohibited | an area within which dredging is not permitted. |
| 10 | dredging restricted | a specified area designated by appropriate authority, within which dredging is restricted in accordance with certain specified conditions. |
| 11 | diving prohibited | an area within which diving is not permitted. |
| 12 | diving restricted | a specified area designated by appropriate authority, within which diving is restricted in accordance with certain specified conditions. |
| 13 | no wake | mariners must adjust the speed of their vessels to reduce the wave or wash which may cause erosion or disturb moored vessels. |
| 14 | area to be avoided | an IMO designated area to be avoided, defined as a routeing measure. (adapted from IHO Chart Specifications, M-4, 435.7) |
| 15 | Construction prohibited | the erection of permanent or temporary fixed structures or artificial islands is prohibited. |
| 16 | discharging prohibited | an area within which discharging or dumping is prohibited |
| 17 | discharging restricted | a specified area designated by an appropriate authority, within which discharging or dumping is restricted in accordance with specified conditions. |
| 18 | industrial or mineral exploration/development prohibited | an area within which industrial or mineral exploration and development are prohibited. |
| 19 | industrial or mineral exploration/development restricted | a specified area designated by an appropriate authority, within which industrial or mineral exploration and development is restricted in accordance with certain specified conditions. |
| 20 | drilling prohibited | an area within which excavating a hole on the sea-bottom with a drill is prohibited. |
| 21 | drilling restricted | a specified area designated by an appropriate authority, within which excavating a hole on the sea-bottom with a drill is restricted in accordance with certain specified conditions. |
| 22 | removal of historical artifacts prohibited | an area within which the removal of historical artifacts is prohibited. |
| 23 | cargo transhipment (lightering) prohibited | an area in which cargo transhipment (lightering) is prohibited. |
| 24 | dragging prohibited | an area in which the dragging of anything along the bottom, e.g. bottom trawling, is prohibited. |
| 25 | stopping prohibited | an area in which a vessel is prohibited from stopping. |
| 26 | landing prohibited | an area in which landing is prohibited. |
| 27 | speed restricted | an area within which speed is restricted. |

Remarks: The official legal statue of each kind of restricted area defines the kind of restriction(s), e.g. the restriction for ‘a game preserve’ may be ‘entry prohibited’, the restriction for an ‘anchoring prohibition’ is ‘anchoring prohibited’.

The complete information about the restriction(s), actually held in handbooks or other publications, may be encoded by the attribute ‘TXTDSC’. A short explanation may be given by the use of the attribute ‘INFORM’.

A.3.17	Logical Connectives

Alpha code: LOGCON

Attribute type: Simple

Camel case: logicalConnectives	Data Type: Enumeration

Definition: ????

APPLIC/VSLMSM/VSLCAR=10/VSLVAL=50.0/COMPOP=1, APPLIC/VSLMSM/VSLCAR=6/VSLVAL=10.0/COMPOP=1, APPLIC/VSLMSM/VSLCAR/LOGCON=1

Implies the limitation applies only when LOA > 50.0 and draught > 10.0

| Code | Name | Notes |
| --- | --- | --- |
| 1 | logical conjunction | all the conditions described by the other attributes of the object, or sub-attributes of the same complex attribute, are true |
| 2 | logical disjunction | at least one of the conditions described by the other attributes of the object, or sub-attributes of the same complex attributes, is true |

A.3.18	Comparison Operator

Alpha code: COMPOP

Attribute type: Simple

Camel case: comparisonOperator	Data Type: Enumeration

Definition:  Comparison operators are standard constructs that are used to compare two values.

| Code | Name | Description |
| --- | --- | --- |
| 1 | greater than | The value of the left value is greater than that of the right.(http://en.wikipedia.org/wiki/Logical_connective) |
| 2 | greater than or equal to | The value of the left expression is greater than or equal to that of the right. (http://en.wikipedia.org/wiki/Logical_connective) |
| 3 | less than | The value of the left expression is less than that of the right. (http://en.wikipedia.org/wiki/Logical_connective) |
| 4 | less than or equal to | The value of the left expression is less than or equal to that of the right. (http://en.wikipedia.org/wiki/Logical_connective) |
| 5 | equal to | The two values are equivalent. (adapted http://en.wikipedia.org/wiki/Logical_connective) |
| 6 | not equal to | The two values are not equivalent. (adapted http://en.wikipedia.org/wiki/Logical_connective) |

Remark: The definition of COMPOP provides the relation between the value given in the model and the real ship's value.

A.3.19	Category of Vessel Registry

Alpha code: VESREG

Attribute type: Simple

Camel case: categoryOfVesselRegistr	Data Type: Enumeration

Definition: The locality of vessel registration or enrolment relative to the nationality of a port, territorial sea, administrative area, exclusive zone or other location.

| Code | Name | Description |
| --- | --- | --- |
| 1 | domestic | The vessel is registered or enrolled under the same national flag as the port, harbour, territorial sea, exclusive economic zone, or administrative area in which the object that possesses this attribute applies or is located. |
| 2 | foreign | The vessel is registered or enrolled under a national flag different from the port, harbour, territorial sea, exclusive economic zone, or other administrative area in which the object that possesses this attribute applies or is located. |

Remarks: No remarks.

Comment: This attribute is proposed to be bound to APPLIC.

Distinction: No distinctions.

A.3.20	Category Of Vessel

Alpha code: CATVES

Attribute type: Simple

Camel case: categoryOfVessel	Data Type: Enumeration

Definition: Types of vessels categorised according to their intended use.  (Tony)

| Code | Name | Description |
| --- | --- | --- |
| 1 | general cargo vessel | a vessel designed to carry general cargo |
| 2 | container carrier | a vessel designed to carry ISO containers |
| 3 | tanker | a vessel designed to carry bulk liquid or gas, including LPG and LNG |
| 4 | bulk carrier | a vessel designed to carry bulk solid material |
| 5 | passenger vessel | a vessel designed to carry passengers; often a cruise ship |
| 6 | roll-on roll-off | a vessel designed to allow road vehicles to be driven on and off; often a ferry |
| 7 | refrigerated cargo vessel | a vessel designed to carry refrigerated cargo |
| 8 | fishing vessel | a vessel designed to catch or hunt fish |
| 9 | service | a vessel which provides a service such as a tug, anchor handler, survey or supply vessel |
| 10 | warship | a vessel designed for the conduct of military operations |
| 11 | towed or pushed composite unit | ??? additional to FC |
| 12 | tug or tow | ??? additional to FC |

A.3.21	Vessels Characteristics

Alpha code: VESCAR

Attribute type: Simple

Camel case: vesselsCharacteristics	Data Type: Enumeration

Definition: The value of a particular characteristic such as a dimension or tonnage of a vessel.

| Name | Type | Notes |
| --- | --- | --- |
| 1 | length overall |  |
| 2 | length waterline | The ship's length measured at the waterline (L.W.L.). (http://en.wikipedia.org/wiki/Ship_measurements; 24 July 2010) |
| 3 | breadth | The width or beam of the vessel. (Adapted from http://en.wikipedia.org/wiki/Ship_measurements; 24 July 2010) |
| 4 | draught | The depth of water necessary to float a vessel fully loaded. (http://en.wikipedia.org/wiki/Ship_measurements; 24 July 2010) |
| 5 | height | The height of the highest point of a vessel's structure (e.g. radar aerial, funnel, cranes, masthead) above her waterline. (UKHO NP100/2009) |
| 6 | displacement tonnage | A measurement of the weight of the vessel, usually used for warships. (Merchant ships are usually measured based on the volume of cargo space; see tonnage). Displacement is expressed either in long tons of 2,240 pounds or metric tonnes of 1,000 kg. Since the two units are very close in size (2,240 pounds = 1,016 kg and 1,000 kg = 2,205 pounds), it is common not to distinguish between them. To preserve secrecy, nations sometimes misstate a warship's displacement. (http://en.wikipedia.org/wiki/Ship_measurements; 24 July 2010) |
| 7 | displacement light | The weight of the ship excluding cargo, fuel, ballast, stores, passengers, and crew, but with water in the boilers to steaming level. (http://en.wikipedia.org/wiki/Ship_measurements; 24 July 2010) |
| 8 | displacement loaded | The weight of the ship including cargo, passengers, fuel, water, stores, dunnage and such other items necessary for use on a voyage, which brings the vessel down to her load draft. (http://en.wikipedia.org/wiki/Ship_measurements; 24 July 2010) |
| 9 | deadweight tonnage | The difference between displacement, light and displacement, loaded. A measure of the ship's total carrying capacity. (http://en.wikipedia.org/wiki/Ship_measurements; 24 July 2010) |
| 10 | gross tonnage | The entire internal cubic capacity of the ship expressed in tons of 100 cubic feet to the ton, except certain spaces with are exempted such as: peak and other tanks for water ballast, open forecastle bridge and poop, access of hatchways, certain light and air spaces, domes of skylights, condenser, anchor gear, steering gear, wheel house, galley and cabin for passengers. (http://en.wikipedia.org/wiki/Ship_measurements; 24 July 2010) |
| 11 | net tonnage | Obtained from the gross tonnage by deducting crew and navigating spaces and allowances for propulsion machinery. (http://en.wikipedia.org/wiki/Ship_measurements; 24 July 2010) |
| 12 | panama canal | Panama Canal / Universal measurement System net Tonnage |
| 13 | suez canal | Suez canal net tonnage system. |
| 14 | length at waterline | The ship's length measured at the waterline (L.W.L.). (http://en.wikipedia.org/wiki/Ship_measurements; 24 July 2010) |

A.3.22	Time Reference

Alpha code: TMEREF

Attribute type: Simple

Camel case: timeReference	Data Type: Enumeration

Definition:

| Code | Name | Description |
| --- | --- | --- |
| 1 | UTC | UTC: Co-ordinated Universal Time |
| 2 | LT | LT: Local time |

A.4	Complex Attributes

A.4.1	Day of the Week Range

Alpha code: DYOFWK

Attribute type: Complex Attribute

Camel case: dayOfWeekRange

Definition: see Day of Week

Remarks:

A range of days of the week, expressed as a complex type whose sub-attributes are the days of the week that begin and end the range. There is only 1 sub-attribute, which gives the day of the week. The multiplicity of this attribute must be exactly 2. The first instance gives the beginning day of the range and the second the ending day (both are included in the range).

Though a range of days of the week that cross the week boundaries is possible (e.g., “Thursday to Monday”) the use of ranges that cross week boundaries is discouraged.

Example:
To code the range “Monday through Friday” use the sequence: DYOFWK=1, DYOFWK=5.

| Name | Type | Notes |
| --- | --- | --- |
| dayOfWeek | enumeration |  |

Relationships

| Multiplicity | Association |
| --- | --- |
| 0..1 | dayOfWeekRange. workingSchedule |

A.4.2	Information

Alpha code: ???

Attribute type: Complex Attribute

Camel case: information

| Name | Type | Multiplicity | Association | Notes |
| --- | --- | --- | --- | --- |
| information | characterstring | 0..* | information. InformationType. |  |
| language | characterstring | 0..* | information. FeatureType. | ISO 639-2 value |

Relationships

| Multiplicity | Association |
| --- | --- |
| 0..* | information. InformationType. |
| 0..* | information. FeatureType. |

A.4.3	Notice Time

Alpha code: ???

Attribute type: Complex Attribute

Camel case: noticeTime

| Name | Type | Notes |
| --- | --- | --- |
| noticeTimeHours | real |  |
| noticeTimeText | characterstring |  |
| operation | enumeration |  |

Relationships

| Multiplicity | Association |
| --- | --- |
| 1..* | noticeTime serviceHours |

A.4.4	Object Name

Alpha code: ???

Attribute type: Complex Attribute

Camel case: objectName

| Name | Type | Notes |
| --- | --- | --- |
| language | characterstring | ISO 639-2 value |
| textValue | characterstring |  |

Relationship

| Multiplicity | Association |
| --- | --- |
| 0..* . | objectName. InformationType |
| 0..* . | objectName. FeatureType |

A.4.5	Textual Description

Alpha code: ???

Attribute type: Complex Attribute

Camel case: textualDescription

| Name | Type | Notes |
| --- | --- | --- |
| language | characterstring | ISO 639-2 value |
| textualDescription | characterstring | links to external file |

Relationships

| Multiplicity | Association |
| --- | --- |
| 0..*. | textualDescription. FeatureType |
| 0..* . | textualDescription. InformationType |

A.4.6	Under Keel Clearance

Alpha code: ???

Attribute type: Complex Attribute

Camel case: underKeelClearance

| Name | Type | Notes |
| --- | --- | --- |
| operation | enumeration |  |
| underKeelAllowanceFixed | real |  |

Relationships

| Multiplicity | Association |
| --- | --- |
| 0..1 | UnderkeelAllowanceVariable. underKeelAllowance |
| 0..1 | underKeelAllowance Applicability |

A.4.7	Vessels Measurements

Alpha code: ???

Attribute type: Complex Attribute

Camel case: vesselsMeasurements

| Name | Type | Notes |
| --- | --- | --- |
| comparisonOperator | enumeration |  |
| vesselsCharacteristics | enumeration |  |
| vesselsCharacteristicsUnit | enumeration |  |
| vesselsCharacteristicsValue | real |  |

Relationship

| Multiplicity | Association |
| --- | --- |
| 0..* | vesselsMeasurements Applicability . |

A.4.8	Working Hours Of Day

Alpha code: ???

Attribute type: Complex Attribute

Camel case: workingHoursOfDay

Comment: If there are a number of working time periods in a day Sub-attributes TIMSTW and TIMENW must be repeated and be in mutual correspondence.

For example, Work time: 0800-1200, 1400-2000 must be encoded as:

TIMSTW=0800 TIMSTW=1400 and TIMENW=1200 TIMENW=2000

| Name | Type | Notes |
| --- | --- | --- |
| timeOfEndOfWork | time |  |
| timeOfStartOfWork | time |  |
| timeReference | enumeration |  |

Relationship

| Multiplicity | Association |
| --- | --- |
| 0..1 | workingHoursOfDay. workingSchedule |

A.4.9	Working Schedule

Alpha code: ???

Attribute type: Complex Attribute

Camel case: workingSchedule

Note: Duplicates or overlaps are not permitted

| Name | Type | Notes |
| --- | --- | --- |
| dayOfWeek | enumeration | Duplicates or overlaps are not permitted |

Relationship

| Multiplicity | /Association |
| --- | --- |
| 0..1 | dayOfWeekRange. workingSchedule. |
| 0..1 | workingHoursOfDay. workingSchedule. |
| 1..* . | workingSchedule. ServiceHours |

# Text boxes

Blank Page