GEO OBJECT CLASSES - NAV MARK

Object Class:	Automatic Identification System as an aid to navigation

Acronym: aisatn		Code: ?

Set Attribute_A:	DATEND; DATSTA; mmsico; NOBJNM; OBJNAM; STATUS; VALMXR;

Set Attribute_B:     	INFORM; NINFOM; NTXTDS; SCAMAX; SCAMIN; TXTDSC;

Set Attribute_C:     	RECDAT; RECIND; SORDAT; SORIND;

Definition:

An AIS transmitter placed on a navigational mark as an aid to navigation.

References:

INT 1: 	;

M-4: 	;

Remarks:

This object class is expected to be required as AIS stations are increasingly deployed as aids to navigation.  An AIS transmitter is viewed logically as simply another equipment object like a light, bell or RACON, which is mounted on the structure.

Distinction:

Object Class:	Light

Acronym: LIGHTS		Code: 75

Light        	LIGHTS	75

Set Attribute_A:	CATLIT; COLOUR; DATEND; DATSTA; EXCLIT; HEIGHT; LITCHR; ltelev LITVIS; MARSYS; MLTYLT; NOBJNM; OBJNAM; ORIENT; PEREND; PERSTA;  SECTR1; SECTR2; SIGGRP; SIGPER; SIGSEQ; STATUS; VERACC; VALNMR; VERDAT;

Set Attribute_B:	INFORM; NINFOM; NTXTDS; SCAMAX; SCAMIN; TXTDSC;

Set Attribute_C:	RECDAT; RECIND; SORDAT; SORIND;

Definition:

A luminous or lighted aid to navigation. (adapted from IHO Dictionary, S-32, 5th Edition, 2766)

References:

INT 1: 	IP 1-30.3, 40-65;

M-4:	470-473.5; 475-475.7; 476-478,5;

Remarks:

A light may be fixed on a buoy, beacon, tower etc. These are separate objects.

Distinction: 	beacon, cardinal; beacon, isolated danger; beacon, lateral; beacon, safe water; beacon special purpose/general; buoy, cardinal; buoy, installation; buoy, isolated danger; buoy, lateral; buoy, safe water; buoy, special purpose/general; light vessel; light float;

Object Class:	Radar transponder beacon

Acronym: RTPBCN		Code: 103

Radar transponder beacon    	RTPBCN	103

Set Attribute_A:	alrsrn; CATRTB; DATEND; DATSTA; NOBJNM; OBJNAM; RADWAL; SECTR1; SECTR2; SIGGRP; SIGSEQ; STATUS; VALMXR;

Set Attribute_B:     	INFORM; NINFOM; NTXTDS; SCAMAX; SCAMIN; TXTDSC;

Set Attribute_C:     	RECDAT; RECIND; SORDAT; SORIND;

Definition:

A transponder beacon transmitting a coded signal on radar frequency, permitting an interrogating craft to determine the bearing and range of the transponder. Also called racon. (IHO Dictionary, S-32, 5th Edition, 4137)

References:

INT 1: 	IS 2-3;

M-4: 	486.1-3;

Remarks:

The object class radar transponder beacon is only used to encode the technical equipment independent of the structure on which it is located (e.g. a beacon, light-vessel or tower).

Distinction:	radar line; radar range; radar station;

Object Class:     Service area

Acronym: svcare			Code: ?

Anchorage area      	ACHARE	4

Set Attribute_A:	catsvc; DATEND; DATSTA; NOBJNM; OBJNAM; PEREND; PERSTA; RESTRN; STATUS;

Set Attribute_B:     	INFORM; NINFOM; NTXTDS; SCAMAX; SCAMIN; TXTDSC;

Set Attribute_C:     	RECDAT; RECIND; SORDAT; SORIND;

Definition:

.

References:

M-3: 	Chapter C Section 2.2

Remarks: This defines the area in which a service to shipping is available.

Distinction: 	?

Comment:

Object Class:     Blank

Acronym:			Code: ?

Anchorage area      	ACHARE	4

Set Attribute_A:	xxxxxx; DATEND; DATSTA; NOBJNM; OBJNAM; PEREND; PERSTA; RESTRN; STATUS;

Set Attribute_B:     	INFORM; NINFOM; NTXTDS; SCAMAX; SCAMIN; TXTDSC;

Set Attribute_C:     	RECDAT; RECIND; SORDAT; SORIND;

Definition:

.

References:

M-3: 	Chapter C Section 2.2

Remarks:

Distinction: 	?

Comment:

# Text boxes

# SNPWG 6/010